## Slide 1: Graduation Project 2 Structural Analysis and Design of Public health center
An-Najah National University
Faculty of Engineering
Civil Engineering Department
Supervisor: Dr. Munther Diab.
Prepared By:
Haya Omariah Sora Salman Farah Hamadoni

## Slide 2
Outlines:
Vertical load analysis
Lateral load analysis
Dynamic design

## Slide 3: materials
1. Reinforced concrete
Unit weight of reinforced concrete = 25 KN/m3.
Slabs , beams 24f’c
Columns 28 f’c
2. Reinforcement Steel:
Yielding strength (fy) = 420MPa.

## Slide 4: Load assumptions Dead load

## Slide 5: Super imposed load

## Slide 6: Live load

## Slide 7: Live load

## Slide 8: Weight of wall
The wall height = 3.64 m
Wall weight = wall height *Σ (thickness of layer * unit weight for each layer)
= (0.05) (26) + (0.15) (25) + (0.1) (12) =6.25 KN /m2 =3.64 *6.645 KN /m =22.75 KN/m

## Slide 9: Modifiers
Slab Modifiers
Beams Modifiers
Column Modifiers

## Slide 10: Slab Modifiers
To convert the ribbed slab into solid slab.
To make it one way instead of two way.

## Slide 11: Slab Modifiers
Finding equivalent slab thickness
Determining the ratio of actual slab to existing (SAP)slab.

## Slide 12: Slab Modifiers

## Slide 13: Slab Modifiers
For example:

## Slide 14: Beams Modifiers
Main Beams
Secondary Beams

## Slide 15: Main Beam Modifiers

## Slide 16: Secondary Beam Modifiers

## Slide 17: Column Modifiers

## Slide 18: SLAB :

## Slide 19: SLAB :
Strip NO.3:
The resulting moment (KN.m):
1D
3D

## Slide 20: BEAM :
BEAM NO.1:
The resulting moment (KN.m):
1D
3D

## Slide 21: BEAM :
BEAM NO.6:

## Slide 22: Dynamic Analysis
Introduction

## Slide 23: Codes
IBC
UBC 97
Euro code

## Slide 24: Dynamic Analysis Methods
Equivalent Static Method.
Response Spectrum Analysis (Modal Analysis).
Time History Analysis.

## Slide 25: 3D Model Modifiers
Slab Modifiers : to convert it to ribbed slab and one way slab
Beams Modifiers : to prevent replication , to reduce the mass.

## Slide 26: Slab Modifiers

## Slide 27: Main Beams Modifiers

## Slide 28: Main Beams Modifiers
For example:
Mass modifier for a beam = (0.5 – 0.2)/0.5 = 0.6

## Slide 29: Secondary Beams Modifiers

## Slide 30: Period of 3D Model

## Slide 31: Modal Mass Participation Ratio

## Slide 32: Equivalent lateral force method

## Slide 33: Steps to determine base shear
Determine Z:
Z = 0.20

## Slide 34: 2. Determine Ss and S1:
Ss =mapped 5% damped, spectral response acceleration parameter at 0.2sec.≈2.5Z = 2.5*0.2 = 0.5
S1 =mapped 5% damped, spectral response acceleration parameter at period of 1sec.≈1.25Z = 1.25*0.2 = 0.25

## Slide 35: 3. Determine Site Soil Classification: soft clay soil → Soil type E.

## Slide 36: 4. Determine Fa and Fv based on site Soil Classification

## Slide 37: 4. Determine Fa and Fv based on site Soil Classification

## Slide 38: 5. Determine SMs and SM1
SMs = the maximum considered earthquake spectral response accelerations for short period.
SMs = Fa *Ss = 1.7*0.5=0.85
SM1 = the maximum considered earthquake spectral response accelerations for 1- second period.
SM1 = Fv*S1 = 3*0.25 = 0.75

## Slide 39: 6. Calculate the design spectral response acceleration (SDS, SD1):
SDs , is the design ,5% damped,spectral response acceleration for 0.2sec period.
SDs = SMs = 0.85
SD1 , is the design ,5% damped,spectral response acceleration at aperiod of 1sec..
SDs = SM1 = 0.75

## Slide 40
To be noted that values obtained from SAP are not the same as ours, and this is due to errors in SAP 16 programming, to overcome this problem, SAP values are been taken.
Fa= 0.9, Fv= 2.4
SMS = Fa × SS = 0.9×0.5 =0.45
SM1 = Fv × S1 =2.4 × 0.25 = 0.6
SDS = SMS =0.45
SD1 = SM1 =0.6

## Slide 41: 7. Determine the Seismic Design Category: Seismic design category is D.

## Slide 42
Categories D (high seismicity): Ss and S1 should not be less than 1.5g and 0.6g (to be modified for 10%) respectively.
Ss and S1 less than 1.5g and 0.6g (to be modified for 10%) respectively, So use 1.5g and 0.6g
(2% probability of exceedance)
Ss = 1.5
S1 =0.6
SMS = Fa × SS = 0.9×1.5 = 1.35
SM1 = Fv × S1 =2.4 × 0.6 = 1.44

## Slide 43
(To be modified for 10% probability of exceedance)
SDS =(2/3) × SMS = 0.9
SD1 =(2/3) × SM1 =0.96

## Slide 44: 8. Determine risk category:

## Slide 45: 9. Importance Factor ( I )

## Slide 46: 10. Determine response modification factor (R)

## Slide 47: Block 1:

## Slide 48
V= Cs*W
Cs =seismic response coefficient = SDs*I/R .
Cs = 0.9*1.5/5=0.27sec.
W = 8077.7365 KN.
V=0.27*8077.7365=2180.99 KN.

## Slide 49
V | Fx | WΧ hnK | hnK | Weight | Story
1272.5 | 1272.5 | 24222.1 | 7.28 | 3327.2095 | 2
2180.95 | 908.45 | 17291.9 | 3.64 | 4750.527 | 1
 |  | SUM=41514 |  |  | 

## Slide 50: By SAP:

## Slide 51: By SAP:

## Slide 52: By SAP:

## Slide 53: VSAP = 2180.826KN. Vnanual=2180.99KN. %of differences = 0.0075%

## Slide 54
% of differences | Base shear manual | Base shear(SAP) | Story
3 | 1272.5 | 1235.518 | 2nd floor
0.009 | 2180.95 | 2180.75 | 1st floor

## Slide 55: Period (T)Check: TSAP =0.84625 seconds

## Slide 56: Rayleigh method T=0.8497sec. %of differences=0.4%

## Slide 57: Modal mass participation ratio

## Slide 58: Response spectrum analysis method
Response spectrum function:

## Slide 59: Response spectrum analysis method
Load cases :
Earth quake –x
* Scale factor= =2.943 for U1

## Slide 60: Response spectrum analysis method
Modal mass participating ratio

## Slide 61: Response spectrum analysis method
More than 90% of modal mass participation ratio
For regular structure VRS ≥ 0.9 VSF
For irregular structure VRS ≥ VSF

## Slide 62: Response spectrum analysis method
Base shear from SAP = 2082.101 KN

## Slide 63: Response spectrum analysis method
Story | Base shear (response spectrum) | Base shear (equivalent )
2nd floor | 924.585 | 1235.518
1st floor | 2082.1 | 2180.75

## Slide 64
Dynamic Design

## Slide 65: Assumptions for Design:
Analysis and design are according to ACI-318-11.
IBC 2012 code for seismic loads (Using Equivalent lateral force method)
Loads are gravity and seismic loads.

## Slide 66: Clarification for the SAP default combinations
Load combinations :
combination 1 = 1.4D
combination 2 = 1.2D+1.6L
combination 3 = 1.2D+1L+1 eq-x
combination 4 = 1.2D+1L+1 eq-y
combination 5= 1.2D+1L-1 eq-x
combination 6 = 1.2D+1L-1 eq-y
combination 7 = 0.9D+1 eq-x
combination 8 = 0.9D+1 eq-y
combination 9 = 0.9D - 1 eq-x
combination 10 = 0.9D - 1 eq-y

## Slide 67: Structural Materials:
Concrete:
* Slabs and beams → fc` = 24 MPa
*Columns → fc` = 28 MPa
Steel (Rebar, shrinkage mesh and stirrups):
*Yielding strength (Fy) = 420 MPa

## Slide 68: 3D Model : Block 1:

## Slide 69: Slab modifiers
To convert it to ribbed slab
One way slab
Cracks
*Torsional constant: 0.35
*Moment of inertia about 2 axis: 0.35
*Moment of inertia about 3 axis: 0.35

## Slide 70: Slab modifiers

## Slide 71: Beam and Column modifiers
Also, for beams and columns the modifiers are as follows:
Beams:
Torsional constant: 0.35
Moment of inertia about 2 axis: 0.35
Moment of inertia about 3 axis: 0.35
Columns:
Torsional constant: 0.7
Moment of inertia about 2 axis: 0.7
Moment of inertia about 3 axis: 0.7

## Slide 72: Design of slabs
The structural system of the Public health center is one way ribbed
slab(20 cm) with drop beams.

## Slide 73: Design of slabs Analysis and Design for flexure
The values of M11 for the first floor

## Slide 74: Design of slabs Analysis and Design for flexure
Strip NO.1 :

## Slide 75: Design of slabs Analysis and Design for flexure
Strip NO.1 :

## Slide 76: Design of slabs Analysis and Design for flexure
Section in slab :

## Slide 77: Design Beams for Flexure

## Slide 78: Design Beams for Flexure

## Slide 79: Design Beams for Flexure
For maximum negative moment.

## Slide 80: Design Beams for Flexure
For maximum positive moment.
Compare with SAP results.

## Slide 81: Design Beams for Flexure

## Slide 82: Design Beams for Flexure
Now we can trust SAP results in flexure.

## Slide 83: Design Beams for Shear
Frame 6 :
Vu is obtained from SAP = 210.212 kN.

## Slide 84: Design Beams for Shear
Frame 6 :
compare with SAP results
SAP in Shear !!!

## Slide 85: Design Requirement
Bottom steel at face of joint ≥ 1/3 top steel at face of joint.
Bottom or top steel at any section ≥ 1/5 top steel at face of joint .
Stirrups shall be computed based on shear force Vu and shall have a maximum spacing as shown in the figure .

## Slide 86: Design Requirement

## Slide 87: Design Requirement
where:
s2 = d/2 d = effective depth of beam. ds = diameter of steel bar used for stirrup. db = diameter of steel bar. ld = development length of steel bars in tension

## Slide 88: Example : Frame 6
Frame No.6 |  |  | 
Span No. | Location | Area of Steel (mm2) | No. of bars
Span No. 1 | Left End (Top) | 2064 | 7Ø20
 | Left End (Bottom) | 1328 | 7Ø16
 | Middle End (top) | 527 | 3Ø16
 | Middle End (Bottom) | 708 | 4Ø16
 | Right End (Top) | 1969 | 7Ø20
 | Right End (Bottom ) | 807 | 4Ø16

## Slide 89: Example : Frame 6
Bottom steel at face of joint ≥ 1/3 top steel at face of joint.
As 1 = 2064
1/3 As 1 = 688
1328 > 688 … ok
As 2 = 1969
1/3 As 2 = 656.33
807 > 656.33 … ok

## Slide 90: Example : Frame 6
Bottom or top steel at any section ≥ 1/5 top steel at face of joint .
1/5 As 1 = 412.8
1/5 As 2 = 393.8
527 and 705 are lager than 412.8 … ok

## Slide 91: Example : Frame 6

## Slide 92: Example : Frame 6
Determining the spacing

## Slide 93: Example : Frame 6
Check max spacing

## Slide 94: Example : Frame 6
S1 = 100 mm for Ø12 and S1 = 110 for larger diameters
use S1 =100mm for both cases.
Use 1 Ø 10 @ 10 cm
S2 = d/2 = 440/2 = 220 mm
Use 1Ø10 @ 22cm

## Slide 95: Column design

## Slide 96: Column design

## Slide 97: Column design

## Slide 98
LS =1.3Ld=1.3*765=994.5mm≈1m which is the distance of splicing.
Use 2Ø10/250mm stirrups in the middle of column.
Use 2Ø10/100mm stirrups in the ends of column (550)of height for each end).