## Slide 1: A conceptual framework for the development of core-set of Hazardous waste management indicators
Prepared by:
Iman Sinokrot
Maram Sbitany
Supervisor:
Prof. Amer El-Hamouz

## Slide 2: Outlines:
Introduction
Standards and constrains.
Literature review.
Methodology
Results and Discussion
Conclusions
Recommendations.

## Slide 3: Introduction:
Wastes are classified as being hazardous when they have one or more hazardous properties, including explosive, irritant, flammable, toxic, oxidizing, harmful, and carcinogenic and any harmful effects on the environment and human health.
Palestine has poor hazardous waste management because of the absence of compulsory force in the implementation of laws on the management of hazardous wastes in addition to political situation where is no hazardous waste treatment facility is allowed to be constructed.

## Slide 4: Basel convention:
The Basel Convention, ratified in 1989, is one of the most important international environmental treaties. It aims to limit and regulate the movement of hazardous wastes between countries, especially from developed to developing countries. It aims to reduce the amount of hazardous wastes generated, treated and disposed of in the same place. And provide assistance to developing countries and to countries with a changing economy.
Palestine has become a party to the Basel Convention since April 2015. Since then, Palestine must take all necessary measures to implement the provisions of the Convention and to harmonize its conditions, laws and national legislation in accordance with these requirements. Ensure that trans-boundary movements of hazardous wastes are minimized, in a manner that protects both human health and the environment.

## Slide 5: Problem Definition:
With the very limited environmental resources and the rapid population growth in the State of Palestine a high pressure is exerted on the environment mainly due to the increase of waste generation and relatively the increase of the amount of hazardous wastes (HZW) without proper management.
This study aims to establish Palestinian HZW information network and build up a group of indicators so we can get accurate data including HZW generated, managed and the HZW which has not managed based on Basel convention.

## Slide 6: Objectives:
The main objective of this project is to formulate HZW indicators that will assist decision makers in building an environmentally sound management plans and decisions leading to effective management of HZW

## Slide 7: Standards and constraints:
Hazardous waste standards and constraints:
The RCRA establishes basic standards for the management of hazardous wastes for people who produce hazardous wastes called hazardous waste generators. The generator regulations ensure that hazardous wastes are identified and handled safely to protect human health and the environment, while minimizing interference with daily business processes.
Israel's restrictions on the disposal and management of hazardous waste:
The Israeli occupation does not only destroy the Palestinian territories and the Palestinian people politically, security and economically, but extends its aggression to destroy the environmental elements and the environmental balance existing in the Palestinian territories.

## Slide 8
The smuggling of hazardous wastes into the Palestinian territories is one of the most serious Israeli violations against the Palestinian environment and violation of all human rights and internationally recognized conventions on the environment. Smuggling attempts continue to be frequent and have become increasingly frequent in recent years.

## Slide 9: Hazardous waste management hierarchy:
The idea of hierarchy emerged from the realization that the disposal of untreated hazardous waste was a mistake. The toxic substances deposited in the soil and through the soil, have migrated to the ground and surface waters, and were emitted into the atmosphere. Such leaflets pose a potentially serious threat to human health and the environment. The natural consequence was hierarchy - the arrangement of waste management options according to their assumed environmental protection capacity.

## Slide 11: Methodology:
The research is comprised of two major stages. The first stage was to adopt a methodology to identify typical indicators, the second stage is to collect data from different sectors, analyze them and use indicators to denote the level of hazardous waste management of the industry.
The methodology has been tested on three sectors in the West Bank; data is collected by interviews and field observations.
First, the methodology was tested on the pharmaceutical sector industry using two companies, after indicators refinement then it was applied to other three pharmaceutical companies; In addition two other industrial sectors were chosen, dry cleaning and universities.

## Slide 12
To create the HZW indicators, literature was reviewed and a number of indicators proposed in other studies were revisited for the suitability of using them in our study. They are shown in figure

## Slide 13
Input and output indicators
Environmental indicators
Technology indicators
Energy indicators
Storage indicators
Economical indicators
Emission/ waste indicators
Transportation indicators

## Slide 14: Pharmaceutical sector
Hazardous wastes in this sector are classified as Y2 and Y3 of the Basel Convention.
For privacy and confidentiality, actual names of companies will not be presented and are given imaginary names A to D.

## Slide 15
Chart: Palestinian Pharmaceutical Market
| company A | company C | company D | company B and other companies
Sales | 0.45 | 0.27 | 0.17 | 0.11

## Slide 16: Input and output indicators:
 | Company (A) | Company (B) | Company (C) | Company (D)
Total materials that bought by the company | 186,286 Kg | Unavailable* | Unavailable* | Unavailable*
Imports of hazardous materials | 11,450 Kg | Unavailable* | 7000 kg | Unavailable*
Total hazardous waste | 120 Kg | Unavailable* | 10488 kg | 38926.81 kg

## Slide 17: Technological indicators:
The origin of machines |  |  |  | 
 | Company A | Company B | Company C | Company D
The origin of machines | Germany and Taiwan | Germany, Italy, India and China | Germany, Taiwan and India | Germany, India, China, France and Italy

## Slide 18: Storage indicators
Environmental indicators

## Slide 19: Water and wastewater
Water system |  |  |  | 
 | Company (A) | Company (B) | Company (C) | Company (D)
Water consumed (m3/year). | 6000 (m3/year) | 7000 (m3/year) | 7440 (m3/year) | 6552 (m3/year)
The usage of treated water | * | In production and other uses. | * | *
Water consumed / hazardous waste generated (m3/kg) | 50 m3/kg | *unavailable | 0.071 m3/kg | 0.153 m3/kg

## Slide 20: Emissions-waste indicators:
 |  |  | Company A | Company B | Company D
Measured gas | Maximum allowed(ppm) | Expected values(ppm) | Measured values(ppm) | Measured values(ppm) | Measured values(ppm)
SO2 | 20 | 1146 | 0 | 0 | 0
CO | 200 | 436 | 65 | 0 | 58.26
NOx | 200 | 326 | 55.6 | 53.64 | 10.1

## Slide 21: Energy indicators
Company A uses 100 KW per 1 kg of hazardous waste generated as solar energy and 850 KW per 1 kg as electrical energy, which indicates a small amount of hazardous waste generated by company A.
However, company C uses 2 KW per 1 kg of hazardous waste, and company D uses 4.2 KW per 1 kg of hazardous waste. As we see company C and company D have almost equal values due to the proximity of the quantities of hazardous waste to each of them, which is much larger than the quantity in the company A.

## Slide 22: Economic indicators
Last but not least, as for the economic concerns for company A, the transportation of wastes by Tabeb Company costs 8000 NIS, 300 NIS for incineration and 450 NIS for the shipments. But there is no enough information about the costs for company B.
As for company C, it pays 3000 to 4000 NIS to dispose of all hazardous waste, on the other hand company D transports 2 shipments annually and every shipment contains 10 to 12 tanks and every tank costs 2000 NIS by Tabeb, which means it cost approximately 40000 to 48000 Nis annually.

## Slide 23: Pharmaceutical sector management
The purchase of specific quantities of hazardous materials to meet the purpose of manufacturing without the existence of excess materials.
Manufacture specified quantities that needed by the market, based on a market study.
There should be units for waste water treatment, and not be used again in the manufacturing process; it can be used in other uses less important such as baths, laundries, etc.
As for machines, it was found that there is an improvement in the efficiency of Chinese and South-East Asian machines and at the appropriate prices to fit the budget of companies.

## Slide 24: Dry Cleaning Sector:
Hazardous wastes in this sector are classified as Y41 of the Basel convention.

## Slide 25: Input indicators
It was found that there are 30 dry cleaning stores in the west bank; 18 of them in Ramallah , 2 in Nablus , 3 in Tulkarem and the rest in Jenin and other cities, A 320 kg machine is distributed to each new store, in addition to a barrel contains 320 kg of PERC.

## Slide 26: Transportation indicators
it has been shown that there is no special treatment in moving PERC to the stores, indicating a poor handling of these materials due to their danger to the environment and the carriers of these materials.

## Slide 27: Output indicators
There are bimonthly orders where every two months there is a hazardous waste of about 50 kg which is compensated, but unfortunately the cleaning is done by towing and disposing of it with normal waste without any treatment.

## Slide 28
A comparison has been done with Haifa's studies in this sector, and it was found that in Haifa the amount of hazardous waste is far more than the hazardous waste in the West Bank.
After calculations, it was found that the total amount of hazardous waste in the west bank equals to 9 tones/year, and the total amount of hazardous waste in Haifa referred to their studies equals to 8759 tones/year.

## Slide 29
After looking at the area of the city of Haifa and the West Bank, we find that the area of Haifa is equal to 63.67 km2, and the area of the West Bank is equal to 5295 km2. If we calculate the amount of hazardous waste per 1 km2, we find that hazardous waste in Haifa = 137569 kg/year per 1 km2 and hazardous waste in the West Bank = 1.7 kg/year per 1 km2.
After examining the population of each of them, it was found that the population of Haifa city is equal to 272181 people, in addition to 300 people who live around the city, while the population of the West Bank is equal to 2.93 million people. And if we calculate the amount of hazardous waste per person, we find hazardous waste in Haifa = 15.3 kg/year per 1 person and hazardous waste in the West Bank = 0.00307 kg/year per 1 person.

## Slide 30: Dry-cleaning sector management
As for PERC that used in dry cleaning, there are multiple alternatives less hazardous such as CO2, silicon and wet cleaning.
There should be a special crew with good experience from the Quality and Environment Authority, which supervises the transfer of the hazardous waste from the dry-cleaning stores to special sites so that they are disposed of properly.

## Slide 31: Universities sectors
Hazardous wastes in universities are classified as Y14 of the Basel convention.

## Slide 32: Input and output indicators
Engineering department:
After analyzing data, it was found that all the materials that provided by university A, department of Engineering, are hazardous and the amount of hazardous materials is approximately 41 kg per semester (11 kg solids and 30 kg liquid materials).

## Slide 33
Chemical Department:
As provided from university B, the amount of hazardous materials is 131 L/semester. Since the number of students is 1500 students per semester divided by the amount of hazardous materials which is 131 L/semester, and then the average number is 0.0873 L/student (87.3 cm3/student).
In chemical department at university C, the number of teaching laboratories is 6 labs, and the number of students in each lab is 120 students per semester, divided by the amount of hazardous materials which is 150 L/semester, then 0.208 L of hazardous materials for each student per semester which equals 208.33 cm3/student.

## Slide 34
Allied Health department:
After analyzing the data from university C, department of Allied Health it was found that the total amount of raw material of this department is about 20 Kitts in addition to 120 L materials per semester.

## Slide 35
Biological Department:
As provided from university C, The total amount of total raw materials imported by biological department is about 220 L/semester, includes 100 L liquids materials and 120 kg solids materials.

## Slide 36: Storage indicators
Emission-waste indicators
Energy indicators

## Slide 37: Transportation indicators:
After analyzing data, there is no hazardous waste being transported by university A and B. However, the Allied Health department of university C has been transported 2 kilograms per month per semester

## Slide 38: Environmental indicators:
 | Amount of water consumed | Amount of Distilled water consumed
University A | 4000 liter | Unavailable*
University B | Unavailable* | Unavailable*
University C |  | 
Chemical | 2000 liter | 500 liter
Allied health | 1000 liter | 20 liter
Biological | 1500 liter | 1500 liter

## Slide 39: Economic indicators:
Costs of raw and hazardous materials |  | 
 | Cost of raw materials | Cost of hazardous materials
University A (Engineering) | 880 J.D | 667 J.D
University B (Chemical) | Unavailable* | Unavailable*
University C |  | 
Chemical | 2000 J.D | 1000 J.D
Allied health | 20000 J.D | Unavailable*
Biological | 15000 J.D | Unavailable*

## Slide 40: Universities sector management
There should be awareness campaigns for students who use the laboratories of the seriousness of some materials and how to deal with them and disposal without recklessness.
There should be an assistant in the laboratory be responsible for these materials.
There must be laboratory launderers attached to a sewer network of hazardous fluids so that they do not mix with ordinary waste, but are treated in such a way that they do not harm the surrounding environment.

## Slide 41: Conclusions:
In general, none of the agencies have developed its overall HWM process in a manner that reduces the risk of the produced HZW. The enormous costs and technical limits to reduce hazardous-waste highlight the need for a more comprehensive, explicit, and systematic approach to setting cleanup priorities.

## Slide 42: Recommendations:
Reduce the amount of hazardous materials.
The Environmental Quality Authority should contribute part of the costs related to the management and disposal of hazardous wastes.
The Environmental Quality Authority must stipulate regulations upon companies to follow proper methods of disposal the hazardous wastes without harming the surrounding environment.

## Slide 43
The Environmental Quality Authority shall do a site screening of lands in order to identify an appropriate location for the hazardous waste to be disposed.
A highly efficient group should be formed by the Environmental Quality Authority to follow up the process of transporting hazardous waste with those responsible for transporting it from companies and universities, and to eliminate the hazardous waste in appropriate ways and in places where it is not harmful to the environment and human.
The Environmental Quality Authority should team up with the Health Authority to set up a hazardous waste management scheme at a practical level.
Computer software can be designed in order to connect the companies and universities with the Environmental Quality Authority so that the Environmental Quality Authority is constantly updated about the hazardous waste that is generated.

## Slide 44: THANK YOU 