## Slide 1: Graduation Project Structural Analysis And Design of Darwich Building
An-Najah National
University
Engineering College
Civil Engineering
Department
Prepared By:
Amer Abufares
Khaled Sleem
Maher Taha
Supervised By:
Dr. Wael AbuAsab
2015

## Slide 2: Project Definition This project will introduce the structural analysis and design of the multi-storey building of “Darwich” Which is located in Nablus.

## Slide 3: Project Description
This building consists of 7 stories with about 300 square meter for each floor.
Each floor has a height of approximately 3m.
From a structural point of view the structural elements, footings, columns, beams and slabs will be designed by hand and then by using SAP2000.

## Slide 4: Codes & Standards
The structure is designed using practice codes and specifications that control the design process and variables.
The following codes and standards are used in this study:
  ACI 318-10: American concrete institute provisions for reinforced concrete structure design.
  UBC-97: code which is used here for seismic load parameters determination.
  ASCE 7-10: For minimum design loads for building

## Slide 5: Loads
Live and superimposed dead load as follow:
Live load was considered to be 2 KN/m2
Superimposed dead load 4KN/m2.

## Slide 6: Materials
B300 Concrete (f’c=24MPa, E=2.33x107 KN/m2).
Unit weight of reinforced concrete = 25 KN/m2
Steel Grade 60 ( Fy= 420 MPa , E= 200GPa)
Soil Bearing Capacity = 300 KN/m2

## Slide 7: The Structural System
This system is a combination of moment resisting frames supported by shear walls.
As the building has relatively short spans the slab system was chosen as one way ribbed slabs with hidden beams.

## Slide 8: Plan

## Slide 9: Preliminary Design “Dimensions”
Slabs & beams

## Slide 10: Slab
Thickness of slab is ( 250mm) according to deflection requirements shown in the table attached previously.
The longest span in the slab is ( 3.55m ) length .
The minimum thickness is ( =0.192 m) , take slab thickness = 250mm

## Slide 11: Beams
Beam ID | Width (mm) | Depth (mm)
B1 | 700 | 250
B2 | 600 | 250
B3 | 800 | 250
B4 | 600 | 250
B5 | 500 | 250
Drop Beam | 300 | 500
Beam Dimensions

## Slide 12: Beams Distribution

## Slide 13: Columns
Take this Column as example

## Slide 14
ØPn = Øλ (0.85 fc` (Ag-As) +fyAs)
Pu From Dead & live = (1.2D + 1.6L) * #of stories
ØPn must be greater than Pu
According to these information we found the dimensions of two columns we used in the building

## Slide 15: Columns dimensions
Column | Dimension | Steel ratio | Area of steel As | Bars | Lo mm | Ls mm | Ties
C1 | 30 * 80 | 1 % | 2400mm2 | 12Ø16 | 500 | 800 | 2Ø10 / 10cm
C2 | 30 * 50 | 1 % | 1540mm2 | 10Ø14 | 500 | 800 | 1Ø10 / 10cm

## Slide 16: 3-D Model

## Slide 17: Equilibrium check
Manual calculation Live load= 290 *2 * 7 = 3990 KN
Sap value From sap = 3987.83 KN
Error = = 0.05 %
Since error < 5% …. It’s Ok

## Slide 18: Compatibility Check

## Slide 19: Stress-strain check
Selected Beam to be checked

## Slide 20: Stress-strain check
The ultimate load on beam Wu=2 * (3.10 +3.10)/2 = 6.2 KN/m
Manual calculation based on live load
Mu = . m
Results from sap2000 is shown in the figure

## Slide 21: Stress-strain check
Mu (From Sap2000)=
Error = = 4.2%
Since error <10 % Check is ok

## Slide 22: Seismic Design
Zone factor, Z = 0.2
Seismic Coefficient Ca = 0.24
Seismic Coefficient Cv = 0.32
Since, B.C = 300 KN/M2 The Soil Profile Coefficient is Sc
Importance factor = I = 1.00
g = 9.81 m/sec2
Over strength factor, R = 6.5

## Slide 23: Periodic check
The natural period is the time required to complete one whole cycle during dynamic loading.
The following equation is used to check T:
T= Ct (hn)3/4 , Ct : a constant = 0.0731
The structure has a period T =0.73750 seconds as shown

## Slide 24: Periodic check
% Error = ((Tmodel – THand)/Tmodel) * 100% = ((0.73750 – 0.71710)/0.73750) * 100% = 2.77% Which is ok

## Slide 25: Footing Design
Area of building = 300 m2
Area of footings (total area ) = Total loads and weights / soil bearing capacity
= 54398KN/ 300KN = 181.3 m2
181.3 > 150
use Mat foundation

## Slide 26: Compatibility & Deformation checks:

## Slide 27: Shear check
For column 30*80
Ps largest =1185 KN
Assume h=700 mm
D=600 mm
ØVc = p x bo x d
ØVc = 0.003 x 2200 x 600 / 1000 = 2376 KN
Vu = 1185 KN < ØVc ..........So punching shear is OK
Take 7Ø 16 top and bottom steel in both direction = 1400mm2 Also we can add 7Ø 25 under columns to make the structure more safe

## Slide 28: Slab Design

## Slide 29: Slab Design
Bending moment for slab

## Slide 30: Slab Design
Use 2Ø10 for top and bottom steel
That was determined after calculations using the moment values
Strip one reinforcement

## Slide 31: Beam Design

## Slide 32: Beam Design

## Slide 33: Beam Design

## Slide 34: Column Design
The dimensions of column are : 30 cm × 80 cm psap = 1% (we use this value for economic considerations). As= p×Ag = 0.01 × (300 × 800) = 2400 mm2 Smax = 150 mm Smin = 50 mm use 12Ø16 .

## Slide 35: Column Design

## Slide 36: Shear Wall Design
A shear wall is a wall that is designed to resist shear, the lateral force that causes the bulk of damage in earthquakes.

## Slide 37: Shear Wall Design
Vx = 15.4531 Vy = 569.2 KN . Axial = 2311 KN Mx = 1129.87 KN.m My = 5 KN.m
Asmin = 0.0025×4400 × 300 = 3300 mm2 Asmin/2 = 1650 mm2 → 17Ø12 on each side S = = = 176 mm → use s = 200 mm use 2 Ø 12 /200 mm → for horizontal steel on both sides

## Slide 38: Shear Wall Design
Small Moment = 60 mm2
Total area of steel needed for moment and axial load : Astotal = 60 + 1687.5 = 1710 mm2 then use 18Ø12 → for vertical steel on each side
use 1Ø12/ 200 mm

## Slide 39: Shear Wall Design

## Slide 40: Stairs Dimensions
Stair dimensions :
Going = 30 cm
Riser = 17 cm
Floor height = 3m
No. of goings = 8
No. of risers = 9

## Slide 41: Stair Design
As stair should be a safe escape root for the residents in the buildings , a slight increase in the loads will be used. This is a residential building with 2 KN/m2, therefore 5 KN/m2will be used on stairs .
Thickness = L/20 = 290/20 = 14.5 cm  use 20 cm
As = p*b*d= 0.000747*1000*170 =127 mm2/m < Asmin
Take 4 φ12

## Slide 42: Bending Moment

## Slide 43: THANK YOU