## Slide 1
An-Najah National University
Facility of Engineering and Information Technology
Civil Engineering department
Redesign Of Residential Building include seismic loads.
Prepared by: Oday Odeh
Hamza Souqi
Hasan Kmail
Supervised by: Dr. Mahmoud Dwekat

## Slide 2
Content:-
-Project description.
-codes.
-Material.
-Loads.
Introduction
01
-Slab preliminary design.
-Beam preliminary design.
-column preliminary design.
Preliminary Design
02
-Introduction.
-Define material, sections
modifiers, and loads.
Modeling and analysis
03
-Introduction.
-Model Checks.
-Design checks.
Checks
04
- Shear wall design.
-Beam design.
-Column design.
-Slab design.
- Footing design.
Design
05
Seismic load calculation
06

## Slide 3
The building consist of 10 floors, with total area of the building = , and Hight of story = 3.0 m.
01 Introduction
Project description:-
Residential Building located at the middle
Of Huwara-south Nablus.
Soil bearing capacity= 350 KN/

## Slide 4
Changes in original plans
The owner of the building complain that the corridors of the building are wide, Therefor we change the width of the corridors and get smaller, because of that some column location changed to fit the drawing.
The ground floor contain stores at the front of the building. All other stories have the same architectural plane.
The same elevation on area of the same floor.
Bracing system used instead of stone wall.

## Slide 5
Project description:-
Figure-1: floor plan.

## Slide 6
Project description:-
Figure-2: north east view.

## Slide 7
Project description:-
Figure-3: North-west view.

## Slide 8
Project description:-
Figure-4: South-east view

## Slide 9
Project description:-
Figure-5: West-south view

## Slide 10
ASTM for material properties and specification.
01 Introduction
Codes and Standard:-
ACI 318-14 for design the elements of the structure.
ASCE 7-10 for loads applied on the structure.
IBC 2012: International Building code used for seismic design
UBC 97: Uniform Building code used for seismic design

## Slide 11
01 Introduction
Material:-
Material | Compressive strength | Modules of elasticity | Unit weight
Concrete | 28 Mpa | 24870 Mpa | 25 KN/
 | Yield strength | Modules of elasticity | Unit weight
Steel Gr (60)A615 | 420 MPa | 200 GPa | 78 KN/
Material | Compressive strength | Modules of elasticity | Unit weight
Concrete | 28 Mpa | 24870 Mpa | 
 | Yield strength | Modules of elasticity | Unit weight
Steel Gr (60)A615 | 420 MPa | 200 GPa | 
Material used in structural element and modeling the structure.

## Slide 12
Material:-
Materials | Unit Weight (KN/)
Tiles | 25
Plaster | 23
Blocks | 12
Masonry Stones | 26
Filling Materials | 18
Concrete Mortar | 23
Materials | 
Tiles | 25
Plaster | 23
Blocks | 12
Masonry Stones | 26
Filling Materials | 18
Concrete Mortar | 23
Material used in superimposed dead load calculation and shall be used in budling construction.

## Slide 13
01 Introduction
Loads :-
Gravity loads: live and dead loads.
Live loads for first two stories = 4 KN/ and for all other stories = 2 KN/m.
Dead load composed of own weight of structure
And distributed load 13.5 KN/m as linear load Represent weight of exterior wall.
Superdead from tiles, mortar , portions and plaster equal 4.05 KN/

## Slide 14
02 Preliminary design
Slabs preliminary design:-
Thickness of slab determined according to ACI code as shown in table 11:
For one-way ribbed slab
Table-3: Minimum thickness of slab.
h = Use 0.25m.
Type of slabs are Ribbed slabs, the floor has two system of Ribbed slabs
One Way Ribbed slab and Two Way-Ribbed slab.

## Slide 15
slab distribution plane:-
Figure- slab distribution plane.

## Slide 16
02 Preliminary design
Beam preliminary design:-
Thickness the same as one way-ribbed slab
Slabs section dimensions
Stem width = 150 mm
Overall depth = 250 mm
Slab thickness = 80 mm
Block width = 400 mm
Rib spacing = 550 mm, for two-way ribbed in both direction.
For Tow Way-Ribbed slab
Figure- section in slab

## Slide 17
02 Preliminary design
beam preliminary design:-
System of beam used is hidden beams between all columns.
Dimension of beam will be determine as the following:
Thickness h as the thickness of slab = 25 cm
b = 2*d = 0.50 m.
Figure main beam dimension
Figure secondary beam dimension
Dimension of secondary beam used 0.25 X 0.3 m

## Slide 18
02 Preliminary design
column preliminary design:-
From planes the maximum tributary for the column equal 90
Therefore, column 70*40 cm used with area = 240000 mm2
column demotion

## Slide 19
02 Preliminary design
Bracing dimension :-
Bracing used instead of stone walls
Depth = L/8 = 3.6/8 = 0.45 m

## Slide 20
All supports will be model as pin support.
Exterior partition as linear load and interior partition as distributed load.
03 Modeling and analysis
Introduction:-
Modeling and analysis will performed by using ETABS 18 program.
All joint will assumed as fixed joint.
Bracing used instead of exterior stone wall.

## Slide 21
03 Modeling and analysis
Define material and sections and loads:-
Figure-8 Material Property

## Slide 22
Sections:
Figure-9 sections used

## Slide 23
Sections:
Figure-10 Main beam section
Figure-11 secondary beam section

## Slide 24
Sections:
Figure-12 One-way ribbed Slab sections
Figure-13 Two-way ribbed Slab sections

## Slide 25
Modifiers
Figure-14 Column modifiers.
Figure-15 beams modifiers

## Slide 26
Modifiers
Figure-17 Bracing modifiers
Figure-16 Slabs modifiers

## Slide 27
04 Checks
The Checks which will be discussed in this section include:
Introduction:-
Model checks, compatibility, equilibrium, internal force checks.
Deflection check
Design checks
Preliminary design checks.

## Slide 28
Model checks:-
compatibility check:
Figure‑23: compatibility animation.

## Slide 29
Model checks:-
Equilibrium check:
Live load:
From program = 13368 KN
Manually =13347
Then, Error 0.15% < 5% ok.
Dead load:
From program = 37198 KN
Manually = 37446
Then, Error 0.667 % < 5% OK
Super dead load:
From program = 49426 KN
Manually =
Then, Error 0.6% < 5% OK
Figure-24 etaps loads

## Slide 30
Model checks:-
3- Internal force check:
Column:
From program M = 461 KN.m
Manually M = 436.8 .m
Then, Error 4.8 % <10% ok.
Beam :
From program M =14.37
Manually M =
Then, Error 2.9% < 10% ok
Figure-26: Beam location.
Figure-25: Column location.

## Slide 31
Model checks:-
3- Internal force check:
Slab:
From program M = 18.4 KN.m
Manually M = 18.6 .m
Then, Error = 2 % <10% ok.
Figure-27: Slab location.

## Slide 32
Design checks:-
4-Deflection check:
Largest panel which has the maximum deflection
Shown in the figure
Longest side = 4962 mm
Deflection = l/240 = 4962 /240 = 21 mm
Figure-29 Largest panel.

## Slide 33
Design checks:-
4-Deflection check:
Using long-term load combination 2D+2S.D+1.25L
Maximum deflection from etaps = 38.5 mm
Calculated maximum deflection = 27 mm
Reduction factor 1.4
27/1.4 = 19.2 mm
L.T all = 4962/240 = 21 > 19.2 OK
To consider sustained live load
Figure-30 Deflection plan view.

## Slide 34
05 Seismic Load Calculation
Introduction:-
Seismic load calculation done acceding to UBC,IBC, and ASCE codes.
Analysis procedures used for the design of building is Response Spectrum Analysis.

## Slide 35
load combinations:-
Qx = EQx + 0.3 EQy
Qy = 0.3 EQx + Eqy
Variability factor = 1.3 , E = Eh + Ev
Ev = 0.12D , Eh = ρEQ
E = 0.12D + 1.3 EQx + 0.39EQy
E = 0.12D + 1.3 EQy + 0.39EQx

## Slide 36
load combinations:-
1.2D + 1.0E + 1.0L
(1.12)
(1.13)
(1.21)
Load combination used with according to ASCE7-10 :
Strength design combination
0.9D + 1.0E
(1.22)
(1.23)
0.9D + 1.0E

## Slide 37
Loads and load combinations:-
D + 0.7E
D+0.75L + 0.252E
(1.24)
(1.25)
(1.26)
(1.27)
Load combination used with according to ASCE7-10 :
Allowable design combination
0.6D + 0.7E
(1.27)

## Slide 38
Loads and load combinations:-
(1.12)
Load combination used with according to ASCE7-10 :
Envelope service combination
Envelope ultimate combination
Deflection combination

## Slide 39
Figure-21 load patterns
Figure-22 load combination

## Slide 40
Determine The Peak Ground Acceleration
Z = 0.2g
Ss = 2.5Z = 0.5
S1 = 1.25Z = 0.25
These equation based on 10% probability of exceedance.

## Slide 41
Determine Site Class
Z = 0.2g
Ss = 2.5Z = 0.5
S1 = 1.25Z = 0.25
An approximation = 0.5 B.C
= 175 KN/m2 = 3655 psf
site class for area of project is C.

## Slide 42
Sms at short period and Sm1at long period
SMS = Fa Ss
SM1 = Fv S1
Determine site coefficient
Fa and Fv from Table 11.4-1
and Table 11.4-2
SMS = Fa Ss = 0.6
SM1 = Fv S1 = 0.3875
site class for area of project is C.

## Slide 43
Determine Design Category SDC
Risk category for the building is II, which give seismic important factor = 1.00
There is no need to convert
SDS = 0.6
SD1 = 0.3875
The seismic calculation done based on 10% probability of exceedance. no need to multiply by 2/3 to convert to 2% .
Seismic design category for the building is D

## Slide 44
Determine of the seismic base shear
The permitted and used in the project Analysis Procedures are equivalent lateral & response spectrum methods.
There is no vertical and structural irregularity in the building.
The vertical load taken by frames and lateral load taken by shear wall. Hence, the structural system is building frame system.
Seismic Force-Resisting System is Special reinforced shear walls

## Slide 45
Response Modification Coefficients
Response Modification Coefficient R = 6, Overstrength factor = 2.5 and, Deflection Amplification Factor Cd = 5.

## Slide 46
Equivalent Lateral Force
The seismic base shear = V = CsW
According to ASCE equations Cs = 0.1
The effective seismic weight, W, of a structure:
W = D + SD + 1.25L
W = 37446.35 + 49136.2 + 13368 *0.25 = 89924.6 KN
V = 0.1 * 89924.6 = 8992.46 KN

## Slide 47
Seismic design using etaps
For Equivalent Lateral Force
a-Define mass source

## Slide 48
Seismic design using etaps
b-Define diaphragm for all stories

## Slide 49
c-Define load cases in X and Y
Seismic design using etaps

## Slide 50
Seismic design using etaps
d-Define load pattern in X and Y.

## Slide 51
Seismic design using etaps

## Slide 52
Seismic design using etaps
e-Check etaps Equivalent Lateral Force by comparing it with hand calculation
Etaps value = 8910.1 KN
Calculated = 8992.5 KN
Error = 0.9 % OK

## Slide 53
Seismic design using etaps
Define response spectrum to etaps.
a-Define response spectrum function
b-Define load cases for response spectrum in X and Y.
Scale factor = g * I/R = 9806.65 *1 /6 = 1634.44

## Slide 54
Response spectrum function

## Slide 55
Load case in X for Eq. Analysis

## Slide 56
Load case in Y for Eq. Analysis

## Slide 57
Seismic design using etaps
According to ASCE 7-10 the difference between RS and EQ methods need to be less than 15% If not modification factor shall be used the following table show the results of RS and the modification factor
Axis | RS | EQ | difference | %diff | modification FACTOR
x | 6683.01 | 8910.1 | 2227 | 24.9951 | 1.13
y | 6679.885 | 8910.1 | 2230 | 25.0302 | 1.13
Scale factor become 1853
Difference < 15% ok

## Slide 58
Model Seismic Checks
Period check.
Ta = Ct * hnx
Cu = 1.44
Ct = 0.0488
X = 0.75
Then Ta = 0.625 s
Tetaps = 0.67 s
Cu * Ta = 1.44*0.625 = 0.9s
0.67<0.9 Okay

## Slide 59
Model Seismic Checks
Model participation mass ratio check
In first 11 model in X 95.97% and in Y 94.6% > 90 % ok

## Slide 60
Model Seismic Checks
Drift check
According to ASCE 7-10 allowable drift as shown in table below
Allowable drift = 0.02h
Δ = = 5*0.001508 =
0.00754 < 0.02 ok

## Slide 61
Model Seismic Checks
P-Delta Effects
stability coefﬁcient (θ) as determined by the following equation is equal to or less than 0.10
Maximum 𝜃 in X=0.0055
Maximum 𝜃 in Y=0.0079
θ<10 % ok

## Slide 62
Model Seismic Checks
Ampliﬁcation of Accidental Torsional
torsional ampliﬁcation factor (Ax)
If Ax < 1 then no need to multiply by amplification factor
All δmax/δavg values are < 1.2
No need to multiply by amplification factor.

## Slide 63
05 Design
Introduction:-
Preliminary dimensions of the different structural members were found. Now, after finishing the model, these members will be tested and evaluated to see if they are adequate or not.
Design checks and full detailed drawing developed include, slabs, beams, columns, shear walls, footing.

## Slide 64
Preliminary design checks.
Figure‑23: Preliminary design checks.
.
This check doing to ensure all element are adequate. Any element shows as red color is not adequate.

## Slide 65
Shear walls reinforcement.
Shear walls checks.
Check the need for special boundary elements at the edges of structural walls
hw = 3m, minimum lw=2m
hw/lw = 1.5 m < 2 then no need for boundary elements.
constraints
The longitudinal spacing of transverse reinforcement at the wall boundary shall not exceed the lesser of 8 in. and 8db of the smallest.
If Vu > Acvλ horizontal reinforcement shall be used.

## Slide 66
Shear walls reinforcement.
Shear walls checks.
select a sample of shear wall to check result as shown in
figure
There is no coupling beam in our structure since Ln/h > 4 in all connecting beam with two wall structure.
Design check

## Slide 67
Shear walls reinforcement.
Shear walls checks.
select a sample of shear wall to check result as shown in
figure
There is no coupling beam in our structure since Ln/h > 4 in all connecting beam with two wall structure.
Design check

## Slide 68
Design check
Rebar value from etap ρl = 0.016 > 0.0025 OK
Use 1 Ø16/ 100 mm
S ≤ 200, 128
Determine Capacity
Figure 6.25 shear wall section in section designer

## Slide 69
Design check
Interaction diagram for M3 and M2 capacity of section as shown in figure.
Figure 6.27 axial and moment 2 capacity
Figure 6.28 axial and moment 3 capacity

## Slide 70
Shear wall checks
Axial capacity = 12962.97 KN
Moment 3 capacity =589.5 KN.m
Moment 2 capacity = 9424.5 KN.m
WALL | Vx(KN) | Vy(KN) | Mx(KN.m) | My(KN.m) | P(KN)
W2 | 1.60 | 2162.47 | 5897.74 | 0.79 | 9979.76
By section cut at the base of the shear walls give the forces in table below.
Figure 6.29 section cut in shear wall
all of value of loads (axial, moment2 and moment3) are less than value of capacity OK.

## Slide 71
Shear wall checks
check Vx
ØVc = 461.15
WALL | f'c | Lw | t | ØVc | Vx | check
W2 | 28 | 3.32 | 0.25 | 461.15 | 1.6 | ok
Design for shear in y direction
ØVcy= = 585.593 KN
Vs = 2162.5/0.75 – 585.6 = 2297.7 KN < Vsmax = 4 * ØVcy = 2342.4 KN OK
WALL | f'c | Lw | t | Vcy | Vuy | Vs | Vs max
W2 | 28 | 3.32 | 0.25 | 585.5 | 2162. | 2297 | 2342

## Slide 72
Shear wall checks
Use 1Ø12 / 100 mm in each side
Check the need for additional horizontal reinforcement
Vu ≤ Avc * ƛ
2162.5 ≤ 250 * 3320 * 1 * = 4392 KN

## Slide 77
Beam Design
1-Check that beam Pu ≤ 0.1 Ag f’c
For main beam = 0.1 * 0.25*500*28 = 350 KN
For secondary beam = 0.1 * 0.25*300*28 = 210 KN
2-Clear span of beam ≥ min {0.3h ,250 mm},
where:
h = total depth
Minimum span length of beam = 1.3 m ≥ 0.3 *250 = 0.075 m OK
≥ 250 mm OK
3-Width of beam ≤ width of supporting column + x
Where x = min {least column dimention ,0.75 maximum column dimention}
Width of supporting column = 35 cm
Width of beam = 50 cm, 50 ≤ 70 OK

## Slide 78
Beam Design
4-At least two top and bottom bars shall be continuous and extend ld in the columns
2Ø14 used in place where in major reinforcement needed
5-Steel ratio at any section shall not to exceed 0.025
6-The beam shall be designed to resist Vu taken as shown in the figure:
Vu = 91.92 + 92.73 = 185 KN
ØVn ≥ Vu OK
Vn = Vc + Vs = 260.16 + = 73 + 285 = 359 KN
Vu = VuETAB + (Mnr+Mnl)/2
VuETAB = 128 KN
Mn = 92.73

## Slide 79
Beam Design
Design for flexural
Check etaps design results
For selected beam M(middle) = 74.4 KN.m give ρ = 0.01
ρ from etaps = 0.0099
Error = 1 % OK
As = 1089 mm2 use bottom steel 4Ø20
ρ end top = 0.73% As = 803 mm2 →use 4Ø14

## Slide 80
Beam Design
Maximum axial force = 33 KN < 0.05*500*250*28 = 175 KN OK
Vu from strength combination = 128.7 KN
Shear due to earth quick = 1 KN <<128 OK
design for torsion and shear
Vc= 97 KN
Vu from strength combination = 128.7 KN
Vs = Vu/0.75 – Vc = 128.7/0.75 – 97 = 74.6 KN
Tu from etaps = 1.6 KN.m << 41.3 KN.m no need for torsion reinforcement
Tth = 41.34 KN.m

## Slide 83
Design check for column
requirement for intermediate column
Columns (Pu > 0.1 Ag f’c)
0.1*750*350 =26.25 all column satisfy this condition
If c1 and c2 are the dimensions of column cross section, c1≥c2, then:
– c2 shall be ≥ 300 mm, 350 > 300 OK
– c2 shall be ≥ 0.4 c1, 350 > 0.4*750=300 OK
Lap splice of bars shall be used at mid-height of the column with lap splice length,
ls = 1.3 ld.

## Slide 84
Design check for column
•Stirrups shall be computed based on shear force Vu and shall have a maximum spacing as shown in the figure
•Within area of congested transverse reinforcement (ends of columns), crossties shall be used as shown in the figure below:

## Slide 85
design column for flexure
slenderness check for column
Slenderness ratio = (k*Lu)/r ≤ 22
= 11.5 < 22 we do not consider slender
As = 0.01*750*350 = 2625 mm
12Ø18
From Etabs longitudinal steel:

## Slide 86
Design for shear in column
Design for shear in column
ØVc = 158.7
Vu from etaps = 1.4 KN < ØVc
From Etabs shear reinforcement as in the figure:
min = max [0.062* , ] = Max [0.6, 0.63]
Minimum tie will used So = 100 mm and S1 = 150 mm

## Slide 87
Design for shear in column
For transfer reinforcement

## Slide 88
Design for shear in column
Ash1 = Max { (} = 438.2 mm2
Ash2 = Max { (} = 195 mm2
Ld = Max [3000/6 = 500 mm, 750, 450] then ld = 750mm
Ls = 1.3 ld = 975 mm use 1 m

## Slide 91
Slab reinforcement design
We use ETABS program to distribute slab steel.
Assume:
2φ12 for top and bottom
As = 226.2 mm2
Mu = ()*(1 - (1 - )2)
= ()*(1 - (1 - )2) = 16.85 kN.m
For one rib Mu = 16.85/0.55 = 30.64 kN.m/m
We compare this value with ETABS and we use different steel section so there is no problems and the design is economical.

## Slide 92
Slab reinforcement design

## Slide 95
Hock at ends for top steel:
According to figure:
The largest diameter of steel we use φ24 so:
Hock length = 24*19 = 456 mm use 460 mm

## Slide 96
Shear design:
φVc = (0.75*b*d)/6 = (0.75**150*210)/(6*1000) = 20.8 kN
for one rib = 20.8/0.55 = 37.88 kN/m
There is some values more than 37.88 kN/m so we will design for shear

## Slide 97
Shear design:
Assuming to put stirrups φ10
Av = 52*π*2 = 157 mm2
S = 300 mm … 4 φ10 /m
Vs = (Av/S)*fy*d = ((157/300)*420*210)/1000 = 46.16 kN
and for one meter = 46.16*4 = 184.6 kN/m
The value that we will check in Safe = 184.6 + 37.88 = 222.5 kN/m

## Slide 98
Footing design:
We use Safe program to design footings, first we transfer the load on base and combinations from ETABS to Safe.

## Slide 99
Foundation checks:
Geotechnical checks:
Settlement check ∆ < ∆ all = 25 mm
We show service gravity with Earth Quick combination

## Slide 100
Foundation checks:
Bearing capacity check:
BC = 350 kN/m2
We show service gravity with Earth Quick combination
According to the figures we see that all values < 350 kN/m2 and all values have minus sign …. Ok

## Slide 101
Foundation checks:
Structural checks:
Punching check:
All values < 1 …. Ok
Max design shear stress < concrete shear stress capacity (for all columns)

## Slide 102
Foundation checks:
Wide beam shear check:
φVc = (0.75**b*d)/6 =
(0.75**1000*750)/(6*1000) = 459 kN/m
Assuming to put stirrups φ10
Av = 52*π*2 = 157 mm2
Using S = 300mm ... 4 φ10 /m
Vs = (Av/S)*fy*d = 164.85 kN and for one meter = 164.85*4 = 659.4 kN /m
The value that we will check in Safe = 659.4 + 459 = 1118.4 kN/m

## Slide 103
Foundation checks:

## Slide 104
Foundation Reinforcement

## Slide 111
Thank you