## Slide 1: An-Najah National University Building Engineering Department Environmentally Friendly Indoor Swimming Pool At An-Najah University
Prepared By :
Essam Nasif Nesreen subeh Tha’er Daragmeh
Supervised by : Dr. Mutasim Baba

## Slide 2
Project Contents:
Types of Swimming Pools.
Construction and Structural Aspects of Pools.
Systems and Accessories of Pools.
Environmental Systems of Indoor Swimming Pools.
Our Project: An Najah Indoor Swimming Pool.

## Slide 3
Types Of swimming Pools:
According to Usage:
Private Pools
Public Pools
Competition Pools
According to The Surrounding Environment:
Indoor Pools
Outdoor Pools

## Slide 4
Competition Pools :
Olympic Pools :
FINA Specifications for Olympic size Pools | 
Length | 50 m
Width | 25 m
Number of lanes | 10
Lane width | 2.5 m
Water temperature | 25–28 °C
Light intensity | minimum 1500 lux
Depth | minimum 2.0 m
Volume | minimum 2,500 (depending on depth)

## Slide 5
Semi-Olympic Pools :
FINA Specifications for Semi-Olympic size Pools | 
Length | 25 m
Width | 12.5 m
Number of lanes | 6
Lane width | minimum 2.0 m
Water temperature | 25–28 °C
Light intensity | minimum 1500 lux
Depth | minimum 1.3 m
Volume | minimum 405 m3

## Slide 6
Types of Pools (According To Surrounding Environment ) :
Indoor Pools
Outdoor Pools

## Slide 7
Construction And Structural Aspects of Pools
Soil and Earthwork
Soil Problems for Swimming Pools :
Expansive soil
Wet soil
Ground water near the surface
(Temporary or permanent condition)
Rock, sand gravel and solid particles
Loose soil

## Slide 8
Types of Pools According to Their Construction Systems:
Gunite (Concrete) Pools
Gunite is a dry mixture of cement and sand that is pushed through a "fire hose" via a large compressor.
Finishing Materials: Marble dust, Exposed aggregate finishes, Ceramic tiles.
Fiber Glass Swimming Pools
The pool’s container is made from an extra strong type of glass fibers placed in an excavated hole.

## Slide 9
Structural Flooring Systems( For swimming pool’s building ):
Concrete Roofs:
Pros:
Resistant to fire and moisture.
Can be shaped in any way desired.
Extremely durable.
Cheap Maintenance
Cons:
Heavy.
Need columns for long spans.
Types:
Flat Slab.
2. Slab with Beams (One way or two way)

## Slide 10
Steel Roofs:
Pros:
Long spans without columns.
Lighter than concrete.
Visually appealing.
Long life span.
Extremely fire-proof.
Requires little maintenance.
Good for fast track projects.
Ductile and resistant to wind loads.
Widely available.
Cons:
Not many workers are familiar with it.
Expensive compared to concrete.
Prone to corrosion if not properly coated.

## Slide 11
Systems and Accessories Of Pools
The water support system contains a lot of sub systems :
Water supply system
Water filtration and circulation system
Water heating system
Drainage system.

## Slide 12
The Filtration System
Composed of four elements:
The filter
The pump and its motor.
The automatic surface skimmers and drains.
The recirculation pipes and fittings.

## Slide 13
Water Heating Systems:
Gas-fired pool heaters
Electrical pool heaters
Solar pools heaters
(usually evacuated tube collectors )

## Slide 14
Drainage system
The Skimmers:
The main drains and the overflow drains

## Slide 15
Thermal Pool’s Covers
Construction:
A thick layer of closed cell foam.
The two woven polyethylene layers.
They are strongly recommended for heated pools.

## Slide 16
Environmental Systems Of Swimming Pools
Main energy consuming systems for indoor pools (SEDAC):

## Slide 17
Main environmental systems
Dehumidification and ventilation system
HVAC system
Indoor lighting system
Underwater lighting system
Acoustical control system

## Slide 18
Dehumidification and ventilation system
ASHRAE 62 Ventilation Air Standard
For Pool Area: 0.5 cfm / ft2
2.5 liters/s per m2
For Spectator Area: 15 cfm / person
8.0 liters/s per person
Since natural ventilation is not the suitable indoor swimming pools, a good dehumidification system to support the air conditioning system of the pool without the enlargement of the heating load of the building is required.

## Slide 19
HVAC System of Pools
Proper duct design will :
Minimize air flow requirements.
2. Ensure a comfortable recreation environment.
3. Optimize humidity control

## Slide 20
Lighting systems
General indoor lighting system
Underwater Lighting System

## Slide 21
Noise control System
Mechanical-born noise
Related to HVAC system and other mechanical equipments .
Many of reduction techniques are based on the use of :
sound absorbing materials
a prober fixation and selection of the mechanical systems
Standard noise reduction equipment such as ducts silencers

## Slide 22
Structural-born Noise
Due to :
High sound reflectance of some materials (water, ceramic tile, glazed finishing materials…)
The lack of the sound absorption materials (fabrics) used in the pool’s hall.
Noise Reduction techniques :
Suspended Acoustical Baffles
Walls’ cavities

## Slide 23
Project’s Case Study: An-Najah University Swimming Pool
General info:
Location: faculty of physical education’s sport complex building-Nablus
Area: 1400 m2 (including the pool’s facilities).
Pool’s Dimensions: Semi Olympic (25m x 12.5 m)
Includes a side seating capacity of 340 seats.
Building includes bathrooms,
shower units and a control room.

## Slide 24
Systems Used in the Building.
Roofing system:
The pool’s roofing system consist of steel beams (I-sections) with covering sheets. Steel columns support the roof.

## Slide 25
Heating system:
Fan coil units around the pool are used to cover the heating load in the pool’s building.
Lighting system:
Suspended Luminairs (metal halide) lamps

## Slide 26
The Main Problems to Be Solved During This Project:
High indoor humidity ratio: causes rust, blistering in paint, dampness, structural deterioration.
Ventilation: Bad ventilation causes respiratory problems.
Acoustical Problems:
-High reverberation time.
-Impact noise on roof.
-Mechanical system noise.
High energy consumption due to heating.

## Slide 27: Thank You