## Slide 1
An-Najah National University Faculty of Engineering & Information Technology Industrial Engineering Department
Development of a Maintenance Management System at AL ARZ Ice Cream Factory
Supervisor: Dr. Yahya Saleh

## Slide 2: Prepared By :
RAGHAD HABAYEB
MAHRAN ABU BASHA
NIDAL AWADEH

## Slide 3: OUTLINE

## Slide 4: About AL ARZ
Founded in 1950
2000 m2 , 10 000 m2 in total
HACCP certificate
4 Million liter of ice cream
Operats 24/7
180 workers
8 production lines

## Slide 5: MARKET SHARE

## Slide 6: Problem Statement
Few documentation
Incorrect documentation
The lack of maintenance reports
The lack of maintenance procedures
The lack of maintenance department
Sudden breakdowns
No labeling system for spare parts
No coding system for spare parts
No computerized maintenance system
No spare parts management
No spare parts sorting

## Slide 7: Objectives
Improve Maintenance System
Establish shelf and coding system
Apply spare parts management
.
Establish computerized maintenance system
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 8: Literature Review

## Slide 9: Literature Review
ABC Inventory Classification
Inventory classification using ABC analysis is one of the most widely employed techniques in organizations. Normally, the items are classified based on the annual use value, which is the product of annual demand and average unit price. Class A items are relatively few in number but constitute a relatively large amount of annual use value, while class C items are relatively large in number but not used so often.
Strengths, weaknesses, opportunities and threats (SWOT) analysis is a device that helps business managers to evaluate the strengths, weaknesses, opportunities and threats involved in any business enterprise. A SWOT analysis can help them gain insights into the past and think of possible solutions to existing or potential problems
SWOT Analysis

## Slide 10: Methodology
Spare Parts Management
Shelving System
Availability
Computerized Maintenance Management System
SWOT Analysis
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 11: SWOT ANALYSIS
S
O
T
W

## Slide 12: CORRECTIVE MAINTENANCE REPORT

## Slide 13: RESULTS
MAINTENANCE coordinator
ABC ANYLSIS
FISH AND BONE
AVAILABILITY
SMART
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 14: Shelving system

## Slide 16: AVAILABILITY
These four distributions were studied for the analysis of the data:
Normal Distribution
Exponential Distribution
Weibull Distribution
Gamma distribution

## Slide 17: Determining mean time to repair
Normal distribution
Exponential distribution

## Slide 18: Determining mean time to repair
Weibull distribution
Gamma distribution

## Slide 19
Goodness of fit for repair time
we can judge the best distribution that best represent the repair time data by two perspectives which are:
The P-value: the bigger the less variation and best represent.
Fitting the straight line
As a result, the normal distribution seems to be the best representation of repair time data

## Slide 20
The resulting MTTR of the repair time data is 98.4 mins.

## Slide 21: Determining mean time between failure
NORMAL DISTRIBUTION
EXPONENTIOL DISTRIBUTION

## Slide 22: Determining mean time between failure
WEIBULL DISTRIBUTION
WEIBULL DISTRIBUTION

## Slide 23: Goodness of fit
Goodness of fit for up time
As a result of the analysis, we can judge the best distribution that best represent the up time data by the same criteria as:
Gamma distribution is the best representation of the up time data.

## Slide 24: Goodness of fit
The resulting MTBF of the up time data is 4197.65 mins.
The availability of the machines is A = MTBF / (MTBF+MTTR) = 4197.65 / (4197.65 + 98.4)= 97.7 %

## Slide 25: Fish and bone diagram

## Slide 26: ABC ANALYSIS
CLASS C
CLASS B
CLASS A
ABC ANALYSIS
Class A
Class B
Class C
About 30% of the spare parts items represent 15% of their consumption
About 50% of the spare parts items represent 5% of their consumption
About 20% of the spare parts items represent 80% of their consumption
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 27
Description | Total number of parts | Percentage of items in the inventory | Cumulative usage value | Percentage of annual sales value | Cumulative of annual sales value
A | 34 | 21.6561% | 21.6561% | 75% | 75%
B | 53 | 33.7579% | 55.414% | 20% | 95%
C | 70 | 44.586% | 100% | 5% | 100%
Total | 157 | 100% |  | 100% | 

## Slide 29
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 30: ABC ANALYSIS CONTROL
Editable SmartArt Graphic – 3 Gears Max
SAFETY STOCK
SS= Z × σLT × D avg
REORDER POINT
Reorder Point = LEAD TIME DEMAND + SAFETY STOCK = REORDER POINT
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 31: Based on experience and judgment

## Slide 32: COMPUTERIZED MAINTENANCE MANAGEMENT SYSTEM
BENEFITS OF CMMS
Reduce downtime and repair costs
Manage work orders efficiently
Reduce overtime
Plan and schedule preventative maintenance
Manage spare parts inventory
A Computerized Maintenance Management System is a computer software that helps in keeping records of all the maintenance procedures and maintenance tasks including scheduling and tracking the maintenance steps, it also keeps a historical record of the maintenance work they performed.
Eliminate paperwork
Increase safety
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 33: Maintenance coordinator
Maintenance coordinator is a maintenance management software and it includes:
scheduling for maintenance activities .
purchasing and receiving of spare parts .
listing all possible vendors and contractors .
managing of equipment (machines) and assets .
Inventory management at spare parts warehouse .
creating repair orders .

## Slide 34: Maintenance coordinator

## Slide 35: Scheduling for maintenance activities

## Slide 36: Purchasing and receiving of spare parts

## Slide 37: listing all possible vendors and contractors

## Slide 38: Inventory management at spare parts warehouse

## Slide 39: Creating repair orders

## Slide 40: ADVANTAGES OF CM
Coordination between all parts helps in finding an overall view about every single shot in the maintenance activities.
All entered data in each part is registered in the overall system so the system is integrated.
.
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 41: Disadvantages of cm
Data entering process isn’t easy. It needs the coordination of multiple parts in the system.
Too much data is required which sometimes isn’t needed and may reduce the efficiency of the process.
After spare parts checkout process, if the number of spare parts is low or lower than the minimum level, no warning alert is shown.
Not easily understood for the employees in the maintenance department so more time is required to register the data and activities.
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 42: smart
SMART is a computerized maintenance management system.
Used due to the fast improvement in the manufacturing sector.
SMART system is a new system designed with the newest techniques that insures the continuity of the machines with the highest efficiency and the lowest cost possible.
SMART system includes many different maintenance management branches including:
Client’s information management.
Contracts management.
Warehouse management system.
Maintenance management system.
Machines management.

## Slide 43: MAIN PAGE

## Slide 44: Client’s information management

## Slide 45: Contracts management.

## Slide 46: Warehouse management system.

## Slide 47: Add a spare part

## Slide 48: Maintenance management system:

## Slide 49: maintenance procedures

## Slide 50: Adding a maintenance procedure

## Slide 51: Machines management.

## Slide 52: Areas where SMART can be used in
SMART can be used in any field that involves machines, devices, or assets either inside or outside the factory
Machines and factories’ devices
Cars and automobiles
Cell phones
Personal computers, printers, and their accessories
Electronic devises and elevators
Phones and communication devices
Faxes
Electrical devices (fridges, washing machines …etc.)
Streets, conservative wall, and sidewalks
Electricity, water and sewage networks
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 53: SMART Characteristics:
Easy to understand
Flexibility in presenting and printing reports
The ability to work on many databases
Multilanguage (English, Arabic)
Multiuser
Ability to control display setting (colors and more)
Indexes available in all screens with many different sorting possibilities
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 54: SMART advantages
1
2
3
4
5
6
7
8
decreases the stoppage time
Decreases the overall maintenance
Reduces the paper work and manual work
Extends equipment life
Keeps your maintenance cost within appropriate budget
Less maintenance operation cost
.
Less overtime cost.
.
Reduced downtime
.
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 55: limitations
Lack of historical data available at the factory
The resistance of change by some of the maintenance employees.
The messy situation in the maintenance department at the factory.
Many of the maintenance reports weren't delivered
No clear job description was implemented
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 56: Conclusion
Implementing a computerized maintenance system helps to manage maintenance effortlessly
Implementing ABC analysis make it easier to track and monitor spare parts
Using fish and bone diagram helps in determining the possible causes of the problems and helps in solving them .
Implementing reliability analysis helps determine the availability of the machines which helps in exceeding it’s life
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 57: RECOMMENDATIONS
Buy the SMART maintenance software as it’s simpler, in Arabic and can be connected with AL SHAMEL
To classify the spare parts based on the importance and the usage value as explained by the abc analysis
Determine the availability of the other machines and apply reliability analysis
Implement the corrective maintenance report we constructed
Determine safety stock and reorder point based on physical data rather than experience
Notes: © Copyright Showeet.com – Free PowerPoint Templates

## Slide 58: Thank You!
Notes: © Copyright Showeet.com – Free PowerPoint Templates