## Slide 1
An-Najah National University
Faculty of Engineering & Information Technology
Department of Building Engineering
“Re-Design of Multi-Function Building “
Prepared by: Bassam Abu Al-Hoos.
Hasan Halbouni.
Saad Ashour.
Supervisor: Eng. Fady Fatayer.
1

## Slide 2: Content:
Site location
Acoustic design
Quantity Surveying & Cost Estimation
SAFETY AND FIRE FIGHTING
Architectural aspect
Structural Design
Electro-Mecenichal Design
Environmental Aspects

## Slide 3: Site location
The location of the building is in Nablus city, Tunis Street, about 542 m above sea level with a total area of 1109 M2 with a total floor area of 8362 M2

## Slide 4
Site Analysis:
Sun Path
Wind Direction
Sound Level
Best view & Surrounding

## Slide 5: Architectural Aspects

## Slide 6: 3d Model for the building

## Slide 7: Second parking floor
After
Before

## Slide 8: First parking floor
Before
After

## Slide 9: First basement floor
Before
After

## Slide 10: Ground floor
After
Before

## Slide 11: First floor
After
Before

## Slide 12: Second & third floor
After
Before

## Slide 13: Forth ,Fifth & Sixth floors
After
Before

## Slide 14: Elevations
Northern elevation
Western elevation

## Slide 15: Sections

## Slide 16: Environmental Design

## Slide 17
Environmental Design
Daylighting
Shading
Thermal design

## Slide 18: Daylighting
The Energy Conservation Measures (ECM) :
Adding Louvers & Cantilevers
Using low transmission glass.
Using insulation materials
The Model of the building in Design builder
The Model of the building in Design builder

## Slide 19: Daylight analysis for the model for the offices & Warehouses
Offices
Warehouses

## Slide 20: Shading & over Shadowing
21 July /On 8:00 AM
21 July /On 6:00 PM
21June /On 8:00 AM
21 June /On 6:00 PM

## Slide 21
Thermal Design

## Slide 22: The materials that were used in design builder
Component | Layers | U-value (W/m2 .k)
External wall | stone | 0.456
 | concrete | 
 | extruded polystyrene | 
 | concrete block | 
 | plaster | 
Internal wall | plaster | 2.1
 | concrete block | 
 | plaster | 
Roof | asphalt roll roofing | 0.278
 | cast concrete | 
 | polyurethane | 
 | cast concrete | 
 | hollow concrete block | 
 | Plaster | 
Glass | Dbl glass | 1.493
External Wall Section
Roof Section
Internal Wall Section

## Slide 23: The comfort graph for the building from Design Builder

## Slide 24
Comfort hour
The site and source energy for the building from Design Builder

## Slide 25
Floor No. | Design capacity (KW)
Basement | 34.66
Ground | 19.53
First | 32.02
Second | 25.36
Third | 23.68
Fourth | 15.99
Fifth | 16.16
Sexth | 22.08
Total | 189.48
Design Capacities :

## Slide 26: Structural design

## Slide 27: Structural design

## Slide 28: Codes, specification & Material:
Codes and specification:
ASCE for loads and combinations.
ACI 318 (American Concrete Institute).
UBC-97 code
Material:
Concrete B400
f'c = 32Mpa, Density = 2500 Kg/ M3.
Steel
Fy = 420 Mpa, Density = 7600.97 Kg/M3.
Hollow Block
(400*200*280) mm.

## Slide 29: Loads:
super imposed dead load (SID): One way
weight of brick (kN/m.rib) =1.34
weight of brick (kN/m2)= 2.44
SID to be added to Etabs = 6.44 KN/m2
Two way
weight of brick (kN/rib^2) =0.54
weight of brick (kN/m^2) =1.78
SID to be added in Etabs =5.78 KN/m2
Live load for retail | 4.79 KN/m2
Live load for residential | 2 KN/m2
Live load for office | 2.4 KN/m2

## Slide 30: Model layout

## Slide 31: Checks:
Equilibrium check
Stress-Strain check
Seismic design check

## Slide 32: Equilibrium check:
Load | Etabs | Manual | Error%
Live | 18904.23 KN | 19040.35 KN | 0.71
SID |  |  | 
One way |  | 8502.78 KN | 
Two way |  | 31359.30 KN | 
Walls |  | 15992.6 KN | 
Total | 55804.38 KN | 55854.68 KN | 0.09
For Live & SID loads

## Slide 33: Equilibrium check:
ذ
Dead | Etabs | Manual | Error %
Column | - | - | -
circular column (90)cm | - | 1025.55 | -
Column (110*60)cm | - | 589.87 | -
Column (30*80)cm | - | 900 | -
Column (80*80)cm | - | 2288 | -
Column (85*85)cm | - | 645.73 | -
Column (65*65)cm | - | 1132.82 | -
Column (75*75)cm | - | 1005.46 | -
Beams | - | 26464.57 | -
Walls | - | 17213.21 | -
One-way slab | - | 27442.11 | -
Two-way Slab | - | 7070.83 | -
Ramp | - | 1614.12 | -
Total | 85983.49 | 87392.27 | 1.61
For Dead load:

## Slide 34: Stress-Strain check:
      Columns:
      beam:
      One way ribbed slab

## Slide 35
For two way slab the checks will be made for column strip, middle strip, frame and beam. Find the column strip width and frame width.
Stress-Strain check:
Two-way ribbed slab:
two way |  |  |  |  |  | Diff% |  |  | 
 |  | frame | CS | MS | Beam | frame | CS | MS | Beam
Etabs | M1 | 201.7 | 144 | 57.7 | 85.3 | 5.32 | 25.69 | -45.49 | 11.48
 | M2 | 193 | 108 | 85 | 80.5 | 3.62 | 21.29 | -18.82 | 8.94
 | M+ | 211 | 115 | 96 | 100.6 | 25.78 | 15.26 | 26.70 | 43.34
safe | M1 | 190.95 | 107 | 83.95 | 75.5 |  |  |  | 
 | M2 | 186 | 85 | 101 | 73.3 |  |  |  | 
 | M+ | 645.2 | 297 | 348.2 | 57 |  |  |  | 

## Slide 36: Seismic design check:
The check consist of:
Modal Mass Participation ratio
Period check
base shear checks
Drift check

## Slide 37: Modal Mass Participation ratio
The check according to UBC code must be greater than 90% in order to use response spectrum analysis.

## Slide 38: base shear checks
in this check base shear from response spectrum cases equal or more than base shear from equivalent static method.

## Slide 39: Drift check:
This check is made to see the difference between the displacements in the story, in the both direction X and Y.
story | height | dis_x | dis_y | drift_x | drift_y | delta_x | delta_y | delta_limit
0 |  | 0 | 0 |  |  |  |  | 
1 | 2500 | 0.084 | 0.186 | 0.084 | 0.186 | 0.3234 | 0.7161 | 50
2 | 3750 | 2.78 | 0.734 | 2.696 | 0.548 | 10.3796 | 2.1098 | 75
3 | 4500 | 0.714 | 1.511 | 2.066 | 0.777 | 7.9541 | 2.99145 | 90
4 | 4250 | 2.251 | 2.827 | 1.537 | 1.316 | 5.91745 | 5.0666 | 85
5 | 3000 | 3.997 | 3.845 | 1.746 | 1.018 | 6.7221 | 3.9193 | 60
6 | 3000 | 4.55 | 4.155 | 0.553 | 0.31 | 2.12905 | 1.1935 | 60
7 | 3000 | 4.56 | 3.99 | 0.01 | -0.165 | 0.0385 | -0.63525 | 60
8 | 3000 | 4.155 | 3.49 | 0.405 | -0.5 | 1.55925 | -1.925 | 60
9 | 3000 | 3.573 | 2.68 | 0.582 | -0.81 | 2.2407 | -3.1185 | 60
10 | 3000 | 3.526 | 2.48 | 0.047 | -0.2 | 0.18095 | -0.77 | 60

## Slide 40: Design of structural elements
Slab:

## Slide 41
Beams:

## Slide 42
Columns:

## Slide 43
columns:

## Slide 44
Shear wall:

## Slide 45
Footing:

## Slide 46
Retaining wall:

## Slide 47
Stairs:

## Slide 48: Electro-Mechanical Design

## Slide 49
Electro-Mechanical Design
Hvac
Artificial lighting
Water supply & Drainage

## Slide 50
Hvac System

## Slide 51: H-vac System
Vrf (Variable refrigerant flow) system has been used.
Equipment from Toshiba company has been used.
Square diffusers for retail stores have been used.
Slot linear diffusers for warehouses & Offices have been used.
Split unit in residential apartments has been used.
Floor No. | Design capacity (KW)
Basement | 34.66
Ground | 19.53
First | 32.02
Second | 25.36
Third | 23.68
Fourth | 15.99
Fifth | 16.16
Sexth | 22.08
Total | 189.48
Design Capacities :

## Slide 52
Outdoor unit
Mini outdoor unit for apartments
Outdoor unit for stores ,warehouses &offices

## Slide 53
Indoor units:
Fan coil
Indoor fresh air intake
Indoor wall mounted
Square Diffuser
Slot linear Diffuser

## Slide 54
The distribution of the ducts and diffusers in the ground floor.

## Slide 55
The distribution of the ducts and diffusers in Warehouses.

## Slide 56
The distribution of the ducts and diffusers in Offices.

## Slide 57
The distribution of the ducts and diffusers in apartments

## Slide 58
Out door units in roof

## Slide 59
Artificial lighting

## Slide 60
Office lighting
Luminaires Selected
Simulation result
Luminaires distribution for office

## Slide 61
Office lighting
Staff room
Manager room
reception
Meeting room
corridor

## Slide 62
Residential apartment lighting
Simulation result
Luminaires Selected
Luminaires distribution for an apartment

## Slide 63
Living room
Master bedroom
Kitchen
Girls bedroom
Boys bedroom
Residential apartment lighting
Living& Dining room

## Slide 64
Retail shop lighting
Luminaires Selected
Simulation result
Luminaires distribution for a store

## Slide 65
Restaurant lighting
Luminaires Selected
Luminaires distribution for the restaurant
Simulation result

## Slide 66
Socket and distribution board
Distribution of circuit breaker in distribution board 15
Distribution of sockets for an office

## Slide 67
Place of main distribution board
The electrical loads on M.D.B
The electrical loads of HVAC & elevators
Ascending system for electrical cables

## Slide 68
Water supply & Drainage

## Slide 69
Water system
For apartments the average day consumption is 159.2L/apt.
For offices the average day consumption is 3.8 L/person.
The pipes used in the building are different from one function to the other.
floor | FU total
b1 | 40
G.F | 40
1ST floor | 20
offices | 100
residentials | 276
total | 476
Total FU for the building

## Slide 70
roof water system layout

## Slide 71
Apartments water system

## Slide 72
Trash shaft

## Slide 73
Apartments drainage
Drainage

## Slide 74
Roof drainage

## Slide 75
Parking drainage

## Slide 76
Pipes in parking ceiling

## Slide 77: Acoustical Design

## Slide 78: Acoustic design:
The spaces that were designed acoustically in the building:
Manager office
Staff room
Guest room
The absorption coefficient for the finished material

## Slide 79
Reverberation time(RT60):
The reverberation time for the guest room according to Sabine
The reverberation time for the staff room according to Sabine

## Slide 80
Sound Transmission Loss (STC)
The sound transmission loss (STC) for the internal walls between different spaces
The sound transmission loss (STC) for the external walls

## Slide 81
Impact Insulation Class (IIC)
The Impact insulation class for the ceiling = 67 dB and the calculated IIC for the ceiling should be more than 50 dB, so it is ok.

## Slide 82: Safety & Fire suppression system

## Slide 83: Fire fighting system
Signs and emergency light
Part of fire fighting system for office floor
Suppression systems
Detection and notifications

## Slide 84
Signs and emergency light
Fire hose
Stand pipe
Heat detector
Smoke detector

## Slide 85
sprinkler
space | Sprinkler type
parking | Water sprinkler
warehouse | Water sprinkler
Restaurant kitchen | Wet chemical sprinkler
space | Extinguisher type
office | Dry powder Extinguisher
warehouse | Dry powder Extinguisher
Residential apartment | Dry powder Extinguisher
kitchen | Wet chemical Extinguisher
Mechanical & Electrical room | CO2 Extinguisher
Extinguisher

## Slide 86
Over-lap between all systems
Over –lap for second parking
Over –lap for offices floors

## Slide 87: Quantity Surveying & Cost Estimation

## Slide 88
Quantity Surveying
The total cost of the building is 13,196,891.66 ILS and the total area of the building is 8362 m2 which means that the total unit cost is 1578.2 ILS/ m2.
Activity | Cost (ILS)
Earth work | 951,314.06
Foundation Work | 830,287.10
Sub Structure Work | 2,754,492.10
b2&b1 Floor work | 561,160.00
ground Floor work | 306,706.40
First to seventh Floor Work | 1,181,824.00
Stair Work | 49,603.00
Finishes | 4,062,322.00
Fire Alarm | 111,400.00
Lighting & Electrical | 849,100.00
Mechanical work | 1,038,683.00
Elevators | 500,000
Total | 13,196,891.66

## Slide 89
Chart: Percentage of each work from total cost of the building
| Earth work | Foundation Work | Sub Structure Work | b2&b1 Floor work | ground Floor work | First to seventh Floor Work | Stair Work | Finishes | Fire Alarm | Lighting & Electrical | Mechanical work | Elevators
 | 951314.0625 | 830287.1 | 2754492.1 | 561160 | 306706.4 | 1181824 | 49603 | 4062322 | 111400 | 849100 | 1038683 | 500000

## Slide 90
The End