## Slide 1
An-Najah National University
Mechatronics Engineering Department
Electric Wheel Chair
Prepared by:
Bassam .H. Subuh
Hamdan .R. Shehadeh
Karim .M. Yasein
Mohammad .R. Beleh
Supervisor:
Dr. Aladdin Salah Masri

## Slide 2: Contents
Introduction
Problem
Design
Electrical part
Features

## Slide 3: Introduction
In this project we design and build an electrical wheel chair trying to help the special needs segment and provide them electric chairs which are highly performance with low price compared with those in the local market.

## Slide 4
A people with special needs is (3-4)% of the total population.
And the latest statistics for the disabled have proved that these is in Palestine, the highest proportion disability in the middle east but in the world by population
and the reason for the high
number of disabled people is
the occupation that use violence
against civilians.

## Slide 5: Problem
The main problem that we intend to solve in our project is to help the disabled to move from place to place without the need to receive help from others
In order to solve this problem we decided to improve the manual wheel chair by Adding motors , joystick and voice recognition.

## Slide 6: Design
As shown in figure the project consist:
Two DC motors.
Four wheels.
Simple structure chair.
Battery.
Microcontroller circuits.
Control unit( push buttons, joystick,
voice recognition ……. )

## Slide 7: Design specifications
Weight Capacity: 165 Lbs. , 75 kg
Maximum Speed: flat surface 6 MPH, 9.5 kmh, : incline sufrace 4 MPH, 6.4 kmh
Turning Radius: 33'' , 83.8 cm
Ground Clearance: 4.5" , 11.4 cm
Range of Travel: 25 miles per charge , 40.25 km
seat Width 18", 20" / 45.7 cm , 50.8 cm
Seat Length 16’’ / 40.6
Seat Depths : 16" , 40.6 cm
Seat-to-Floor Height 19.5" / 49.5
Backrest Height 17.5’’ / 44.5
Overall Length: 41" , 104.1 cm
Overall Width: 23.5" to 27.5" , 59.7 cm to 69.9 cm
Overall height : 36.5 , 93 cm
Wheels: 12.5' , 31.8 cm" Drive /8' , 20.3 cm" Caster
Heaviest Piece: 100 Lbs ,45 kg

## Slide 8: Design of the chair
Ay=130N by=345N CY=75N
We will take a factor of safety (n) =2

## Slide 9: Electrical part
Motor selection
Electrical motors are DC permanent magnet motors.
High degree of efficiency (up to 88%) and by low operating noise (45dB)
Motors can be run for a short time up to four times their rated torque.
Rated power from 350 Watt to 550 Watt
rated speed from 1500 to 4000 rpm(revolutions/minute)
Operating voltage 24V.
2 poles.

## Slide 10: Electrical part
Battery
(2×26Ah) 12v dry battery
Rechargeable
Safe operation
Long life cycle

## Slide 11: Electrical part
H Bridge
We will use H-Bridge
to control the speed and direction of the motor.

## Slide 12: Electrical part
PWM is a commonly used technique for controlling power to inertial electrical devices, made practical by modern electronic power switches.
Pulse Width Modulation (PWM)

## Slide 13: Features
The position of the joystick is calculated from
the two potentiometers in the joystick.
The joystick can move in two dimensions
which typically would represent any two
dimensional quantity (X and Y ).
To read the potentiometers we
use the analog Read() function(ADC).
Joystick

## Slide 14: Features
Voice recognition
In our project we will rely on the voice in the process of controlling the electric chair, since the users of this electric chair are disabled with four parties, so we will use voice recognition technology so that we can achieve this process.

## Slide 15: Any Questions?