## Slide 1
An-Najah National University Faculty of Engineering and Information Technology Industrial engineering department
An-Najah National University
Faculty of Engineering and Information Technology
Industrial Engineering Department
2))Graduation Project
Assessment of the Implementation of Lean Manufacturing Concepts in the AL Sharif foodstuff factory.
جامعة النجاح الوطنية كلية الهندسة وتكنولوجيا المعلومات قسم الهندسة الصناعية
Prepared By:
Tasneem Mallah
Raghad Habayeb
Zahra Sharif
Supervised By:
Dr Ahmed Al Ramahi

## Slide 2: Outline:
Introduction
Problem statement
Objective
Methodology
Results & Gap Analysis
Framework to implement lean manufacturing
Conclusion
Recommendations

## Slide 3: Introduction:
Al-Sharif foodstuff manufacturing and trading company was founded in 1990 AD in Hebron city. For the production of syrup and western desserts. The factory began to produce different syrup tastes with high quality and international standards that can compete with other products founded in Palestine. Two years later, the company began to produce western desserts with more than 10 categories.

## Slide 4: Cont …
Al-Sharif company production lines:
Concentrated syrup production line.
production line of glacier.
Production line of Chips.
Pastry production line.
Biscuit production line.
Ice cream production line.
Cake production line.

## Slide 5: Problem statement
The company produces its primary products at a rate that would not meet a sales forecast, a number that would double the current rate of demand if the main problems were studied, analyzed and solved.
The main reason of that is the reliance of the company on traditional production and administrative approaches which affects directly productivity, quality and profitability.
The company wants to follow a strategy to reduce costs, increase productivity and gain a competitive advantage., and know the weaknesses in the company and the possibility of improving them to increase product quality and the efficiency of the company's performance at all levels.

## Slide 6: Objective
The main goal of this project is to assess level of implementation of lean manufacturing concepts in Al Sharif company; this is to be done through focusing on the extent to which lean manufacturing tools are practiced in the factory. Within this goal; the project aims to satisfy the following objective:
    Come up with clear gap analysis and solid recommendations that highlight opportunities for the company development, improve its performance and increase productivity through the adaptation of lean manufacturing concept.

## Slide 7: Methodology
Conduct comprehensive literature review about lean manufacturing Philosophy, principles, tools, and benefits.
Collect primary comprehensive data and information at Al-Sharif factory.
The factors and obstacles faced by productive processes can be identified
Develop an assessment tool that commensurate with the production processes at Al-Sharif factory.

## Slide 8: Con …
Design data collection tools
Data collection tool consists of two section:
a. The first section of the questionnaire:
This section of the questionnaire was created based on lean manufacturing tool
b. The second section of the questionnaire:
Considering an important issue could be regarded as the more important than assessing the implementation of lean manufacturing tools, this issue is to assess knowledge of plant management about lean manufacturing concept in terms of its benefits, limitations and the factors that help to implement it.
Analyze collected data to come up with clear gab analysis, weaknesses, strengths, and solid recommendations that highlight opportunities of industry and performance development in the factory via the adaptation of lean manufacturing concept.

## Slide 9: Gap Analysis & Results
Description of respondents individuals
The sample included eight individuals who filled out the questionnaire for the project :
Chairman
Executive manager
Production Manager
Production Manager
quality manager
Inventory and Warehouse Manager
Director of Personnel
Maintenance manager

## Slide 10: Cont …
Prior knowledge of the concept of lean manufacturing
Chart: Prior knowledge of the concept of lean manufacturing
| Yes | No
 | 6 | 2

## Slide 11
Perceptions company about lean manufacturing
Benefits of lean manufacturing:
shows the results of perception of the respondents on the benefits of lean manufacturing. with a mean of " 4.0125 " and the standard deviation of " 0.525 ", this indicates that most of the company managers and administrators who filled the Questionnaire have a positive perception about the benefits of lean manufacturing and the importance of lean manufacturing application in the company; Of course this is after explaining o hem about lean manufacturing as a concept.
Factors helping in implementing concept of lean manufacturing:
shows the perception of the company about the factors which help to implement the concept of lean manufacturing in their company, also show results that the company have factors help to implement lean manufacturing have a mean of " 4.437" and a standard deviation of "0.535 ", and percentage (88.74%) . This indicates the company's acceptance and willingness to apply lean manufacturing practice.
Cont …

## Slide 12: Cont …
Obstacles in implementing lean manufacturing:
shows the perception of the company for obstacles in implementing lean Manufacturing, the results show that the obstacles that could prevent the application of lean manufacturing are weak, that has mean (2.15), the standard deviation is (0.53) and percentage of obstacles is (42.9%). This is an indication of the company’s ability and Portability to apply lean manufacturing without significant barriers preventing the company from applying it.

## Slide 13: Analysis of the implementation of lean tools
value stream mapping.
 | V.S.M |  | M | STD
Q1 | A map of the production process is used starting from the receipt of the raw materials to the delivery of the final products to the customers explaining the needs of each stage of the raw materials and the Period of time and the number of workers that each process need ? |  | 1.22 | 0.441
Q2 | If such as this map is used, the manufacturing process is improved depending on it |  | 2.11 | 0.928
M |  |  | 1.64 | 0.6844

## Slide 14
Total productive maintenance
 | TPM | Mean | S.D
Q1 | Immediately repair faults | 4.49 | 0.66
Q2 | Periodic maintenance | 3.34 | 0.48
Q3 | Spare part | 4.06 | 0.48
Q4 | Recording failure and analysis | 3.37 | 1.11
Q5 | Preventive maintenance | 2.91 | 0.28
Q6 | Predictive maintenance | 1.80 | 0.80
Q7 | Simple failure by worker | 2.94 | 0.97
Mean |  | 3.27 | 0.7

## Slide 15
5S (Housekeeping):
 | 5S | M | S.D
Q1 | Sort | 4.8974 | 0.307
Q2 | Set in order | 4.5128 | 0.506
Q3 | Shine | 4.2308 | 0.986
Q4 | Standardize | 3.6154 | 0.493
Q5 | Sustain | 3.8974 | 0.307
Mean |  | 4.23 | 0.519

## Slide 16
Poka- Yoke
 | Poka- Yoke | Mean | STD
Q1 | Inspection and test | 4.00 | 0.00
Q2 | Defect detectors | 1.25 | 0.67
Q3 | Sensing devices | 1.38 | 1.01
Q4 | Standardize work | 3.63 | 0.71
Q5 | SPC tools | 1.25 | 0.67
Mean |  | 2.3 | 0.612

## Slide 17
Just in time
 | JIT | M | S.D
Q1 | Production lot size | 3.76 | .739
Q2 | Production use by forecasting | 3.28 | .922
Q3 | customer demand | 3.93 | .961
Q4 | Access raw materials in right time | 4.59 | .501
Q5 | The quantity of inventory of finished products is small | 4.48 | .688
Q6 | The amount of inventory of raw materials is sufficient | 4.59 | .501
Q7 | Delivery of orders to customers | 4.59 | .501
M |  | 4.17 | 0.687

## Slide 18
SMED
SMED | SMED | M | S.D
Q1 | Change tools and templates used in production | 4.25 | 0.71
Q2 | Time to change tools or templates Used in the production process | 4.50 | 0.53
M |  | 4.375 | 0.62

## Slide 19
Kaizen
 | Kaizen | M | STD
Q1 | Stability of production lines | 4.15 | 0.364
Q2 | Problems of production lines | 2.61 | 0.704
Q3 | Effectiveness | 3.27 | 0.452
Q4 | integrated team | 4.00 | 0.000
Q5 | Workers on production lines are given powers to intervene in production process decisions | 3.11 | 0.435
Q6 | information for employees | 4.64 | .489
-Q7 | Development Programs | 2.12 | .927
Q8 | Improvement of production lines | 3.85 | .364
M |  | 3.42 | 0.466

## Slide 20
JIDOKA
 | Jidoka | M | S.D
Q1 | All production lines are automated | 2.13 | .991
Q2 | The production line stops itself | 1.38 | .744
Q3 | Self-maintenance | 1.38 | .744
Q4 | Packing and filling automation | 1.38 | .744
M |  | 1.56 | 0.806

## Slide 21
Heijunka
Hejunka | Hejunka | M | S.D
Q1 | Production changes from period to period | 2.50 | .535
Q2 | Stability of annual demand for production | 3.75 | .463
Q3 | Excess of inventory of final products | 2.00 | .926
Q4 | over time | 1.38 | .744
Q5 | Change the number of workers | 2.50 | .535
M |  | 2.43 | .640

## Slide 22: key performance indicator
 | The extent of implementing KPI | 
Q1 | There is an indicator that monitors the factory profits continuously every month | Yes
Q2 | Monitoring and documentation corresponds to the available resources daily with the amount of work that must be carried out | No
Q3 | There is an index documenting the profit margin (the percentage of the gross profit for the total income that the factory collects on a monthly basis) | No
Q4 | There is an indicator to measure and evaluate the annual performance of workers | No
Q5 | Staff recruitment and change are monitored and documented | Yes
Q6 | Returned quantities of products It is tuned and documented daily | No
Q7 | There is an indicator to measure the efficiency of production lines | Yes
Q8 | There is an indicator to measure productivity | Yes
Q9 | The company adopts a complaints system from distributors and customers. | No
Q10 | Delays in delivering products to customers are monitored and documented. | No
Q11 | The absence rate of workers is monitored and documented frequently | Yes
Q12 | The company has a strategic development plan | Yes
Q13 | All performance indicators are quantitative indicators | No
Q14 | Are the measurement indicators updated periodically? | No

## Slide 23: Framework to implement lean manufacturing
a framework to implement lean manufacturing for Al Sharif company will be created to improve practices of lean manufacturing tools.
This will help Al Sharif company in reducing wastes in production process and in the administration, which in turn reflected in lower costs, increase profits, raise quality, minimization in defective products, and customer's satisfaction.

## Slide 25: VALUE STREAM MAPPING (VSM): (mean=“3.27”)
Using VSM | Select the product or product family. Mapping the current value stream, from the beginning of the arrival of the raw materials to deliver the finished goods to the customer. Create a VSM for each product manufacturing process Analyze the current value flow map, identify problem areas, get rid of activities that do not add or reduce any value to a minimum, then create a future map. 5. Estimate the results by comparing future maps with the initial map

## Slide 27: total productive maintenance: (mean=“3.27”)
Choosing which data to gather, analyze and act upon. take a pragmatic approach and analyze the data that their machines already produce. Create predictive maintenance schedule for machines, which help control the stock of spare parts. | Predictive maintenance
Special guide is available for machines that should be used in preventive maintenance operations . Scheduling preventive maintenance and Follow-up the procedures and confirm it by the maintenance officer. | Preventive maintenance
Identify the minor errors that any operator can fix. Training workers who works on machines to repair simple failures. Rebuilding culture and raising awareness about the importance of maintenance for workers. | Simple failure by worker
Make a periodic inspection schedule for the machine according to its type and the type of work required of it | Periodic maintenance
Record errors if it occurs by using failure. Analysis of faults for each machine using statistical methods. Classification of faults in terms of severity. | Recording failure and analysis

## Slide 28: Avoid mistakes and prevent them (Poka-Yoke): (mean=“3.27”)
Using control chart of production processes. Use acceptance sample of raw and primary material. | SPC tools (Statistical method)
Placement of control devices. The machine stops immediately when any malfunction occurs. It corrects the error automatically, without human intervention. It has a high ability to achieve zero defect. | Defect detectors
the line is provided with a device to monitor the size of the piece when it passes on the line, before the packaging process. A device to monitor the operation of the production lines, as it gives a signal if something goes wrong, so the defect is fixed immediately | Sensing devices

## Slide 29: Just In Time(JIT)
the company must accurately forecast demand for a short period seasonal product. Examine sales patterns to see when sales have shown peaks and valleys, this will give you an idea of when to be ready for rising and falling sales. (Seasonal sale) | Forecast (MEAN=3.28)

## Slide 30: Kaizen
Create training sessions for staff and workers Create a staff performance assessment system helps raise as adaptability and motivation | Development programs
Form Problem-Solving Teams Collect Data to Find the Most Efficient Work Sequence. Create A Work Standard Practice the Sequence Up to Ten Times. If Employees Can Repeat It Exactly and Consistently, Then It Is A Viable Sequence. | problems of production line
Using leadership techniques, selecting supervisors who have skills and art in dealing with workers. Introducing the implementation of this strategy Apply modern management concepts Providing the information required for the worker. | Enable the worker to make a decision
Train workers to do more work in one work station so as to increase the utilization of workers. Give employees decisions to intervene in the production process in the event of technical problems and lack of presence of responsible | Effectiveness

## Slide 31: JIDOKA
use automation for machining, creating, and shaping parts, as well as for assembling products. Placing Warning devices: to stop the machine from running, and to alert the operator if something wrong is going to happen. It uses voice and optical warning systems, as well as color-coding. | JIDOKA

## Slide 32: key performance indicator
Write a clear objective for your KPI
Share your KPI with stakeholders
Review the KPI on a weekly or monthly basis
Make sure the KPI is actionable
Evolve your KPI to fit the changing needs of the business
Check to see that the KPI is attainable
Update your KPI objectives as needed
Bringing it all together

## Slide 33: Conclusion:
in this project, we develop a questionnaire for the assessment of the implementation of lean manufacturing concepts in our factory, the assessment is performed by focusing on lean manufacturing tools and its concepts, which helps companies to analyze the gap existing in implementing this concept. This questionnaire contains 10 tools, each tool identifies principles of implementing lean manufacturing in qualitative perspective. This questionnaire may not cover all performance indicators that have a potential to assess lean concepts in companies, but we believe it captures the most critical ones.

## Slide 34
We noted from the questionnaire that 25% of people who knew about its predecessor were lean manufacturing productivity.
As a conclusion for implementing lean manufacturing practices with a mean of " 4.0125 " and a standard deviation of " 0.525 “, most of the company managers and administrators who filled the Questionnaire, have a positive perception and a good understanding of the importance of applying lean manufacturing for the current system and performance in the company, and its benefits for the whole management system and their.
Cont …

## Slide 35: Recommendations:
After development the questionnaire it’s clear that the company have weak knowledge or understanding about concept of lean manufacturing due to implementing traditional management rather than implementing lean manufacturing concepts which gain powerful competitive advantage in the globalized market place for any industry. These are some recommendations that the company would prefer to take to apply lean manufacturing tools:

## Slide 36
Mapping the current value stream, Create a VSM for each product manufacturing process, Analyze the current value flow map, identify problem areas, get rid of activities that do not add or reduce any value to a minimum, then create a future map. Estimate the results by comparing future maps with the initial map.
the company must accurately forecast demand for a short period seasonal product. And examine sales patterns to see when sales have shown peaks and valleys, this will give you an idea of when to be ready for rising and falling sales.
Use automation for machining, creating, and shaping parts, as well as for assembling products. Placing Warning devices: to stop the machine from running, and to alert the operator if something wrong is going to happen