## Slide 1
Wireless charging
AN-NAJAH NATIONAL UNIVERSITY
FACULTY OF ENGINEERING AND INFORMATION TECHNOLOGY
ELECTRICAL ENGINEERING DEPARTMENT
Supervised by: Dr. Moien Omar
Prepared by: Maram fatouh.
Amani mansour.

## Slide 2: Outlines
Introduction
The importance of this project .
General view about the project .
Design .
Hard ware.
Results.
Conclusions(summary , cost , future work).

## Slide 3: Introduction
Charging is the process of transferring electrons from one device to another one.
Wireless charging is one methods of charging batteries without using cable which called inductive coupling.

## Slide 4: The importance of this project
The main objective of the wireless charging:
Suitable for emergency cases.
Reliable.
Efficient.
Fast.
Low maintenance cost.

## Slide 5: Advantages
Greater convenience for the charging of everyday electronic devices
No wires.
Reduce cost.
Safe power transfer .
Eliminate sparks and debits associated with wired contact.

## Slide 6: General view about the project
The project work as the below figure show :

## Slide 7: Design
Main scheme diagram of wireless charging

## Slide 8: Hard ware
Primary side
Coils:
Made from copper.
10 turns.
Diameter of the wire(1 mm).
With a base of non conducting
Magnetic material to decrease the losses.

## Slide 9: NE555P IC (Timer):
To create high frequency pulses(40-50 KHZ), then this pulses drive a transistor which switches on and off are at the primary winding of the coil.

## Slide 10: Transistor with heat sink
The transistor works as a switch and it amplifies the current.
The heat sink made from aluminum to reduce the heat of transistor.

## Slide 11: Potentiometer & Capacitors
Use the potentiometer 100 k connected with the timer.
Capacitor to Store energy in the on area and discharge it in the off area.

## Slide 12: Secondary side
Coils
Made from copper.
40 turns.
Diameter of the wire(0.1mm).
With a base of non conducting
Magnetic material to decrease the losses .

## Slide 13: Bridge recifier
It consist of 4 diodes 1N4935
Convert from AC to DC.

## Slide 14: Buck converter
step-down converter is a DC-to-DC power converter which steps down voltage from its input (19.3 volt) to its output (load 5 volt ). It typically containing at least two semiconductors )diode and a transistor(.

## Slide 15: parameters affects the wireless charging
Distance
Maximum efficiency is achieved when the devices are relatively close to one another.
The distance between two coil around(0.5) cm.

## Slide 16: parameters affects the wireless charging
Frequency
Adjusting the frequency of the timer in the range of (40- 50) kilo hertz that the transferring operation reaches the maximum status .
When increase the frequency the volt increaseat the secondry
V= N*4.44*f*flux .

## Slide 17: Conclusion
Summary
Overall, this finished project met all the expectations. It was stated in the proposal to design a mobile wireless charger that eases the daily life of people, especially in the emergency cases, transfer power wirelessly to charge electronic equipment, vehicles, and other mobile systems.

## Slide 18: Conclusion
Cost Details and Economical Dimensions
Part number | Quantity | Price/each$ | Total cost$
Coil |  |  | 4
Resistor /potentiometer |  |  | 1
Capacitor |  |  | 1
Transistor |  |  | 0.5
Buck converter |  | 1 | 1
timer |  |  | 0.5
Wire Bridge rectifier | 1 | 1 | 0.5 1
Part number | Quantity | Price/each$ | Total cost$
Coil |  |  | 4
Resistor /potentiometer |  |  | 1
Capacitor |  |  | 1
Transistor |  |  | 0.5
Buck converter |  | 1 | 1
timer |  |  | 0.5
Wire Bridge rectifier |  |  | 0.5 1
The following table shows all the elements and their related cost:

## Slide 19: Conclusion
Future Work
It can improve the project in many ways:
Display the charger at more distance between the coils.
Increase the efficiency by increasing the output power