## Slide 1: An Najah National University Civil Engineering Department
Analysis and design of AL- Ashqar
commercial mall
By:
-Eman Abu jazar.
-Saja Issa.
-Noor Ghorpeyha.
Supervisor : Dr. Riyad Awad.

## Slide 2: Outline
Introduction.
What we do in graduation project 1.
Dynamic analysis:
-Modes and period.
-Response spectrum analysis.
Design of structural element.

## Slide 3: Introduction
AL –ashqar mall is a commercial building located in Tulkarem city, it consists of three basements, ground floor and five floors.
Structural elements will be designed as reinforced concrete members according to strength and serviceability criteria as specified in ACI 318 for gravity load and as specified in UBC 97 for seismic load.

## Slide 4
* 3 Basements are garages.
*Ground floor & 1to 3 floors are stores .
* 4 &5 floors are offices.

## Slide 6: What we do in GP1?
Definitions Of Material.

## Slide 7: What we do in GP1?
Garages &stores =5kN/m^2
Offices=2.5KN/m^2
Dead
Superimposed
Live
Gravity Load

## Slide 8: Structural Systems
Two way solid slab
3 Basements
Two way ribbed slab
GF &1to 5 floor
30cm thickness
20cm thickness

## Slide 9: Design and dimensions

## Slide 11: 3D Model

## Slide 12: DYNAMIC ANALYSIS
Response Spectrum Analysis
Modes and Period
Drift Check

## Slide 13: Definition of mass resource

## Slide 14: Seismic Parameters
0.15 | z
Soft Rock(SC) | Soil
0.18 | Ca
0.25 | Cv
1 | I
5.5 | R

## Slide 15: Seismic Zone Factor Z

## Slide 16: Site Classification Sc

## Slide 17: Seismic Coefficient Ca

## Slide 18: Seismic Coefficient Cv

## Slide 19: Seismic Importance Factor I

## Slide 20: Response Modification Coefficient R

## Slide 21: Define Of Response Spectrum Function

## Slide 22: Response Spectrum In X-Direction
gI/R = 9810 * 1 /5.5 = 1783.64
(1/3)*1783.64
=594.33

## Slide 23: Response Spectrum In Y-Direction
gI/R = 9810 * 1 /5.5 = 1783.64
(1/3)*1783.64
=594.33
𝐸y=𝐸y+0.3 𝐸x

## Slide 24: Finding the Base Shear by equivalent lateral force method (V):
from UBC code
min from → 2.5Ca = 2.5*0.18=0.45
Cv/T=0.25/0.594=0.4209
min = 0.4209
→ (0.4209/5.5)*192825.6 = 14755.55
EQx = 14409.58 < 14755.55→ ( not OK)
EQy = 15071.6 > 14755.55→ (OK)
try to change scale factor
So we try EQ = 16000

## Slide 27
EQx max =15592.7 > 14755.55
EQy max =15645.9 > 14755.55
→ ( OK).

## Slide 28: Modal Mass Participation Ratio
According to UBC Code, we should have Modal Participating Mass Ratio (MPMR) more than 90% in both directions
at 10 modes we achieve 90%

## Slide 29: Check Period
Period in mode 1 → T= 0.74 sec.

## Slide 30
Period in mode 1 → T= 0.585 sec.

## Slide 31
→ T = Ct*h3/4
= 0.0488*283/4 = 0.594
→ T = 1.4*0.594 = 0.83
T from ETABS < T from UBC code
T from UBC code

## Slide 32: Drift Check
the elastic drift from ETABs
the plastic drift from UBC code
Δ plastic X = 0.7*5.5*2.97=11.4mm
Δ plastic Y = 0.7*5.5*1.96=7.55mm
Δ (allowable) from Code = L/50 = 3000/50 =60mm
Δ plastic X = 11.4 < 60mm → (OK)
Δ plastic Y =7.55 < 60mm → (OK)

## Slide 33: Verifications of structural analysis
Equilibrium Check
Local equilibrium check
Check deflection(Immediate and long term )
Check shear

## Slide 34: Equilibrium
Hand calculations
Hand Calculation
ETABS

## Slide 35: Equilibrium

## Slide 36: Stress-strain

## Slide 37: Immediate deflection
* Allowable Deflection on solid slab:
From ACI 318-08 maximum deflection
= L/240
=(7.12*1000)/240=29.6 mm.
* Allowable Deflection on ribbed slab:
From ACI 318-08 maximum deflection
= l/240
=(7.3*1000)/240=31.5 mm.

## Slide 38: Immediate deflection in solid slab
maximum deflection in Solid slab = 17.291 mm

## Slide 39: Immediate deflection in ribbed slab
maximum deflection in ribbed slab
= 26.896

## Slide 40: Long Term Deflection
The long term deflection is given by the following equation:
Δ Long term = Δ L + λ∞ x Δ D + λt x Δ SL
To find T
Where:
λt = λ∞ , since we assumed that the live load will sustained for 5 years ≈ ∞
λ = (such that is the compression steel ratio, T is a multiplier for long term deflection)
Δ L= deflection due to live load
Δ D= deflection due to dead load
Δ SL= deflection due to sustained live
As we notice from the figure at time 5 years
(60 months):
λ= = 2

## Slide 41: Long Term Deflection
* ∆Lt on ribbed slab
=5.2 + 2 × 11.4 + 2 × 2.8 = 33.5 mm > 31.5 mm
→ 33.5mm more than allowable deflection but we can assume it OK.
* ∆Lt on solid slab
=5.9 + 2 × 6.6 + 2 × 2.9 = 24.9 mm< 29.6
→(OK).

## Slide 42: Check shear
Solid Slab
Vu from ETABs = 82.8KN.
→ 82.8 < 97.9 KN.
→ ( OK ).

## Slide 43: Check shear
φVc = (1/6)*0.75*√24*150*260*1.1/(1000*(0.55*0.55))
= 86.85KN.
Vu from ETABs=73.5KN.
→ 73.5 < 86.85 KN.
→ ( OK ).
Ribbed Slab

## Slide 44: Design of structural element.
Load combinations
DESIGN OF SLAB
DESIGN OF BEAMS
DESIGN OF COLUMNS
Design of shear wall
Design of stair
DESIGN OF FOOTINGS

## Slide 45: Load Combination
U = 1.4D (9-1)
U = 1.2D + 1.6L + 0.5(Lr or S or R) (9-2)
U = 1.2D + 1.6(Lr or S or R) + (1.0L or 0.5W) (9-3)
U = 1.2D + 1.0W + 1.0L + 0.5(Lr or S or R) (9-4)
U = 1.2D + 1.0E + 1.0L + 0.2S (9-5)
U = 0.9D + 1.0W (9-6)
U = 0.9D + 1.0E (9-7)
Where:
U: ultimate load
D: dead load
L: live load
W: wind load
E: earthquake Load
H: load due to weight or pressure of soil
ACI 318M-11-Equations (9.1-9.7)

## Slide 46: DESIGN OF SLAB
design of Ribbed slab
DESIGN OF solid SLAB

## Slide 48: M22 in X direction:
Width of column strip : 1.325m/S.C
Max negative moment in C.S
→ Mu = 37 KN.m/S.C.
Mu /rib = 37/(1.325/0.55) =15.36KN.m/rib .
ρ = 0.00418 .
As =163.02 mm2.
→ use 2φ12
M22 for section cut in ribbed slab

## Slide 49: M22 in X direction:
Width of column strip : 1.325m/S.C
Max positive moment in C.S
→ Mu = 52.8 KN.m/S.C.
Mu /rib = 52.8/(1.325/0.55)
= 22 KN.m/rib .
ρ = 0.00159 <ρ(min) = 0.00333 .
As(min) =129.87 mm2.
→ use 2φ12
M22 for section cut in ribbed slab

## Slide 50: M22 in X direction:
Width of middle strip : 3.39m/S.C
Max negative moment in M.S
→ Mu = 34.4 KN.m/S.C
→ use 2φ12 .
Max positive moment in M.S
→ Mu = 94 KN.m/S.C
→ use 2φ12/rib.
M22 for section cut in ribbed slab

## Slide 51: M11 in Y direction:
M11 for section cut in ribbed slab

## Slide 52: Design of ribbed slab for flexure

## Slide 53: two way solid slab
As min= 360mm2.
→ use 4φ12mm/1000mm.
φMn =21.3 KN.m
M11 from ETABS in solid slab

## Slide 54: Top steel (Moment (11))
→ use 6φ12mm/2000mm.

## Slide 55: two way solid slab
As min= 360mm2.
→ use 4φ12mm/1000mm.
M22 from ETABS in solid slab
φMn =21.3 KN.m

## Slide 56: Top steel (Moment (22))
→ use 7φ12mm/2000mm.

## Slide 57: Design of beams

## Slide 59: Designed Beam

## Slide 60: Design of columns

## Slide 62: Designed column
Longitudinal section on column600*600
Cross section in C14 (600*600)

## Slide 63: Designed shear wall under gravity load
𝑆ℎ𝑒𝑎𝑟 𝑤𝑎𝑙𝑙 ( 𝑋∗𝑌)
= ( 250𝑚𝑚∗6500𝑚𝑚).
𝐶𝑜𝑣𝑒𝑟 =40𝑚𝑚.

## Slide 64: Designed shear wall under gravity load

## Slide 65: 𝐶ℎ𝑒𝑐𝑘 for 𝑠ℎ𝑒𝑎𝑟
X-Direction
Y-Direction
Shear Reinforcement
Vu
φVc
NO Need
Minimum
402.8KN
680 KN
11.23 KN
121.5 KN

## Slide 66
For Pu = 5939 KN , Mux(M2) =260 KN.m.

## Slide 67
For Pu = 5939 KN , Mux(M2) =10 KN.m

## Slide 68: Design Of Shear Wall
Use minimum Shear reinforcement.
→Use 𝜌min=0.0025
𝐴𝑠,ℎ𝑜𝑟𝑖𝑧𝑜𝑛𝑡𝑎𝑙
= 𝜌𝑚𝑖𝑛∗𝑏∗ℎ=0.0025∗1000∗250=625𝑚𝑚2.
625/2=312.5 𝑚𝑚2 on each side.
Assume ϕ10→4 ϕ10 / m in each side.
As, Vertical :
𝑈𝑠𝑒 𝐴𝑠,𝑚𝑖𝑛 = 𝜌𝑚𝑖𝑛∗𝑏∗ℎ=0.0025∗1000∗250=625 𝑚𝑚2.
Assume ϕ10 → 4 ϕ10 / m in each side.

## Slide 69: Design Of Stair
Thickness of flight = 20cm
Load on stair:
*Dead = 5 𝑘𝑁/𝑚2
*Live = 5 𝑘𝑁/𝑚2
*Superimposed = 3 𝑘𝑁/𝑚2

## Slide 70: Checks for stair
Checks for deflection
Max immediate deflection due to service load from
Etabs( Δ )=0.3mm.
Deflection limitation:-
Δ 𝐿,𝑎𝑙𝑙𝑎𝑤𝑎𝑏𝑙𝑒 ≤ 𝑙/240
=2210/240 =9.2𝑚𝑚

## Slide 71
Check For Shear
∅ 𝑉𝑐 = 112.4 𝑘𝑁 /𝑚
The counter range from -33 - 38.5
→ all reading smaller than 112.4KN.
→ then no need for shear. reinforcement

## Slide 72: Design of Flexure for stair
Moment (22)
Flight
𝐴𝑠,𝑚𝑖𝑛 = 0.0018 ∗ 𝑏 ∗ ℎ =
0.0018×200×1000=360𝑚𝑚2 (2∅16/𝑚).
→ use 2φ16mm/1000mm
Max M22 (positive) = 9.6 KN.m
→ ρ = 0.00088 < 0.0018
Use ρ = 0.00018

## Slide 73
Landing
Max M22 (positive) = 9.6 KN.m
→ ρ = 0.00023 < 0.0018
Use ρ = 0.00018
𝐴𝑠,𝑚𝑖𝑛 = 0.0018 ∗ 𝑏 ∗ ℎ
=0.0018×200×1000=360𝑚𝑚2 (2∅16/𝑚).
→ use 2φ16mm/1000mm

## Slide 74
Design for Transverse steel
Moment (11)
𝐴𝑠 𝑠ℎ𝑟𝑖𝑛𝑘𝑎𝑔𝑒 = 𝐴𝑠 𝑚𝑖𝑛 =0.0018×200×1000=360𝑚𝑚2.
in both face (Use 2 ∅16/1m for each layer)

## Slide 75: Design Of Mat Foundation
Mat foundation dimensions:
Assume h=110mm.

## Slide 76: Checks of Mat Foundation
Check for deflection

## Slide 77: Bearing capacity of the soil (𝑞𝑎𝑙𝑙 ) =250 kN/m2
Check for stress

## Slide 78
Check for punching

## Slide 79: Check Of Punching
Load on this column:
- Dead =2669.2KN.
-Superimposed dead = 1877.7 KN.
- live =1514.4 KN.
Ultimate load on column (Vu)
1.2*(2669.2+1877.7)+1.6*(1514.4) = 7879.3 KN.
∅Vc=0.75/3*√28*6480*1020/1000=8744 KN
Vu< ∅Vc→ OK

## Slide 80: Design for Flexure
𝐴𝑠,𝑚𝑖𝑛 = 0.0018 ∗ 𝑏 ∗ ℎ = 0.0018 ∗ 1000 ∗ 1100 = 1980𝑚𝑚2/𝑚 (7∅20/𝑚).
→ use 7φ20mm/1000mm
φMn,min =750.3 KN.m
Moment (11)

## Slide 81: Design for Flexure
→ use 7φ20mm/1000mm
φMn,min =750.3 KN.m
Moment (22)