## Slide 1: Feasibility study for precast concrete factory
Group Members :
Ashraf Al Amleh
Dalal Nabulsi Jehad Hasiba Lama Emad Wala' Bostami
Supervised by:
Eng.Suleiman Daifi

## Slide 2: Outline
Introduction
Problem Statement
Market Study
Technical Study
Financial Analysis
Conclusion & Recommendations
Questions

## Slide 3: Introduction
Concrete is one of the main materials used in the construction of most buildings in the world.
There are two methods for producing concrete:
In site concrete.
Precast concrete.

## Slide 4: Some Advantages of Precast
Quality
Durability
Speed of construction
Design flexibility
Can be cut to suit
High margins of design safety
Reduces noise from building sites

## Slide 5: Prestressed Concrete

## Slide 6: Hollow Core Slabs
Features : 1- Light Weight 2-Large spans 3-Material savings 4-Hold heavy loads 5-Sound insulation

## Slide 7: Walls & Panels
Features: 1-High level of insulation 2-Complex shapes 3-less finishing process
4- Speed in construction

## Slide 8: Problem Statement
The idea of the project comes from the attributes that is characterized by precast concrete compared with in place concrete.
Widespread use of precast concrete around the world and not used in Palestine.
This project deals with undertake a feasibility study, with all of its components .

## Slide 9: Feasibility Study Components
Market Study
Financial Analysis
Feasibility Study
Technical Study

## Slide 10: Market Study
Market Study estimates the demand of precast concrete
products, and the market share of new products.
Market Study methodology to estimate the demand on precast concrete products:
Interviews
Questionnaires

## Slide 11: Interviews
We made Conservation contractors in order to :
To observe the opinion about precast concrete
To take a general view about the engineers ability to accept this type of factory
To know the advantages of precast concrete

## Slide 12: Interviews Results
Many contractors confirm the necessity of establishing a Precast Concrete
There is an appetite for this type of products, and that enhances us to continue the feasibility
Precast concert have many benefits to the society and also for customers
Most preferred area were in Ramallah as the percentage of construction is increasing there quickly

## Slide 13: Questionnaire Form

## Slide 14: SPSS Analysis
Type | Demand percentage according to the 1st year | Demand percentage from 2nd to 4th year | Demand percentage from 5th to 8th year | Demand percentage from 9th to 10th year
Floors | 13.27% | 21.10% | 30.85% | %41.16
Walls | 14.86% | 23.34% | 32.87% | 43.66%
Bases | 3.12% | 4.58% | 7.37% | 10.48%
Columns | 4.14% | 7.05% | 10.45% | 12.98%
Fences | 16.34% | 24.97% | 34.68% | 43.97%
Percentage of expected areas on precast concrete with respect to the total consumption size

## Slide 15: Questionnaire Results
Noticeable acceptance of this product is shown if it is established here in Palestine.
Preferable products to be produced were walls and floors
Expected demand on precast concrete products with respect to the total consumption size

## Slide 16: Total Expected Demand

## Slide 17: Market Share
30% market share of the demand
Year | Floors | Fences | Walls
2015 | 76272.96 | 35964.42 | 1115785
2016 | 162243.8 | 69389.11 | 1752518
2017 | 111254.9 | 46299.03 | 1752518
2018 | 96839.25 | 50279.17 | 1752518
2019 | 140141.7 | 50422.1 | 2468092
2020 | 167501.2 | 55520.73 | 2468092
2021 | 211410.6 | 73912.55 | 2468092
2022 | 292672.6 | 108255.6 | 2468092
2023 | 439458.6 | 161193.2 | 3278275
2024 | 453496.3 | 168546.9 | 3278275

## Slide 18: Technical Study :
Technical Study should include the following:
Floors Production
Walls Production
Plant Layout
Gantt Chart
Establishment Cost
Operational Cost

## Slide 19: Floors Production Steps
Bed Preparation
Prestressing
Concrete transporting
Casting
Cutting
Storing

## Slide 20: Gantt Chart

## Slide 21: Walls Production

## Slide 22: Administrative Building

## Slide 23: Organizational Structure
Production &Manufacturing
Sales & Marketing
Finance & Accounting
HR
Quality Department
Maintenance
Production management
Inventory management
CRM
Procurement
Accounting
IT
Sales
Transportation & Movement unit
Company car driver
Forklift driver
CAT driver
HR
marketing
Administration

## Slide 24: Plant Layout
Batching and mixing
Production lines
Storage area
Parking
Administrative building

## Slide 25: Establishment Cost
Item | Cost( $ )
Land space required | 260,526.316
Precast concrete plant | 1,712,231.76
Batching and Mixing Plant | 145,322.45
factory licenses | 5,000
Water network for the administrative buildings | 868.42
Electricity | 1,200
tel. & internet | 276.315
admin. Building construction | 217,105.63
admin. Furniture | 20,000
Fences | 15,000
Hangers | 1,252,800
control lab. | 10,000
Guard room | 5,862
Equipment | 2,895
Forklift | 80,000
CAT | 100,000
Company car | 48,000
Cameras | 3,263.15
Fire fighting system | 10,000
Gates | 7,000
Inside factory water network | 3,000
Inside Factory Electricity network | 10,000
Working capital | 775,602.38
Reserve for emergencies and unforeseen costs | 518595.3
Item | Cost ( $ )
$ 5,185,953.42

## Slide 26: Operational Cost
Staff salaries
Raw Materials
Electricity
Depreciation
Maintenance
Administrative Expenses
The annual operating cost of the factory is estimated by
$ 8,002,013

## Slide 27: Total Salaries
Production & Manufacturing
Finance and accounting
Transportation & movement
Human Recourses
Sales & marketing
# of employees = 55
The total yearly salaries
$ 332,968.38/yr

## Slide 28: Production Capacity of The Precast Concrete Products
Walls Production Capacity = 900 m2
80% for Interior (Walls (720m2
20% for exterior walls (180m2)
production capacity of HC-slab
570 m2/day.

## Slide 29: Cost of Materials Used to Produce Walls
Direct Material for Exterior Walls ( 180m2) |  |  |  | 
Direct material | Quantity (kg/m3) | Quantity (kg/m2) | Material cost ($/kg) | Material cost ($/m2)
Cement | 360 | 72 | 0.13157 | 9.473684211
Coarse aggregate | 1145 | 229 | 0.6842 | 1.566842105
Water | 160 | 32 | 0.00289 | 0.092631579
Fine aggregate (Sand) | 630 | 126 | 0.017 | 2.155263158
Steels | 86.91358025 | 17.38271605 | .7631 | 13.26575699
D.M.C for 1 m2 |  |  |  | 26.55417804
Monthly D.M.C |  |  |  | 114,714.0491
Yearly D.M.C |  |  |  | 1,376,568.6

## Slide 30: Cost of Materials Used to Produce Walls
Direct Material for Interior walls ( 720 m2 ) |  |  |  | 
Direct material | Quantity (kg/ m3) | Quantity (kg/ m2) | Material cost ($/kg) | Material cost ($/m2)
Cement | 360 | 72 | 0.13157 | 9.473684211
Coarse aggregate | 1145 | 229 | 0.6842 | 1.566842105
Water | 160 | 32 | 0.00289 | 0.092631579
Fine aggregate (Sand) | 630 | 126 | 0.017 | 2.155263158
Steels | 15.80246914 | 3.160493827 | .7631 | 2.411955815
D.M.C for 1 m2 |  |  |  | 15.70037687
Monthly D.M.C |  |  |  | 271,302.5123
Yearly D.M.C |  |  |  | 3,255,630.142

## Slide 31: Steel Usage for Walls
for 1m length the weight of steel = (D2/162)
Cost of1 m2 = weight * # of bars * Price
8 mm diameter
$ 2.41
12 mm diameter
interior
exterior
$ 13.26

## Slide 32: Cost of Materials Used to Produce HC-slab
Direct material | Quantity (kg/m2) | Material cost (NIS/kg) | Material cost ($/1.2m2)
Cement | 9.36 | 0.131 | 1.23
Coarse aggregate | 247.6 | 0.68 | 1.69
Water | 2573.16 | 0.00289 | 7.44
Fine aggregate (Sand) | 4.25 | 0.017 | 0.072
Cables | 3.16 | .7631 | 2.41
Total D.M.C for (1 m2) |  |  | 12.85
Total D.M.C for(1.2 m2) |  |  | 15.43
Monthly cost for 1.2 m2 |  |  | 211,108.3
Yearly cost for 1.2 m2 |  |  | 2,533,300.7
D =14.52 cm
1.2 m
20 cm

## Slide 33: Electricity Consumption In The Factory
Electricity of the factory include
Administrative building electricity
= $3,092/yr
Batching & mixing electricity
HC-slab electricity
Walls electricity

## Slide 34: Batching & Mixing Electricity
Batching & Mixing
1/3 Floors
2/3 Walls
$15.067/hr
Machines Electricity =84.2 kw
1 kw = .68 NIS

## Slide 35: HC-slab Electricity
Yearly cost = $ 64,364.3136/yr
# | Machine | Electricity (kw) | Electricity ($)/hr | Electricity ($)/hr
1 | Electric skip for HC-slab production | 1.1 | 0.197 | 0.196
2 | Stressing abutment p7-300 | 5.5 | 0.984 | 0.984
3 | Maturity control e9-8mc | 5 | 0.895 | 0.894
4 | Casting module extruder s5-1200e | 0.38 | 0.068 | 0.068
5 | Saw preparer s5-400p | 116 | 20.758 | 20.757
6 | Lifting clamps p7-4 | 0.066 | 0.0118 | 0.0118
 | Total cost |  |  | 22.9
Total electricity cost for hollow core slab/hr =
22.913 + 0.33 * 15.067
= $ 27.93

## Slide 36: Total electricity cost walls = $101,113/year
# | Machine | Electricity(kw) | Electricity ($)/day
1 | Pulling device for transfer wagon | 5.5 | 0.98
2 | Multifunction wagon s5-26 | 15 | 2.68
3 | Maturity control e9-8mc | 5 | 0.894
 | Total | 25.5 | 4.56
Total electricity cost = 4.56 + 0.66 * 15.067= $ 14.6/hr
Walls Electricity

## Slide 37: Depreciation for Production Lines
HC-slab Depreciation =
$44,361/yr
Walls Depreciation =
$ 48,515/yr

## Slide 38: Depreciation of other items
 | Expected life | Cost($) | Depreciation/year | Dep./month
Admin. Building construction | 40 yr | 217105.6 | 5427.64075 | 452.3
Admin. Furniture | 10 yr | 20000 | 2000 | 166.66
Fences | 20 | 15000 | 750 | 62.5
Hangers | 20 | 1252800 | 62640 | 5220
control lab. | 20 | 10000 | 500 | 41.66
Guard room | 40 | 5862 | 146.55 | 12.2125
Equipment | 5 | 2895 | 579 | 48.25
Forklift | 20 | 80000 | 4000 | 333.33
CAT | 20yr with S.V $20000 | 100000 | 4000 | 333.33
Company car | 10yr | 48000 | 3010.3488 | 250.368
Cameras | 10 | 3263.15 | 326.315 | 27.19
Gates | 20 | 7000 | 350 | 29.16
Total cost |  |  | 88,729.85 | 7393.66
 | Expected life | Cost($) | Depreciation/year | Dep./month
Admin. Building construction | 40 yr | 217105.6 | 5427.6 | 452.3
Admin. Furniture | 10 yr | 20000 | 2000 | 166.66

## Slide 39: Company Car Depreciation Calculations
Item | Value
Car price($) | 3,482
Expected car life(km) | 500,000
salvage value ($) | 13,158
Expected car life(yr) | 10
Distance(km)/yr | 43,200
Rate | 0.0864
Year | Market Value | Usage Percent | Dep. Value /yr | Dep./month
0 | 34842 | 0 | 0 | 0
1 | 31831 | 0.0864 | 3010.3 | 250.8
2 | 29081 | 0.0864 | 2750.2 | 229
3 | 26568 | 0.0864 | 2512.6 | 209
4 | 24273 | 0.0864 | 2295.5 | 191.2
5 | 22176 | 0.0864 | 2097.2 | 174.7
6 | 20260 | 0.0864 | 1916 | 159.6
7 | 18509 | 0.0864 | 1750.4 | 145.8
8 | 16910 | 0.0864 | 1599.2 | 133.2
9 | 15449 | 0.0864 | 1461 | 121.7
10 | 13158 | 0.0864 | 1334.8/yr | 111.2

## Slide 40: Operational Cost Summery
# | Item | Cost($)
1 | Total salaries | 332968
2 | Material for walls | 4632198
3 | Materials for HC-slab | 2533300
4 | Electricity for administrative building | 3092
5 | Electricity for HC-slab | 64364
6 | Electricity for walls | 101113
 | Deprecation (walls) | 48515
7 | Depreciation (HC-slab) | 44361
8 | Depreciation of other items | 85970
9 | Water consumption (administrative building) | 3157
10 | Other operational costs | 152,968
 | Total costs | 8,002,013

## Slide 41: Financial Evaluation
Reveals the project's ability to generate income to cover its financial obligations.
Financial Study includes the following :
Pay Back Period
Net Present Value-NPV
Break-Even Point
National profitability of the project
Sensitivity Analysis
Risk Analysis

## Slide 42
variable cost per unit ($) | 
HCS | 13.7
Interior walls | 16.3
Exterior walls | 27
Fixed Cost($) | 34910
Over Head($) | 8216.8
Cost for each unit in $ =Total variable cost+(( Fixed + Overhead) /31920) | 
Product Type | Cost/Unit ($)
HCS | 15
Interior walls | 17
Exterior walls | 28
Pricing :

## Slide 43: Price of the Factory Products
HCS = $ 17.9
Interior walls =$ 21
Exterior Walls = $ 34

## Slide 44: Financial Analysis
Net Present Value = $ 15,743,225
The Rate Of Return = 34.44%
Pay Back Period = 3.1 year
i = 5%

## Slide 45: Break Even Point
Overhead + Fixed Cost = P1X1+ P2X2 + P3X3
Where :
X1 : # of hollow core slab items
X2 : # of interior walls items
X3 : # of exterior walls items
By solving the equations we get :

## Slide 46: Break Even Point
With 0.05 scrap rate Break Even Point
For HC-S = 4110*(1+.05) =
4316
Exterior walls = 6231*(1+.05) =
6542
Interior walls = 1577*(1+.05) =
1656
X1 = 4110
X2 = 6231
X3 = 1577

## Slide 47: Sensitivity Analysis
Steel price is increasing 25% of its value
Cement price is increasing by 10% of its original value
70% of plant full capacity is used
Net Present Value = $ 6408966
Rate Of Return = 18.18 %
Pay Back Period = 6.22 years
Break Even Point = Hollow core slabs = 4316
Interior walls = 6542
Exterior walls =1656
i = 5%

## Slide 48: Simulation Analysis
By using excel we used Random Between function and doing 1000 iteration to compute NPV for the expected life of the project then we estimated the average NPV=15,049,866 , and standard deviation = 339,101

## Slide 49: Simulation Analysis
95% confidence that the NPV is more than 114502825

## Slide 50: Comparison
 | Fresh concrete | Precast concrete
Cost | For solid slabs ($65-$70) + Bleaching cost($8) T.C = $75 | For HC-slabs $21 +installation cost($3)+ transportation cost ($10) T.C=$34
 | For exterior walls $60 + bleaching cost ($8) T.C= $68 | For exterior walls $40+$3+$10 T.C=$53
 | For interior walls(concrete) $35+bleaching cost ($15) T.C=$50 If bricks T.C=$17+$15 T.C=$32 | For interior walls T.C = $18+$3+$10 T.C =$31
Time needed to build floor of 500 m2 | Exterior walls= 2 weeks Interior walls =2 weeks Bleaching = 3 weeks Total = 7 weeks | 7-10 days

## Slide 51: Conclusion :
From the results of Market study, Technical Study and Financial analysis results we can see that the project is Feasible

## Slide 52: Risk Analysis
Refusal of the Israeli national electricity company to provide the needed electricity
Finding suitable land with 12 donum area, with a suitable location
Using suitable Crain for precast products
The stability of the political and economic situation, in order to increase the demand on precast products.

## Slide 53: Production Line Recommendations :
Use material economically
Contract with best vendors (quality, logistics and price)
Avoid excess amount of concrete to reduce waste cost
Avoid excess inventory
On time delivery
Reduce defective products (training)
Establish preventive maintenance
Using mobile crane to facilitate the assembly in construction site
Contract with best transportation companies

## Slide 54: General Recommendations
Starting the implementation of the project after obtaining the necessary licenses from the relevant authorities.
Choose suitable land which needs less settling to reduce the cost of preparation
Engineering association should spread awareness between people about precast and its advantages comparable to fresh concrete
Buying trucks in future to transport precast products since the cost of precast products doesn't include transportation cost and the one who purchase precast products incurred the cost of transportation