## Slide 1: Color Sorting System (CSS) Meera Saymeh Masa Al-Sayyed

## Slide 2: Table of contents 01 02 03 04 05 06
Overview
Comparision
Challenges
Tools used
Future Work
Demo

## Slide 3: Overview & Main features
Retreiving
Objects either to the beginning point or to a container for exporting.
Sorting
Metalic Objects according to their color, each color is sorted in a specific column.
Color Sorting System (CSS): is a robotic system that aim to:

## Slide 4: Our CSS vs. Others
 | Our CSS | Others
Angels | All angels | Diagonal some static
Object Material | Metalic | Plastic
Ability to Retrieve objects after sorting | Yes | No
Simplicity | Complex | Simple
Others, ex: Rice sorting machine , Plastic sorting system, colored balls sorting system

## Slide 5: Challenges
Robotic Arm
Not smooth when moving, since it moves in x and y axis and needed three servo motors.
Color sensor
Needs to redetect the colored objects RGB values when changing the light of the place , and can’t be exposed to sunlight.
Magnet
Sence the servo motor didn’t gave it enough flexibility, even though the wire acheived that but still the magnet shift it’s position a little.
It was hand made which took a lot of time for it to be ready.
The first servo motors broke and burnt out.
The area ariund it should be clear from any obstecles otherwise the servo motors will break.

## Slide 6: Tools and Devices Used
Arduino mega

## Slide 7: Tools and Devices Used
Servo motors
We Used three servo motors: - At the base rotates from 0 – 180 - Two used for the arm (shoulder , elbow)

## Slide 8: Tools and Devices Used
Dual H-bridge Motor Drive
To provide the magnet with the 12 volts it needs to operate properly.

## Slide 9: Tools and Devices Used
Color Sensor
TCS3200
Light-to- frequency convertor.
Output: square wave that will be given to the microcontroller to map the frequency to color RGB.

## Slide 10: Tools and Devices Used
Color Sensor
TCS3200
S2,S3 (Output) : Used to select the color select the array of photodiodes of the sensor.
S2 | S3 | Color Filter
Low | Low | Red
High | High | Green
High | Low | Blue
Low | High | No filter

## Slide 11: Tools and Devices Used
Color Sensor
TCS3200
S0,S1 (Output) : Used for frequency scaling. 20% is the recommended.
S0 | S1 | Frequency
Low | Low | Power-Down
Low | High | 2%
High | Low | 20%
High | High | 100%

## Slide 12: Tools and Devices Used
Push Buttons
Used to retrieve the object according to it’s position near the starting point, first row 1 them row 2.

## Slide 13: Tools and Devices Used
Keypad
Each object is sorted in a specific cell, when the cell number is pressed from the keypad the object from this cell will be retrieved to a container for exporting.

## Slide 14: Tools and Devices Used
Power supply

## Slide 15: Future Work
Adding sensor for each position.
Increase slot capacity for each color category to hold more goods
Create a simple user interface or mobile application that enables remote monitoring and control of the color sorting system
enhancing the arm to cover a wider range, and to hold heavier objects.

## Slide 16: Demo

## Slide 17: Thanks
Do you have any questions?