## Slide 1
Analysis of Ammar Tower on Ramallah city
By:
Karsou Othman (11819320)
Osaid Abu Shanab (11821753)
Mahmoud Najjar (11821751)
Under supervision of:
Dr. Munther Diab

## Slide 2
outline
3
Seismic analysis
2
Preliminary Dimensions
1
Introduction

## Slide 3
Introduction
1
The project name is ammar tower
2
3
4
Located at It's located at Al-ersal center in Al-biereh
Consist of 19 floors
The basement area is 3781
Project description

## Slide 4
Introduction
5
Project description
Ground floor to the 4th floor has an area equal to 2140
6
7
8
5th floor up to the roof have an area equal to 1036
In this project the structure was analyzed 25 floors
Consist to 3 basements and 22 floors

## Slide 5
A photograph of Ammar Tower in Ramallah

## Slide 6
Left part It was not implemented in reality.

## Slide 7
Ground floor , first floor , second floor , third floor and fourth floor have the same plan view.

## Slide 8
fifth floor up to the roof have the same plan view.

## Slide 9
Hight | Floor | Hight | Floor
4 | f10 | 3.5 | Basement 3
4 | f11 | 3.5 | Basement 2
4 | f12 | 5.1 | Basement 1
4 | f13 | 4 | Ground floor
4 | f14 | 4 | f1
4 | f15 | 4 | f2
4 | f16 | 4.5 | f3
4 | f17 | 4 | f4
4 | f18 | 4 | f5
4 | f19 | 4 | f6
4 | f20 | 4 | f7
4 | f21 | 4 | f8
 |  | 4 | f9
Introduction

## Slide 10
value | Property
30 | Compressive strength, fc ( MPA )
25.7 | Modulus of elasticity, Ec (GPa)
25 | Unit wight (kN./m3)
Introduction
Materials
Value | Property
420 | Yielding strength, fy (Mpa)
200 | Modulus of elasticity, Es (GPa)
Concrete.
Steel.

## Slide 11
Introduction
Materials
Other materials.
Ɣ in kN/m³ | Material
12 | Blocks
18 | Filling Materials
26 | Tiles
23 | Plaster
13 | Aggregate
23 | Concrete Mortar
30 | Masonry Stone

## Slide 12
Introduction
Load type
The load was calculated according to ASCE 17-16 code.
As the following:
Value | Type
5 kN./m2 | Live load
5 kN./m2 | Super dead load
Program calculated | Dead load

## Slide 13
Preliminary Dimensions
1
Types of structural systems.
2
3
Shear wall system
Wall-frame system (dual system)
Frame system
The system used in this project is wall-frame system (dual system)

## Slide 14
Preliminary Dimensions
The dimension were calculated according to ASCI 318-19 code.
Thickness | Type
300 mm | Flat slab
400 mm | Voided slab
400 mm | Waffle slab
250 mm | solid slab
350 mm | Ribbed slab

## Slide 15
Preliminary Dimensions
width | Depth | Frame section
700 mm | 700 mm | Column
500 mm | 800 mm | Beam
thickness | Type of wall
300 mm | Shear wall
250 mm | Retaining wall

## Slide 16
3D- Modeling by ETAPS software.

## Slide 17
Preliminary Dimensions
Verification of Structural Analysis.
Compatibility Check.

## Slide 18
Preliminary Dimensions
Verification of Structural Analysis.
Equilibrium Check.
Value | Check load
10000 kN | ETAPS result
10000 kN | Hand calculation
0% | Percentage of error

## Slide 19
Preliminary Dimensions
Verification of Structural Analysis.
Internal force check.
On slab:
Percentage of error | Hand calculation | ETAPS RESULT | Type
8.72% | 289.97 kN.m | 269.67 kN.m | Moment

## Slide 20
Preliminary Dimensions
Verification of Structural Analysis.
Internal force check.
On beam:
Percentage of error | Hand calculation | ETAPS RESULT | Type
7.01% | 207.33 kN.m | 192.8 kN.m | Moment

## Slide 21
Preliminary Dimensions
Verification of Structural Analysis.
Internal force check.
On column:
Percentage of error | Hand calculation | ETAPS RESULT | Type
6.12% | 371.57 kN | 348.8 kN | Axial force

## Slide 22
seismic analysis
Equivalent static.
value | Factor
0.275 | S1
0.075 | Ss

## Slide 23
seismic analysis
Importance factor.

## Slide 24
seismic analysis
Site class.
Site classification is B

## Slide 25
seismic analysis
Response Modification factor.

## Slide 26
seismic analysis
All the factors were entered to the ETABS To calculate the forces.

## Slide 27
seismic analysis
Response Spectrum method.

## Slide 28
seismic analysis
Analysis results.
forces distribution:
Force from Response X(KN) | Story
1309.4909 | Story 25
2040.4849 | Story 24
2325.9373 | Story 23
2254.6798 | Story 22
1995.7456 | Story 21
1799.6382 | Story 20
1864.0019 | Story 19
2129.907 | Story 18
2408.2908 | Story 17
2590.8769 | Story 16
2672.8416 | Story 15
2709.2003 | Story 14
2758.6831 | Story 13
2836.2656 | Story 12
2908.3585 | Story 11
2930.3995 | Story 10
2887.2278 | Story 9
2963.3312 | Story 8
3539.9181 | Story 7
4398.1353 | Story 6
5256.9583 | Story 5
5899.4813 | Story 4
6507.9784 | Story 3
6834.9871 | Story 2
6976.8105 | Story 1
V (KN) | Story
767.7182 | Story 25
1422.357 | Story 24
2032.444 | Story 23
2596.195 | Story 22
3120.229 | Story 21
3602.773 | Story 20
4044.912 | Story 19
4447.767 | Story 18
4812.498 | Story 17
5140.31 | Story 16
5432.458 | Story 15
5690.252 | Story 14
5915.065 | Story 13
6108.344 | Story 12
6271.618 | Story 11
6406.521 | Story 10
6514.804 | Story 9
6692.745 | Story 8
6827.951 | Story 7
6913.062 | Story 6
6959.858 | Story 5
6976.957 | Story 4
6976.957 | Story 3
6979.385 | Story 2
6976.435 | Story 1

## Slide 29
seismic analysis
The distribution of the base shear on each individual story is shown in the following tables:
In x direction:
Vx(KN) | Story
767.7182 | Story 25
654.6383 | Story 24
610.0871 | Story 23
563.7514 | Story 22
524.034 | Story 21
482.5443 | Story 20
442.1389 | Story 19
402.8546 | Story 18
364.7308 | Story 17
327.8122 | Story 16
292.1481 | Story 15
257.7939 | Story 14
224.8132 | Story 13
193.2786 | Story 12
163.2747 | Story 11
134.9024 | Story 10
108.2837 | Story 9
177.9402 | Story 8
135.2059 | Story 7
85.1114 | Story 6
46.7965 | Story 5
17.0983 | Story 4
0 | Story 3
0 | Story 2
0 | Story 1
In Y direction:
Vy(KN) | Story
767.7182 | Story 25
654.6383 | Story 24
610.0871 | Story 23
563.7514 | Story 22
524.034 | Story 21
482.5443 | Story 20
442.1389 | Story 19
402.8546 | Story 18
364.7308 | Story 17
327.8122 | Story 16
292.1481 | Story 15
257.7939 | Story 14
224.8132 | Story 13
193.2786 | Story 12
163.2747 | Story 11
134.9024 | Story 10
108.2837 | Story 9
177.9402 | Story 8
135.2059 | Story 7
85.1114 | Story 6
46.7965 | Story 5
17.0983 | Story 4
0 | Story 3
0 | Story 2
0 | Story 1

## Slide 30
seismic analysis
Horizontal irregularity:
Irregularity check.

## Slide 31
seismic analysis
Horizontal irregularity:
Irregularity check.
value | Modal ratios
0.72 | Sum of UX
0.67 | Sum of UY

## Slide 32
seismic analysis
The results are confirmed with the results of the torsional irregularity check.
In x direction:
In Y direction:
Torsional irregularity X |  |  |  | 
Story Number | Max Drift | AVG Drift | Ratio | Check
Story 25 | 4.83 | 4.824 | 1.00 | regular
Story24 | 4.963 | 4.905 | 1.01 | regular
Story23 | 5.118 | 5 | 1.02 | regular
Story 22 | 5.287 | 5.104 | 1.04 | regular
Story 21 | 5.455 | 5.208 | 1.05 | regular
Story 20 | 5.619 | 5.305 | 1.06 | regular
Story 19 | 5.767 | 5.386 | 1.07 | regular
Story 18 | 5.893 | 5.447 | 1.08 | regular
Story 17 | 5.991 | 5.482 | 1.09 | regular
Story 16 | 6.056 | 5.485 | 1.10 | regular
Story 15 | 6.085 | 5.453 | 1.12 | regular
Story 14 | 6.074 | 5.38 | 1.13 | regular
Story 13 | 6.019 | 5.263 | 1.14 | regular
Story 12 | 5.919 | 5.096 | 1.16 | regular
Story 11 | 5.771 | 4.875 | 1.18 | regular
Story 10 | 5.574 | 4.595 | 1.21 | irregular
Story 9 | 5.339 | 4.236 | 1.26 | irregular
Story 8 | 5.187 | 2.197 | 2.36 | irregular
Story 7 | 5.206 | 2.187 | 2.38 | irregular
Story 6 | 3.899 | 1.647 | 2.37 | irregular
Story 5 | 3.132 | 1.338 | 2.34 | irregular
Story 4 | 2.136 | 0.953 | 2.24 | irregular
Story 3 | 0.501 | 0.347 | 1.44 | irregular
Story 2 | 0.219 | 0.145 | 1.51 | irregular
Story 1 | 0.124 | 0.078 | 1.59 | irregular
Torsional irregularity Y |  |  |  | 
Story Number | Max Drift | AVG Drift | Ratio | Check
Story 25 | 2.513 | 2.399 | 1.05 | regular
Story24 | 2.658 | 2.53 | 1.05 | regular
Story23 | 2.83 | 2.684 | 1.05 | regular
Story 22 | 3.016 | 2.847 | 1.06 | regular
Story 21 | 3.203 | 3.009 | 1.06 | regular
Story 20 | 3.381 | 3.162 | 1.07 | regular
Story 19 | 3.545 | 3.302 | 1.07 | regular
Story 18 | 3.688 | 3.423 | 1.08 | regular
Story 17 | 3.806 | 3.524 | 1.08 | regular
Story 16 | 3.895 | 3.601 | 1.08 | regular
Story 15 | 3.949 | 3.65 | 1.08 | regular
Story 14 | 3.964 | 3.668 | 1.08 | regular
Story 13 | 3.93 | 3.649 | 1.08 | regular
Story 12 | 3.837 | 3.587 | 1.07 | regular
Story 11 | 3.664 | 3.467 | 1.06 | regular
Story 10 | 3.381 | 3.267 | 1.03 | regular
Story 9 | 2.938 | 2.91 | 1.01 | regular
Story 8 | 2.641 | 2.068 | 1.28 | irregular
Story 7 | 2.693 | 2.112 | 1.28 | irregular
Story 6 | 2.096 | 1.641 | 1.28 | irregular
Story 5 | 1.755 | 1.374 | 1.28 | irregular
Story 4 | 1.221 | 0.963 | 1.27 | irregular
Story 3 | 0.203 | 0.142 | 1.43 | irregular
Story 2 | 0.068 | 0.053 | 1.28 | irregular
Story 1 | 0.051 | 0.039 | 1.31 | irregular

## Slide 33
seismic analysis
To deal with this irregularity, the eccentricity must be calculated.
the Center of mass and rigidity |  |  |  |  |  |  |  |  |  |  | 
Story | Diaphragms | Mass X | Mass y | C.M |  | Cumulative x | Cumulative Y | XCCM | YCCm | C.R | 
 |  |  |  | xm | ym |  |  |  |  | XCR | YCR
Story25 | Diaphragm2 | 2042488.85 | 2042488.85 | 45.2803 | 77.8734 | 2042488.85 | 2042488.85 | 45.28 | 77.87 | 46.10 | 75.48
Story24 | Diaphragm2 | 1862736.16 | 1862736.16 | 45.333 | 77.7295 | 3905225.01 | 3905225.01 | 45.31 | 77.80 | 46.05 | 75.33
Story23 | Diaphragm2 | 1862736.16 | 1862736.16 | 45.333 | 77.7295 | 5767961.17 | 5767961.17 | 45.31 | 77.78 | 46.01 | 75.18
Story22 | Diaphragm2 | 1853604.6 | 1853604.6 | 45.2702 | 77.635 | 7621565.77 | 7621565.77 | 45.30 | 77.75 | 45.97 | 75.01
Story21 | Diaphragm2 | 1862812.64 | 1862812.64 | 45.3337 | 77.7303 | 9484378.41 | 9484378.41 | 45.31 | 77.74 | 45.93 | 74.84
Story20 | Diaphragm2 | 1862812.64 | 1862812.64 | 45.3337 | 77.7303 | 11347191.05 | 11347191.05 | 45.31 | 77.74 | 45.88 | 74.65
Story19 | Diaphragm2 | 1862812.64 | 1862812.64 | 45.3337 | 77.7303 | 13210003.69 | 13210003.69 | 45.32 | 77.74 | 45.82 | 74.45
Story18 | Diaphragm2 | 1862812.64 | 1862812.64 | 45.3337 | 77.7303 | 15072816.34 | 15072816.34 | 45.32 | 77.74 | 45.75 | 74.22
Story17 | Diaphragm2 | 1862812.64 | 1862812.64 | 45.3337 | 77.7303 | 16935628.98 | 16935628.98 | 45.32 | 77.74 | 45.65 | 73.96
Story16 | Diaphragm2 | 1862812.64 | 1862812.64 | 45.3337 | 77.7303 | 18798441.62 | 18798441.62 | 45.32 | 77.74 | 45.51 | 73.66
Story15 | Diaphragm2 | 1862812.64 | 1862812.64 | 45.3337 | 77.7303 | 20661254.26 | 20661254.26 | 45.32 | 77.74 | 45.34 | 73.30
Story14 | Diaphragm2 | 1862812.64 | 1862812.64 | 45.3337 | 77.7303 | 22524066.9 | 22524066.9 | 45.32 | 77.74 | 45.09 | 72.85
Story13 | Diaphragm2 | 1862812.64 | 1862812.64 | 45.3337 | 77.7303 | 24386879.54 | 24386879.54 | 45.32 | 77.73 | 44.75 | 72.26
Story12 | Diaphragm2 | 1862812.64 | 1862812.64 | 45.3337 | 77.7303 | 26249692.18 | 26249692.18 | 45.32 | 77.73 | 44.26 | 71.48
Story11 | Diaphragm2 | 1862812.64 | 1862812.64 | 45.3337 | 77.7303 | 28112504.82 | 28112504.82 | 45.33 | 77.73 | 43.53 | 70.35
Story10 | Diaphragm2 | 1862812.64 | 1862812.64 | 45.3337 | 77.7303 | 29975317.46 | 29975317.46 | 45.33 | 77.73 | 42.38 | 68.66
Story9 | Diaphragm2 | 1862812.64 | 1862812.64 | 45.3337 | 77.7303 | 31838130.1 | 31838130.1 | 45.33 | 77.73 | 40.59 | 66.04
Story8 | Diaphragm2 | 3966595.7 | 3966595.7 | 35.6258 | 64.8273 | 35804725.8 | 35804725.8 | 44.25 | 76.30 | 38.49 | 62.99
Story7 | Diaphragm2 | 4131906.92 | 4131906.92 | 35.3321 | 64.239 | 39936632.72 | 39936632.72 | 43.33 | 75.06 | 38.13 | 62.88
Story6 | Diaphragm2 | 4131906.92 | 4131906.92 | 35.3321 | 64.239 | 44068539.63 | 44068539.63 | 42.58 | 74.04 | 37.80 | 62.90
Story5 | Diaphragm2 | 4095492.81 | 4095492.81 | 35.3187 | 64.2501 | 48164032.44 | 48164032.44 | 41.96 | 73.21 | 37.50 | 63.00
Story4 | Diaphragm2 | 4097790.34 | 4097790.34 | 35.3066 | 64.2301 | 52261822.78 | 52261822.78 | 41.44 | 72.50 | 37.12 | 62.85
Story3 | Diaphragm2 | 7137329.14 | 7137329.14 | 31.8843 | 55.747 | 59399151.92 | 59399151.92 | 40.29 | 70.49 | 35.51 | 59.16
Story2 | Diaphragm2 | 7264433.61 | 7264433.61 | 31.7232 | 55.8356 | 66663585.53 | 66663585.53 | 39.36 | 68.89 | 35.37 | 60.09
Story1 | Diaphragm2 | 7178821.08 | 7178821.08 | 32.198 | 55.8127 | 73842406.61 | 73842406.61 | 38.66 | 67.62 | 35.48 | 60.51

## Slide 34
seismic analysis
To deal with this irregularity, the eccentricity must be calculated.
the Eccentricity |  |  |  |  |  |  | 
Eccentricity |  | Dimension |  | ex/Dx result |  | ey/Dy result | 
ex | ey | Dx | Dy | % |  | % | 
0.82 | 2.40 | 31 | 39 | 2.6 | Ok | 6.1 | Ok
0.72 | 2.39 | 31 | 39 | 2.3 | Ok | 6.1 | Ok
0.67 | 2.55 | 31 | 39 | 2.2 | Ok | 6.5 | Ok
0.70 | 2.62 | 31 | 39 | 2.3 | Ok | 6.7 | Ok
0.60 | 2.89 | 31 | 39 | 1.9 | Ok | 7.4 | Ok
0.55 | 3.08 | 31 | 39 | 1.8 | Ok | 7.9 | Ok
0.49 | 3.28 | 31 | 39 | 1.6 | Ok | 8.4 | Ok
0.41 | 3.51 | 31 | 39 | 1.3 | Ok | 9.0 | Ok
0.31 | 3.77 | 31 | 39 | 1.0 | Ok | 9.7 | Ok
0.18 | 4.07 | 31 | 39 | 0.6 | Ok | 10.4 | Ok
0.00 | 4.43 | 31 | 39 | 0.0 | Ok | 11.4 | Ok
0.24 | 4.88 | 31 | 39 | 0.8 | Ok | 12.5 | Ok
0.58 | 5.47 | 31 | 39 | 1.9 | Ok | 14.0 | Ok
1.07 | 6.25 | 31 | 39 | 3.5 | Ok | 16.0 | Not Ok
1.81 | 7.38 | 31 | 39 | 5.8 | Ok | 18.9 | Not Ok
2.95 | 9.07 | 31 | 39 | 9.5 | Ok | 23.2 | Not Ok
4.74 | 11.69 | 31 | 39 | 15.3 | Not ok | 30.0 | Not Ok
2.86 | 1.84 | 52 | 81.1 | 5.5 | Ok | 2.3 | Ok
2.80 | 1.36 | 52 | 81.1 | 5.4 | Ok | 1.7 | Ok
2.46 | 1.34 | 52 | 81.1 | 4.7 | Ok | 1.7 | Ok
2.18 | 1.25 | 52 | 81.1 | 4.2 | Ok | 1.5 | Ok
1.81 | 1.38 | 52 | 81.1 | 3.5 | Ok | 1.7 | Ok
3.62 | 3.41 | 70.5 | 96.915 | 5.1 | Ok | 3.5 | Ok
3.65 | 4.26 | 70.5 | 96.915 | 5.2 | Ok | 4.4 | Ok
3.28 | 4.70 | 70.5 | 96.915 | 4.7 | Ok | 4.8 | Ok

## Slide 35
seismic analysis
Drift check.

## Slide 36
seismic analysis
Drift check.
In X direction:
Story Drift X |  |  |  |  |  | 
Story | Height(m) | Δ Elastic(mm) | Δ Inelastic(mm) | Δ Service(mm) | Δ Allowable(mm) | Check
25 | 100.6 | 126.816 | 557.9904 | 390.59328 | 1509 | OK
24 | 96.6 | 121.626 | 535.1544 | 374.60808 | 1449 | OK
23 | 92.6 | 116.267 | 511.5748 | 358.10236 | 1389 | OK
22 | 88.6 | 110.711 | 487.1284 | 340.98988 | 1329 | OK
21 | 84.6 | 104.939 | 461.7316 | 323.21212 | 1269 | OK
20 | 80.6 | 98.951 | 435.3844 | 304.76908 | 1209 | OK
19 | 76.6 | 92.753 | 408.1132 | 285.67924 | 1149 | OK
18 | 72.6 | 86.363 | 379.9972 | 265.99804 | 1089 | OK
17 | 68.6 | 79.807 | 351.1508 | 245.80556 | 1029 | OK
16 | 64.6 | 73.119 | 321.7236 | 225.20652 | 969 | OK
15 | 60.6 | 66.339 | 291.8916 | 204.32412 | 909 | OK
14 | 56.6 | 59.511 | 261.8484 | 183.29388 | 849 | OK
13 | 52.6 | 52.685 | 231.814 | 162.2698 | 789 | OK
12 | 48.6 | 45.919 | 202.0436 | 141.43052 | 729 | OK
11 | 44.6 | 39.275 | 172.81 | 120.967 | 669 | OK
10 | 40.6 | 32.823 | 144.4212 | 101.09484 | 609 | OK
9 | 36.6 | 26.645 | 117.238 | 82.0666 | 549 | OK
8 | 32.6 | 21.166 | 93.1304 | 65.19128 | 489 | OK
7 | 28.6 | 15.782 | 69.4408 | 48.60856 | 429 | OK
6 | 24.1 | 10.364 | 45.6016 | 31.92112 | 361.5 | OK
5 | 20.1 | 6.296 | 27.7024 | 19.39168 | 301.5 | OK
4 | 16.1 | 3.017 | 13.2748 | 9.29236 | 241.5 | OK
3 | 12.1 | 0.774 | 3.4056 | 2.38392 | 181.5 | OK
2 | 7 | 0.274 | 1.2056 | 0.84392 | 105 | OK
1 | 3.5 | 0.101 | 0.4444 | 0.31108 | 52.5 | OK

## Slide 37
seismic analysis
In Y direction:
Drift check.
Story Drift Y |  |  |  |  |  | 
Story | Height(m) | Δ Elastic(mm) | Δ Inelastic(mm) | Δ Service(mm) | Δ Allowable(mm) | Check
25 | 100.6 | 84.651 | 372.4644 | 260.72508 | 1509 | OK
24 | 96.6 | 81.553 | 358.8332 | 251.18324 | 1449 | OK
23 | 92.6 | 78.282 | 344.4408 | 241.10856 | 1389 | OK
22 | 88.6 | 74.816 | 329.1904 | 230.43328 | 1329 | OK
21 | 84.6 | 71.145 | 313.038 | 219.1266 | 1269 | OK
20 | 80.6 | 67.272 | 295.9968 | 207.19776 | 1209 | OK
19 | 76.6 | 63.208 | 278.1152 | 194.68064 | 1149 | OK
18 | 72.6 | 58.973 | 259.4812 | 181.63684 | 1089 | OK
17 | 68.6 | 54.587 | 240.1828 | 168.12796 | 1029 | OK
16 | 64.6 | 50.076 | 220.3344 | 154.23408 | 969 | OK
15 | 60.6 | 45.468 | 200.0592 | 140.04144 | 909 | OK
14 | 56.6 | 40.794 | 179.4936 | 125.64552 | 849 | OK
13 | 52.6 | 36.087 | 158.7828 | 111.14796 | 789 | OK
12 | 48.6 | 31.388 | 138.1072 | 96.67504 | 729 | OK
11 | 44.6 | 26.74 | 117.656 | 82.3592 | 669 | OK
10 | 40.6 | 22.201 | 97.6844 | 68.37908 | 609 | OK
9 | 36.6 | 17.855 | 78.562 | 54.9934 | 549 | OK
8 | 32.6 | 13.857 | 60.9708 | 42.67956 | 489 | OK
7 | 28.6 | 10.441 | 45.9404 | 32.15828 | 429 | OK
6 | 24.1 | 6.951 | 30.5844 | 21.40908 | 361.5 | OK
5 | 20.1 | 4.232 | 18.6208 | 13.03456 | 301.5 | OK
4 | 16.1 | 1.951 | 8.5844 | 6.00908 | 241.5 | OK
3 | 12.1 | 0.382 | 1.6808 | 1.17656 | 181.5 | OK
2 | 7 | 0.136 | 0.5984 | 0.41888 | 105 | OK
1 | 3.5 | 0.058 | 0.2552 | 0.17864 | 52.5 | OK

## Slide 38
seismic analysis
In X direction:
Delta effect.
P-Delta X |  |  |  |  |  |  | 
Story | Height(m) | Δ Elastic(mm) | Δ Elastic service (mm) | P | Vx | Theta | check
25 | 100.6 | 126.816 | 88.7712 | 35052.525 | 767.7182 | 0.040289 | OK
24 | 96.6 | 121.626 | 85.1382 | 56679.1536 | 1422.3565 | 0.035121 | OK
23 | 92.6 | 116.267 | 81.3869 | 78305.7831 | 2032.4436 | 0.033862 | OK
22 | 88.6 | 110.711 | 77.4977 | 99842.8622 | 2596.1951 | 0.033638 | OK
21 | 84.6 | 104.939 | 73.4573 | 121470.9915 | 3120.2291 | 0.033803 | OK
20 | 80.6 | 98.951 | 69.2657 | 143099.1211 | 3602.7733 | 0.034134 | OK
19 | 76.6 | 92.753 | 64.9271 | 164727.2507 | 4044.9123 | 0.034519 | OK
18 | 72.6 | 86.363 | 60.4541 | 186355.3801 | 4447.7668 | 0.034889 | OK
17 | 68.6 | 79.807 | 55.8649 | 207983.5096 | 4812.4976 | 0.035194 | OK
16 | 64.6 | 73.119 | 51.1833 | 229611.6393 | 5140.3098 | 0.035392 | OK
15 | 60.6 | 66.339 | 46.4373 | 251239.7705 | 5432.4579 | 0.035439 | OK
14 | 56.6 | 59.511 | 41.6577 | 272867.9637 | 5690.2519 | 0.035294 | OK
13 | 52.6 | 52.685 | 36.8795 | 294496.0934 | 5915.0651 | 0.034908 | OK
12 | 48.6 | 45.919 | 32.1433 | 316124.224 | 6108.3436 | 0.034229 | OK
11 | 44.6 | 39.275 | 27.4925 | 337752.354 | 6271.6183 | 0.033197 | OK
10 | 40.6 | 32.823 | 22.9761 | 359380.4843 | 6406.5207 | 0.031746 | OK
9 | 36.6 | 26.645 | 18.6515 | 381008.6146 | 6514.8044 | 0.029803 | OK
8 | 32.6 | 21.166 | 14.8162 | 428796.2769 | 6692.7446 | 0.029118 | OK
7 | 28.6 | 15.782 | 11.0474 | 477298.1388 | 6827.9505 | 0.027002 | OK
6 | 24.1 | 10.364 | 7.2548 | 525085.8006 | 6913.0619 | 0.022865 | OK
5 | 20.1 | 6.296 | 4.4072 | 572873.5137 | 6959.8585 | 0.018048 | OK
4 | 16.1 | 3.017 | 2.1119 | 620684.5519 | 6976.9567 | 0.01167 | OK
3 | 12.1 | 0.774 | 0.5418 | 713367.7733 | 6976.9567 | 0.004578 | OK
2 | 7 | 0.274 | 0.1918 | 798083.5826 | 6976.9567 | 0.003134 | OK
1 | 3.5 | 0.101 | 0.0707 | 884575.5845 | 6976.9567 | 0.002561 | OK

## Slide 39
seismic analysis
In Y direction:
Delta effect.
P-Delta y |  |  |  |  |  |  | 
Story | Height(m) | Δ Elastic(mm) | Δ Elastic service (mm) | P | Vx | Theta | check
25 | 100.6 | 84.651 | 59.2557 | 35052.525 | 767.7182 | 0.026894 | OK
24 | 96.6 | 81.553 | 57.0871 | 56679.1536 | 1422.3565 | 0.023549 | OK
23 | 92.6 | 78.282 | 54.7974 | 78305.7831 | 2032.4436 | 0.022799 | OK
22 | 88.6 | 74.816 | 52.3712 | 99842.8622 | 2596.1951 | 0.022732 | OK
21 | 84.6 | 71.145 | 49.8015 | 121470.9915 | 3120.2291 | 0.022917 | OK
20 | 80.6 | 67.272 | 47.0904 | 143099.1211 | 3602.7733 | 0.023206 | OK
19 | 76.6 | 63.208 | 44.2456 | 164727.2507 | 4044.9123 | 0.023523 | OK
18 | 72.6 | 58.973 | 41.2811 | 186355.3801 | 4447.7668 | 0.023824 | OK
17 | 68.6 | 54.587 | 38.2109 | 207983.5096 | 4812.4976 | 0.024073 | OK
16 | 64.6 | 50.076 | 35.0532 | 229611.6393 | 5140.3098 | 0.024238 | OK
15 | 60.6 | 45.468 | 31.8276 | 251239.7705 | 5432.4579 | 0.02429 | OK
14 | 56.6 | 40.794 | 28.5558 | 272867.9637 | 5690.2519 | 0.024194 | OK
13 | 52.6 | 36.087 | 25.2609 | 294496.0934 | 5915.0651 | 0.02391 | OK
12 | 48.6 | 31.388 | 21.9716 | 316124.224 | 6108.3436 | 0.023397 | OK
11 | 44.6 | 26.74 | 18.718 | 337752.354 | 6271.6183 | 0.022602 | OK
10 | 40.6 | 22.201 | 15.5407 | 359380.4843 | 6406.5208 | 0.021472 | OK
9 | 36.6 | 17.855 | 12.4985 | 381008.6146 | 6514.8044 | 0.019971 | OK
8 | 32.6 | 13.857 | 9.6999 | 428796.2769 | 6692.7447 | 0.019063 | OK
7 | 28.6 | 10.441 | 7.3087 | 477298.1388 | 6827.9505 | 0.017864 | OK
6 | 24.1 | 6.951 | 4.8657 | 525085.8006 | 6913.0619 | 0.015335 | OK
5 | 20.1 | 4.232 | 2.9624 | 572873.5137 | 6959.8585 | 0.012131 | OK
4 | 16.1 | 1.951 | 1.3657 | 620684.5519 | 6976.9568 | 0.007546 | OK
3 | 12.1 | 0.382 | 0.2674 | 713367.7733 | 6976.9568 | 0.00226 | OK
2 | 7 | 0.136 | 0.0952 | 798083.5826 | 6968.9567 | 0.001557 | OK
1 | 3.5 | 0.058 | 0.0406 | 884575.5845 | 6968.169 | 0.001473 | OK

## Slide 40
seismic analysis
Vertical irregularity.

## Slide 41
seismic analysis
Vertical irregularity.
In X direction:

## Slide 42
seismic analysis
In Y direction:
Vertical irregularity.

## Slide 43
all for listening
Thank you