## Slide 1
Prepared By : Somoud Yaseen
Israa Nassasrah
Under Supervision of: Dr. Ryiad Abdel-karim
Structural Analysis and Design
of AL-ARZ Building

## Slide 2
Outline
1 Project description.
2 The Codes Used in Project .
Materials
3
4 Gravity Loads
Preliminary Design
5
Etabs Model
6
Etabs model checks
7.
8
Design of footing, Basement wall and stair
9.
Design Of Slab, Beam And Column

## Slide 3: Project Description
Height (m) | ( Area ( | Function | Floor Name
2.5 | 359 | Parking | Basement Floor 1
2.75 | 359 | Parking | Basement Floor 2
4.75 | 320 | stores | Basement Floor 3
3.25 | 322.97 | Stores and gallery | Ground Floor
3.25 | 373.49 | Gallery | First Floor
3.25 | 373.49 | Gallery | Second Floor
3.25 | 373.49 | Offices | Third Floor
23 | 2481.44 |  | Total
Height (m) |  | Function | Floor Name
2.5 | 359 | Parking | Basement Floor 1
2.75 | 359 | Parking | Basement Floor 2
4.75 | 320 | stores | Basement Floor 3
3.25 | 322.97 | Stores and gallery | Ground Floor
3.25 | 373.49 | Gallery | First Floor
3.25 | 373.49 | Gallery | Second Floor
3.25 | 373.49 | Offices | Third Floor
23 | 2481.44 |  | Total

## Slide 4: Codes:
ACI 318-14 (American Concrete Institute )
UBC -97 (Uniform Building Code )
ASCE-7(2010)

## Slide 5
SOFTWARE
SAP2000
ETABS 16

## Slide 6: Materials:
1. Concrete
B400 | B300 | 
25KN/ | 25KN/ | Unit Weight
32MPa k | 24MPa | Concrete Compressive Strength
3.51MPa | 3.04MPa | Concrete Flexural Strength
1.87 MPa | 1.62MPa | Concrete Tensile Strength
26587MPa | 23025MPa | Modulus of Elasticity
0.2 | 0.2 | Poisson Ratio
B400 | B300 | 
 |  | Unit Weight
32MPa k | 24MPa | 
3.51MPa | 3.04MPa | 
1.87 MPa | 1.62MPa | 
26587MPa | 23025MPa | 
0.2 | 0.2 | Poisson Ratio

## Slide 7: Materials:
A955 G60 | Steel
420MPa | Yielding strength , fy
620MPa | Tensile strength , fu
200 GPa | Modulus of Elasticity , E
2. Steel `

## Slide 8
(Unit Weight (KN/ | Material
23 | Mortar and Plastering
23 | Filling Material
12 | Blocks
27 | Masonry Stone
24 | Tiles
 | Material
23 | Mortar and Plastering
23 | Filling Material
12 | Blocks
27 | Masonry Stone
24 | Tiles
Materials :

## Slide 9: Gravity Loads:
Dead Load =Own Weight of structure
Super Imposed Dead Load = 5 KN/
Live Load for Garages =4.79 KN/
Live Load for Offices =2.5 KN/

## Slide 10
Preliminary Design :
Slabs Structural Systems
Slabs Structural Systems:
Two –Way solid slab
.

## Slide 11
Preliminary Design
Preliminary Slabs Thickness :
h =25cm

## Slide 12: Preliminary Design :
Design Of Interior Frame:

## Slide 13: Preliminary Design :
The frame section dimensions :

## Slide 14: Preliminary Design :
frame loads:
Live load for floors =2.5×8=20 KN/m

## Slide 15: Preliminary Design :
Bending Moment Diagram for the Frame :

## Slide 16: Preliminary Design :
Bending moment diagram for the column strip.

## Slide 17: Preliminary Design :
Beam moments:
The beam in each span should resist 85% of column strip moments.

## Slide 18: Preliminary Design :
The slab in the column strip takes the difference between the column strip moments and the beam moments

## Slide 19: Preliminary Design :
Moments for slab in middle strip:
The slab in the middle strip should resist the difference between the frame moment and the column strip moments.

## Slide 20: Preliminary Design :
Dimensions of column strip, middle strips, and beams:

## Slide 21: Preliminary Design :
Sections of slabs in column and middle strips in each span

## Slide 22: Preliminary Design :
Check Wide Beam Shear in slab:
Thickness is adequate.

## Slide 23: Preliminary Design :
Design of slab in column strip for flexure:
Maximum positive moment,
Use

## Slide 24: Preliminary Design :
Design of slab in column strip for flexure:
Maximum negative moment,
Use

## Slide 25: Preliminary Design :
Design of slab in middle strip for flexure:
Maximum positive moment,
Use

## Slide 26: Preliminary Design
Design of slab in middle strip for flexure:
Maximum negative moment,
Use

## Slide 27
Preliminary Design :
Preliminary Design of Beam :
Structural member | Thickness(mm) | Width(mm)
Main beams for garages | 600 | 300
Main beams for floors | 600 | 300

## Slide 28: Preliminary Design
Design of beam B6 for shear and flexure:
Design for shear:
transmission of loads into beam B6.

## Slide 29: Preliminary Design
Design For Shear :
Shear reinforcement is required.

## Slide 30: Preliminary Design
Design For flexure:
maximum positive moment,
maximum negative moment,

## Slide 31
Preliminary Design of Column
Column No. | Tributary area (m2) | Dead load (KN) | Live load (KN) | Ultimate load (KN) | Gross area (mm2) | Column dimensions (mm)
C1 | 8 | 1991.543 | 367.824 | 2359.367 | 145760.9 | 600*300
C2 | 19 | 2921.708 | 857.232 | 3778.94 | 233461.6 | 800*400
C3 | 21.6 | 3136.34 | 925.0848 | 4061.425 | 250913.4 | 800400
C4 | 19.2 | 2647.973 | 812.6976 | 3460.67 | 213799 | 800*400
C5 | 6.8 | 1162.867 | 238.8173 | 1401.684 | 86595.58 | 600*300
C6 | 33.9 | 3641.464 | 1196.206 | 4837.67 | 298869.6 | 800*400
C7 | 41.6 | 4452.69 | 1469.645 | 5922.335 |  | 800*400
C8 | 37.3 | 4138.563 | 1319.148 | 5457.711 | 337175.4 | 800*400
C9 | 6.2 | 1206.068 | 216.5606 | 1422.628 | 87889.47 | 600*300
C10 | 8.8 | 1536.48 | 310.8864 | 1847.366 | 114129.6 | 600*300
C11 | 13.4 | 2033.163 | 459.3952 | 2492.558 | 153989.4 | 600*300
C12 | 28.1 | 3425.961 | 956.7168 | 4382.678 | 270760.3 | 800*400
C13 | 28.3 | 3041.643 | 983.7824 | 4025.425 | 248689.4 | 600
Column No. | Tributary area (m2) | Dead load (KN) | Live load (KN) | Ultimate load (KN) | Gross area (mm2) | Column dimensions (mm)
C1 | 8 | 1991.543 | 367.824 | 2359.367 | 145760.9 | 600*300
C2 | 19 | 2921.708 | 857.232 | 3778.94 | 233461.6 | 800*400
C3 | 21.6 | 3136.34 | 925.0848 | 4061.425 | 250913.4 | 
C4 | 19.2 | 2647.973 | 812.6976 | 3460.67 | 213799 | 800*400
C5 | 6.8 | 1162.867 | 238.8173 | 1401.684 | 86595.58 | 600*300
C6 | 33.9 | 3641.464 | 1196.206 | 4837.67 | 298869.6 | 800*400
C7 | 41.6 | 4452.69 | 1469.645 | 5922.335 |  | 800*400
C8 | 37.3 | 4138.563 | 1319.148 | 5457.711 | 337175.4 | 800*400
C9 | 6.2 | 1206.068 | 216.5606 | 1422.628 | 87889.47 | 600*300
C10 | 8.8 | 1536.48 | 310.8864 | 1847.366 | 114129.6 | 600*300
C11 | 13.4 | 2033.163 | 459.3952 | 2492.558 | 153989.4 | 600*300
C12 | 28.1 | 3425.961 | 956.7168 | 4382.678 | 270760.3 | 800*400
C13 | 28.3 | 3041.643 | 983.7824 | 4025.425 | 248689.4 | 600
Preliminary Design

## Slide 32: ETABS Model

## Slide 33: ETABS Model Checks
Compatibility
Equilibrium
Stress - Strain
Checks

## Slide 34: ETABS Model Checks
Compatibility Check

## Slide 35: ETABS Model Checks
Equilibrium Check:
%Difference | Manually KN | Fz (Etabs) KN | Load case
2.8% | 32564 | 3166.32 | Dead
1.6% | 7237.3 | 7351.3 | Live
2% | 11394 | 11665.1 | SID

## Slide 36: ETABS Model Checks
Stress – Strain Check (For Beam)
span to be checked L=6.8m
For internal main beam:
Moment from ETABS:
Moment from hand calculations:
Error=9%<10% OK

## Slide 37: ETABS Model Checks
Stress – Strain Check (For Column)
Make check on column (C7)
The ultimate axial load on column C7 from ETABS=6519KN
The ultimate load by hand on column C7=6043
%deference = =7%

## Slide 38: ETABS Model Checks
Deflection Check:
According to ACI 318-14:
From Figure :

## Slide 39: Design Of Slab, Beam And Column
Design of slab:
check of slab for wide beam shear
the maximum shear in X-direction :
No need for shear reinforcement.

## Slide 40: Design Of Slab, Beam And Column
Design of slab:
check of slab for wide beam shear
the maximum shear in Y-direction :
Thickness is adequate.

## Slide 41: Design Of Slab, Beam And Column
Design the slab for flexure:
For negative moment:
The maximum negative moment from M11=29.49KN.m/m
=.0018×1000×250=
Use As=450→4Ø12

## Slide 42: Design Of Slab, Beam And Column
Design the slab for flexure :
For positive moment:
maximum positive moment from M11=31.95KN.m/m
As=0.00195*1000*210=409.5
USE As=409.5 →4Ø12

## Slide 43: Design Of Slab, Beam And Column
Design the slab for flexure :
For negative moment:
Maximum negative moment from M22=18.75KN.m/m
ρ = 0.001136
As=As min=0.0018×1000×250=450 mm2
Use As=450→4Ø12

## Slide 44: Design Of Slab, Beam And Column
Design the slab for flexure :
For positive moment:
Maximum positive moment frome M22=32.7 KN.m/m
ρ= 0.002
As =0.002×1000×210= 420 mm²
Use As=450→4Ø12

## Slide 45: Design Of Slab, Beam And Column

## Slide 46: Design Of Slab, Beam And Column
Design of Beams:
For a sample of calculation B6 is taken: Beam dimension: 300×600 mm

## Slide 47: Design Of Slab, Beam And Column
Design of Beams:
Design of B6 for Shear:
Vn = 284 KN Vc = 132.3 KN Vs = Vn - Vc = 151.7 KN = = =0.67 mm2/mm Assume stirrups diameter (10 mm ) Av = 157 mm Use S = 200 mm1 φ 10 /20cm

## Slide 48: Design Of Slab, Beam And Column
Design of Beam:
Design B6 for flexure :
For maximum negative moment: =0.008
As = *b*d =0.008*300*540 =1296 mm2
Use 8Ø16

## Slide 49: Design Of Slab, Beam And Column
Design of Beam:
Design B6 for flexure :
For maximum negative moment = 0.004138
As = *b*d =0.004138*300*540 =670.36 mm2
Use 4Ø16

## Slide 50: Design Of Slab, Beam And Column
Design of Beam:
Longitudinal reinforcement to resist moment:

## Slide 51: Design Of Slab, Beam And Column
Stirrups for shear reinforcement :

## Slide 52: Design Of Slab, Beam And Column
Design of column :
The column are divide into 5 groups these groups have the same dimensions
NO. of group | Size(mm) | Bars | Ties |  | 
 |  |  | A | B | C
C1 | 1500*600 | 26Ø22 | 1Ø10/125mm | 1Ø10/125mm | 1Ø10/125mm
C2 | 1200*400 | 20Ø18 | 1Ø10/100mm | 1Ø10/100mm | 1Ø10/100mm
C3 | 1000*300 | 16Ø16 | 1Ø10/100mm | 1Ø10/100mm | 1Ø10/100mm
C4 | 1200*600 | 24Ø20 | 1Ø10/100mm | 1Ø10/100mm | 1Ø10/100mm
C5 | 800 | 10Ø25 | 1Ø10/100mm | 1Ø10/100mm | 1Ø10/100mm

## Slide 53: Design Of Slab, Beam And Column
Design of Column:

## Slide 54: Design of footing and Basement wall
Design of footing:
Suitable footing system:
the allowable bearing capacity for the soil is 250kN/.
Mat footing has used in our project because total area of footings >50% × area of building
AF = =
50%*Area of building=203
The thickness of mat footing=0.9m

## Slide 56: Design of footing and Basement wall
Checks of mat foundation:
Compatibility:
By making start animation for the deformed shape of SAFE model, it was noticed that the structural elements are compatible and all of them are moving together,

## Slide 57: Design of footing and Basement wall
Allowable displacement in the mat foundation is10mm.
The maximum displacement of the footings is shown in figure
and it is lees than 10mm → ok

## Slide 58: Design of footing and Basement wall
Check soil pressure:
Maximum allowable 𝑠𝑡𝑟𝑒𝑠𝑠𝑖𝑠 250 𝑘𝑁/𝑚2
Maximum stress on the footing from SAFE =225 is KN/m2 < 250 KN/m2 → OK
Show figure

## Slide 59: Design of footing and Basement wall
Check for Punching shear
Punching shear check is done by SAFE.
Punching shear is the actual load over the ultimate load, so if the values of punching shear design less than 1, so it’s OK
By Hand:
Check for Punching.
Pu=7567KN.
ΦVcp=0.75***(2×1450+2×2350)*850*10-3.
=7911.85 KN >Pu............. So it's ok

## Slide 60: Design of footing and Basement wall
Design the footing:
Design for shear:
Vu=480KN
ØVc=0.75×1/6××1000×850/1000= 520.5 KN
Vu<ØVc
Design of flexure:
We divide the slab into column strip and middle strip as shown in the figure below

## Slide 63: Design of footing and Basement wall
Design and Calculation of Basement Wall:
Design Loads:
_Bulk density () =18KN/m3
_Angle of internal friction (Ø) =30˚
_Active coefficient in cohesion less s soil (Ka) =0.333
_Load from building =19.5 KN/m
_Soil load:
q1=0 KN/m2 →at Z=0
q2=60 KN/m2 →at Z=10
_use sap 2000 to design basement wall

## Slide 64: Design of footing and Basement wall
Design for Shear:
=0.17*0.75*
=0.17*0.75*156.15KN
Thickness is ok.

## Slide 65: Design of footing and Basement wall
Design for flexure:
Use As min.
Use1 /200mm c/c
Exterior face of wall:
=0.0015*1000*300= 450mm2
Use1 /350mm c/c
=0.0025*1000*300= 750mm2
Front face =
Rare face =
Use for front face
Use1 /350mm c/c for rare face

## Slide 66: Design of footing and Basement wall

## Slide 67: Design of stairs
Dimension of stairs:
The thickness of stair slab is assumed = 18 cm
The figure below shows the plan of stairs

## Slide 68: Design of stairs
Loads on stairs:
The total loads on stairs are:
The own weight of stairs = 0.18∗25𝑚 =4.5𝑘𝑁/𝑚2
The live load is assumed =4.5 KN/m2.
The SD =3 KN/m2

## Slide 69: Design of stairs
Check for defection based on the long term deflection:
Max. immediate deflection due to service load from SAP( ∆ )=0.52 mm
Deflection limitation:-
∆ 𝐿,𝑎𝑙𝑙𝑎𝑤𝑎𝑏𝑙𝑒( 𝐿𝑜𝑛𝑔𝑡𝑒𝑟𝑚) ≤ 𝑙/240 = 2400/240 = 10𝑚𝑚
0.52<10 → OK

## Slide 70: Design of stairs
Check for shear:
Vu=20.12KN/m from figure
𝑑 = 180-30 = 150 𝑚𝑚
∅𝑉𝑐 = 0.75× ×√𝑓𝑐` 𝑏 ×𝑑 =
=0.75× × ×1000
Since ∅𝑉𝑐 =99𝑘𝑁>𝑉𝑢 = 20.12 ,
there is no need for shear reinforcement.

## Slide 71: Design of stairs
Design for longitudinal steel with stairs using (M22):
- In flight:
For the middle M22 (positive) =8.5KN.m
Bottom steel
𝜌= 0.001
𝜌<𝜌min=0.0033
So the 𝐴𝑠 = 0.0033 ×150×1000 = 495𝑚𝑚2
𝑢𝑠𝑒𝐴𝑠 (4 ∅124/ 1m)
Use (4 ∅14/1m) for all longitudinal steel ( main steel )
- In landing:
M22 in the Landing= 1kN.m and it is positive moment (bottom steel)
𝜌 = 0.0001
𝜌<𝜌min
Use As min.=0.0033*1000*150=495 mm2 (4 ∅14)

## Slide 72: Design of stairs
Design for Transverse steel with stairs using (M11):
the transverse moment =3KN.m
𝜌=0.000353
𝜌<𝜌min.
Use As min
𝐴𝑠 𝑠ℎ𝑟𝑖𝑛𝑘𝑎𝑔𝑒 = 𝐴𝑠 𝑚𝑖𝑛 = 0.002×180×1000 = 360 𝑚𝑚2
in both face (Use 5 ∅10 /1m for each layer)

## Slide 73: Design of stairs