## Slide 1
An-Najah National University
Engineering Faculty
Building Engineering Department
Integrated Design of a Digital Media Center in Nablus
Prepared by: Ahmad Atif
Loorene Murad
Sondus Yaseen
Supervised by: Dr. Muhannad Haj Hussien

## Slide 2: Contents
Introduction
Brief Insight
Architectural Design
Environmental Analysis
Structural Design
Electro-Mechanical Design
Quantity Surveying

## Slide 3
Introduction
“The Digital Media Center is a multimedia lab space as well as an equipment, printing and knowledge resource for people interested in exploring creative uses of emerging media and technology to communicate their ideas.”

## Slide 4
Brief insight

## Slide 5
Architectural design

## Slide 6: Architectural Plans before and after modification

## Slide 7
Basement floor
Before
After

## Slide 8
Additional basement plan

## Slide 9
Emergency evacuation plan

## Slide 10: Elevations before and after modification

## Slide 11
South elevation
Before
South elevation
After

## Slide 12
West elevation
Before
West elevation
After

## Slide 13
East elevation
Before
East elevation
After

## Slide 14
North elevation
Before
North elevation
After

## Slide 15: sections before and after modification

## Slide 16
Section A-A
Before
Section A-A
After

## Slide 17
Section B-B
Before
Section B-B
After

## Slide 18
environmental analysis

## Slide 19
Environmental analysis
Shading Analysis
1
Daylight Factor
2
Solar irradiation
3
Thermal Analysis
4

## Slide 20
Shading and over shadowing
In Winter:
At 8:00 AM
At 12:00 PM
At 2:00 PM

## Slide 21
Shading and over shadowing
In Summer:
At 8:00 AM
At 12:00 PM
At 2:00 PM

## Slide 22: Daylight factor
Before treatments

## Slide 23: Treatments used

## Slide 24: Daylight factor
after treatments

## Slide 25: Solar irradiation
Annual solar irradiation
Surface elevation | Solar irradiation before (W/m2) | Solar irradiation after (W/m2)
Roof | 299 | 236
Floors | 17 | 13
South | 206 | 156
East | 79 | 64
North | 69 | 53
West | 70 | 49

## Slide 26: Construction layers and U-value
For External wall
U-value = 0.353 W/m2.K
U-value = 1.961 W/m2.K
For internal wall

## Slide 27: Heating load
Total design heating capacity = 245.23 KW

## Slide 28: cooling load
Total design cooling capacity = 416.6 KW

## Slide 29: Simulation output
energy portfolio manager standard for mixed use property is 248.2 KWh/m2
PMV – Set

## Slide 30
Structural analysis and design

## Slide 31
Structural analysis and design
Codes
Material Properties
Validation Checks
Seismic Checks
Design and Detailing

## Slide 32
ANALYSIS AND DATA COLLECTION
Codes
ACI 318M-14
UBC 1997
ASCE-16
Material Properties
Reinforced Concrete
24 MPa
28 MPa (used for slabs and beams)
32 MPa (used for columns, shear walls and foundation)
Reinforcing Steel with yielding strength = 420 MPa

## Slide 33
Structural building blocks

## Slide 34
Validation checks
Compatibility Check
Deflection Check
Equilibrium Check
Stress – Strain Check
Block 1
Block 2
Block 3

## Slide 35
Validation checks
Compatibility Check
Deflection Check
Equilibrium Check
Stress – Strain Check
Block 1
Block 2
Block 3
the permissible deflection =

## Slide 36
Validation checks
Compatibility Check
Deflection Check
Equilibrium Check
Stress – Strain Check
Block 1 | Dead Load | SID Load | Live Load
Manual | 26349.38 | 9925.338 | 9905.7312
ETABS | 25802.729 | 9955.039 | 9620.6454
%Error | 2.11 | 0.29 | 2.96
Block 1 | Dead Load | SID Load | Live Load
Manual | 21008.234 | 11199.642 | 11050.7376
ETABS | 20081.783 | 11081.726 | 10795.6464
%Error | 4.61 | 1.064 | 2.36
Block 1 | Dead Load | SID Load | Live Load
Manual | 46823.34 | 24655.24 | 19029.04
ETABS | 47288.36 | 24655.24 | 19029.20
%Error | 1.14 | 0 | 0
%Error should be less than 5%

## Slide 37
Validation checks
Compatibility Check
Deflection Check
Equilibrium Check
Stress – Strain Check
%Error should be less than 10%
%ERROR | For column | For beams
Block 1 | 1.1 | 2.05
Block 2 | 8.2 | 6.4
Block 3 | 5.5 | 7.4

## Slide 38
Seismic inputs
Seismic Zone  Z = 0.2
Soil Profile  SE
Occupancy Category  I = 1.25
Structural System  R = 5.5 (building frame system with shear walls)
Seismic Coefficient  Ca = 0.34
Cv = 0.64

## Slide 39
Seismic checks
Period and modal participation ratio check
Block 1
Block 2
Block 3

## Slide 40
Seismic checks
Base – Shear check
Block 1
Block 2
Block 3

## Slide 41
Seismic checks
Drift check
Block 1
Block 2
Block 3

## Slide 42
Block 1
Block 2
Block 3
Slabs system
Voided slab H=40 cm with hidden beams
Voided slab H=40 cm with hidden beams
Voided slab H=60 cm with hidden beams

## Slide 43
Slabs detailing
Section in slab H=40 cm for block 1 & 2
Section in slab H=40 cm for block 3
Section in slab H=20 cm for SOG

## Slide 44
Beams design
Beam #. | B×H(m) | Longitudinal reinforcement |  |  |  | Transverse reinforcement |  |  | 
 |  | position | Ln | #ØD | L(m) | stirrups at support |  | stirrups at middle | 
 |  |  |  |  |  | s1 | # | s2 | #
3 | 0.7*0.4 | AI | 12.15 | 10Ø20 | 3.45 | 2legs Ø10/80mm | 68 | 4legs Ø10/170mm | 36
 |  | AM | 12.15 | 2Ø20 | 6.98 |  |  |  | 
 |  | AJ | 12.15 | 7Ø20 | 8.10 |  |  |  | 
 |  | AB | 12.15 | 8Ø20 | 13.29 |  |  |  | 
11 | 0.6*0.4 | AI | 8.43 | 9Ø20 | 2.52 | 2legs Ø10/80mm | 47 | 4legs Ø10/170mm | 25
 |  | AM | 8.43 | 2Ø20 | 5.43 |  |  |  | 
 |  | AJ | 8.43 | 5Ø20 | 5.62 |  |  |  | 
 |  | AB | 8.43 | 5Ø20 | 9.57 |  |  |  | 
14 | 0.6*0.4 | AI | 6.81 | 12Ø20 | 2.11 | 2legs Ø10/80mm | 38 | 4legs Ø10/170mm | 20
 |  | AM | 6.81 | 3Ø20 | 4.76 |  |  |  | 
 |  | AJ | 6.81 | 4Ø20 | 4.54 |  |  |  | 
 |  | AB | 6.81 | 6Ø20 | 7.95 |  |  |  | 

## Slide 45
Beam #. | B×H(m) | Longitudinal reinforcement |  |  |  | Transverse reinforcement |  |  | 
 |  | position | Ln | #ØD | L(m) | stirrups at support |  | stirrups at middle | 
 |  |  |  |  |  | s1 | # | s2 | #
4 | 0.6*0.4 | AI | 8.11 | 16Ø20 | 5.41 | 4legs Ø10/80mm | 51 | 4legs Ø10/170mm | 24
 |  | AM | 8.11 | 4Ø20 | 5.30 |  |  |  | 
 |  | AJ | 8.11 | 6Ø20 | 5.41 |  |  |  | 
 |  | AB | 8.11 | 14Ø20 | 9.25 |  |  |  | 
9 | 0.6*0.4 | AI | 13.95 | 7Ø20 | 9.30 | 4legs Ø10/80mm | 87 | 4legs Ø10/170mm | 41
 |  | AM | 13.95 | 2Ø20 | 7.73 |  |  |  | 
 |  | AJ | 13.95 | 10Ø20 | 9.30 |  |  |  | 
 |  | AB | 13.95 | 8Ø20 | 15.09 |  |  |  | 
10 | 0.6*0.4 | AI | 11.86 | 11Ø20 | 7.91 | 4legs Ø10/80mm | 74 | 4legs Ø10/170mm | 35
 |  | AM | 11.86 | 4Ø20 | 6.86 |  |  |  | 
 |  | AJ | 11.86 | 10Ø20 | 7.91 |  |  |  | 
 |  | AB | 11.86 | 7Ø20 | 13.00 |  |  |  | 
Beams design

## Slide 46
Beams design
Beam #. | B×H(m) | Longitudinal reinforcement |  |  |  | Transverse reinforcement |  |  | 
 |  | position | Ln | #ØD | L(m) | stirrups at support |  | stirrups at middle | 
 |  |  |  |  |  | s1 | # | s2 | #
1 | 0.6*0.4 | AI | 5.90 | 5Ø20 | 1.89 | 4legs Ø10/80mm | 37 | 4legs Ø10/170mm | 17
 |  | AM | 5.90 | 3Ø20 | 4.05 |  |  |  | 
 |  | AJ | 5.90 | 5Ø20 | 1.89 |  |  |  | 
 |  | AB | 5.90 | 5Ø20 | 6.72 |  |  |  | 
2 | 0.6*0.4 | AI | 8.42 | 6Ø20 | 2.52 | 4legs Ø10/80mm | 53 | 4legs Ø10/170mm | 25
 |  | AM | 8.42 | 2Ø20 | 4.84 |  |  |  | 
 |  | AJ | 8.42 | 5Ø20 | 2.99 |  |  |  | 
 |  | AB | 8.42 | 5Ø20 | 9.24 |  |  |  | 
15 | 0.6*0.4 | AI | 11.50 | 3Ø20 | 3.29 | 4legs Ø10/80mm | 72 | 4legs Ø10/170mm | 34
 |  | AM | 11.50 | 3Ø20 | 7.15 |  |  |  | 44
 |  | AJ | 11.50 | 10Ø20 | 2.99 |  |  |  | 44
 |  | AB | 11.50 | 7Ø20 | 12.32 |  |  |  | 44
12 | 0.7*0.4 | AI | 10.80 | 6Ø20 | 3.11 | 4legs Ø10/80mm | 68 | 4legs Ø10/170mm | 32
 |  | AM | 10.80 | 1Ø20 | 6.63 |  |  |  | 42
 |  | AJ | 10.80 | 6Ø20 | 2.99 |  |  |  | 42
 |  | AB | 10.80 | 6Ø20 | 11.62 |  |  |  | 42

## Slide 47
Columns design

## Slide 48
Columns design

## Slide 49
Shear walls design

## Slide 50
Mat foundation design
GENERAL INFORMATION
Soil capacity 180 KN/m2
Thickness of 1500 mm.
Top cover for the foundation=70 mm
Bottom cover for the foundation= 70 mm
CHECKS
Deflection check
Punching shear check

## Slide 51
Stair section

## Slide 52
Electro-Mechanical Design

## Slide 53
Mechanical systems
Water System
Drainage System
HVAC System
Fire System

## Slide 54
Water System

## Slide 55
Design of solar flat plate system
      Design data
Plate pitch angle = 30° south facing
Design for January 21st.
Total water volume = 5 m3.
Average water temperature in winter = 8 C°
Required temperature = 22 C°
   17 Collectors are needed

## Slide 56
Drainage System

## Slide 57
Drainage System
Gray Water riser
Black Water riser

## Slide 58
HVAC System
Indoor unit
Outdoor unit
Fan coil unit from Trane Company
Outdoor unit from Carreir Company
#of outdoor unit is 26 unit

## Slide 59
HVAC System
Diffuser unit
Diffuser unit from Air Master Emirates Company
Square diffuser
Slot linear diffuser

## Slide 60
Diffuser and duct distribution

## Slide 61
Fire System

## Slide 62
Electrical systems
Sockets distribution
Artificial lighting design
Acoustical design

## Slide 63
Sockets distribution

## Slide 64
Distribution board

## Slide 65
Artificial lighting design
Design of Digital game lounge
Luminaires used

## Slide 66
Artificial lighting design
Illuminance and glare results

## Slide 67
Artificial lighting design
Render results

## Slide 68
Artificial lighting design
Lights and switches distribution

## Slide 69
Acoustical design
Cinema design
Face | Material
Walls | Plaster
Walls behind cinema | Plywood
Stage floor | Wood floor
Floor under seats | Carpet
Seating area | MTSEAT FABRIC
Floor | Tiles
Ceiling | Gypsum
Doors | Wooden Solid doors

## Slide 70
Acoustical design
Cinema design
SPL Contour map
AL Contour map
STI Contour map

## Slide 71
Acoustical design
STC & IIC

## Slide 72
Quantity surveying and cost analysis

## Slide 73
Quantity Surveying and cost analysis
The budgeted cost of the project is 23400114.3 ILS.
The unit cost of the project is 2412.4 ILS.
The budgeted cost of structural system is 9765649.5 ILS.
The budgeted cost of mechanical system is 590886.1 ILS.
The budgeted cost of electrical system is 980000.0 ILS.

## Slide 74
3D LUMION model