## Slide 1: Water Works For Marj-Ibn Amer Analysis & Design

## Slide 2: Outline
1.Study Area
2.Objectives
3.Design Methodology
4.Analysis of Population & WW production
5.Design of Trunk Pipe lines
6.Design the Treatment Plant
7. Conclusion

## Slide 3: Study Area
Location:
In the northeast of the Jenin city in the northern of the West Bank .

## Slide 5: Topography
Elevation for each village above MSL

## Slide 6: Major Problems
1- Absence of Water Distribution Network .
2- Suffering from the drainage of waste water

## Slide 7: Objective
1.Design the Trunk pipe Lines.
2. Design a wastewater treatment plant .

## Slide 8: Design Methodology

## Slide 9: Population
P(t) = P0(1+i)n

## Slide 10: Population growth rate (i)
Design Period = 30year
The design period for this project was falling in the last two phases, so the number of population was estimated as the following:

## Slide 11
Village | Number of population in 2045
Aabah | 506
Deir Abu Da'ef | 14179
Jalamh | 5113
Arrana | 4954
Arbuna | 2011
Beit Qad | 3592
Deir Ghazala | 2223
Jalboun | 5933
Faqqu'a | 8606
Total | 50000Capita
Forecasted number of population in 2045

## Slide 12: WW Design Load

## Slide 13: Water Demand
Phase | Water Consumption(m3/capita.day)
2000-2010 | 50
2010-2040 | 57
Greater than 2040 | 83
The following equations were used to estimate the water demand:

## Slide 14
The amount of waste water produced in each village calculated as the following:
Factors:
Wastewater generation factor = 0.8
Peak factor = 2
The infiltration rate = 0.2

## Slide 15
Village | Average Flow (m3/day) | Design Load (m3/day)
Aabah | 79.69 | 159.36
Deir Abu Da’ef | 2217.6 | 4435.2
Jalamh | 799.68 | 1599.36
Arrana | 774.72 | 1549.44
Arbuna | 314.88 | 629.76
Beit Qad | 561.6 | 1123.2
Deir Ghazala | 347.52 | 695.04
Jalboun | 928.32 | 1856.64
Faqqu’a | 1345.92 | 2691.84
Total | 7368 (m3/day) | 14736 (m3/day)
(Wastewater Design Load for each village)

## Slide 16: Design of Trunk Lines

## Slide 18: Design Criteria

## Slide 19: The Results

## Slide 20
Treatment Plant

## Slide 21: Mechanism of Designing the Treatment Plant

## Slide 22
1.BOD
2.TN
3.TP
4.COD
5.TSS
WW Characteristics

## Slide 23: Estimation of BOD
Assume BOD Production Rate = 70 (g/capita.day)
Qavg = 7368 m3/day

## Slide 24
The same method was used to estimate the amount of TN & TP, by replacing BOD production rate with N production rate, and repeated it for P production rate.
Estimation of COD and TSS:

## Slide 25: WW Treatment Processes
This process include:
1.Preliminary Treatment
2.Primary Treatment
3.Secondary Treatment
4.Tertiary Treatment

## Slide 26: Preliminary Treatment
The main objectives for Preliminary Treatment:
1) Removal of untreatable solid materials
2) Protection and improvement of the performance of subsequent treatment units
Preliminary Treatment consist of:
1) Coarse Screens
2) Fine Screens
3) Grit Chamber

## Slide 27: Coarse & Fine Screen
Objectives:
is to remove the large objects such as rags, paper, plastics, metals These objects, if not removed, may damage the pumping and sludge removal equipment, and block valves, and pipelines.

## Slide 28: GPS-X
Facilitate the design process
Making a simulation for the plant

## Slide 29: Grit Chamber
Objectives
* Protect moving mechanical equipment and pumps from unnecessary wear and abrasion
* Prevent clogging in pipes, heavy deposits in channels

## Slide 30
Criteria | Value | Assumptions
Detention Time | 2-5 min | 4 min
Depth of water | 2-5 m | 2m
width | 2.5-7.5m | 2.5m
length | 7.5-20 m | 
Design Criteria of Grit chamber

## Slide 31: Design criteria for the grit
Volume = WW flow rate * detention time = 10.233 * 4 = 40m3
S.A= Volume / water depth = 40/2 = 20 m2
Length equal to area divided on width = 20/2.5 =8 m
Assume free board = 0.5 m
So the total depth equal to 2.5m

## Slide 32: Primary Treatment
The main objective: Removing of settleable organic solids
PST remove1. 1. BOD 30 to 40 % 2. TSS 50 to 70%

## Slide 33: Physical Dimension of PST
Assume Over Flow Rate = 40 then
A= 7368 / 40 = 185 m Assume :
W= 5m,,,,,,,,D = 3m L= 37m
2

## Slide 34: Design Criteria of PST
Criteria | value
Over flow rate (V0) | (24.5 to 49)
Detention time (t0) | (1 – 3)hr
L:W ratio | min 4:1
L:D ratio | min 7:1
Side Water Depth (SWD) | 3 – 5 m
Criteria | value
Over flow rate (V0) | 
Detention time (t0) | (1 – 3)hr
L:W ratio | min 4:1
L:D ratio | min 7:1
Side Water Depth (SWD) | 3 – 5 m

## Slide 35: The Results of the PST
 | Unit of measurement | Influent | Effluent
TSS | mg/L | 753.4109 | 301.7945
cBOD5 | mg/L | 487.0694 | 268.20023
COD | mg/L | 682.1054 | 378.13168
TKN | mg/L | 49.43192 | 39.781958
TP | mg/L | 48.56843 | 24.250534
HRT | hour | 2.095 | -
Over flow rate | m3/m2.day | 39.61 | -

## Slide 36
Secondary Treatment
Extended Aeration Tank
Secondary Clarifier

## Slide 37: Extended Aeration Tank
Objective:
treatment of the effluent from PST to remove the residual organics and suspended solids
Design of AT will be restricted on the volume of the tank

## Slide 38: Physical Properties

## Slide 39: Design Criteria
Criteria | Unit of measurement | Value
MLSS | mg/l | 2000 - 8000
F/M ratio | gBOD/gMLSS.d | 0.2 – 0.5
BOD Loading | gBOD/m3.d | 320 - 640
RAS ratio | % | 2 - 40

## Slide 40: The Results of the AT
Criteria | Unit of measurement | Value
MLSS | mg/L | 2694.733
F to M Ratio | gBOD5/(gMLSS.d) | 0.45952
BOD Loading | gBOD5/(m3.d) | 436.7492
RAS Recycle Ratio | % | 28.04312

## Slide 41: Secondary Clarifier
The main objectives of this unit are:
 1. separate biomass from liquid and then return abortions of it to the Aeration Tank
 2. meet total suspended solids discharge limit

## Slide 42: Physical Properties
Criteria | value
Over flow rate (V0) | (30 to 50)
Detention time (t0) | (2 – 4)hr
Side Water Depth (SWD) | 3 – 5 m
Criteria | value
Over flow rate (V0) | 
Detention time (t0) | (2 – 4)hr
Side Water Depth (SWD) | 3 – 5 m
Design Criteria

## Slide 43: The Results of the SST
 | Unit of measurement | Influent | Effluent
TSS | mg/L | 2695 | 16.83
cBOD5 | mg/L | 584 | 4.235
HRT | hour | 2.118 | -
Over flow rate | m3/m2.day | 31.93 | -

## Slide 44: Tertiary treatment
The main objective :
kill types of micro organism like fecal coliform .
Three agents are used for disinfecting waste water
1-chlorine gas or chlorine-based disinfectant
2-Ozone (O3)
3- Ultraviolet (UV) Radiation .

## Slide 45: Physical Dimension for Longitudinal-serpentine basins

## Slide 46: The Results
Design Criteria

## Slide 47: Disinfection Results
Criteria | Unit of measurement | Value
Detention Time | min | 50.01
Eff. Coliform Density | MPN/100mL | 65.5

## Slide 48: Sludge Treatment
This stage include two units:
1. Thickening process
2. Digestion process
Sludge Thickening:
the process used to increase the solids content of sludge by the separation and removal of a portion of the liquid phase.

## Slide 49: Design of Thickener 1
Total Depth = 3m

## Slide 50: Results
As shown, all results was falling within the design criteria..... so everything is OK

## Slide 51: Anaerobic Digester
Objectives:
1. To reduce the amount of sludge that needs to be disposed
2. Treatment of organic sludge and concentrated organic industrial wastes

## Slide 52: Results
Calculation of Dimensions

## Slide 53: Conclusion

## Slide 54: Comparison between Influent, Specification, Effluent
Chart: 
| Influent | Standard Value | Effluent
TSS | 800 | 30 | 16.83
COD | 700 | 50 | 44.48
BOD | 500 | 20 | 4.235
TN | 50 | 30 | 28.07
TP | 50 | 30 | 5.607

## Slide 55: Comparison between the various types of Aeration Tank
Type | Efficiency (%) | Standard value of BOD (mg/l) | Influent BOD (mg/l) | Effluent BOD (mg/l) | Comment
Extended Aeration Tank | 95 | ≤ 20 | 500 | 25 | Effluent value Less than Standard Value…. Acceptable
Conventional Aeration Tank | 90 | ≤ 20 | 500 | 50 | Effluent value More than Standard Value …. Rejected
Trickling Filter | 85 | ≤ 20 | 500 | 75 | Effluent value More than Standard Value …. Rejected
The extended aeration tank that is the only type has achieved a value for BOD effluent less than the standard value , so, the extended aeration tank was used.

## Slide 56: Thank You