## Slide 1: Integrated Redesign of an Al-Rahma dispensary Building
Graduation Project 2
Prepared by :-
Ahlam Damra
Asil Abu Lail
Duaa Ghazal
Supervisor :-
Dr. Monther Dwaikat

## Slide 2
Outlines
Site Analysis.
Architectural and Passive Design.
Structural Design.
Electro-mechanical Design.
Safety Design.
Quantity Survey.

## Slide 3
Site Analysis

## Slide 4
Architectural and
Passive Design

## Slide 5
Architectural Design
Site plan
Old building
New building

## Slide 6
Architectural Design
Basement plans: in the new design there is two basement plan for parking with area 1135 m2 for each floor, and 40 car parks.
Old car parking
New car parking

## Slide 7
Architectural Design
Ground floor: in the new design .
The floor area equal 751 m2.
Contains: emergency, clinics, pharmacy, registration.
Old building
New building

## Slide 8
Architectural Design
First floor: in the new design .
The floor area equal 771 m2.
Contains: storage, clinics, doctor’s room, nurse’s room, kitchen, w.c.
Old building
New building

## Slide 9
Architectural Design
Second floor: in the new design .
The floor area equal 771 m2.
Contains: storage, radiology, MRI department, CT scan, ultra-sound, kitchen, w.c.
Old building
New building

## Slide 10
Architectural Design
Third floor: in the new design .
The floor area equal 771 m2.
Contains: storage, kitchen, W.C, administration department and laboratories.

## Slide 11
Architectural Design
Old building: in the new design .
Contains: Nuclear department, Laundry.
Old design
New design

## Slide 12
Architectural Design
3D View

## Slide 13
Architectural Design
South Elevation:-
Old building
New building

## Slide 14
Architectural Design
North Elevation:-
Old building
New building

## Slide 15
Architectural Design
East Elevation:-
15
Old building
New building

## Slide 16
Architectural Design
West Elevation:-
Old building
New building

## Slide 17
Architectural Design
Sections in the plan:-

## Slide 18
Architectural Design
Sections :-
Section A-A

## Slide 19
Architectural Design
Sections :-
Section B-B

## Slide 20
Passive Design
Thermal Design
Acoustical Design

## Slide 21
Thermal Design
Design builder programme 3D model :
New building
Old building

## Slide 22
Thermal Design
Material : External wall
New building
U-value = 0.45 w/.K
U-value = 1.62 w/.K
Old building

## Slide 23
Thermal Design
Material :
U-value = 0.731 w/.K
Internal wall
Old building
U-value = 2.033 w/.K
New building

## Slide 24
Thermal Design
Material : Floor
U-value = 0.424 w/.K
New building
Old building
U-value = 1.41 w/.K

## Slide 25
Thermal Design
Shading :
1- In winter 21 -1 at 9:00AM
New building
Old building

## Slide 26
Thermal Design
Shading :
2- In winter 21 -1 at 11:00AM
New building
Old building

## Slide 27
Thermal Design
Shading :
3- In summer 21 -7 at 9:00AM
New building
Old building

## Slide 28
Thermal Design
Shading :
4- In summer 21-7 at 11:00AM
New building
Old building

## Slide 29
Thermal Design
cooling and heating capacity
 | New building | Old building
Cooling | 127.35 kW | 194.71 kW
Heating | 45.76 kW | 186.96 kW

## Slide 30
Thermal Design
Site energy
New building
Old building

## Slide 31
Thermal Design
Simulation : comfort range

## Slide 32
Acoustical Design
Reverberation time (RT60)
Ecotect program
Manager Room : The standard value = 0.4- 0.7 secound
Surface | Material
Floor | Tile (Terrazzo)
Walls | Plaster
Ceiling | Wood fibreboard
Door | Hollow core plywood
Window | Double glazing (aluminium frame)
Ceiling absorption
materials

## Slide 33
Acoustical Design
RT60 values

## Slide 34
Acoustical Design
Sound transmission class (STC)
Insul program
External wall with window: the standard of STC equal 50 dB.
TLc combined Value
External wall layer

## Slide 35
Acoustical Design
Sound transmission class(STC)
Insul program.
internal wall.
Internal wall layer
Function | Adjacent | STC
Meeting& Manager Room | Public space | 50
 | Patient room | 50
Clinic | Public space | 50
 | Clinic | 50
MRI | Patient room | 60
 | Public space | 50

## Slide 36
Acoustical Design
Impact Insulation class (IIC):
Insul program.
ceiling
IIC Value
Ceiling layer

## Slide 37
Acoustical Design
Noise reduction (NR):
In clinic room
NR= 46.85 dB
Noise= 75 dB
IL in clinic =75 – 46.85= 28.5
standard = 25-30 dB in clinic
In old design | STC
External wall | 38 dB
Internal wall | 48 dB

## Slide 38
Acoustical Design
Loud speaker distribution:
Emergency Room: We used PC-1867FC ceiling mount speakers with 90 coverage angle.
Corridor

## Slide 39
Structural and
Seismic Design

## Slide 40: Codes of design:
The American Concrete Institute code ACI 318-08.
The American Concrete Institute code ACI 350.3.
The seismic design according to UBC-97.
The analysis and design were done using ETABS, SAP, and SAFE programs.
Structural Design

## Slide 41: Design Data :
Concrete Compressive Strength :
f’c =24 Mpa For Slabs, Beams.
f’c =28 Mpa For Columns, Shear walls, and Footing
Yielding Strength Of Steel :
The Yield strength of steel Fy= 420Mpa
Structural Design

## Slide 42: Design Data :
Loads:
Live load = 5 kN/m2.
Superimposed dead load = 4 kN/m2.
Structural Design

## Slide 43: Design Data :
Sections of beams and columns used in design
Structural Design
Beam name | Dimension (cm)
Main beam | 80*50
Secondary beam | 40*50
Dropped beam | 80*100
Column name | Dimension (cm)
C60*30 | 60*30
C60*40 | 60*40
C60*60 | 60*60
C80*60 | 80*60
C110 | 110

## Slide 44
Structural Design
 | Old Design | New Design
System of slab | Ribbed slab with hidden beams | Voided slab with hidden and drop beams
Thickness of slab | 25 cm | 50 cm

## Slide 45
The old distribution of columns and shear walls in the building:
Structural Design

## Slide 46
The new distribution of columns and shear walls in the building:
Structural Design

## Slide 47
3D modeling from ETABS Program for new design:
Structural Design
Block 1
Block 2

## Slide 48
Check model: 1- Compatibility Check
Structural Design

## Slide 49
2- Equilibrium Check:
Structural Design
Load | Manual calculation | Calculation from ETABS (kN) | Difference (%)
Dead load | 56279 | 57164 | 1.56
Live load | 22750 | 22878 | 0.56
Superimposed Dead load | 18200 | 18302 | 0.56
Load | Manual calculation | Calculation from ETABS (kN) | Difference (%)
Dead load | 6781 | 6807 | 0.37
Live load | 2866 | 2866 | 0
Superimposed Dead load | 2293 | 2293 | 0
For Block 1
For Block 2

## Slide 50
Internal Force Check For Block 1 (slab and beams using Equivalent Frame Method):
Structural Design
 | Manual calculation |  |  |  | ETABS result |  |  | Difference % MBeam | Difference % Cs | Difference % MS
 | MBeam* | %CS | CS* | MS* | M | CS | MS |  |  | 
1 | 5.6 | 98.3 | 5.5 | 0.1 | 7.02 | 7.54 | 0.13 | 25 | 36 | 30
2 | 30.68 | 76.3 | 23.04 | 7.64 | 25 | 30 | 10 | 18.5 | 30.2 | 30.9
3 | 25.93 | 77.05 | 20 | 5.93 | 38 | 27 | 4.5 | 31.7 | 35 | 24
4 | 6.85 | 98.5 | 6.75 | 0.1 | 10 | 9 | 0.15 | 46 | 33.3 | 50
5 | 18.14 | 82.8 | 15 | 3.14 | 24 | 20 | 5 | 32.30 | 33.3 | 59
6 | 16.4 | 87.3 | 14.32 | 2.08 | 26 | 20 | 2.8 | 58.5 | 39.6 | 34.6

## Slide 51
Internal Force Check For Block 1 (columns):
Structural Design
 | Manual calculation | ETABS result | Difference %
Column 1 | 10820.72 | 11738 | 8.4
Column 2 | 107.04 | 97.5 | 8.9
Column 3 | 5635.34 | 6073 | 7.7

## Slide 52
Internal Force Check For Block 2 (slab and beams using Equivalent Frame Method):
Structural Design
 | Manual calculation |  |  |  | ETABS result |  |  | Difference % MBeam* | Difference % CS | Difference % MS
 | MBeam* | %CS | CS* | MS* | M | CS | MS |  |  | 
1 | 23.84 | 88.3 | 21 | 2.79 | 20 | 17 | 3.5 | 16 | 19.23 | 25.4
2 | 23.84 | 88.3 | 21 | 2.79 | 20 | 17 | 3.5 | 16 | 19.23 | 25.4
3 | 10 | 69.8 | 7 | 3.02 | 8 | 8 | 4 | 20 | 14.6 | 32.45

## Slide 53
Internal Force Check For Block 2 (column):
Structural Design
 | Manual calculation | ETABS result | Difference %
Column 1 | 1200 | 1166 | 2.4
Column 2 | 438 | 411 | 5.89
Column 3 | 39.15 | 39.3 | 0.38

## Slide 54
W = 63971.52 KN
Soil type SD
Z = 0.2
I = 1.5
R = 5.5
Cv = 0.40
Ca = 0.28
Seismic Design Using Response Spectrum – UBC 97:
Structural Design

## Slide 55
Period check (T) for the building:
Structural Design
 | T(Sec) for Block 1 | T(Sec) for Block 2
ETABS Value | 0.72 | 0.10
Manual Value | 0.79 | 0.25

## Slide 56
Structural Design
Base shear check for the building:
Load case/comp | T (sec) | Vmanual | VETABS
EQx | 0.72 | 9549.4 | 11789.88
EQy | 0.72 | 9549.4 | 11947.98
Load case/comp | T (sec) | Vmanual | VETABS
EQx | 0.10 | 1436 | 1800
EQy | 0.10 | 1436 | 1800
For Block 1
For Block 2

## Slide 57
Slab Structural systems for old design (one way ribbed slab):
Structural Design

## Slide 58
Slab Structural systems for new design (Two way voided slab):
Structural Design

## Slide 59
    1. New Slab Design :
Structural Design

## Slide 60
    1. Typical section in ribbed slab:
Structural Design

## Slide 61
    1. Typical section in voided slab:
Structural Design

## Slide 62
    2. Main Beam Detailing :
Structural Design

## Slide 63
    2. Main Beam Sections :
Structural Design

## Slide 64
    3. Column Design Detailing:
Structural Design

## Slide 65
    4. Footing Design : the new design of footing is Mat Footing
Structural Design

## Slide 66
    Footing design
    (Mat Footing):
Structural Design

## Slide 67
    Footing design
    (Mat Footing):
Structural Design

## Slide 68
    5. Shear walls design :
Structural Design

## Slide 69
    7. Water tank design :
Structural Design

## Slide 70
    Water tank design :
Structural Design

## Slide 71
    8. Stair design :
Structural Design

## Slide 72
    8. Ramp design :
Structural Design

## Slide 73
Elector-mechanical
Design

## Slide 74
Electrical Design
Lighting Design
Sockets Design
Circuit Breaker Design

## Slide 75
Electrical Design
Lighting Design
DIAlux evo programm
Pharmacy Room
Luminaire type
Reflection factor
Surface | Finish material | Reflection factor
Ceiling | Paint White + blue plaster | 85%
Wall | Paint White +blue tile | 85% + 56% with cover 8%
Floor | White porcelain | 75% with cover 11%
 | Standard | Design
illuminance | 500 | 560
Glare (UGR) | 19 | 18.8

## Slide 76
Views:
Pharmacy Room
Pharmacists Office

## Slide 77
Electrical Design
Lighting Design
DIAlux evo program
Other functions Results
In old design
 | Clinic | Meeting | Registration | MRI | Waiting
Illuminance(Lux | 507>500 | 309> 300 | 451 > 400 | 70>50 | 298>200
Glare (UGR) | 18>19 | 16> 22 | 15.1 >19 | - | 16.4>22
 | Clinic | Meeting | Pharmacy | Emergency
Illuminance(Lux | 333 | 377 | 481 | 700
Glare (UGR) | 26 | 22 | 21 | 20

## Slide 78
Views:
Patient Room
MRI
Meeting Room
Clinic
Emergency
Blood Lab

## Slide 79
Lighting Arrangement in ground floor:

## Slide 80
Electrical Design
Sockets Design
Sockets number in each floor :
Floor | Total power from lighting (Watt) | NO. Of Normal Outlet | NO. Of Special Outlet | Total Load (Amp)
Basement 2 | 3080 | 10 | 0 | 20
Basement 1 | 3080 | 10 | 0 | 20
Ground floor | 21212 | 124 | 1 | 258
First floor | 11859 | 85 | 3 | 200
Second floor | 1830.5 | 55 | 11 | 220
Third floor | 9711.5 | 145 | 1 | 300
Old floor | 1293 | 42 | 3 | 114

## Slide 81
Sockets arrangement in ground floor:

## Slide 82
Circuit Breakers Calculations :
Ground floor
Number of circuit breaker for lighting = 15 CB’s
Number of circuit breaker for general sockets = 31 CB’s
Number of circuit breaker for special sockets = 1 CB’s

## Slide 83
Mechanic Design
1- HVAC system VRF system used with the following components:
Out door unit
Controller
indoor unit (Fan coil)
Linear Slot
Ducts

## Slide 84
Mechanic Design
VRF Design:
Out door unit was selected from Toshiba company SMMSi Outdoor Units (MMY-AP4824HT8-E).
The fan coil was selected from TOSHIBA Company (MMD-AP0486BHP-E with flowrate = 0.58m3/s.
Linear slot diffuser was selected from TROX company (VSD50) with 0.02 m3/s flow rate .
Cooling load for building is 127.35kW .
For ground floor, cooling load = 22.34 kW.
2 fan coil needed in ground floor.
Each Fan coil can connect to 29 linear slot .

## Slide 85
Electro Mechanic Design
VRF Design: For first fan coil
Duct section | Volumetric flowrate m3/s | Velocity m/s | diameter (m) | ⍙P/EL
A-B | 0.57 | 5 | 0.2 | 1.3
B-C | 0.06 | 3.5 | 0.15 | 1.3
B-D | 0.51 | 5.9 | 0.34 | 1.3
D-E | 0.19 | 4.6 | 0.23 | 1.3
D-F | 0.32 | 5.2 | 0.28 | 1.3
F-G | 0.14 | 4.3 | 0.21 | 1.3
F-H | 0.18 | 4.6 | 0.23 | 1.3
H-I | 0.14 | 4.3 | 0.21 | 1.3
H-J | 0.04 | 3.2 | 0.13 | 1.3
J-K | 0.04 | 3.2 | 0.13 | 1.3

## Slide 86
Mechanic Design
2- Water supply system :
The standard quantity of water consumption in the dispensary is 392 L/m2 yearly .
The water consumption of the building
standard L/m2 yearly | Area (m2) | L/ year | L/ day | M3 / day | M3/week
441 | 3086 | 1360926 | 3728.6 | 3.73 | 26.1
442 | 470 | 207740 | 569.2 | 0.57 | 4.0

## Slide 87
Mechanic Design
Pipes diameter : in ground floor, first collector

## Slide 88
Mechanic Design
Pipes diameter : in ground floor , first collector
Feeder | Diameter (inches) | Loss
MVF | 2 | 8.3
MHF | 1.25 | 1.09
MHB | 1 | 3.78

## Slide 89
Electro Mechanic Design
Pipes diameter : in first floor , second collector

## Slide 90
Electro Mechanic Design
Pipes diameter : in first floor, second collector
Feeder | Diameter (inches) | Loss
MVF | 2.5 | 1.33
MHF | 1.5 | 2.5
MHB | 1 | 4

## Slide 91
Electro Mechanic Design
Pipes diameter :
Old building
Feeder | Diameter (inches) | Loss
MVF | 2 | 1.66
MHF | 1.5 | 0.7
MHB | 1.5 | 0.6

## Slide 92
Rain water :
The quantity of rain water = 600 mm, surface area of the building is 723 m2
The amount of rain water falling on the roof will be 723 * 0.6 = 433m3 .

## Slide 93
Electro Mechanic Design
3- Drainage system

## Slide 94
Electro Mechanic Design
3- Drainage system : for third floor
pipe | diameter | slope
stack | 4" | 0%
sewer | 4" | 1%
branch | 4" | 1%

## Slide 95
Safety Design

## Slide 96
Safety Design
1- Detectors system : In old floor
Flame detector
Smoke detector

## Slide 97
Safety Design
1- Detectors system : In first floor

## Slide 98
Safety Design
2- Alarms System
- Automatic and manual alarm.

## Slide 99
Safety Design
3- Firefighting system : For basement 1 floor
Hose station

## Slide 100
Safety Design
3- Firefighting system : For second floor
FM200 sprinkler
Extinguishers k
Extinguishers D
Water sprinkler

## Slide 101
Safety Design
3- Firefighting system : For old building floor

## Slide 102
Safety Design
Escape plan in ground floor

## Slide 103
Reflected Ceiling in Ground Floor

## Slide 104
Quantity Survey

## Slide 105
Bill Of Quantity
Items | Total cost (NIS)
Architectural items | 2387032
Structural items | 8157219
Electrical items | 13552.00
Mechanical items | 413740
Fire items | 36610
Total cost | 11008155
Unit cost | 2343 NIS/m2