## Slide 1: An-Najah National University Faculty of Engineering Civil Engineering Department Graduation Project 2 2021-2022

## Slide 2
Untreated wastewater in East Nablus: characteristics and design
for treatment
  Prepared By : Ameer Draidi
  Reema Balsheh
  Mays Zakarni
Under Supervision of: Dr. Abdelhaleem Khader

## Slide 3
Outline
1 Introduction.
2 Problem Statement.
3 Objectives.
4 Literature Review.
5 Methodology.
6 WW analysis and treatment plant design.
7 Discussion.
8 Conclusion and recommendations.
9 Errors and constrains

## Slide 4
Project Introduction
In Gaza and WB about 417.9 million cubic
meters of water is available annually
Chart: 
| Israeli domination | For Palestinian
Sales | 83 | 17
Palestinian per capita consumption of water is
about 81.9 liters per day
According to the WHO, 100 liters of water is
recommended for consumption per capita day

## Slide 5
Project Introduction

## Slide 6
Project Introduction
94%
of untreated sewage is released
to the ground and surface water
50%
of total groundwater that recharged from precipitation is wastewater

## Slide 7
Problem Statement
the lack of exploitation of treated WW has become a political and social problem
mix with rainfall then infiltrate into groundwater aquifers
A significant amount of
untreated WW

## Slide 8
Objectives
Suggest a proper solution for high pollutants rate.
Preliminary design for the plant.
Conduct a software model (STOAT) for the plant
Analysis of the WW sample with clarification of pollutant values.

## Slide 9
Literature Review
  WW characteristic
1
Many pollutants expected to be in the selected sample: Temperature, PH, Chemical oxygen demand (COD), Biochemical Oxygen Demand (BOD), Solids Measurements (Gravimetric Method), Nitrite, Nitrate, Sulfate, phosphorous and Total Kjeldahl Nitrogen (TKN) which are a part of WW characterization.

## Slide 10
Literature Review
WW Treatment Method
Physical treatment
Chemical treatment
Biological
treatment

## Slide 11
Methodology
  Study Area
1
Regions | Total Population 2017 | Total Population 2045 Estimated | Study Area %
East Nablus Askar and Balata Camps | 81567 | 138163 | 76.22%
Azmout | 3410 | 5776 | 0.98%
Deir al Hatab | 2813 | 4765 | 3.76%
Salem | 6212 | 10523 | 1.59%
Beit Furik | 13360 | 22630 | 12.23%
Kufr Qalil | 3003 | 5087 | 1.24%
Rujeib | 5912 | 10015 | 3.99%
Total | 116277 | 196959 | 100%

## Slide 12
Methodology

## Slide 13
Estimated in 2045
A maximum flow (assuming only sewage network)
is 451.36 L/s
  Flow rate
2
Methodology

## Slide 14
  Water Sampling
3
The sample was collected from a representing manhole in east Nablus that charges in wadi al Sajour before the slaughterhouse of Nablus city on 21/9/2021 at nine o’clock in the morning.
Manhole coordination globally is 32°13'38.2 North
35°15'35.7 East
Methodology

## Slide 15
Methodology
  Quality Analysis
4
Parameter | Instruments | Device
Temperature | Temperature meter | 
pH | pH meter | 

## Slide 16
Methodology
  Quality Analysis
4
Parameter | Instruments | Device
COD | COD Vials (High and Medium range), Micro -pipette, COD Reactor, COD reagent vial Cooling Rack, DR 900 Colorimeter | 

## Slide 17
Methodology
  Quality Analysis
4
Parameter | Instruments | Device
BOD | BOD bottles and sensors, Traps, Sensor, Incubator, Stirring bars, Potassium hydroxide (KOH) | 

## Slide 18
Methodology
  Quality Analysis
4
Parameter | Instruments | Device
Solids | Buchner Funnel, Filter Paper Pore size:1.5 µm, Crucible, Flask with arm, Micro -Pipette, Sensitive electronic balance, Vacuum pump, Oven | 

## Slide 19
Methodology
  Quality Analysis
4
Parameter | Instruments | Device
Nitrite | Micro -Pipette, vial, DR 900 Colorimeter, distilled water, Nitrite Reagent for 5ml sample | 

## Slide 20
Methodology
  Quality Analysis
4
Parameter | Instruments | Device
Nitrate | Micro -Pipette, vil, DR 900 Colorimeter, distilled water, Nitrate Reagent for 10ml sample | 

## Slide 21
Methodology
  Quality Analysis
4
Parameter | Instruments | Device
TKN | Kjeldahl Device and Digester, Flask, Kjeldahl Device, Fume Hood | 

## Slide 22
Methodology
  Quality Analysis
4
Parameter | Instruments | Device
Sulfate | 10mm vial, DR 900 Colorimeter, Micro –pipette, distilled water, sulfate reagent for 10ml sample | 

## Slide 23
Methodology
  Quality Analysis
4
Parameter | Instruments | Device
Phosphorus | Spectro photometer, Cuvettes, (1cm Light path), test tube holder, 50 and 100ml graduated cylinders, 100ml volumetric flasks, funnels, 2,5ml pipette bulb, 200ml Erlenmeyer flask, beakers | 

## Slide 24
Wastewater analysis
Parameter | unit | value
Temperature | o C | 24.9
PH | --- | 6.2
COD | mg/L | 1412
BOD5 | mg/L | 746
TS | mg/L | 1620
TSS | mg/L | 331
TDS | mg/L | 997
Nitrite | mg/L | 67
Nitrate | mg/L | 26
Sulfate | mg/L | 35
Phosphorus | mg/L | 17.6
TKN | mg/L | 134.1

## Slide 25
Wastewater Treatment Plant location

## Slide 26
Treatment plant design
  Preliminary treatment
Parshall flume device : For Q max=1625m3/hr.
W= 0.3m D = 0.84m
Channel : Channel width equal flow measurement
inlet 0.84m.
Bar rack : 34 bar
Horizontal-flow grit chamber : Area = 1.13m2
Height =1.34m , Total Depth = 2m , T=0.5min

## Slide 27
Treatment plant design
  Primary & sedimentation treatment
Primary Clarifier :
Depth =2.1 m , Volume =3250 m3
Anoxic Tank :
Volume= 3250 m3
Secondary Clarifier : Volume =6500 m3
Depth = 5.5m with 0.5m freeboard
Aerobic Tank : Volume = 48488 m3
Depth = 5m Internal recycling =38998m3/d

## Slide 28
STOAT software

## Slide 29
Result comparison
Parameter | Unit | Effluent -2021 | PSI Guidline,2012 |  |  | 
BOD5 | mg/l | 4.28 | 20 | 20 | 40 | 60
COD | mg/l | 41.17 | 50 | 50 | 100 | 100
TSS | mg/l | 13.23 | 30 | 30 | 50 | 90
TP | mg/l | 6.64 | 30 | 30 | 30 | 30
Nitrate | mg/l | 9.11 | 20 | 20 | 30 | 40
PH | - | 7 | 6-9 | 6-9 | 6-9 | 6-9

## Slide 30
Recommendations
Implementing treating units inside the factories this will reduce the burden on the plant
The elevated concentration of NH3 due to slaughterhouse needs to special treatment before introducing WW to the treatment plant.
Split the total design period into different phases, owing to financial constrains.
Establish a new network for storm water in order to decrease the load burden especially in winter.
Sludge handling by anaerobic digester.
Add tertiary treatment (disinfection) using ultra violet radiation or chlorination to be applicable for instant use.

## Slide 31
Errors
4
5
Error in taking the sample.
Human error.
Mechanical error.
1

## Slide 32
Constrains
Equipment
Time
Age of Data
Literature Accessibility