## Slide 1: Seismic Design of Fatima Al Zahra Mosque
By: - Khattab Salawdeh
- Mohammad Oraib
- Mohannad Abdo
Under Supervision of: Dr.Abdulrazzaq Tuqan

## Slide 2: Seismic Design of Fatima Al Zahra Mosque
Just a reminder.
Models.
Checks.
Response spectra.
Design and detailing.
Shear wall design
Rapid visual screening.
Recommendations.
Conclusion.
Outline:

## Slide 3: Just a reminder
Fatima Al Zahra mosque is an old prominent landmark in Qaffen-Tulkarm city where engineering offices do not design for seismic loads.
This mosque, consists of a ground floor and a first floor with a total area of 476m2 (238m2 for each).
Structural elements will be designed as reinforced concrete members according to strength and serviceability criteria as specified in ACI 318, for seismic design IBC2012 code will be used.

## Slide 4: Revit Model
Export to
AutoCAD Drawing
Revit
Physical Model
Analytical Model
ETABS
Verify it.

## Slide 5: Revit Model
Exporting to ETABS …

## Slide 6: Analytical 3D model in Revit.

## Slide 7: ETABS Model

## Slide 8: ETABS Model
- Model Check -
Checks
Compatibility
Stress-Strain
Equilibrium
Period
Checks

## Slide 9: ETABS Model
RUN…

## Slide 10: ETABS Model
Compatibility
Checks
OK

## Slide 11: ETABS Model
Equilibrium
Checks
TABLE: Base Reactions |  |  | 
Load Case/Combo | FZ: ETABS | Manually | %difference
 | kN | kN | 
Dead | 8449.9 | 8399 | -0.0061
Live | 2344.6 | 2349.4 | 0.0021
SID | 2246.1708 | 2250 | 0.0017

## Slide 12: ETABS Model
Period Check (Rayleigh Method):
Total Mass = 1090 tons (ETABS).
By Applying a 1kN/m2 force(Y-Direction): Max displacement for first and second floor are 0.00004 m and 0.00007 m respectively.
Thus, Tn = =
% Difference = ....OK.
Checks

## Slide 13: ETABS Model
Stress – Strain Check
Checks
Column Check

## Slide 14: Seismic Design
Using Response Spectrum
Site soil classification and seismic zone factor
- Site Classification -
- Zone Factor Z=1.5 -

## Slide 15: Seismic Design
SS = 2.5 x Z = 2.5 x 0.15 = 0.375
S1 = 1.25 x Z = 1.25 x 0.15 = 0.1875
SMS = Fa x SS = 1 x 0.375 = 0.375
SM1 = Fv x S1. = 1 x 0.1875 = 0.1875
x = SMS = 0.375
x = SM1 = 0.1875
Determine SDS and SD1

## Slide 16: Seismic Design
Risk Category
Risk Category

## Slide 17: Seismic Design
Seismic design category is determined based on:
- Risk category
- Values of SDS and SD1.
Seismic Design Category
“Seismic Design Category: C”

## Slide 18: Seismic Design
See ASCE 7-10 Table 1.5-2, I = 1.25
Importance factor

## Slide 19: Seismic Design
Bearing wall system: walls carrying gravity and lateral loads.
Building frame system: Frames carrying gravity loads, and shear walls take a lateral loads.
Moment resisting frame: Frames walls carrying gravity and lateral loads.
Selection of structural system type

## Slide 20: Seismic Design
Table 12.14-1 ASCE10-7
Determine Response modification factor (R)

## Slide 21: Seismic Design
Define mass source
Define Load patterns
Seismic, ASCE10-7 Code
R = 5
I = 1.25
SDS = 0.375
SD1 = 0.1875
Determine of Base shear using IBC2012
- Seismic Loading -

## Slide 22: Seismic Design
VEtabs = 900.11 kN
Weight of opening = 230 kN
Wnet = 1710 – 230 = 894 kN
TS = SD1/SDS = 0.1875/0.375 = 0.5 sec.
Ty = 0.07 Sec < 0.5 sec. So,
Cs =
V = Cs x W = 0.09375 x (10650-894) =915 kN.
% Difference =
Tx = 0.068 < 0.5 s
Determine of Base shear using IBC2012

## Slide 23: Seismic Design
SS = 3 x 0.375/2 = 0.5625
S1 = 3 x 0.1875/2 = 0.2812
SDS = 0.375
SD1 = 0.1875
Response spectrum analysis using ETABS 2015
- Response Spectrum Function Definition -

## Slide 24: Seismic Design
Define Response in X, and Y directions
U1 = 2451.66
U2 = 735.5
- X – Direction -
X Scale up factor = 778/612.26 = 1.27

## Slide 25: Seismic Design
Δm = ∆Etabs*Cd/I < h/200 = 8.4/200 = 0.042 m = 42 mm
Check for inelastic response displacement
TABLE: Diaphragm Center of Mass Displacements |  |  |  | 
Story | Diaphragm | Load Case/Combo | UX | Uxm
 |  |  | mm | mm
Level_3 | D2 | RS-X Max | 0.1 | 0.36
Level_2 | D1 | RS-X Max | 0.04748 | 0.17
TABLE: Diaphragm Center of Mass Displacements |  |  |  |  | 
Story | Diaphragm | Load Case/Combo | UX | UY | Uym
 |  |  | mm | mm | mm
Level_3 | D2 | RS-Y Max | 0.02673 | 0.1 | 0.36
Level_2 | D1 | RS-Y Max | 0.01494 | 0.04758 | 0.17

## Slide 26: Design and Detailing
Single Footing
Check DIM
Check Shear
Reinforcement
Check by SAP2000
-Compatibility
-Stress
-Moment and
reinforcement

## Slide 27: Design and Detailing
Single Footing
- Detailing -

## Slide 28: Design and Detailing
DIM
Reinforcement
Check by ETABS
-Displacement
-Stress
-Moment and
reinforcement
Walls Footing

## Slide 29: Design and Detailing
Walls Footing

## Slide 30: Design and Detailing
Rebar percentage = 1%
(Area of steel = 0.01 x 500 x 500 = 2500 mm2
Column
- ETABS check -
S0 = 150 mm
- Detailing -

## Slide 31: Design and Detailing
1.2D + 1.6L
-Moment Additional requirement:
-Shear M+ ≥ 239mm2
M- (@ middle ) = M,max,face/5 176mm2
1.2D + L+ E
-Moment
-Shear
Beam
- Detailing -

## Slide 32: Design and Detailing
Vu, gravity = 1.2D + L = 1.2*61 + 45.1 = 127.3 kN
= = Then, S = 174.6mm use S = 150 mm.
Beam

## Slide 33: Design and Detailing
Dome
Meridian forces ()
Hoop forces()

## Slide 34: Design and Detailing
- From own weight-
- From SID Load -
- From Live load -
Dome
Ultimate = C As minimum
Ultimate = T As minimum

## Slide 35: Design and Detailing
Shear Wall
 | L | Moment | As,min | D (mm) | # of bars | use
Wall-A | 10.6 | 420.00 | 3801.6 | 12 | 33.6 | 34
Wall-B | 6.6 | 172.00 | 2376.0 | 12 | 21.0 | 22
Wall-I | 14.4 | 256.00 | 5184.0 | 14 | 33.7 | 34
Wall-1 | 12.7 | 456.00 | 4572.0 | 14 | 29.7 | 30
Wall-2 | 2.1 | 225.00 | 756.0 | 12 | 6.7 | 8
Wall-5 | 6.0 | 237.00 | 2160.0 | 12 | 19.1 | 20
IW A-C | 4.6 | 300.00 | 1654.4 | 12 | 14.6 | 16
IW H-I | 4.6 | 300.00 | 1654.4 | 12 | 14.6 | 16
Since Fy = 420 MPa and db < 16 mm:
- ρhorizontal = 0.002
- ρvertical = 0.0012

## Slide 36: Design and Detailing
Chart: 
| 0 | 7857.2070999999996 | 13708.440199999999 | 17928.661 | 20523.667700000002 | 21519.919600000001 | 24242.005300000001 | 25317.759699999999 | 19395.446800000002 | 11013.9936 | 0
Shear wall 5 | 22538.602 | 22538.602 | 22364.6646 | 19535.0768 | 16673.9765 | 13771.1748 | 12675.2638 | 11026.4564 | 7006.7097 | 2985.1323 | -1094.8351
Current forces | 1152
Check for ETABS

## Slide 37: Design and Detailing
mm2
Shear Wall

## Slide 38: RVS
RVS
What is new ?
For the mosque

## Slide 39: What is new?!
An “optional Level 2” Data Collection Form has been added.

## Slide 40: What is new?!
The number of seismicity regions has been expanded from three to five.
Based on MCER ground motions (rather than the two-thirds of MCE ground motions)
Low.
Moderate.
Moderately High.
High.
Very High.
New

## Slide 41: What is new?!
Screening buildings with additions is provided.

## Slide 42: What is new?!
Geologic hazards.
Liquefaction.
Landslide.
Surface Rupture.

## Slide 43: What is new?!
Pounding and adjacency are now considered.
Falling hazards from taller adjusting building.

## Slide 44: What is new?!
Exterior Falling Hazards.

## Slide 45: What is new?!
Vertical and plan irregularities have been updated.
Moderate Vertical Irregularities:
Sloping Site.
In-Plane Setback.
Split Levels.
Sever Vertical Irregularities:
Weak and/or Soft Story.
Out-of-Plane Setback.
Short Colum.

## Slide 46: What is new?!
A minimum score has been included, F.Smin.
Probability of failure%:
Where n: Final Score.

## Slide 47: What is new?!
Soil Type CD Rather Than AB.

## Slide 48: RVS For Mosque
SS = 0.375 x 1.5 = 0.5625
S1 = 0.1875 x 1.5 = 0.2812

## Slide 49
Probability of failure:
Recommendations:
Concrete frame with unreinforced masonry-
walls.
Falling hazard.
F.S = 1.4 < 2.
Detailed Structural Evaluation is required.
Not-acceptable.

## Slide 50
Recommendations:
Concrete shear wall building.
F.S = 2.9 > 2.
Acceptable building.
Probability of failure:

## Slide 51: Recommendations
Recommendations:
It is preferred to eliminate super dead load, by using false-ceiling (by the way we need false-ceiling for sound isolation).
Stone should be fixed with shear walls.
Provide a small, and BRACED water tank.
Non-structural elements should be fixed and designed.
It is preferred to provide Refuge.
It is NOT permitted at all to remove any of shear walls.
We need to develop our own RVS.

## Slide 52: Conclusion
{وَلا تَقْفُ مَا لَيْسَ لَكَ بِهِ عِلْمٌ}
{قُلْ إِنَّمَا أَعِظُكُمْ بِوَاحِدَةٍ أَنْ تَقُومُوا لِلَّهِ مَثْنَى}
{خَلَقَ السَّمَاوَاتِ بِغَيْرِ عَمَدٍ تَرَوْنَهَا}
Humility
Back-Up-System
Shear Walls

## Slide 53: Quality!
{إن الذين آمنوا وعملوا الصالحات إنا لا نضيع أجر من أحسن عملاً}
Quality control is the first lesson in seismic design.
Be honest, be honest, and be honest.

## Slide 54: Questions & Comments