## Slide 1
Graduation Project
(Part One)
Building on Difficult Soils
Prepared By:
Anwar Salahat
Hussein Deeb
Sajida Numan
Thabet Mashaqi
Supervised By: Dr. Isam Jardaneh

## Slide 2
Content
Chapter One: Introduction
Chapter Two: Expansive Soil
Chapter Three: Collapsible Soils
Chapter Four: Building on Top of Landfill
Chapter Five: Landslides
Chapter Six: Caves and Sinkhole

## Slide 3: Introduction
Building on difficult soil must have several consideration before start to
construct any building and this is to avoid problems which may result as
failure. This causes Economic problems and Danger to human life which
is the most important effect.

## Slide 4
Chapter Two
Expansive Soil
Expansive soils are soils that experience significant volume change
associated with changes in water contents.
Effect of Expansive Soil on Foundations:
Foundation soils which are expansive will “heave” and can cause lifting of
a building or other structure during periods of high moisture. Conversely
during periods of falling soil moisture, expansive soil will “collapse” and
can result in building settlement. Either way, damage can be extensive.

## Slide 5: Significant cracks often appear at the corners of windows and doors, in walls, walkways

## Slide 6: Ways to Minimize the Effects of Expansive Soil
Remove large trees that grow within about ten feet of the house.
Utilize drip irrigation systems to water vegetation.
compact the soil around the foundation into a hard surface.
Slope the soil or concrete away from the foundation.

## Slide 7
Treatment of Expansive Soil
Sub-Excavation and removal of expansive soil and replacement with non-expansive soil.
Compaction
Moisture Barriers
Geosynthetics
Chemical stabilizers
Lime
Cement

## Slide 8: Chapter Three Collapsible Soils
Definitions
Collapsible soils are also known as metastable soils. They are unsaturated
soils that undergo a large volume change upon saturation.
Collapsible Soil Properties
Collapsible soils show relatively high apparent strength (cohesion) in
their dry state, but have a low density, porous structure and are
susceptible to large settlements upon wetting.

## Slide 10: Human activities that Facilitate Soil Collapse include
Irrigation.
Water impoundment.
Watering the lawn.
Changing the natural drainage.
Disposal of wastewater.

## Slide 11: Avoid Collapsible Soils and Ground Modification
Various ground modification methods can be used to prevent or limit
collapse from occurring. These methods include:
partial removal
replacement of the collapsible soils compacted
densification of the collapsible soil in-place.

## Slide 12: Chapter Four Building on Top of Landfill
Definition of Landfill
Sanitary landfill is a method of waste disposal utilizing soil in the elimination of discarded foods, fibers, and artifacts.

## Slide 13: Operations on Landfill
Confined waste to as small an area as possible.
Compact waste to reduce volume.
Covered waste (usually daily) with layers of soil.

## Slide 14: Leachate
is the liquid that drains from a landfill , extracts dissolved and suspended
matter from waste material, the liquid contains: decomposition of waste,
rainfall, surface drainage and Groundwater.

## Slide 15: Landfill Closure and Redevelopment
The major engineering limitations associated with redevelopment of
closed landfills are the potential for large total and differential
settlement.
Environmental challenges related to post closure development include:
hazards of landfill gas
risk of waste by-product migration, either in soil, groundwater, or the atmosphere

## Slide 16: Landfill closure cap

## Slide 17: Foundation Construction on Reclaimed Landfills
It is a challenging task since it requires considering unusual aspects
related to the mechanics of wastes.
Golf course on top of a landfill

## Slide 18: Chapter Five Landslides
Introduction
The geologist regard landslides as one of the many natural processes
which act on the surface of the earth as part of the general geological
cycle. The engineer, on the other hand, tries to determine the maximum
angle at which a slope is stable and studies the stability of a slope in terms
of a factor of safety.

## Slide 20: Causes of Landslides
Gravity
Water
Earthquakes
Wildfires
Volcanoes

## Slide 21: Classification of Landslides
criteria for identification and classification including
Rate of movement
Type of material
Nature of movement

## Slide 22: Chapter Six Karst features
Introduction
Karst features occur primarily in limestone and dolomite rock masses.
They include cavities, sinkholes and open fractures.
A full understanding of the nature of karst as well as the method of
surface and subsurface detection are very important to avoid the risk of
sudden collapse of constructed buildings.

## Slide 23: Sink Hole
is a natural depression or hole in the surface topography caused by the
removal of soil or bedrock, or by water.

## Slide 24: Causes a Sinkhole
factors that combine to cause a sinkhole:
Water dissolved minerals in the rock
Water washes away the soil and residue from the voids in the rock.
Lowering of groundwater levels
Change to the hydrologic system
changes in the groundwater table, freeze and thaw of the ground, and extremes in precipitation

## Slide 25: Caves and Sinkhole Treatments
Several engineering methods have been used as treatment for sinkhole
and caves :
engineering fill
geosynthetic materials
concrete filling
cement grout low pressure injection.
The most recorded cases of karst treatment are depending on concreting
and cement grout injection filling

## Slide 26: The Process Of Foundation Bedrock Treatment
The near surface narrow open fractures, caves less than 1m width can be treated by manual cleaning the silt and loose material then filling with high slump concrete
The relatively deep (greater than 2m depth) caves and sinkholes can be treated by high slump concrete or cement grout low pressure.
Deeper-seated cavities are treated by pumping a cement-grout or cement-sand grout mixtures through injection.