## Slide 1
Structural Analysis and Design of Al-Mallah building in Nablus city
An-Najah National University
Faculty of Engineering
Civil Engineering Department
Graduation Project II

## Slide 2
Under Supervision of : Dr. Hind Tbaileh
Academic Year: 2021-2022
Prepared by:
Musa’b Imad Fahed
“Mohammad Eyad” Samer Al-Amoudi
Ali Raef Salous
“Mohammad Khaled” Jamal Hennawi
Omar Bassam Shami

## Slide 3
Outline
General background review
Seismic load analysis and design
Model Verification
Design of the structural element
Limitations

## Slide 4
General Background Review

## Slide 5
Project Description :
This project is analysis and design Al-Mallah building in Al-Quds street in Nablus
city, This building has five floors, two of them Underground (basement) and Three
above ground . This building includes: Parking garage, Storage and residential
floors.

## Slide 6
Floors | Area (m2) | Heights (m) | Cumulative height
Basement 2 | 1043.54 | 2.95 | 2.95
Basement 1 | 1295.61 | 2.95 | 5.9
Ground floor | 1423.15 | 5.55 | 11.45
Floor 1 | 1267.73 | 3.38 | 14.83
Floor 2 | 1267.73 | 3.38 | 18.21
stairs | 80.65 | 3.25 | 21.46

## Slide 7: Residential floors Layout

## Slide 8
  Codes and standards
  American Society for Civil Engineering (ASCE 7-16).
  American Society for Materials (ASTM).
  American Concrete Institute (ACI 318- 14)
  International Building Code (IBC- 2012).

## Slide 9
ETABS V.19.1 to Build a 3D model for the structure, and to take reinforcing steel results for structural elements.
AutoCAD 2018 to draw plans, and reinforcing details.
Safe 2020 to design the footings
Computer Software :

## Slide 10
Structural element materials :
    For concrete
    For Steel :
    Materials
Property | Value
Cylindrical Compressive strength ( fc ) | 40 MPa
Modulus of elasticity ( Ec) | 29.725 GPa
Unit weight (Ɣ) | 25 KN/m3
Property | Value
Yielding strength (fy) | 420 MPa
Modulus of elasticity ( Es) | 200 GPa
ASTM

## Slide 11
2. Nonstructural element materials :
Material | Unit Weight Ɣ(kN/m3)
Tiles | 25
Blocks | 12
Masonry Stones | 25
Filling Materials | 18
Plaster | 23
Concrete Mortar | 23
ASTM

## Slide 12: Loads
The common types of loads on the structures are as follow:
Gravitational loads such as: Live, Dead and Superimposed Dead loads.
Lateral Loads: Soil pressure, Earthquake.

## Slide 13: Live load values:
Garages (Passenger cars) | 4 KN/m2
Private rooms and corridors | 2.5 KN/m2
Public rooms and corridors | 5 KN/m2
Storage ware houses | 6 KN/m2
Roof | 5 KN/m2
ASCE 7-2016

## Slide 14
Basic service load combinations (IBC-2012):
D
D + L + H
D + (Lr or S or R) + H
D + 0.75L+ 0.75(Lr or Sor R) + H
D + (0.6W or 0.7E) + H
D + 0.75(0.6W) +0.75L+0.75L (Lr or Sor R) + H
D + 0.75(0.7E) +0.75L+0.75S+ H
0.6D + 0.6W+ H
0.6D + 0.7E+ H

## Slide 15
Basic ultimate load combinations (IBC-2012):
1.4D
1.2D + 1.6L + 0.5(Lr or S or R) + 1.6H
1.2D + 1.6(Lr or S or R) + (f1L or 0.5W) + 1.6H
1.2D + 1.0W+L+0.5(Lr or Sor R) + 1.6H
1.2D + 1.0E+ L+ 0.2S + 1.6H
0.9D+ 1.0w + 1.6H + 0.9D +1.0E + 1.6

## Slide 16: Structural System Design and Analysis.

## Slide 17
Preliminary dimensions of structural element
Slab thickness:
Beams dimensions:
Width (mm) | Depth (mm) | Beam name
1700 | 320 | B1
300 | 320 | B2
900 | 320 | B3
300 | 500 | B4
1300 | 320 | B5
400 | 600 | B6
300 | 300 | B7

## Slide 18
Name | Dimensions(mm) | 
C1 | Diameter | 750
 | Length | Width
C2 | 750 | 750
C3 | 650 | 650
C4 | 800 | 800
C5 | 1100 | 400
C6 | 1200 | 400
C7 | 1300 | 400
C8 | 1400 | 400
C9 | 1000 | 400
C10 | 900 | 300
3. Columns dimensions:
The columns centers layout attach to the hard copy

## Slide 19
4.Walls Dimensions:
Thickness (mm) | Wall name | NO.
300 | Retaining wall | W1
200 | Elevator shear wall | W2
400 | Middle shear wall | W3

## Slide 20
Modifiers For Structural Elements
Beam modifiers
Column and wall modifiers

## Slide 21
One way X slab modifiers
One way Y slab modifiers

## Slide 22
Two way slab modifiers

## Slide 23: 3D Model For The Left Side

## Slide 24: 3D Model For The Right Side

## Slide 25: Beam Layout

## Slide 27
The Actual Dimensions Of Beams

## Slide 28: Columns and walls new distribution

## Slide 29
Left Block
Right Block

## Slide 30
The Actual Dimensions Of Columns

## Slide 31
Thickness (mm) | Wall name
300 | Retaining wall
300 | Elevator shear wall
300 | Middle shear wall
The Actual Dimensions Of Walls

## Slide 32: Seismic Load Analysis And Design

## Slide 33: Ss and S1 values:

## Slide 34: Fa and Fv values:

## Slide 35: SDs and SD1 Calculations: SMs = Fa*Ss = 0.748 SM1= Fv*S1 = 0.3042 SDs = 2/3 SMs = 0.50 SD1 = 2/3 SM1 = 0.2028

## Slide 36: Seismic Design Category

## Slide 37: The Design System

## Slide 38: R, Ω and Cd Values

## Slide 39: For Calculating The Period Cu Coefficient

## Slide 40: Ct and X Coefficient

## Slide 41: Period Calculation
Ta = Ct ×hn ^ x × Cu = 0.0488 × 〖21.46〗 ^ 0.75 × 1.5 = 0.73 sec
Cs = SDs / (R ⁄ Ie)=0.50 / (6 ⁄ 1.25) = 0.104
Cs,max = SD1 / (TR ⁄ Ie) = 0.2028 / (((0.73*6)) ⁄ 1.25) = 0.057
Cs,min = 0.0445 × SDs × Ie = 0.0445 × 0.50 × 1.25 = 0.0275
Since Cs larger than Cs,max then take Cs = Cs,max = 0.057

## Slide 42: Definitions of Seismic Parameters

## Slide 43: Defining The Seismic Load Pattern

## Slide 44: Acceleration Parameters

## Slide 45: Define The Load Cases

## Slide 46: Define The Load Case Data

## Slide 47: Define The Mass Source Data:

## Slide 48: Response Spectrum Data

## Slide 49: Define The Response Spectrum Function

## Slide 50: Define The Diaphragm

## Slide 51: Model Verifications

## Slide 52: Compatibility Check

## Slide 53: Deflection Check

## Slide 54
L=4200 mm
=19.4−((3.87+16+7+9)/4)=10.44 𝑚𝑚

## Slide 55: Equilibrium Check
 | Hand | Etabs | Error %
Live Load | 11430.61 | 11502.9846 | 0.63 %
Dead Load | 25586.668 | 24795.2943 | 3.1 %
Super Dead | 12770.18 | 13106.4424 | 2.63 %

## Slide 56: Internal Force Check
For The Column:
Pu=T.A.*Wu*#of floors
Pu By Hand = 20.31 * 17.4*5 =1767 KN
Pu Etab= 1945 KN
% Error = OK

## Slide 57
For The Beam:
L2=4 m, Ln=4.15 m, LL=4 KN/m2
W=LL*L2=4*4=16 KN/m
M0=
% Error = < 10

## Slide 58: Seismic Checks

## Slide 59: Period Check
The period of a building is the time that the building takes in order to naturally vibrate back and forth and then coming back into its original shape before vibrating again .

## Slide 60
Ta calculated by hand = 0.73 sec
For the right block:
Ta from Etabs = 0.64
So Ta = 0.64 is taken
For the left block:
Ta from Etabs = 0.591
So Ta = 0.591 is taken

## Slide 61: P-Delta Check
For the P-delta effect on the building, this check is usually done to see if there is
going to be some extra moment due to the axial force that is acting on the building,
this moment appears if θ is larger than 0.1, then the vertical load will be inducted on
the horizontal displacement causing extra moments on the columns

## Slide 63: For the story drift check, this sort of deflection takes into account the lateral displacement in the diaphragm generated by lateral forces such as earthquakes. Story drift begins soon after an earthquake strikes the structure
Story Drift Check

## Slide 65
Table: Elastic and inelastic Drift Result Etabs in X Direction for Right Block

## Slide 66: Base Shear Check
This check is done to compare the base shear forces that affect the building from
the earthquake when the building gets hit by it with the allowable force that the
same building can handle, it gives an indication whether the building is going to
survive the earthquake forces applied on it or it will just collapsed for being over
stressed.

## Slide 67
For The Right Block
Hand calculations:
Cs =
Since Cs larger than Cs,max then take Cs = Cs,max = 0.071

## Slide 68
W = (D + SD + 0.25L) = 39029.1432 + 21728.2746 + 19329.9872 = 65589.9146 KN
Vhand = Cs * W = 0.71 * 655589.9146 = 4670.461 KN
Vetabs = 4507.715 KN
%error = = 3.4%......... Acceptable
For the equivalent factor:
For X direction:
For Y direction:

## Slide 69
Design Of Structural Elements

## Slide 70
After making sure that the checks are all good, the project now moves to the
final step which is the design phase.
ACI 318-14 has been used to design the structural elements.

## Slide 71
Beam Design

## Slide 73: Sample Calculations
Ast = 1190
Asb= 1000
By using, obtain 6
By using 10 mm 2 legs,

## Slide 77
Column Design

## Slide 78
Center Lines Of Columns

## Slide 80: Sample Calculations
Area of steel required is equal to 0.01 Section area from ETABS

## Slide 83
Slab Design

## Slide 85
Base 1 Floor Rib Reinforcement
A
A

## Slide 86
Section A-A in slab

## Slide 87
Footing Design

## Slide 88
The bearing capacity is assumed to be 250 KN/m2.
Therefore the best footing that can be chosen according to the assumption of the bearing capacity is Mat foundations.

## Slide 90
Left Block
Right Block

## Slide 91
Limitations
A 3D view of the building wasn’t available.
There wasn’t any soil investigation nor soil testing for the site.
Architectural plans were changed a little by adding three columns to reduce the long spans.