## Slide 1
TahiniRoute
Majd Marabe & Anwar Aqraa
Supervisor:
Dr. Abdallah Rashed

## Slide 2
Content
01
02
03
04
05
Main idea
Features
Structure
Hardware Modules
Web
Application
Future
Work
06

## Slide 3
Main idea
Our project, TahiniRoute, is about creating a smart, fully automated machine that makes tahini starting from white sesame seeds. The user can choose how much tahini they want and how much salt or pepper to add. The machine then takes care of the entire process—from checking ingredients to grinding, mixing, and filling the final product. This helps make tahini in a faster, cleaner, and more accurate way, which is great for small businesses or home use.

## Slide 4
Features
Grinding
Mixing
Filling
Sealing
Adding
ingredients
Sesame dispensing

## Slide 5
How to use the machine
keypad
Web Application

## Slide 6
Structure

## Slide 7
Hardware
Modules
Arduino MEGA
PC Power supply

## Slide 8
Sesame dispensing stage
This stage consists of two components:
  NEMA 23 Stepper Motor
    Controlled by a microstep driver.
    Rotates a knob to release white sesame seeds from the container.
  Ultrasonic Sensor
    Measures the amount of sesame available.
    Ensures there is enough to meet the user's selected quantity before starting the process.
NEMA23
MOTOR
TB6600 MICROSTEP
DRIVER
ULTRASONIC
SENSOR

## Slide 9
Grinding stage
This stage mainly consists of three components:
  The Grinder
    Connected to a one-channel relay.
  NEMA 23 Motor
    Connected to a Microstep Driver.
    Used to move the grinder to fill it with sesame and pour the mixture.
  DC Motor
    Connected to a two-channel relay.
    Used to move the grinder up and down.
NEMA23
MOTOR
TB6600 MICROSTEP
DRIVER
RELAY
2-CHANNEL
CAR WIPER
MOTOR

## Slide 10
Ingredient Addition and Mixing Stage
This stage mainly consists of:
  12V DC Pump
  Controlled by a one-channel relay.
  Used to add the oil.
  Servo Motors for Salt and Black Pepper
  Dispense salt and black pepper based on the selected quantities.
  Blender
  Controlled using a one-channel relay.
  Used to mix all the ingredients.
RELAY
2-CHANNEL
SERVO
MOTOR
12V DC
PUMP

## Slide 11
Drop the box stage
This stage includes two main components:
  3D-Printed Holder
    Designed to carry the tahini boxes.
  NEMA 17 Stepper Motor
    Connected to an H-bridge driver.
    Rotates the holder to deliver each box to the production line.
H-BRIDGE DRIVER
NEMA 17

## Slide 12
Filling stage
H-BRIDGE DRIVER
NEMA23
MOTOR
ULTRASONIC
SENSOR
This stage is made up of four components:
  NEMA 23 Stepper Motor
    Opens the mixer tap.
  LDR and Laser
    Detect when a box is directly below the tap and stop its movement.
  Ultrasonic Sensor
    Mounted above the box to measure the filling level.
LDR AND LASER

## Slide 13
Sealing stage
As the production line moves, the box picks up the lid.
  NEMA 17 Stepper Motor
  Lowers a 3D-printed part onto the box to press the lid in place.
  DC Motor
  Rotates the lid to close it.
  LDR and Laser to stop the box.
NEMA17
MOTOR
H-BRIDGE
DRIVER
DC MOTOR
LDR AND LASER

## Slide 14
Web Application

## Slide 15
Web Application
It displays each stage of the process in real time, along with the time elapsed

## Slide 16
Web Application

## Slide 17
Future
Work
01
02
03
Reducing System Size.
Automated Cleaning.
Larger Filling Containers.
04
Support More Products.
to improve on this project we can work on ...

## Slide 18
Thank you!