## Slide 1
Supervisor:
Dr. Issam Jardaneh
Presenter:
Mohammad Soqy
Mohammad Ateeq
Noor AL Deen Omar

## Slide 2: Analysis and design of foundation of Al Eyman building-Jenin

## Slide 3
  glance of the project:
  The project is located in Jenin city – Nazareth street.
  The project is a residential building consists of seven stories each storey has a two apartments.
  The area of each story is 342 meter square.
  The building does not have any commercial areas.

## Slide 4: Foundation types

## Slide 5: Recommendation of Site investigation:
  Site investigation:
In this project, the soil is improving by at least 1.2m (0.8 m of compacted rockfill and 0.4m of compacted basecourse according to standards) in this case the allowable bearing capacity is (2 Kg/cm²).

## Slide 6
  Foundation System:
  single footing distribution
service load (KN) | type of footing | Dimension | THICKNESS
from 1200 to 1500 | F3 | 2.6 * 2.2 | 65
from 800 to 1150 | F1 | 2.1 * 1.7 | 65
from 600 to 750 | `F2 | 3.0 * 2.6 | 65
  8 of these single footing are overlapped
  The over all percentage of footing to the hole building is 56%.
  Due to the overlaps and 56% percentage this system is not recommended.
  Single Footing System:

## Slide 7
  Foundation System:
  Because the single footing method fails to fulfil the design process Mat foundation will be used.
  The way to choose the correct thickness is by trial and error.
  After several tries 60 cm thickness succeeded to pass the tests.
  Mat foundation System:

## Slide 8: The concrete is B300 F’C = 24 Mpa
  Safe Design:
Model from safe to our project
  The steel yielding strength 420
  Mat thickness = 600 mm
  Stiff thickness under column = 600 mm
  Soil capacity = 2 kgm/cm2
  Mat concrete cover = 60 mm
  Dead load pattern = 1 (to calculate mat self weight

## Slide 9: In order to continue the design and steel calculation process four checks must be done:
  Checks:
Compatibility check
Deflection check
Pressure under footing from service load
Punching shear check

## Slide 10: After the animation of the model started, all elements moved together as one body, which means that the model is compatible.
  Compatibility Check:
Compatibility Check

## Slide 11: The allowable deflection is 10 mm
  Deflection Check:
Service load deflection shape
The max deflection in the project =9.11 mm
The deflection check passes

## Slide 12: The allowable pressure under footing is 200 kN/m2
  Pressure under footing from service load Check:
Pressure under footing from service load
The max pressure in the project = 180 kN/m2
The Pressure under footing from service load check passes

## Slide 13: All value less than 1 → <1
  Punching shear Check:
Punching shear Check
< 1 → Vu <
The Punching shear check passes

## Slide 14: Steel reinforcement from safe

## Slide 15: As min = 0.0018 * 1000 * 600 = 1080 mm2 → 6ᴓ16/m The bar distribution: 1080/201 = 6ᴓ16/m Moment M11 max (top steel in X-direction and Y-direction) Moment M22 min (bottom steel in X-direction and Y-direction) the steel distribution is 1ϕ16/ 15 cm overlap equal 960mm
  Foundation Reinforcement:

## Slide 16: Steel bars distribution

## Slide 17: The square meter costs approximately = 490 NIS
  Bell of quantity (BOQ):
cost (NIS) | unit price (NIS) | unit | quantity | term | no
4510 | 11 | m3 | 410 | excavation | 1
3300 | 12 | m3 | 275 | rockfill | 2
6235 | 43 | m3 | 145 | landfill | 3
62100 | 300 | m3 | 207 | concrete | 4
70950 | 4.3 | kg | 16500 | steel | 5
20520 | 60 | m2 | 342 | labor | 6
167615 | total cost |  |  |  | 

## Slide 18: Thanks for listening