## Slide 1: The Autonomous navigation Robot
By:
1- Aws Al-Nabulsi
2- Ibrahim Wahbeh
3- Odai Abdallah
Supervised by: Dr. Kamel Saleh

## Slide 2
Overview
The main idea of the project is to create an open source hardware and software robotic platform that can be easily adapted to do several tasks.
Features of this platform:
Map construction
Localization
Path planning and obstacle avoidance
speech and object recognition

## Slide 3
Map Construction and path planning
Estimated position (X1,Y1)
Target position (X2,Y2)
Optimum path
Move

## Slide 4
Hardware Design
1) Mother Board
2) Kinect sensor
3) Base
4) Wheels
Body Design showing the various parts of the robot

## Slide 5
The Base Controller
The Base controller contains:
1)Microcontroller
2)Drive Circuit
3)Two Stepper motors
4)Battery

## Slide 6
Choosing the motors
Torque calculations:
F friction = µ * m * g
T = F friction *R
The following formulas were used to determine the required torque
the estimated parameters for the robot are:
R= 6 cm , µ = 0.35 , m= 7 kg , g=9.81 m/ S2
Substituting these parameters into the equations,
We get a required torque of T = 7.3545 Kg-cm per motor.

## Slide 7
Motors used:
Two steper motors
Specifications Size: Nema 23 Phase: 2 Phase Step Angle: 1.8 Degrees Voltage: 70V Max Rated Current: 2.8A Inductance: 4.7mH Dual Shaft Bipolar 4 Wire

## Slide 8
stepper motor sequence

## Slide 9
Differentially steered system

## Slide 10
Drive circuit
A dual H-bridge with a maximum total current of 4 A will be used
to drive the motors

## Slide 11
The arduino microcontroller
Main tasks:
send/receive data.
Odometry calculations.
Motor commands.

## Slide 12
Kinect sensor
Features of the kinect:
RGB image
IR image
Depth map
Skeleton and object tracking

## Slide 13
Software

## Slide 14
odometry calculations
The term odometry means the robot coordinates in x, y and theta. And the velocity v of the robot
ϴ
∆ Distance= ∆ encoder pulses * Distance per pulse
Right distance = previous right distance + ∆ right distance.
Left distance = previous left distance + ∆ left distance.
∆ X = ∆ distance * cos (ϴ).
∆ Y = ∆ distance * sin (ϴ).
X= previous x + ∆ x.
Y= previous y + ∆ y.
Now to calculate the heading (ϴ):
∆ ϴ = (∆ right distance - ∆ left distance) / b.
Where b is the distance between the wheels.
And ϴ = previous ϴ + ∆ ϴ.

## Slide 15
Translating the desired linear and angular velocities into motor commands:
VR = V + (b * W)/2
VL = V – (b* W)/2

## Slide 16
Proportional and integral (PI) speed controller:

## Slide 17
Thank you for your attention
Questions?