## Slide 1
Conveyor-Dryer Handling Machine
Prepared by : Saad Sami Halaweh Omar Husni Odeh Omar Taher Tuffaha Yahya Hisham Abu-Bieh
An-Najah National University
Faculty of Engineering
Supervised by:
Dr. Osayd Abdel Fattah

## Slide 2: Outline:
What is it all about ?
Conveyor design
Frame Design
Bolts Design
Welding Design
Torque Calculations
Bearing Design and Selection
Motor Selection
Sprockets Design and Selection
Chain Selection
Drying System Design
dryer cover
Heat exchanger
Fan Selection
Drying experiments

## Slide 3
What is it all about ? - Problem definition - Why to use such a machine ? - How does it contribute to the company ?

## Slide 4
Conveyor design
1- Frame Design
for the leg we assumed b=h ,but in horizontal beams h=1.5*b and yield strength(Sy)=180Mpa,
Modules of Elasticity (E) =207Gpa
and the safety factor (n) is1.8

## Slide 5
The equations that help us in design the frame:
 | Mx (N.m) | My (N.m) | Mz (N.m) | T (N.m) | Length (mm) | assumption | Normal force(P)(N) | Shear force(v)(N)
Small beam | 148.5 | 0 | 0 | 1517.3 | 350 | h=1.5*b | 0 | 424.3
long beam | 0 | 0 | 1577.3 | 148.5 | 3570 | h=1.5*b | 0 | 424.3
Each leg | 148.5 | 0 | 1577.3 | 0 | 1000 | h=b | 424.3 | 0
summary for forces analysis

## Slide 6
this results for identical four legs which L=b=h=40mm
Cross section
this results for identical four beams which b=40mm, h=60

## Slide 7
2- Bolts Design
Km = E *d * A *exp(B*d/l)
Kb =
C =
Fb = Fi +CF
Fm = (1-C)*F –Fi
Ϭi =
Ϭservise = Ϭi +
Nl =
N = sp/Ϭ
Some eqn. may help us
Carbon steel : E = 207 GPa
Grid length (ℓ) = 19 mm
L = 30 mm
Lt = 26 mm
Ld = L – Lt = 4 mm
Lt = l – ld = 15 mm
F = 100 KN
Fi = 13.4 N
Sp = 830 MPa
A = 0.78715
B = 0.62873
N=1.5
Recommendations and needed
At = 14.2 mm2
M 5 *0.8 class 9.8

## Slide 8
3- Welding Design
N=1.5
Sy=100Mpa
Ϭ” =
Ϭ’ =
Ϭ”’ =
That gives us the area which equals
6.74*10-4 m2
And the inertia is
2.666*10-5 m3
So the thickness of weld is
6mm
Ϭ= Ϭ’ + Ϭ” + Ϭ”’
N=Sy/ Ϭ

## Slide 9: CAD Design

## Slide 12: Actual Design

## Slide 13
- This machine is considered as light-weight belt conveyor. - One of the most common formulas to calculate the torque for heavy-weight belt conveyors :
4- Torque Calculations
- Alternatively, the torque was calculated By using the following procedure :

## Slide 14
Experimental Procedure to calculate the torque

## Slide 15
- It was found that the added mass required to drive the system equals 45 kg (441 N) – inserted to the pulley which has a diameter of 12 cm. - So the torque induced on the drive shaft is : T = Force*distance = (P) (Pulley diameter / 2) = 441 * 0.06 = 26.46 N.m - The force is moved to act on the sprocket which has a diameter of 14 cm. 26.46 = T * 0.075 T = 353 N Where T is the radial force on the drive sprocket – 14 cm in diameter.

## Slide 17
5- Bearing Design and Selection
Xo = 0.02 () = 4.439 b = 1.483 = 1.3 (Machinery with light impact)

## Slide 18
From angular contact select the bearing which has the following dimensions: - UCF201 - Bore = 10 mm - Outer diameter (OD) = 30 mm - Width (A1) = 11 mm. - Fillet radius = 0.6 mm. - Shoulder diameters N = 11.5 mm, S = 11.5 mm - C10 = 4.94 KN. - Co = 2.12 KN.

## Slide 20
6- Motor Selection
The required Power transmission by the motor equals 2 * 133 = 266 watt (For two identical conveyors)
Three-phase Squirrel-cage Induction Motor
torque = 102 N.m
speed=28 rpm
Rated power= 300 watt = 0.40Hp
Efficiency = 0.8
Why not to use 3-phase synchronous motor ?
Three-phase Squirrel-cage Induction Motor
Rated torque = 0.5 N.m
Rated speed=1473 rpm
Rated power= 300 watt = 0.40Hp
Efficiency = 0.8
Built-in Speed reducer

## Slide 21
7- Sprockets Design and Selection
- Two Identical Belt Conveyors
- Motor Parameters : Induced Torque = 102 N.m Rated Speed = 28 rpm
- The torque required to drive the system without “ belt slipping “ is : 26.5 N.m
- The motor - sprockets - chain system acts as a speed reducer.

## Slide 23
8- Chain Selection
We chose chain number 40
P=0.5 in
Max power can withstand is 0.37Hp=276 watt
The total horse power needed to drive the conveyor is
266 watt

## Slide 25
9- Belt Selection

## Slide 26: Drying System:
What is drying?
Drying means removal of relatively small amounts of solvent from solid materials.
What is our task?
Our task is to design a process to remove solvent from adhesive material taking into account the above constrains to minimize the time of drying as short as possible.
10- Drying System Design

## Slide 27: Drying time depends on
the temperature of drying air
air flow rate (amount of air)
drying surface area
Humidity of drying air (solvent content)

## Slide 28: Investigations of drying rate parameters
Experimentally, It was found that the optimal parameters of drying rate after carrying out few experiments :
Air temperature is 70C
Drying air flow rate is 90-100 L/min
Amount of adhesive to dry : as the same used on tin plate in the factory (about 5g/tin)
The drying time of the adhesive sample (50-52s).

## Slide 29: Dryer with pipe manifold air distribution :
Previously Heated air in heat exchanger is distributed ensuring enough drying capacity to solvent on adhesive material

## Slide 30: Cover of dryer parameters:
X=2.5mm k=54 for carbon steel
X=10mm k=0.045 for Rockwool
Q Losses)cover)= 318.18 W
Q Losses (conveyer) = 150 W
Q (overall)=468.18*3=1404 W Factor =3

## Slide 31: Heat exchanger :
Length of tube ()=4.2 m
Q initial=4000 watt
Q for keeping the temperature constant =3000watt

## Slide 32: Ventilator (Fan Selection):
Power Supply : Electric
Power:0.5kw
Type : Centrifugal Fan
Model NO. : DF Series
Type of drive :AC single speed

## Slide 33
experiments

## Slide 34
Drying experiments

## Slide 36
Its flow rate is determined by rotameter (20-180) l/min. The air is heated through copper coil fitted in hot water. The heating rate is controlled by controllable hot plate. The hot air temperature is measured by digital industrial thermometer (-199-+199) T = 50 c
•Switch on the power of air compressor
•Heating the water bath that contain the copper coil and heating the air flow, see the
•Portioning the proper amount of adhesive on the bottom metal sheet
•Drying the adhesive by hot air measuring the time of drying and air temperature.
•Drying means that the adhesive material does not stick your finger if you touch it.
•The experiment is repeated many times fixing the drying temperature and changing the air flow rate. This results different drying times.
The drying steps:

## Slide 37
we have conducted many experiments to obtain an equation relates air flow rate, temperature and time
110 | 100 | 90 | 80 | Air flow rate (l/min)
50 | 50 | 50 | 50 | Temperature ©
46 | 52 | 67 | 78 | Time (s)
Experimental design :

## Slide 38
Chart: Q as t
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
 | 259.9234 | 175.3317 | 139.2645 | 118.2702 | 104.1911 | 93.9411 | 86.0656 | 79.7793 | 74.6166 | 70.2822
relationship between air flow rate and time
Q =961.3*t -0.568 Q: air flow rate t : time
- According to this equation, we have determined the fundamental specifications of the overall system such as the length and the width of the conveyor, heat exchanger design, the required speed to drive the conveyor .

## Slide 39: Total cost
Motor
Q=266 watt
Cost per hour =0.7 NIS
Operating time=8 hr
Running Cost per day=0.266*8*0.7=1.5 NIS

## Slide 40
Heat exchanger
Q Initial =4000 watt
Q for keep heat constant =3000 watt
Operating time=8 hr
Running Cost per day (initial)=4*0.7*1=2.8 NIS
Running Cost per day(keep heat constant )=3*0.7*8=16.8 NIS
Running Cost per day )Heat exchanger)=2.8+16.8=19.6 NIS

## Slide 41
Ventilator
Q=0.5 Kw
Operating time=8 hr
Running Cost per day=8*0.5*0.7=2.8 NIS
Total cost=2.8+19.6+1.5=23.7 NIS

## Slide 42: Conclusion
We can conclude :
1- Conveyor-Dryer handling machine contributes to the mitigating of the workforce and reducing the monthly costs. 2- No more time-consuming activities in the drying of the coated plates. 3- The efficiency of the tin production line is greatly increased.

## Slide 43: Thank You Any Question ?