## Slide 1: An-Najah National University Engineering & IT Faculty Civil Engineering Department
Structural Analysis And Design of Rama Building
By: muataz ismaeel (11142898)
Ramzy hammad (11143072)
Jafar ismaeel (11105731)
Ayham kamal (11105861)
Under supervision of : Dr. Munther Diab

## Slide 2: Outline:
Introduction.
Gravity and Lateral loads.
3D modeling using SAP.
Design of Slab.
Design of Beams.
Design of Columns and Shear walls.
Design of Footings and Ground Beams.

## Slide 3
INTRODUCTION

## Slide 4
Rama Building
Location : Ramallah
7 Floors.
Floor area : 473 m²
Total Area : 3311 m²

## Slide 5
Floors consists:
Three Residential Apartments.

## Slide 7
Codes
ACI 318-11 (American Concrete Institute)
IBC-2012 (International Building Code)
UBC-97 (Uniform Building Code)
ASCE-2010 (American Society of Civil Engineers).
Jordanian National Building Code.

## Slide 8: Preliminary Design The choice of the system for slab in the building is very important to resist the internal forces and stability.
International Journal of Current Engineering and Technology
Comparison | Solid Slab | Ribbed Slab
Weight | Heavier than ribbed | Light
Area of steel | More | Less
Beams | Bigger | Smaller
framework | Approximately the same | 
Cost | Bigger | smaller

## Slide 9
GRAVITY & LATERAL
LOADS

## Slide 10
Loads
Gravity
Lateral
Seismic
Dead
live
Superimposed

## Slide 12
Shear resisting
system

## Slide 13
SDS=2/3*SMS
SMS= Fa * Ss
R
System
I
Fa→ site class(B), Ss
Ss= 2.5 *Z
Z→ site class(B)→ soil type
Risk category)
Use of Buildings and Structures

## Slide 14
Response spectrum
  A response spectrum is a plot of the maximum response amplitude (displacement, velocity, or acceleration) versus the modal period

## Slide 15: Seismic design factors
R= Modification factor
Cd= Deflection Amplification Factor

## Slide 16
Code | Value of base shear (Hand Calc.)(kN)
IBC-2012 | 2216
UBC-97 | 1833

## Slide 17
Load combinations
U = 1.4D
U = 1.2D + 1.6L + 0.5(Lr or S or R)
U = 1.2D + 1.6(Lr or S or R) + (1.0L or 0.5W)
U = 1.2D + 1.0W + 1.0L + 0.5(Lr or S or R)
U = 1.2D + 1.0E + 1.0L + 0.2S
U = 0.9D + 1.0W
U = 0.9D + 1.0E

## Slide 18
THREE DIMENSIONAL STRUCTURAL ANALYSIS

## Slide 19
Modifiers for each element
Modifier | Element
0.7 | Column
0.35 | Beam
0.35 | Slab
0.7 | Shear wall

## Slide 22
Rebar percentage
All is okay
Shear & torsion
No red elements
No problems
Strength check

## Slide 23
Compatibility of structural model

## Slide 24
Equilibrium

## Slide 25
Slab moments
The difference percentage is 5.15 %, which is less than 10%, OK.
Stress Strain relationship
(internal equilibrium)

## Slide 26
Beams moments
The difference percentage is 7.01%, which is less than 10%, OK.

## Slide 27
Lateral loads check
Seismic load, IBC
Direction | Hand calculation base shear(kN) | Sap base shear (kN)
X | 2216 | 2301
Y | 1644 | 1932

## Slide 28
Period and modal participation ratio

## Slide 30
Structural period( hand calculation)
𝑇𝑥=0.45 Sec
ASCE, Equation 15.4-6
Floor | Area (𝒎𝟐) | Mass (ton) | Δ (𝒎m) | Force (𝒌𝑵) | Force* Δ 𝒌𝑵.𝒎 | Force* Δ2 𝒌𝑵.𝒎
Ground | 473 | 453 | 0.50 | 473 | 0.23 | 0.12
First | 473 | 453 | 1.25 | 473 | 0.59 | 0.74
Second | 473 | 453 | 2.30 | 473 | 1.09 | 2.50
Third | 473 | 453 | 3.47 | 473 | 1.64 | 5.70
Fourth | 473 | 453 | 4.68 | 473 | 2.21 | 10.36
Fifth | 473 | 453 | 5.89 | 473 | 2.79 | 16.41
Sixth | 473 | 453 | 7.04 | 473 | 3.33 | 23.44

## Slide 31
DESIGN OF SLAB

## Slide 32
Solid slab.
Thickness = 20 cm.
Shear on slab:
Max Vu = 65kN
Vc = 112.5 kN
112.5 >65so,
shear is OK
80

## Slide 33
Steel reinforcement:
Using a uniformsteel mesh with 5Ø14/ 1m (Top and Bottom) for all floors and roof.
(Negative and positive)
When the moment not exceeds 51.3kN.m/m , use 5Ø14/ 1m (Top and Bottom)

## Slide 34
Mx : All moment less than 51.3 kN.m/m

## Slide 35
DESIGN OF BEAMS

## Slide 37
ACI318-11 Code requirements:
The value of moment and shear
computed by taking twicethe
earthquake load in the load
combinations.
The first hoop shall be located not more than 50 mm from the face of a supporting member.
  .

## Slide 38
For shear and torsion |  | For flexure
 |  | As = ρbd
For shear and torsion |  | For flexure
 |  | As = ρbd
Equations:

## Slide 39
Beam ID | Dimension(h/d) | Longitudinal Steel |  | transverse steel until 2h(S1) | transverse steel (S2)
B1 | (700/350) | Top | 6Ø20 | 5Ø10/m | 4Ø10/m
 |  | Torsion | 5Ø16 |  | 
 |  | Bottom | 5Ø16 |  | 
B2 |  | Top | 5Ø16 |  | 
 | (700/350) | Torsion | 5Ø16 | 5Ø10/m | 4Ø10/m
 |  | Bottom | 3Ø16 |  | 
B3 |  | Top | 5Ø16 |  | 
 | (700/350) | Torsion | 3Ø16 | 5Ø10/m | 4Ø10/m
 |  | Bottom | 3Ø16 |  | 
B4 | (700/350) | Top | 6Ø16 | 5Ø10/m | 4Ø10/m
 |  | Torsion | 5Ø16 |  | 
 |  | Bottom | 4Ø16 |  | 
B5 | (300/200) | Top | 3Ø16 | 4Ø10/m | 3Ø10/m
 |  | Torsion | 3Ø16 |  | 
 |  | Bottom | 2Ø16 |  | 
B6 |  | Top | 3Ø12 |  | 
 | (300/200) | Torsion | 3Ø12 | 4Ø10/m | 3Ø10/m
 |  | Bottom | 3Ø12 |  | 

## Slide 40
Beams section

## Slide 41
DESIGN OF COLUMNS AND SHEAR WALLS

## Slide 43
Two columns in the project:
1. C1: (60x30), 9 columns.
2. C2: (70x40), 10 columns.
3. C3: (70x40), 3 columns.
4. C4: (80*35) ,4 columns.
5. C5: (90*40) , 1 column.
6. C6: (60*40) , 1 column.
7. C7: (35*35) , 1 column.
Design methodology:-
The design based on taking the critical edge, intermediate, and corner columns.
Drawing the interaction diagram for the columns.
Using SAP to get the axial force and moments on each column.
Choosing the proper steel ratio.
Determining the spacing between hoops.

## Slide 44
ACI318-11 code requirements:
The value of moment and shear computed by taking 3 times the earthquake load in the load combinations.
Hoops Equations (ACI318-11):

## Slide 46
Vu(KN) | Mu(KN.m) | Pu(KN) | Colum ID
22 | 23.1 | 1066 | C1
29.8 | 58.7 | 2690 | C2
24 | 16.4 | 1137 | C3

## Slide 47
The distribution of (M,P) point for check columns on C1,C2and C3 interaction diagram
c3
1%

## Slide 48
Using a steel ratio of 1% is safe and economical for all columns.
The longitudinal steel is:
8 20for C2 and C3 (70 x 30).
8 16 for C1 (60 x 30)
Hoops:
For All columns: provide Ø10/10 cm at a distance of 0.85 m from the top
and bottom joints of columns, and Ø10/15cm on mid of column.
Start with hoops at a distance of 5 cm from the face of supports.
Provide a lap splice length = 0.6 m.
The splicing of bars is made on the middle of columns.

## Slide 50
Design of shear wall :

## Slide 51
Minimum reinforcement in shear walls according to ACI318-11
Minimum ratio of vertical reinforcement area area, ρ, shall be:
  0.0012 for deformed bars not larger than 16mm in diameter with Fy not less than 420 MPa.
Minimum ratio of horizontal reinforcement area, ρ, shall be:
  0.002 for deformed bars not larger than 16mm in diameter with Fy not less than 420 MPa.
Vertical and horizontal reinforcement shall not be spaced farther apart than three times the wall thickness, nor farther apart than 450 mm.

## Slide 52
Equations:
  Compressive strength:

## Slide 53
Length of SW = 6 m.
Thickness of SW = 0.25 m
…. The thickness is accepted
Using SAP :
Vu (kN) | Muy (kN.m) | Mux (kN.m) | Pu (kN) | SW ID
750 | 5960 | 750 | 7560 | SW

## Slide 54
Use total cover = 30mm.
, therefore, use the minimum horizontal steel according to ACI318-11:
Then, for each face of wall, → use 1Ø10/250 mm

## Slide 55
on the two sides.
on each side.
The total longitudinal steel in SW for each side =
→ Use 1Ø16/15cm, or 6Ø16mm/1m.

## Slide 56: DESIGN OF FOOTING

## Slide 57
Soil type : Rock.
Allowable Bearing Capacity: 300 kN/m²
Grouping of footings are shown in table below:
Groups ID | Capacity in service load (KN) | Dimensions (m) | Group column
Group 1 (F1) | 850 | 1.70x1.70*0.60 | C2,c3,c7,c28,c29
Group 2 (F2) | 1500 | 2.30x2.30*0.60 | C1,c5,c6,c8,c9,c13,c14,c17,c18,c19,c20,c21,c27
Group 3 (F3) | 1800 | 2.50x2.50*0.60 | C10,c12,c15,c27,c24,
Group 4 (F4) | 2200 | 2.70x2.70*0.60 | C4,c11,c16,c23,c26
Group 5 (F5) | 2500 | 2.90x2.90*0.60 | C25

## Slide 59: Design of Footing F5
Maximum load on F5 comes from C4.
Envelop Ultimate load | Service load(kN) | Footing Dim. | Column Dim. | Footing ID | Column ID
1892 | 1490 | 2.3 x 2.3 | 0.3*0.6 | F2 | C20

## Slide 60
As(mm²) Tran. | As(mm²) Long. | MutransKN.m | Mu long KN.m | Thickness(m) | Vpu (kN) | Vp (kN) | Vu (kN) | Vc (kN)
1080 | 1080 | 129 | 257 | 0.60 | 1893 | 2567 | 137 | 324
As(mm²) Tran. | As(mm²) Long. | MutransKN.m | Mu long KN.m | Thickness(m) | Vpu (kN) |  | Vu (kN) | 
1080 | 1080 | 129 | 257 | 0.60 | 1893 | 2567 | 137 | 324
Transvers steel | Longitudinal Steel
8 16 / m (15 bars along 2.3 m) | 8∅16 or 1∅16/ 15cm (15 bars along 2.3 m)
Transvers steel | Longitudinal Steel
 | 8∅16 or 1∅16/ 15cm (15 bars along 2.3 m)

## Slide 61
Cross section in F5

## Slide 62
DESIGN OF GROUND BEAMS

## Slide 63
Ground beams:
- GB : (600/250).
Design philosophy:
By applying a 2 mm displacement at a joint under a footing that have the tallest ground beam.
Then, determine the area of steel by using a half of steel ratio resulting from the moment.

## Slide 64
Transverse steel | Bottomsteel | Top steel | Vu (kN) | Mu (kN.m) | GB ID
5 8 / m | 2 16 | 2 16 | 15.3 | 14.3 | GB1
Transverse steel | Bottomsteel | Top steel | Vu (kN) | Mu (kN.m) | GB ID
 |  |  | 15.3 | 14.3 | GB1