## Slide 1
Design of Pedestrian Bridge at Al-Academia Street-Nablus
Prepared by:
Dina Aqra
Shatha Bast
Supervised by:
Dr. Munther Diab

## Slide 2
Contents
Problem Definition
Design Criteria (Codes and materials)
Gravity Loads
Lateral Loads
Analysis and Design of Steel Bridge
Analysis and Design of Concrete Bridges

## Slide 3
Problem Definition

## Slide 4
Design Criteria
Codes
(ASCE 7-10).
Jordanian Code for Loads-2006.
(AASHTO).
(AISC 360-10).
(IBC 2012).
(ACI 318-14).

## Slide 5
Design Criteria
Materials:
Concrete
Unit Weight | 25 kN/m3
Concrete Compressive Strength | 28 MPa
Concrete Flexural Strength, | 3.28 MPa
Concrete Tensile Strength, | 1.75 MPa
Modulus of Elasticity, | 24870 MPa
Poisson’s Ratio | 0.2
Unit Weight | 25 kN/m3
 | 28 MPa
 | 3.28 MPa
 | 1.75 MPa
 | 24870 MPa
Poisson’s Ratio | 0.2

## Slide 6
Design Criteria
Materials:
Steel:
Reinforcing steel
76.97 kN/m3 | Unit weight,
200 Gpa | Modulus of elasticity, E
620 MPa | tensile strength, fu
420 MPa | yielding strength, fy

## Slide 7
Design Criteria
Materials:
Steel:
ASTM-Gr 50 (A572)
76.97 kN/m3 | Unit weight,
200 Gpa | Modulus of elasticity, E
455MPa | tensile strength, fu
350MPa | yielding strength, fy

## Slide 8
76.97 kN/m3 | Unit weight,
200 Gpa | Modulus of elasticity, E
400MPa | tensile strength, fu
250MPa | yielding strength, fy
Design Criteria
Materials:
Steel:
A36

## Slide 9
Design Criteria
Materials:
Polygal Standard
It is a covering material for roof, sides of the bridge, and sides of the stairs. It has a specific unit weight of 1.67KN/m3, and the modulus of elasticity, E is 2400MPa.

## Slide 10
Dead Load : own weight of the structure
Live Load: 5KN/ m2
Roof Live Load: 5KN/ m2
Super Imposed Dead Load: 1KN/m or 0.5KN/ m2
Snow Load: 0.75 KN/m2
Gravity Loads

## Slide 11
Wind Loads
Velocity pressure: qz = 0.613 Kd Kzt Kz V2
V: basic wind load speed = 51m/s.
Kd: wind directionality factor = 0.85.
Exposure: C open terrain.
Kzt: topography =1 (flat).
Kz or Kh: velocity pressure exposure
Lateral Loads

## Slide 13
Lateral Loads
Seismic Loads: 3 procedures to analyze seismic loads:
Equivalent lateral force analysis (equivalent static).
Modal response spectrum analysis.
Seismic response history procedure (time history).

## Slide 14
Seismic loads:
Site class is D.
Risk category ш , importance factor=1.25.
The design parameters:
SDS = 0.7 and SD1 = 0.475.
Seismic design category D.
Lateral Loads

## Slide 15
Lateral Loads
Seismic Loads
Response modification factor: R = 2
Deflection Amplification Factor (Cd) = 2
System Over Strength Factor (Ω0) = 2

## Slide 16
Pedestrian Bridge layout

## Slide 17
Pedestrian Bridge layout

## Slide 18
3D modeling:

## Slide 19: Analysis and design
Checks
Compatibility

## Slide 20: Analysis and design
Equilibrium
Error% | Manual | ETABS | 
1.14 | 3795.47 | 3839.26 | Dead
0.01 | 1154.00 | 1153.87 | Live
0.02 | 56.89 | 56.90 | Roof Live
0.00 | 258.43 | 258.43 | Snow
2.54 | 438.70 | 427.85 | wx
0.33 | 683.60 | 685.89 | wy
2.47 | -438.70 | -427.85 | (-wx)
0.39 | -683.60 | -686.29 | (-wy)

## Slide 21: Analysis and design
Stress-Strain Relationship
ETABS = 11.22 KN.M.
M= = 11. 25KN.m.
Error = 0.27%

## Slide 22
Analysis and design
3D without separating
High ductility
Low ductility
Separate steel and concrete
High ductility
Low ductility

## Slide 23: Analysis and design
Front view of the bridge

## Slide 24
Pedestrian Bridge layout

## Slide 25: Analysis and design
Layout of walls

## Slide 26: Analysis and design
Section in the beam
Part of plan at elevation 6m

## Slide 27: Analysis and design
Low ductility (separated) | High ductility (separated) | 3D Low ductility | 3D High ductility | Group name
C 30 | C 30 | C 30 | C 30 | Cables
TUPO 140*140*8 | TUPO 140*140*8 | TUPO 140*140*8 | TUPO 180*180*12.5 | Arch
TUPO 60*60*3.6 | TUPO 60*60*3.6 | TUPO 80*80*5 | TUPO 140*140*10 | Main truss
TUPO 70*70*4.5 | TUPO 70*70*4.5 | TUPO 90*90*5.4 | TUPO 180*180*12.5 | Sec. truss
TUPO 80*80*5 | TUPO 80*80*5 | TUPO 80*80*5.4 | TUPO 120*120*8 | Roof arch
L60*4 | L60*4 | L60*4 | L60*4 | Roof bracing
TUPO 80*80*5.9 | TUPO 100*100*7.1 | TUPO 80*80*5.9 | TUPO 100*100*10 | Bridge sides members
L 60*4 | L 60*4 | L 75*5 | L 80*8 | Bridge sides bracing
HI 140B | HI 140B | HI 140B | HI 160B | Main beams
HI 100B | HI 100B | HI 100B | HI 120B | Main beams 2
HI 100A | HI 100A | HI 100A | HI 160B | Sec. beams
L80*6 | L80*6 | L100*7 | L100*7 | Deck bracing
TUPO 60*60*6.3 | TUPO 60*60*6.3 | TUPO 60*60*3.6 | TUPO 60*60*3.6 | roof members
TUPO 60*60*4 | TUPO 60*60*4 | TUPO 60*60*4 | TUPO 60*60*4 | Bridge sides top

## Slide 28: Analysis and design
Design of the bridge deck (slab)
Depth = 100mm.

## Slide 29: Analysis and design
Design of concrete beams
Width = 450mm, depth = 620mm.

## Slide 30: Analysis and design
Design of stair’s slabs and flights
Width = 2.5m, rise height = 15cm and 10 steps at each flight.
Stair’s flights

## Slide 31: Analysis and design
Design of stair’s slabs and flights
Depth = 250mm.