## Slide 1: An Najah National university Graduation Project (design and analysis of alhyat building)
Made by :
Amjad Janajreh
Husam Habaib
Mohamed Estati
submitted to : Dr. Mahmoud Dwaikat

## Slide 2: Introduction
Al Hyatt is a residential building consists of a nine stories of reinforced concrete building, located in Nablus city.
Each story has an area of 300 m2

## Slide 3: Scope of the Project
In this report we carry out complete analysis for the building under gravity loads. We design specific elements in details (such as beams, columns and slabs).
The analysis and design of the building for lateral load will be done in Part 2 of the project.
The analysis is mainly done by use of computer program, and manual calculations were made where necessary to check on the results.

## Slide 4: Materials
Structural materials:
Concrete properties
fc’= 28 MPa.
= 248,70 MPa),
𝛾 = 25 kN/m3
Reinforced Steel properties :
fy = 420 MPa
= 200,000 MPa
Steel Grade 60.
Non-structural material
Material | Unit weight (KN/m3)
concrete | 25
Blocks | 12
Masonry stone | 27
Sand and gravel for fillers | 20

## Slide 5: Design Code and method
ACI 318-08 (American Concrete Institute): building code requirements of structural concrete and commentary.
ASCE-2009 (American Society of Civil Engineers)
The structural system to be used is two way waffle slab with drop beams in both directions
Structural System

## Slide 6: Structural Loads:
Dead load:
Own weight of all structural and non-structural elements.
Super imposed dead load

## Slide 7: Live loads:
It is based on function of the building. It’s specified that the live load is taken from Table 4-1 in ASCE/SEI 7-05 code and in this project.
a live load of 4 KN/m2 will be used in 4th and 5th basements the other floors will be used as 2 KN/m2 residential areas.
Wind load is a dynamic force that effects on the whole structure. That will be in project 2.
Seismic load is a dynamic force that effects on the whole structure. That will be discussed in project 2.
Wind Load:
Earthquake Load :

## Slide 8: •Building structural system:
Slabs :
floors supported by columns and shear walls .Two-way Waffle slabs .
Beams:
The beam is an element of the structural buildings which is designed to transmit the tributary loads from the slabs to columns.

## Slide 9: • Load Combinations :
Columns:
The column is an element of the structural building that receives the load from the beams on all floors and transfers it to the foundation.
through this design process some combinations are chosen this stage of analysis and design:
U = 1.4 D
U = 1.2 D + 1.6 L
Where:
U: ultimate load
D: dead load
L: live load

## Slide 10: Preliminary Design -Manual calculation
  Slabs :
  h
  hmin = .15m so we will use h = .23 m
slab own weight for one unit
D.L=own weight + SDL
D.L = 8.18 KN/m2
Structural Elements :

## Slide 11
Wu = 1.2 * D.L + 1.6*L.L = 13.02 KN/m2
Flexural design of slab:
Frame 1 on the edge beam.

## Slide 12
Determine M0
Wu L2 Ln12/ 8 = 498 KN.m
B.M.D. on frame 1.
C.S & M.S on the edge beam.

## Slide 13
B.M.D. on C.S.
B.M.D. on M.S.

## Slide 14
  Preliminary analysis and design of beams
Beams plane.

## Slide 15
Beam Design:
h =
h =.32 m
Use h = 0.50 m b=0.30m
Wu, beam = 1.2*D.L +1.6 L.L=
B.M.D. on beam 10
For maximum negative moment M = 178.09 KN.m on the face of the support:
ρ = 0.0044
As = ρ *b*d
As=562 mm2
As min =495 mm2
As >Asmin
Use 6Φ12

## Slide 16
For maximum positive M= 96 KN/m:
ρ = 0.0023
As = ρ *b*d As=297 mm2
As min =495 mm2
As <Asmin Use 6Φ12
  Preliminary analysis and design of columns.
    Load computation:
Tributary area equal for C3 =16.14
Pu=1.2*Dl+1.6*L.L
►1194.57 KN

## Slide 17
 | Axial Load | DIMENSIONS |  | ø16
Column ID | Pu | b | used Depth | used No of bars
C1 | 688.39 | 250.00 | 200.00 | 4.00
C2 | 1364.07 | 250.00 | 400.00 | 6.00
C3 | 1630.60 | 250.00 | 460.00 | 6.00
C4 | 1630.60 | 250.00 | 460.00 | 6.00
C5 | 663.80 | 250.00 | 200.00 | 4.00
C6 | 452.34 | 250.00 | 200.00 | 4.00
C7 | 1007.05 | 250.00 | 400.00 | 6.00
C8 | 1363.08 | 250.00 | 400.00 | 6.00
C9 | 1429.96 | 250.00 | 400.00 | 6.00
C10 | 3808.11 | 250.00 | 1100.00 | 14.00
Columns groups in all floors.

## Slide 18
Columns distribution.
Flexural Design
Choose Column Type:
Assuming zero moment on column;
=
= 28.76 < 34
► so short column.

## Slide 19
• Design example C3 is chosen:
ɸPn = ɸ*λ*(0.85*f'c*(Ag-As) + Fy*As)
As = ρ * Ag
= 0.01 Ag
Ag = 113000.69 mm2
Assume width = 250 mm
Depth = Ag / width = 452 mm
Try depth = 460 mm.
As = ρ*b*d
= 1150 mm2
Use 6 ɸ 16 bars
• Ties Spacing
S = 250 mm.
Cross section in C3.

## Slide 20
Finite Element Analysis
Revit plane plan view of the building.

## Slide 21
Integration process exporting Revit
geometric model to Robot FE program.

## Slide 22
Material Definitions:
Model plane in Robot.

## Slide 23
Structural elements identifications:

## Slide 24
Load Identification & combination

## Slide 25
Mesh generation

## Slide 26
Analysis process

## Slide 27
Section through panels(comb 2).
Envelope B.M in Beam 1.

## Slide 28
B.M maps on (Y-Y) direction for the whole structure (comb 2).

## Slide 29
Design process
Longitudinal section in B1.
Cross section A-A in beam 1.

## Slide 30
Slab # 1 reinforcement.
Cross section A-A in column 10.

## Slide 31
That’s it !
………………
Thank You