## Slide 1: Paving machine
Gradating Project 1

## Slide 2
Supervisor : Prof. Mohammed Abu Hilal
Akram Al Madmouj
Zaid kalboneh
Mohmmed Othman
Ehsan Zeer

## Slide 3: Table of content :
History.
Discussing the problem.
Solution.
Machine Parts.

## Slide 4: History
History of paving : Paving has been around for 5000 years ago. The oldest road was discovered in Giza, Egypt. The road was built 4600 years ago as a route used to transport large stones and many other goods. It was 12 km length and 2 m in width. This road was paved with thousands of sands stone and limestone's and some logs of petrified wood.

## Slide 5: History
Nablus old city

## Slide 6: `
Paving by manual workers to needs to a lot of workers, time and money. Also the worker who paves the road had a lot of medical conditions due to long working hour on his knees. Paving needs a lot of machine to make the work good.
Discusses the problem

## Slide 7: Road paving in Nablus

## Slide 8: Tiger stone

## Slide 9: The solution
Mechanical paving machine is the solution. Why ??
It’s reduce time, effort and money.
Help the worker to be work more comfortable.
Reduces the number of machine needed
Multi-task machine.

## Slide 10: Paving Machine

## Slide 11: Machine Parts
Steel Frame
Compactor
Sliding frame
Brushes
Sand Tank
Tension spring and steel plate
Sliding rod
Track

## Slide 12: Steel Frame
Steel Frame : Is made by the type of steel was selected variable in market and have allowable stress 1400 kg/cm2 . The width dimension of frame was select to include 8 bricks (126 cm) and the height is (80 cm) to help the employer to but the bricks, the long are (100 cm) , it can hold 8 bricks.

## Slide 13: compactor
The compactor : is made by steel sheets wrapped up. Its weight is high to make sure the bricks compressed well to the ground.

## Slide 14: Sliding frame
The sliding frame consisted of pipes parallel to each other inclined by a specific angle to make sure the bricks slide by its weight. The goal of making it cylindrical shape to minimum the friction force the occurred by the sliding bricks. The angle is made to make sure that the bricks slides by its weight without any external force.

## Slide 15: Brush
The main purpose of using brushes is to fulfill the space between the bricks and to clean the bricks after the sand is compacted by the compactor. The brush is coarse to make sure that it does its job

## Slide 16: Sand tank
The sand tank is used to store sand and to put sand above the bricks to fulfill the space between bricks to hold it out .

## Slide 17: Tension spring and steel plate
The tension spring with steel plate will be used to hold the bricks in the paving machine and to move the bricks from above to bottom slowly and in order. The moving plate angle will the same with the sliding frame to insure the brick will move in order .

## Slide 18: Sliding rod
The sliding rod mission is to hold the bricks is to hold the bricks and to move the bricks slowly and to ordinary. The wheels mission is to make sure that the bricks move slowly.

## Slide 19: Track
The track mission is to make sure that the machine moves smoothly on sand. And its mission is to hold the big weight on the machine.