## Slide 1: Analysis and Design of Al-Quds International Airport Main Terminal Building
By: Ahmad Abu Arra
Baker Bozeyeh
Under Supervision of :
Dr. Ibrahim Mohammad

## Slide 3: INTRODUCTION

## Slide 4: Background Info.
Location: Qalandia, Palestine
Near Qalandia Airport Site
Site geology: Dolomite with a surface layer of Alluvium
Bearing capacity = 400 KN/m2
INTRODUCTION
Figure1. Map of Palestine
Figure2. Site location
Figure3. Geological map of the proposed location

## Slide 5: Conceptual Design
Pier-type terminal
Based on ACRP Report 25 : Air passenger terminal planning and design
INTRODUCTION
Figure4. Schematic diagram of the main terminal
Figure5. ACRP Report 25

## Slide 6: Architectural Design
3 Stories
Total area of 64,000 m2
Total height = 18 m
INTRODUCTION
Table1. Floors areas and heights
Table2. Piers areas and height

## Slide 8
Figure7. First floor plan

## Slide 9
Figure6. Ground floor plan

## Slide 11
Figure8. Second floor plan

## Slide 12: Structural Design
Structural system:
Terminal: Divided into 4 blocks
Special moment resisting frames. Two way Slabs with drop beams
Piers: Composite steel and concrete structures
INTRODUCTION
Figure9. Schematic diagram of the terminal building

## Slide 13: INTRODUCTION
Dead Loads: Own weight
Super-imposed dead load = 3.1 KN/m2
Live load = 5 KN/m2
Snow load = 1.428 KN/m2
Self-straining loads (temperature loads)
Loads

## Slide 14: INTRODUCTION
Seismic Design Parameters:
Risk category IV
Seismic importance factor = 1.5
Site class: B
Seismic design category : D
Response spectrum
Seismic Loads
Chart: Design Response Spectrum
| 0 | 9.4500000000000001E-2
 | 0.2988 | 0.747
 | 0.747 | 0.747
 | 0.7463 | 0.353 | 0.1765 | 0.11767 | 0.08825 | 0.0706 | 0.058833 | 0.050429 | 0.044125 | 0.039222
 | 0.039222 | 0.03177 | 0.026256 | 0.022062 | 0.018799 | 0.016209 | 0.01412
Table3. Seismic parameters
Table4. Seismic design coefficients
Figure10. Design response spectrum

## Slide 15: INTRODUCTION
Ultimate Load Combinations:
1.4D
1.2D + 1.6L + 0.5Lr
1.2D + 1.6L + 0.5S
1.2D + 1.6Lr + L
1.2D + 1.6S + L
1.2D + 1.0E + L + 0.2S
0.9D + 1.0E
Load Combinations
Service Load Combinations:
D
D + L
D + Lr
D + S
D + 0.75L + 0.75Lr
D + 0.7E
D + 0.75L + 0.75(0.7E) + 0.75S
0.6D + 0.7E
Where:
D = Dead Loads
L = Live loads
Lr = Roof live load
E = Earthquake load
S = Snow load

## Slide 16: Part One: Concrete Structure

## Slide 17: Initial Dimensions
Concrete 32MPa.
Grade60 steel
PRELIMINARY DESIGN
Materials
Beams: 800X400 mm
Slab thickness = 250mm
Columns: circular, D = 800mm

## Slide 18: GF Beams Layout (Block A)

## Slide 19: GF Beams Layout (Block B)

## Slide 20: 3D Model
Equal spans, 10m c/c
Acceptable deflections: 41.6mm for slabs, 20.8mm for spandrel beams
Slab stiffness modifier = 0.35
Combination : ∆ =2×∆𝐷+1.5×∆𝐿
Resulting deflection = 66mm > allowable
PRELIMINARY DESIGN
Figure11. 3D preliminary model
Figure12. Top view of preliminary model
Figure13. Deflections in slab

## Slide 21: Preliminary Model Modifications
Slab Thickness = 300mm
Spandrel beams 1500 X 350 mm
Interior beams 800 X 800 mm
Neglect sustained live load
Resulting deflection = 37.1mm < 41.6 mm
PRELIMINARY DESIGN
Figure14. 3D preliminary model
Figure15. Top view of preliminary model
Figure16. Deflections in slab

## Slide 22: 3D Modeling & Analysis

## Slide 23: Structural Modeling
Four building blocks
Section properties
Concrete 32MPa.
Grade60 steel
3D ANALYSIS
Table5. Section properties
Figure16. Building Blocks

## Slide 24
Block A
Figure18. 3D view of block A model
Figure17. Top view of block A model

## Slide 25
Block B
Figure20. 3D view of block B model
Figure19. Top view of block B model

## Slide 26: Loads Definitions
Load Patterns
Load Cases
Response spectrum function
Seismic load cases
EDx = Dynamic seismic load case in X- direction
EDy = Dynamic seismic load case in Y- direction
3D ANALYSIS
Figure21. Load patterns
Figure22. Load cases
Figure23. Response spectrum function definition
Table6. Seismic load cases

## Slide 27: Analysis Verification
Equilibrium check
Internal forces check
Slab moments
Column loads
3D ANALYSIS
Figure24. Sample panel in block A
Table7. Equilibrium check summary for block A
Table8. Equilibrium check summary for block B
Figure25. Sample panel in block B
Figure26. Sample column in block A
Figure27. Sample column in block B
Table9. Internal forces check summary

## Slide 28: Structural Irregularities
Horizontal irregularities check
Torsional irregularity (1a) exists in both blocks
Reentrant corner irregularity exists in block A
Vertical irregularities check
Stiffness-extreme soft story
Irregularity exists in block B
3D ANALYSIS
Table10. Horizontal irregularities
Table11. Vertical irregularities

## Slide 29: Torsional Irregularity
Accidental torsion amplification factor
For block A = 1.21
For block B = 1.03
3D ANALYSIS
Table12. Maximum and average displacements in block A
Table13. Maximum and average displacements in block B

## Slide 30: Stiffness-extreme soft story irregularity
3D ANALYSIS
Table14. Soft story check for block B

## Slide 31: Story Drifts Check
3D ANALYSIS
Table15. Story drifts
Allowable drift
where hsx is story height
Story drift exceeds allowable limit

## Slide 32: Modifications on models
Add tie beams in block B at height of 5.5m to increase stiffness
3D ANALYSIS
Table16. Block B story stiffness
Table17. Modified Drifts
To decrease drifts:
- Increase diameter of circular columns to 1300 mm
- Increase dimensions of Rectangular columns to 1800X900
- Increase dimensions of Tie beams to 1500X800mm

## Slide 33: Modal Mass Participation Ratios
3D Analysis
Structural Periods
Table18. MMPR for block A
Table19. MMPR for block B
Table21.Model Periods for block B
Table20. Modal Periods for block A
- Manually calculated period = 0.88

## Slide 34: Long-Term Deflections
Deflections in block A
Maximum deflections = 43.2mm
Deflections in block B
Maximum deflections = 47.9mm
SAFE cracking section analysis results
Maximum deflection in 1st floor slab from ETABS = 42 mm
Maximum deflection in 1st floor slab from SAFE = 41.7 mm
3D Analysis

## Slide 35: Concrete Structural Details

## Slide 36
Cross section in Beams:
:
Continuity in bars:
d/4. 6db. 150 mm. spacing = 100 mm.
≤
Beams Detailing

## Slide 37
Cross Sections:
≥ Depth of member.
≥ 1/6 of clear span of column.
≥ 450 mm.
Lap splices:
Transverse steel:
≤ ¼ minimum member dimension.
≤ 6 db.
≤
Columns Detailing

## Slide 38
Bottom and Top steel:
Lap splices:
Slabs Detailing:

## Slide 39
Single footings:
Footings Detailing:

## Slide 40: Part Two: Steel Structure

## Slide 41: Steel Structure
Dead Loads: Own weight
Super-imposed dead load = 2.7 KN/m2
Live load = 5 KN/m2
Snow load = 1.428 KN/m2
Construction Load = 2.4 KN/m2
Wind load
Loads

## Slide 42: Steel Structure
Structural System:
Moment Frames in Y
Braced Frames in X
Composite Floor System
Steel Deck Section
Construction Load = 2.4 KN/m2
Roof structural design
3D Model

## Slide 43: Steel Structure
Composite steel beams:
Non-shored construction
Partial composite action (50%), 30 shear studs per joist
Composite Floor System
Manual Design
Bending capacity and deflection
Steel Design
Composite Steel and Floor Design

## Slide 45: Steel Structure
Beam-Column Flange Connection
Extended moment-end-plate
Stiffeners are used
Beam-Column Web Connection
Double Angle Connection
Beam-Girder Connection
Double Angle Connection
Steel Connections

## Slide 46: THANK YOU 