## Slide 1: Energy generation using palm waste for Heating applications, case study for Palestine
Supervisour: Eng.Luqman Herzallah
Prepared by:
Ahmad Abu Arra
Dirar Hara
Firas Mansour
An-Najah National University
Faculty of Engineering and Information Technology
Mechanical Engineering Department
Wednesday,7 February 2024

## Slide 2: Introduction I Literature Review II Methodology III Conclusions V Recommendations VI Feasibility study VII Agenda
Results
IV

## Slide 3: Introduction I

## Slide 4: Introduction
Tropical and subtropical tree
Phoenix dactylifera
1
2
Jericho and Jordan Valley regions and the Gaza Strip
3
What is the city that is dubbed the "City of Palms"?
4

## Slide 5: Palm Tree Parts
Leaf
Length 3-6 m
Lifespan 3-6 yrs
Produce 20kg/yr from the dry leaf
Female inflorescence
Essential for the production of dates
Requires pollination from male trees
Fruit
Length 3-7 cm
Contain sugar, proteins, calcium, phosphorus, iron, and vitamins of the B and A group
Male inflorescence
The male date palm yields flowers that produce the pollen
The main structural part of the tree that supports the branches and leaves
Kernel
Root
Absorb water and nutrients from the soil
Stem
Represent 10% of palm fruit waste
Used in cosmetics, as it reduces the visible signs of aging

## Slide 6: SOLUTION PROBLEM Problem Statement
Large quantities of date palm waste can be converted into :
Environmental
Emergence of the red date palm weevil.
Fertilizer
Animal food
Energy
Heating applications

## Slide 7: Literature review II

## Slide 8: Applications
Fertilizer
Biofuels and Biogas
Animal food
Insulation
Energy production
Lightweight wood
Thermal conductivity of 0.083 (W/m.K)

## Slide 9: Methodology III

## Slide 10: Methodology
Step I
Step II
Step III
Step IV
Step V
Data collection
Data Analysis
Literature review
Laboratory Analysis
Evaluation

## Slide 11: Experiments Methods
Crucible lid loosely closes
Moisture (M)
Weight 1 g
Approximating Analysis
Ash (A)
Volatile matter
(VM)
Put the crucible inside the Decomposition vessel
Fill the Decomposition vessel with oxygen gas.
Weigh 0.5 grams of benzoic acid
Place the Decomposition vessel inside calorimeter.
Add water to the calorimeter.
Take out Decomposition vessel from calorimeter, empty it of oxygen
Wait for the complete combustion
Experiments Methods
Fixed carbon
(FC)
Higher Heating Value (HHV)
Time 1 hour
Furnace at 105 C
Cooling inside desiccator
Time 2 hours
Furnace at 600 C
Cooling inside desiccator
Time 7 minutes
Furnace at 950 C
Cooling inside desiccator
Crucible lid opened
Weight 1 g
Crucible lid tightly sealed
Weight 1 g
Repeat the same steps for the three samples (Date Kernel, palm leaf, and Palm frond petiole).

## Slide 12: Results and Analysis IV

## Slide 13: Results and Analysis
Chart: 
| Total number of palm trees in Palestine | Number of palm trees included in the questionnaire
Series 1 | 311000 | 77074
Chart: type of palm tree
| Alhayani | Barhi | Majhool
 | 2.5 | 2.5 | 95

## Slide 14: Results and Analysis
Chart: Palm Waste type
| Fruit bunch | Stem | Leaves
 | 17.2 | 16.5 | 18.9
Chart: Type of waste generated from palm trees
| Palm fronds | The fronds with their base and the kernel of dates
 | 82.5 | 17.5

## Slide 15: Results and Analysis
Chart: Mass(%)
| Moisture | Ash | Volatile Matter | Fixed carbon
Date Kernel | 6.7382 | 2.208 | 86.5414 | 4.5125
Palm Leaf | 4.7195 | 11.574 | 75.6364 | 8.0701
Palm frond petiole | 8.5941 | 8.1412 | 77.2881 | 5.9765
Chart: Types of palm waste
| Palm frond petiole | Palm leaf | Date Kernel
 | 15.9897 | 16.8873 | 17.1267

## Slide 16: Results and Analysis
Sinokrot Factory
Al-Qawasme Factory
  Amount of waste
  130 tons during the past year
  will increase to approximately 180 tons this year.
  Amount of waste
  54 tons of date seeds
  6 tons of damaged dates
  No information about the quantity of date paste
  Type of waste for date paste
  date seed
  damaged dates
  date paste (a mixture of date pulp and date seeds).
  Waste disposal methods
  in Garbage
  cooperation with the Ministry of Agriculture, which uses it as animal feed
  Challenges
  financial and environmental
  occupying large spaces
  negatively affecting the final product

## Slide 17: Feasibility Study V

## Slide 18: production line
NOTE: https://www.youtube.com/watch?v=f0OTbmMtwNY&t=3s
Remove Nails
Hot air

## Slide 19
Economical data
  Electricity Consumption=158 NIS
Glue Consumption=431 NIS
Engineer Salary=200 NIS
Transportation Cost= 100 NIS
Operational Costs / Day
Total operational Cost= 1190 NIS
Worker Salaries(3workers)=300 NIS
  Blocks Produced Per Day=1670 blocks
Cost per block= 0.72
Production Details
Market Price per Block=1 NIS
  Investment Costs=414000NIS
Investment cost

## Slide 20
Economical data
SPP
863 days
Annual Profit
150240 NIS/year
ROI
36.3%

## Slide 21: Conclusions VI

## Slide 22: Conclusions
Determine the Higher Heating Value (HHV)
Conducting approximate analysis experiments
Comparing the results
Transforming palm waste into wooden blocks
Conducting an economic feasibility study

## Slide 23: Recommendations VII

## Slide 24: Recommendation
Comprehensive Feasibility Study for the Market
Government Intervention and Support
Local Manufacturing
1
3
4
New Applications and Product Diversification
2

## Slide 25: Thanks

## Slide 26: Questionnaire