## Slide 1: Graduation project ii: 3-axis cnc milling machine
Supervisor: Eng. Salameh Abdul Fattah. Team: Enas Fouqha, Mahmoud Radwan, Rimal Zaareer Wala’ Blebleh, and Zaid Hmaid

## Slide 2: Presentation Layout
Introduction
Mechanical Part
Electrical Part
Control
Conclusion

## Slide 3: Introduction

## Slide 4: Machining and milling
One of the most important manufacturing processes.
Milling is an example of machining.
A rotating cylindrical tool removes parts of the work piece

## Slide 5: Types of milling operations

## Slide 6: What is CNC ?
Computer Numerical Control
Complete integration between machine and computerized control

## Slide 7: Mechanical part

## Slide 8: Mechanical design
Frame design
Transmission systems

## Slide 9: Frame design
From CAD design to practice
Materials
Assembly

## Slide 10: Frame design
Withstand effects of - Static loads: weight of machine parts weight of work piece - Dynamic loads Vibrations due to spindle and motors bending of axes and screws
Optimum in dimensions and materials

## Slide 11: From CAD to practice
2D drawings
3D models
Practical models

## Slide 12: Materials
Green MDF (wood)
Galvanized steel

## Slide 13: Assembly
Wood and metal screws
Bolts-and-nuts, and Ellen bolts
Welding

## Slide 15: Transmission systems
Rails
Lead screw
Bearings

## Slide 16: Rails
Y, Z & X rails

## Slide 17: Bearings
Linear guide bearings
Shaft ball bearings

## Slide 18: Rails
Rails used in each Axis :
Specifications | X-axis | Y-axis | Z-axis
Rail type | SBR12 | SBR12 | SBR12
Diameter | 12 mm | 12 mm | 12 mm
Length | 835mm X2 | 575mm X2 | 260mm X2

## Slide 19: Lead screw

## Slide 20: X, Y and Z Motor tuning (screw)
The screws that used in the project is single start that mean :
For X and Y axes :-
Lead () = Pitch = 1.75 mm/rev
steps per millimeter = = 228.57 Steps/mm

## Slide 21: X, Y and Z Motor tuning (screw)
The screws that used in the project is single start that mean :
For Z axis :-
Lead () = Pitch = 1.5 mm/rev
steps per millimeter = = 266.67 Steps/mm

## Slide 22: Electrical part

## Slide 23: Electrical Part
Power
Control

## Slide 24: Power
Power supply units
Electrical protections
Motors

## Slide 25: Power supply units
Switching power supply for stepper motor drivers.

## Slide 26: Electrical protections
Guard against over current
Fuses : Used to prevent over current from destroying the electrical devices. In this project, fuses provide protection for the drivers and the power supply.
Isolate inputs/outputs from controller Opto-couplers : The main function of opto-couplers is to isolate the microcontrollers from the I/O signals

## Slide 27: Electrical protections
Fuses
Opto-isolators

## Slide 28: Motors
AC spindle
Stepper motors

## Slide 29: Spindle specifications

## Slide 30: Stepper motors
What are stepper motors good for?
Good position control : Since steppers move in repeatable steps, Speed control : allow for excellent control of rotational speed for process automation and robotics, by sending a pulses with different frequency.
Low-speed torque : A Stepper motor has maximum torque at low speeds, so they are a good choice for applications requiring low speed.

## Slide 31: Stepper motor specifications
NEMA 23 stepper motors
2-phase
Bipolar connection
Rated current = 2A
Maximum torque = 3N.m
Step angle = 0.9 degrees/step

## Slide 32: Stepper motor drivers

## Slide 33: Hardware control
Limit and home switches

## Slide 34: Hardware control
Emergency switch

## Slide 35: Hardware control
Breakout board

## Slide 36: Software

## Slide 37: CAD Drawing Software
Computer Aided Drawing
It draws the part as a vector image
Saved as DWG

## Slide 38: CAD Software
Computer Aided Manufacturing
It converts the DWG to machine instruction language G-Code
Parameters needed to be optimized is
  Offset
  Speeds

## Slide 39: Control software
It converts the G-Code into Pulse signals through the parallel port

## Slide 40: MACH 3
Flexible
Customizable
Provides Adjustable Acceleration
Can handle with several inputs and feedback

## Slide 41: Conclusion