## Slide 1: Structural Design for International Hotel Building in Nablus
An-Najah National University
Faculty of Engineering
Civil Engineering Department
Graduation Project II
Prepared by :
Abdul-Rahman Sedih
Ihsan Taweel Supervisor:
Yazan Asia Ibrahim Arman

## Slide 2: Outline
          Introduction Preliminary Design
3-D Modeling

## Slide 3: Introduction
Project Description :

## Slide 5
This project is about structural analysis and design for the International Hotel Building which is located in Nablus city - Rafedia , and it rises around 400m above mean sea level (AMSL).
The building is five floors concrete structure.
Floor | Height | Area of Part (m2)
Basement | 5 | 2100
Ground | 5 | 2100
First | 5 | 2100
Second | 5 | 1025
Third | 5 | 650

## Slide 6
American Concrete Institute (ACI 318- 2014).
American Society for Civil Engineering – Minimum Design Loads for Buildings and Other Structures (ASCE 7-2010).
International Building Code (IBC- 2012).
Jordanian Code for Loads and Forces.
Unified Facilities Criteria (UFC).
Codes and Standards

## Slide 7
Computer programs
ETABS
Word and Excel
AutoCAD
SAFE
Computer Programs Used

## Slide 8: Materials Structural Materials:
Property | Value
Compressive strength of concrete, (fʹϲ) | 28 MPa
Modulus of elasticity, (Eϲ) | 24.87×10³ 𝑀𝑝𝑎
Unit weight of plain concrete, 𝜸 | 23 𝑘𝑁/
Unit weight of reinforced concrete, 𝜸 | 25 𝑘𝑁/
Property | Value
Compressive strength of concrete, (fʹϲ) | 28 MPa
Modulus of elasticity, (Eϲ) | 24.87×10³ 𝑀𝑝𝑎
Unit weight of plain concrete, 𝜸 | 
Unit weight of reinforced concrete, 𝜸 | 
Concrete:
Property | Value
Steel Grade | Grade 60
Yield strength (Fy) | 420 𝑀𝑝𝑎
Ultimate strength (Fu) | 620 𝑀𝑝𝑎
Steel:

## Slide 9: Materials Nonstructural Materials:
Material | Unit weight, 𝜸 in KN\m³
Plaster | 23
Tiles | 25
Aggregate, fill | 18
Masonry stone | 26
Brick | 12
Concrete mortar | 23

## Slide 10
Loads
Gravity
Dead
Live
Lateral
Snow
Seismic
Soil
Temperature

## Slide 11
  Slab superimposed dead load= 4.3 KN/m²
  Superimposed dead load of external walls = 4.4 KN/m²
  The maximum value of the live load which was obtained from table 4-1 in ASCE7-10 is 4.8 KN/m², But we used a live load value of 5 KN/m².
  According to Jordanian Code we found the value of snow load equals 1 KN/m².
Gravity Loads Dead Load:
Live Load:
Snow Load:
Temperature Load:
From Jordanian Code the expected value of temperature changes is 25 C˚.

## Slide 12: 2. Site Coefficients and Adjusted Maximum Considered Earthquake (MCEᴿ) Spectral Response Accelerations(SMS & SM1):
1. Mapped Spectral Response Acceleration Parameters:
Ss and S1 parameters were obtained from Spectral Response Acceleration maps from Israeli code to be (Ss=0.6 and S1 = 0.14 ).
Lateral Load Seismic Loads:
By assuming Site Class is B, we obtained values of Fa and Fv from tables 11.4-1 and 11.4-2 in ASCE 7-10 where both coefficients equal 1.
SDs = SMS = = 1 × 0.6 = 0.6
SD1 = SM1 = = 1 × 0.14 = 0.14

## Slide 13: 3. Importance Factor and Risk Category(Ie):
The risk Category was decided to be Ш from table 1.5-1 in ASCE7-10, so the Importance Factor is equal 1.25 according to table 1.5-2 in ASCE7-10.
4. Seismic Design Category:
According to the tables 11.6-1 and 11.6-2 in ASCE7-10, Since the value of SDs= 0.6, and the Risk Category is Ш. So, it’s found that the seismic design category is D.

## Slide 14
From table 12.8-2 below, it’s found that values of Ct and x equals 0.0488 and 0.75, respectively.
Since = 25 m, then T= = 0. 545 sec.
6. Structure Fundamental Period:
Since the Seismic Design Category is D, considering the type of Seismic Force-Resisting System is Building Frame System with Special reinforced concrete shear walls, from table 12.2-1 it’s found that the response modification coefficient (R=6)and overstrength factor (Ωo=2.5) and deflection amplification factor(Cd=5).
5. Design Coefficients and Factors for Seismic Force-Resisting Systems:

## Slide 15
Ɣ = 20 kN/m³
Ø = 35˚
Ko =1-sin (Ø) =1-sin (35) =0.43
the value of the surcharge live load (w) = 12 KN/m²
The figure below shows the total earth pressure on the basement shear wall including seismic earth pressure .
Lateral Loads Soil Load:

## Slide 16: Load Combinations.
Ultimate Load Combinations Service Load Combinations

## Slide 17: Preliminary Design
Notes: Preliminary Design is the first phase of the design process. In this stage of the project a preliminary dimensions was selected in order to build the 3-D model. To check the validity of 3D model, three verification checks will be made which are compatibility, equilibrium and stress-strain relationships. After studying the 3D model and results, a change of these dimensions could be occurred to get the most suitable dimension that will achieve the strength needs.

## Slide 18
The structural system used is two way solid slab
Slab thickness

## Slide 19
The Critical Panels
Panel 1 dimensions
(12.96m x 8.11m)
Panel 2 dimensions
(9.50m*7.90m)

## Slide 21: Beams
Beam | Dimensions (mm)
B1 | 250*500
B2 | 250*600
B3 | 250*800
B4 | 300*600
B5 | 300*800
B6 | 400*800
B7 | 500*1000
B8 | 500*1200
The preliminary sections of beams:

## Slide 23
 | Preliminary Dimensions (mm) | Final Dimensions (mm)
C1 | 500*500 | 500*500
C2 | 500*500 | 600*600
C3 | 500*500 | 800*800
Columns dimensions are shown in table:

## Slide 24
    Columns
By using tributary area method, we found the ultimate load and determine the dimensions of columns.

## Slide 25: Shear Walls
Wall | Thickness (mm)
Wall 1 | 250
Wall 2 | 300

## Slide 26: 3-D Modeling
Structural Modeling in Etabs.

## Slide 27
seismic loading data according to Equivalent Static Method

## Slide 28
Design Load Combinations
Ultimate Load Combinations Service Load Combinations

## Slide 29
Loads Assignments
Temperature Load Assignment Soil Load Assignment

## Slide 30
Response Spectrum Function

## Slide 31
Compatibility Check

## Slide 32
Equilibrium Check

## Slide 33
Seismic analysis method

## Slide 34
Check Base Shear Equilibrium
Cs = 0.125
in X-direction = = 0.1034
in Y-direction = = 0.0863
Difference percentage for Vx = × 100% = 3% → OK.
Difference percentage for Vy = × 100% = 3.1%→ OK

## Slide 35
Checking for Dynamic Response Spectrum Analysis
The scale factor = (𝑔 𝐼)/𝑅 = (9810 × 1.25)/6 = 2043.05
The scale factor in Etabs shall be multiplied by 0.85 = 0.85 = 1.18
The scale factor will become 1.1718 × 2043 = 2410
Percent of dynamic to equivalent base shears after modifying: In X-direction: × 100% =85 %

## Slide 36
Check Period
Displacement values for each story of the structure
By applying Rayleigh equation, T = 0.387 sec.
T in Y-direction from Etabs = 0.339 sec.
The difference between the two values is acceptable.

## Slide 37
Checking Type of Lateral Force Structural System
Percent of base shear in shear walls= = ×100%= 98.5%

## Slide 38
Horizontal Structural Regularity Check
Types 1a (Torsional Irregularity): maximum story drift >1.2 times the average of the story drifts of the two ends of the structure.
1b (Extreme Torsional Irregularity): maximum story drift >1.4 times the average of the story drifts of the two ends of the structure.

## Slide 39
Type 2 (Reentrant Corner Irregularity): Projections of the structure beyond these reentrant corner >15% plan dimension of the structure in the direction considered.
In Y- direction:
The projection beyond the re-entrant corner is = 40% > 15%.
In X- direction:
The projection beyond the re-entrant corner is = 52% > 15%.

## Slide 40: Type 4 (Out-of-plane offset irregularity):Exists when there are discontinuities in a lateral force path (diaphragms)
Type 3 (Diaphragm discontinuity irregularity): floor or roof has a large open area comprising >50 % of the gross enclosed area of the diaphragm
We find from Etabs that the Stiffness ratio in X-direction of story 5 to story 4 = = 0.55 ×100 % =55 % >50%
So, this type of irregularity is existing in this project.

## Slide 41
Vertical Structural Regularity Check
Types 1a (Stiffness – soft story Irregularity):story in which the lateral stiffness is less than 70% of that in the story above or less than 80% of the average stiffness of the three stories above.
Types 1b (Stiffness – Extreme soft story Irregularity):story in which the lateral stiffness is less than 60% of that in the story above or less than 70% of the average stiffness of the three stories above.

## Slide 42: Type 2 (Weight (Mass) Irregularity):effective mass of any story is more than 150 percent of the effective mass of an adjacent story.
The mass ratios of story 4 to story 5 = × 100 % =159 % > 150 %. So, this type of irregularity is existing

## Slide 43: Type 3 (Vertical Geometric Irregularity):horizontal dimension of the seismic force-resisting system in any story is more than 130% of that in an adjacent story.
× 100 % = 212 % > 130 %.

## Slide 44
Direction | X |  |  |  |  | Y |  |  |  | 
Number of Story | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 4 | 5
First Point | 0.527 | 1.177 | 1.698 | 2.101 | 3.464 | 0.439 | 0.941 | 1.336 | 1.997 | 2.304
Mid-Point | 0.588 | 1.436 | 2.283 | 3.036 | 3.579 | 0.522 | 1.122 | 1.581 | 4.205 | 2.420
Last Point | 0.580 | 1.556 | 2.52 | 3.292 | 3.700 | 0.561 | 1.79 | 2.95 | 3.83 | 2.49
Avg(first+second)×2 | 1.107 | 2.733 | 4.21 | 5.393 | 7.164 | 1.00 | 2.73 | 4.28 | 5.83 | 4.80
Rigid/Flexible | rigid | rigid | rigid | rigid | rigid | rigid | rigid | rigid | rigid | rigid
UX, midpoint = 0.588 mm < mm.
UY, midpoint = 0.522 mm < mm.
Type of Diaphragm

## Slide 45
= + +
Load Case | Slab defelction(mm) | Average beams deflections (mm) | Relative deflection* (mm)
D | 12.593 | 2.032 | 10.561
D + L | 20.054 | 3.262 | 16.792
D + 0.25 L | 14.490 | 2.913 | 11.577
Immediate and Long Term Deflection

## Slide 46
Elastic and Plastic Deflections and Story Drift
δx =
The allowable drift is equal to 0.015 hSX
0.0155 = 0.075m
Story No. | Displacement (mm) | Inelastic displacement (mm) | Drift (mm)
1 | 0.624 | 2.496 | 0.4992
2 | 1.566 | 6.264 | 0.7536
3 | 2.59 | 10.36 | 0.8192
4 | 3.884 | 15.536 | 1.0352
5 | 4.584 | 18.336 | 0.56
6 | 5.08 | 20.32 | 0.3968
Story No. |  |  | Drift (mm)
1 | 0.624 | 2.496 | 0.4992
2 | 1.566 | 6.264 | 0.7536
3 | 2.59 | 10.36 | 0.8192
4 | 3.884 | 15.536 | 1.0352
5 | 4.584 | 18.336 | 0.56
6 | 5.08 | 20.32 | 0.3968

## Slide 47
Verification of Structural Design for Beam
Beam | ETABS Result | Area of Steel From ETABS | Hand Cal. For As
Moment | 729.43 | 2039 | 1866.66
Torsion | 53.06 | 2552 | 
Shear | 396.11 |  | 584
Beam | ETABS Result | Area of Steel From ETABS | Hand Cal. For As
Moment | 729.43 | 2039 | 1866.66
Torsion | 53.06 | 2552 | 
Shear | 396.11 |  | 584
ØTth= 0.75

## Slide 48
Verification of Structural Design for Columns
Ultimate Axial Force on C10 = 2740 KN.
ØPn = 0.65x 0.8 ((0.85 x 28 (500x500 – Ast) +Ast 420(= 2740000N
Use Asmin

## Slide 49: Design of Beams
Figure shows the location of B9 that used as a sample in design of beams.

## Slide 50
General Key for reinforcement distribution of simple beams

## Slide 51: Flexural Design for Beams
Figure Shows Area of Longitudinal Reinforcement for B9 in the first floor from Etabs.
Figure Shows Torsional Longitudinal Reinforcement for B9 from Etabs.
Note: For torsional reinforcement, area of steel equals 1044 mm2, the torsional reinforcement shall be distributed along the perimeter of section of beam, in such a way that the torsional reinforcement will be divided into three parts, the first part will be added to (BARS C) and the second part will be added (BARS A) and the last will be put at the middle of the beam (BARS F).

## Slide 52
Area of steel for BARS A = 3283 + 1/3 × 1044 = 3631 mm².
Try 8 Ø 25 mm = 491 x 8 = 3920 mm2.
Area of steel for BARS B = 0, because the amount of reinforcement for the bottom middle of the span is covered by BARS A.
Area of steel for BARS C = 1681 + 1/3 × 1044 = 2029 mm².
Try 7 Ø 20 mm = 314 x 7 = 2198 mm2.
Area of steel for BARS D = 0, because the amount of reinforcement for the top left joint is covered by BARS C.
Area of steel for BARS E = 4517-1681 = 2836 mm2.
Try 4 Ø 32 mm = 804 x 4 = 3216 mm2.
Area of steel for BARS F = 1/3 × 1044 = 348 mm2.
Try 4 Ø 14 mm = 154 x 4 = 616 mm2. (Two layers)

## Slide 53
Length of BARS A, C and F = Ln + SA + SB – 0.08 + 2 (16 db /1000)
Length of BARS B = Ln – (2 Ln / 8) = 3 Ln / 4
Length of BARS D = Ln / 4 + SA – 0.04 + (16 db /1000)
Length of BARS E = Ln / 4 + SB – 0.04 + (16 db /1000)
Seismic Requirements of Longitudinal Bars:
1. All beams have more than two continuous bars at both top and bottom faces. And at any section the reinforcement ratio ρ is less than 0.025
2. Positive moment strength at joint face is not to be less than 1/2 of the negative moment strength provided at the face of the joint.
Figure shows that the ultimate negative moment at the face of joint = 768 KN.m.

## Slide 54
= 0.015
One-half of moment equal 768 x 0.5 = 384 KN.m.
So, the reinforcement ratio (ρ) equal 0.015 / 2 = 0.0075,
But the minimum (ρ) equal ,
The area of steel equal As = 0.01 x 300 x 720 = 2160 mm2 < 3283 mm2 from figure 3.58, OK
3. The negative or positive moment at any section along the member is not to be less than 1/4 the maximum moment strength provided at the face of either joint.
Ultimate negative moment at the face of joint = 768 KN.m.
One-fourth of moment equal 768 x 0.25 = 192 KN.m.
So, the reinforcement ratio (ρ) equal 0.015 /4 = 0.00375,
But the minimum (ρ) equals 4/3 ρ_calc=(4 ×0.00375)/3=0.005,
The area of steel equal As = 0.005 x 300 x 720 = 1080 mm2 <1681 mm2 from figure 3.58, OK

## Slide 55
Shear Design for Beams
- Stirrups Ø 10 mm will be used, with area of steel 78.5 mm2.
For Zone A, S min is:
d/4 = 720 x 0.25 = 180 mm.
6 db = 6 x 20 = 120 mm.
24 ds = 24 x 10 = 240 mm.
150 mm
Use S min = 100 mm
For Zone B, at least S = d/2 = 720/2 = 360 mm, Use S = 350 mm.

## Slide 57
Design of Columns
Seismic Requirements for Columns of Special Moment Frames:

## Slide 58
The required areas for reinforcement for all floors are 4230, 4266, 4295, 4327 and 4399 mm2 in order from the first floor to the fifth floor.
For uniformity issues the required area for reinforcement is the maximum which is equal 4399 mm2, use 12Ø 22 mm.
So, ρ =.
Lap Splice for longitudinal bars shall be extended the value of 1.3 development length:
Ldt =.
Lap splice = 1.3 x 1030 = 1339 mm, use 1.4 m
Distance (Lo­):
Lo = max. of
Assume Lo equal 0.8
Sample Detailing of Column C34

## Slide 59
Transverse Reinforcement
Stirrups of a diameter Ø12 mm will be used for this column.
So = 100 mm.
Note: hx (distance between legs) = 500 – (50+50) = 400 mm, but use hx = 350 mm because by code hx ≤ 350 mm.
Stirrups spacing within the distance Lo, (S1) = min. of
So, S1 = 100 mm.
Stirrups spacing beyond the distance Lo, (S2) = min. of
Use S2 = 100 mm.
equation:

## Slide 60
Design of Tie Beams
Longitudinal Reinforcement
Design strength = KN
But ρ min = 0.00333
As min = 0.00333 x b x d
Where all tie beams has a cross section with b = 600 mm and h = 900 mm.
So, Asmin = 0.00333 × 600 × 820 =1639 mm2.
Use 6Ø20 at top and bottom of the tie beams.
At the middle of the tie beams cross section, skin reinforcement were used at 3 layers (each layer has 2Ø12 as shown in figure).

## Slide 61
Transverse Reinforcement:
The first hoop shall be located at a distance not more than 50 mm from the face of the supporting member. Maximum hoop spacing is not to exceed the smallest of:
(a): d/4.
(b): 6 db, where db is the diameter of the smallest longitudinal bar.
(c): 150 mm
- Stirrups Ø 10 mm will be used, with area of steel 78.5 mm2.
d/4 = 820 x 0.25 = 205 mm.
6 db = 6 x 20 = 120 mm.
150 mm
Use S min = 100 mm
Transverse reinforcement spacing shall not exceed d/2 throughout the length of the beam.
d/2 = 820 / 2 = 410 mm
Use S min = 400 mm

## Slide 62
Design of Slabs
For shear reinforcement, by applying equation 3-12:
Vc = → Vc =
Vc = 145 KN.

## Slide 64
For flexural design in both direction X and Y:
Width of rib (b) = 1000mm.
Effective depth (d):
= 220mm. (for slab of thickness = 250 mm)
So, minimum area of steel (Asmin) for slab of thickness = 250 mm:
= 0.0018 x 200 x 1000 = 396 mm2.
Use 4 Ø 12 mm / 1000mm. ( Asmin = 452 mm2

## Slide 66
Design of Shear Walls
Sample Design and Detailing for Shear Wall (SW1):
- Dimensions of shear wall:
Height per story = 5 m. (this shear wall extends for 3 stories)
Thickness of first floor shear wall (basement) = 0.3 m
Thickness of the second and third floors shear wall = 0.25 m
Length = 10.45 m
Effective depth of shear wall (d) = 0.8 L = 0.8 x 10450 = 8360 mm.
- Internal forces in shear wall in first floor.
Mu (Major) = 2561 KN.m Mu (Minor) = 210 KN.m
Vu = 1955 KN. Pu = 6660 KN.

## Slide 67
For horizontal shear reinforcement:
.
But, S from section 3.5.2.4.1, the maximum spacing for horizontal reinforcement:
Smax=
So, Smax = 450 mm.
For two curtains (layers) of reinforcement with Ø 10 mm.
< 450 mm ⟹ Ok.
Use 2 Ø10 / 200 mm.

## Slide 68
For vertical shear reinforcement:
.
So,
.
The maximum spacing for vertical reinforcement:
Smax=
So, Smax = 450 mm.
For two (layers) of reinforcement with Ø 10 mm.
< 450 mm ⟹ Ok.
Use 2 Ø10 / 200 mm.

## Slide 69
- Concrete shear capacity of the wall as shown:
4915 KN.
2950 KN.
Vu (from Etabs) = 1955 KN
So, Vu < ØVc ⟹ Ok.
As, provided = 5 x 2 x 78.5 = 785 mm2/m ⟹ Ok.

## Slide 70
- Special boundary elements check:
Special boundary elements are needed if the stress σ > 0.2 f'c
σ = 0.2 x 28 = 5.6 Mpa.
To compute stress from equation
σ =
Where:
I: Moment of inertia equal mm4.
C: Equal 0.5 x 10450 = 5225 mm.
So, σ = Mpa < 5.6 Mpa.
So, there is no need for boundary elements.

## Slide 71
Wall pier design:
The dimensions for wall pier are:
Length = 965 mm. Thickness = 300 mm.
Height = 1500 mm. Effective depth (d) = 0.8 x 965 = 772 mm.
Since, Lw / bw = 965 ÷ 300 = 3.2 > 2.5, so the piece can be as pier.
Ultimate shear force (Vu) = 32 KN.
Pu = 232 KN
Capacity of concrete for shear (Vc) = 377 KN.
So, Ø Vc = 0.6 x 377 = 266 KN > 32 KN. ⟹ Ok.
So, As = 0.0025 x 1000 x 300 = 750 mm2/m.
Use 2 Ø 10 mm / 200 mm, in both directions (horizontal and vertical).
So, As, provided = 5 x 2 x 78.5 = 785 mm2 > 750 mm2 ⟹ Ok.

## Slide 73
Design of Footings

## Slide 74
The assumed width of wall footing equal to 3.0 m, and with depth equal to 0.8 m, with effective depth equal 0.7 m.
Allowable bearing capacity of soil 450 KN/m2

## Slide 75
- Design of Single Footing:
P service=4900 KN
Q allowable= 450
Af
The footing is square  B=L=
Use B=L = 3.5 m
Wide beam shear:
= Vu=400(1.5-d)
After solve two equations we found the value of d=0.565 m
Punching shear check:
ϕVc,p=3180 KN<Vu,p→Not O.K→Increse depth of footing
Try d=0.7m

## Slide 76
Design for flexural :
Mu=(W l^2)/2=(400×〖1.5〗^2)/2=450 KN.m
ρ=(0.85 fc)/fy (1-√(1-(2.61 Mu)/(bw d^2 fc))=0.0025
As= ρ b d=1750 〖mm〗^2→4ϕ25/m
As,min=As,shrinkage=0.0018 bh=1440 〖mm〗^2<As→O.K
Use As=1341.13 〖mm〗^2→1ϕ25/250mm
Use

## Slide 77
Design of Stairs
For the first and second stairs:
1) Dimensions of stairs:
They have the following dimensions as shown in the architectural plans in Appendix A:
- Riser: 0.165 m. - Going: 0.30 m. - Landing length: 1.6 m.
- Step width: 1.5 m.
-span length= 1.5m.
- Assume the thickness of slab equal to 0.1m, d= 0.07m.

## Slide 78
2) Loads on stairs:
- Live load: 5 KN/m - Super imposed dead load: 4.4 KN/m.
- Dead load: 0.1 x 25 = 2.5 KN/m.
3) Design of stairs:
Ultimate loads on slab equal (1.2D + 1.6L) = (1.2x (4.4+2.5) + 1.6x(5)) = 16.28 KN/m2.
MU= (W L²)/8= (16.28 ×(1.5)²)/8=4.58 KN.m.
- Longitudinal reinforcement ratio (ρ) from equation:
So, the longitudinal area of steel As = 0.0026 x 1000 x 70 = 182 mm2.
As, Shrinkage = 0.0018 x 100 x 1000 = 180 mm2
To control crack
Smax ≤ 450mm
≤3h
≤250mm
Use 1Ø10 /250mm in each direction .
Vu =