## Slide 1: Structural Analysis and Design of Educational-Cultural Building in Nablus city
Submitted By
Heba Sameer Sabrin Suwan Tala Dwaikat Supervisor
Dr. Munther Diab
An-Najah National University Faculty of Engineering and Information Technology |  | Department of Civil Engineering 2018

## Slide 2: Outline
Project Description.
Materials.
Loads.
Preliminary dimensions of slab, beams and columns.
ETABS modeling and checks.
Dynamic design.
Design of steel Truss.
Design of footing.

## Slide 3: Basement plan

## Slide 4: Ground floor:

## Slide 5: First floor

## Slide 6: Second floor

## Slide 7: Site Plane
Separate blocks to Avoid differential settlement

## Slide 8: Description of the project
Level | Floor No. | Floor height (m) | Area () | Volume ()
Basement floor level | B1 | 4 | 2069 | 8276
Ground floor level | G | 4 | 5504 | 22016
First floor level | 1 | 3 | 5504 | 16512
Second floor level | 2 | 3 | 5504 | 16512
Grand total |  |  | 18581 | 63316
Level | Floor No. | Floor height (m) |  | 
Basement floor level | B1 | 4 | 2069 | 8276
Ground floor level | G | 4 | 5504 | 22016
First floor level | 1 | 3 | 5504 | 16512
Second floor level | 2 | 3 | 5504 | 16512
Grand total |  |  | 18581 | 63316

## Slide 9: Materials *Concrete
*Steel
Yielding strength (Fy) = 420MPa.
Structural Element | Fc’ (MPs) | Concrete Type | Modulus of Elasticity (MPs)
Slab, Beams, columns, Shear walls | 28 | B350 | 24870

## Slide 10: *Soil Properties The bearing capacity of the soil in the region is estimated to be 2.5 Kg/cm2
*Loads
Gravity loads:
Dead Load
Slab own weight = 5 KN/m2
Superimposed load= 3.825 KN/m2
Wall load=24 KN/m.
Live Load
According to ACI 318-14 the value of live load = 5 kN/m2
Lateral loads:
Seismic load

## Slide 11: *Codes and standards:
ACI 318-12
UBC-97
ASCE7-10 code
IBC 2012

## Slide 12: Computer Programs
ETAPS 2016 is used to analyze and design the structural elements (3D).
AutoCAD is used for plans and some detailing.
Sap2019 is used to design 2D truss and footing

## Slide 13: Slab Selection
There are many reasons to use solid slab instead of ribbed slab
1. Ribbed slab is bad in seismic design
2. Ribbed slab is difficult in solving problem of celling after removing formwork
Two way solid slab with drop beam was chosen (t=0.2m)

## Slide 14: Block1 (with slab, beams and columns)

## Slide 15: Slab Thickness *Critical panel

## Slide 16: Slab Thickness
L/B=1.1<2…… Two way solid slab
Thickness of slab=0.2m
I for interior beams = 12.57*10-3
I for exterior beams = 9.87 *10-3
, ,
check for αfm = 3.8>2

## Slide 17: Preliminary Dimensions *Beam
 | Depth(m) | Width(m) bw | Width(m) bf | Description for beam
Beam*1 | 0.7 | 0.6 | 1.7 | L-Section
Beam*2 | 0.6 | 0.55 | 2.7 | T-Section
Beam*3 | 0.6 | 0.5 | - | Rectangular

## Slide 18
Name of column | Depth(mm) | Width(mm)
Interior | 650 | 400
Edge | 600 | 400
Corner | 400 | 400
Preliminary Dimensions *Column

## Slide 19: Block 1 *Checks

## Slide 20: Compatibility Check
Period=0.53<1

## Slide 21: *Equilibrium check
Live load by hand=12840
For live load % of error=0.03%
Deflection from sap <allowable deflection
(Acceptable)
*Deflection check

## Slide 22: Stress Strain Check *Frame in x-Direction
** % of Error =11% >>>> Acceptable

## Slide 23: *Frame in Y-Direction
** % of Error =1.03% >>>> Acceptable

## Slide 24: Block 2
All check are done and acceptable

## Slide 25: Block 3
All check are done and acceptable

## Slide 26: Dynamic analysis for block 1:
Equivalent static method
UBC-97

## Slide 27: Seismic Zone Factor Z
Nablus city……2B
Z=0.2

## Slide 28: Site class

## Slide 29: Risk category

## Slide 30: Seismic Importance Factor I:

## Slide 31: Response Modification Coefficient R

## Slide 32: Seismic coefficient
Ca=0.24
Cv=0.32

## Slide 33: Seismic Load combinations:
a) 1.34D+1.0L+1.0EQx + 0.3EQy
b) 1.34D+ 1.0L -1.0EQx – 0.3EQy
c) 1.34D+1.0L+1.0EQy + 0.3EQx
d) 1.34D+ 1.0L -1.0EQy - 0.3EQx
e) 0.9D+ 0.71 EQx +0.231 EQy
f) 0.9D- 0.71 EQx -0.231EQy
g) 0.9D+ 0.71 EQy +0.231 EQx
h) 0.9D- 0.71EQy -0.231EQx

## Slide 34: Structural Period for block1:
Ta=Ct * hnx
Ta=0.0488 * 19 0.75 =0.45 Sec

## Slide 35: Check for period:
Period from ETABS < Cu × Ta
The period in X direction from SAP ( Tx) =
0.425 second < 1.4× 0.45 =0.63
The period in y direction from SAP ( Ty)=
0.375 second< 1.4× 0.45 =0.63
Check for period …….. Ok

## Slide 36: Drift check:
To eliminate drift and torsion we add shear wall.

## Slide 37: Check for Base Shear reaction:
Wight of structure= D + SD +0.25L
W = 59482.22 KN
V Max. = {(2.5 * Ca * I)/R.} * W.
={(2.5 * 0.24 * 1.25)/5.5.} * 59482.22=8111.2KN
V Min. = (0.11 * Ca * I} * W.
= (0.11 * 0.24 * 1.25} * 59482.22. =1963KN

## Slide 38: Base Shear from ETABS:
Vx=7982.7KN
Vy=7982.7KN
Check for Base shear …OK

## Slide 39: Drift check:
Allowable drift=0.02h
From story 5 the value of drift is
=0.000603<0.02*19=0.38
To eliminate drift and torsion we add shear wall.

## Slide 40: Dynamic analysis for block 2:
Equivalent static method
IBC-2012

## Slide 41: Seismic Zone Factor Z
Z= 0.2
S1 = 1.25*Z= 0.25
Ss= 2.5*Z =0.5

## Slide 42: Site coefficient:
Fa=1.2
Fv =1.55
SDS = Ss *Fa = 0.5*1.2 = 0.6
SD1 = S1 * Fv = 0.25 *1.55 =0.39

## Slide 43: Check for period:
Period from SAP > Cu × Ta
Ta = 0.0466*(19)0.9 =0.66
Ta *Cu=0.66*1.4=
Period from ETABS=1.425
Take 0.66 for calculate base shear

## Slide 44: Check for Base shear:
W = 74601KN
CS minimum of 0.147, 0.15
V = 74601x 0.147= 10966 KN
Base shear from ETABS=10992.5KN

## Slide 45: Drift in X direction:
story Drift in X direction

## Slide 46: Drift in Y direction:
story Drift in Y-direction

## Slide 47: After modification on block 2:
TETABS<Ta*Cu
Period from ETABS=0.649Sec
Base shear by hand=11119KN
Error3% …..OK

## Slide 48: Drift for Block 2 after adding shear wall:
Drift in x-direction Drift in Y-direction
All values of drift less than 0.02hx.............OK

## Slide 49: Dome design:
Dead load (g) = 0.12*25 = 3 kN\m2 , Radius (R) =8.7m , Thickness (T) = 0.12m
Live load (q) =1.5 kN\m2 Φ=75 ͦ ,
For dead load:
N⦶
Nϴ=
For live load:
N⦶ =
Nϴ ==

## Slide 50: Force from ETABS:
Hand calculationNΦ@75 ͦ =-20.9KN/m

## Slide 51: Dome design:
Ultimate load:
NΦmax =1.2*20.9+1.6*10.44=41.8 KN/m
Nθmax=1.2*14+1.6*7=28 KN/m
φPu=φλ(0.85f’c (Ag-As)+FyAs)
=0.65*0.8*0.85*28*1000*120/1000=1485 KN > NΦmax, Nθmax
So, use Asmin=0.003*1000*120=360 mm2/m ……….. 1φ10/200mm

## Slide 52: Truss Design:
In our project we have designed a steel truss 2D(roof) for Theater with dimension(20*20m) tube section for welding connection only
All check are done and acceptable

## Slide 53: Dimension for Bracing:
Tubo 10*10*0.5

## Slide 54: Design of comp. and tension member:
For compression member:
From ETABS…. Pu=543KN
Section type: Tubo100*100*8
r=0.0373 m , Ag=28.8*10-4 m2 ,
From tables we found that
øPn = 556 KN > Pu=543….. ok .

## Slide 55
For tension member:
From ETABS
Section type: Tubo 100*100*5
Design of Ten. Member:
By fraction:-
øFfrac. = øFu (A gross -A hole )*t
øFfrac> so the member is safe for fracture.

## Slide 56: Design of Weld connection:
0.9*8*0.6*248
Lw=126.7mm….use Lw=130mm
Check for size and length of weld……OK

## Slide 57: Design for circular column:
Live load=130KN
Dead load=82KN
Pu=306.5kn
Ag=20211mm2…...D=165mm
Use ρs = 0.018
Use 1 ∅10/70mm

## Slide 58: Designed Beam:
        For Block 1

## Slide 59: Designed column:
        For Block 1

## Slide 60: Design for stairs:
Thickness of flight = 19cm
Load on stair:
*Live = 5 𝑘𝑁/𝑚2
*Superimposed = 2.5𝑘𝑁/𝑚2

## Slide 61: Design for Flight , Landing:
Design for Longitudinal steel
Max M33(Negative) = 3.6 KN.m
→ ρ = 0.0003 <0.0018
Use ρ = 0.0018
→ use 5φ14/m
Design for Transverse steel
𝐴𝑠 𝑠ℎ𝑟𝑖𝑛𝑘𝑎𝑔𝑒 =0.0018×190×1000
=324𝑚𝑚2.
→ Use 1 ∅12/250mm

## Slide 62: Design for footing:
single footing
Area of footing= (PD+PL)/qall
B=3m,l=3.9m
Check punching : d=0.78m…OK

## Slide 63: Design for footing:
Combined Footing
*Col (C5) =C1 (0.6*0.3) *Col (D5) =C2 (0.6*0.3)
PD1=580KN , PD2=670KN
PL1=312KN , PL2=423KN
B=2m, L=5m
d=0.7m, h=0.85m

## Slide 64: Design for footing:
Shear wall footing:

## Slide 65: Footing plan:

## Slide 66
Thank you