## Slide 1
Jenin Cultural Center
Prepared by : Hani Shahateet
Mo’men “ Qasim Suliman “
Qutaiba Ghaneem Mohammed Daghlas
Supervisor : Eng . Nermeen Albarq

## Slide 2: Outline:
Introduction
Architectural Design
Structural Design
Mechanical Design
Safety Design
Environmental Design
Electrical Design
Quantity surveying and cost estimation

## Slide 3: Introduction :
Location:
  - In Jenin City, near ‘Yahya Ayash’ Traffic circle.
At ‘Al-madares‘ street.
The area of the site (3434 m2 ) .

## Slide 4: Architectural Design:
Site plan and Accessibility
The plans
Sections
Elevations

## Slide 5: Site plan:

## Slide 6: Ground floor plan Area : 1185 m2.

## Slide 7: First floor plan Area : 1185 m2.

## Slide 8: Second floor plan Area : 612 m2.

## Slide 9: Sections
Section A-A

## Slide 10: Sections
Section B-B

## Slide 11: Elevations:

## Slide 12: Elevations:

## Slide 13: Elevations:

## Slide 14: Structural Design
Structural Design:
1- Design codes
2- Loads
3- Sap model and checks
4- Structural elements and detailing

## Slide 15: Design Codes:
ACI-318-08 for reinforced concrete design .
UBC-97 for earthquake load computations .
ASCE for load computations

## Slide 16: Loads:
Type of loads | Load
Live load | 5KN/m2
Super imposed | 4KN/m2
Exterior walls | 21KN/m

## Slide 17: Slab system :
- one way ribbed slab (38 cm thickness )

## Slide 18: Sap model:

## Slide 19: Cheeks
1-Compatiblity check
2-deflection cheek .
3-Equlibrume check
4-Stres strain check

## Slide 20: Checks for model : model 1
1. Compatibility check:

## Slide 21: Deflection check:

## Slide 22: 2. Equilibrium check:
load | Manual | E-Tab | %Error
dead | 16450 | 17051 | 3.6%
live | 5700 | 5757 | 1%
S.D | 7182 | 7254 | 1%
Error < 5%
So ok

## Slide 23: 3. Internal Forces Check:
 | Manual | E-Tab | Error%
For beam | 53711444 | 1325 | 8.2%
Slab | 96 | 88 | 8%
column | 5371 | 5370 | 0%

## Slide 24: Seismic Design Response Spectrum
UBC-97
I = 1
Z= 0.2
R= 5.5
Ca= 0.24
Cv= 0.32
T = 0.36 sec
W=23894KN,
Include D.L+S.D+0.25LL

## Slide 25:  Period check
T= 1.4 * 0.36 = 0.51 sec.
The maximum modal period from ETABS is 0.61
therefore the period check is suitable
So ok

## Slide 26: Base Shear check:

## Slide 27: Base Shear check:
the percentage of error was 0 % for X-Direction
the percentage of error was 0 % for X-Direction
less than 5% . So it is OK

## Slide 28: Modal Participating mass ratio check
The 6th mode will satisfy the needed value of 0.9

## Slide 29: Drift Check:
According to UBC 97 Code:
Δ story (elastic) ≤ L story/40 for T≤0.7 Δ story (elastic) ≤ L story/50 for T > 0.7 T=0.25 <0.7 Take the average of the two values
Δelastic = ( 0.001 + 0.4 ) /2 =0.2 mm Δinelastic =0.7*R*Δelastic = 0.77mm < L/40 =4500/40=112.5 mm OK

## Slide 30: Slab Design :
As shrinkage
As, sh = ρmin * b * h
= 0.0018 * 1000 * 380 =684 mm2/m Use 9 Ø 10/1m in both directions
Moment in slab from E-Tab

## Slide 31: Slab design :

## Slide 32: Beams Reinforcement
Main Beam

## Slide 33: Beam Reinforcement

## Slide 34: Beam Reinforcement :
Sec. Beam

## Slide 35: Beam Reinforcement :

## Slide 36: Column Reinforcement

## Slide 37: Wall Reinforcement

## Slide 38: Footing Reinforcement
Single footing

## Slide 39: Footing Reinforcement
Combined footing

## Slide 40: Footing Reinforcement
Wall footing

## Slide 41: Stair

## Slide 42
Building in Design Builder

## Slide 43
Daylight factor in Multipurpose Hall:

## Slide 44
Daylight factor in Library:

## Slide 45
Sun path and shadow on building at 15:00pm

## Slide 46
Thermal Analysis
Total cooling load (KW) = 145 KW In 21/7
Total Heating load (KW) = 130 KW In 21/12

## Slide 47
Materials :
External wall of U = 0.521 W/m2.K

## Slide 48
Internal wall of U = 1.61 W/m2.K

## Slide 49
Roof of U = 0.26 W/m2.K

## Slide 50
Ground Floor of U = 0.814 W/m2.K

## Slide 51
Glass material :
The windows consist of two layers (double glazing) with air gap =6mm
U = 3.159 W/m2.K

## Slide 52: Acoustical Design for Theater
Model in ecotect

## Slide 53: Reverberation Time RT60
The reverberation time for Music room and small theater is 0.8-1.5

## Slide 56: HVAC System(VRF):

## Slide 57: HVAC System(VRF):

## Slide 58: HVAC System(VRF):

## Slide 59: HVAC System(VRF):
Required pipe diameter for library

## Slide 60: HVAC System(VRF):
Required pipe diameter for restaurant

## Slide 61: HVAC System(VRF):
In door unit distribution in restaurant

## Slide 62: HVAC System(VRF):
In door unit distribution in library

## Slide 63: Lighting for theater:

## Slide 64: Lighting for hall:

## Slide 65: Water supply:

## Slide 66: Electrical boilers:

## Slide 67: Drainage design:

## Slide 68: Quantity surveying:
The unit cost of the project is : 2175 NIS
The total cost of the project is : 6483194 NIS