## Slide 1: ETHER: An Adaptive Solar Tracking System
Mohammad Raed & Mohammad Matar
Supervisor: Dr. Suleiman Abu Kharmeh

## Slide 2: Table of contents 01 04 02 05 03
Introduction
Workflow & Implementation
FPGA Kalman Filter
Analysis & Results
Conclusion & Future Work

## Slide 3: Introduction 01

## Slide 4: What is ETHER?
To maximize solar energy capture
Embedded control
IoT monitoring
FPGA-accelerated filtering
ETHER is an intelligent dual-axis solar tracker.

## Slide 5: Project Context & Motivation
Global Need
Rising demand for renewable energy, with solar as a key sustainable source.
Problem
Fixed solar panels capture limited energy; traditional trackers are either simple but noisy, or advanced but impractical.
Goal
Design a high-precision, adaptive solar tracker using a heterogeneous architecture that is both accurate and deployable.

## Slide 6: Why This Matters
Solar trackers can increase energy yield by a high margin compared to fixed panels.
Real-time filtering reduces mechanical wear and improves system lifespan.
Wireless monitoring enables remote operation and performance analytics.
1
2
3

## Slide 7: Key Features
FPGA- Accelerated Kalman Filter
IoT Dashboard with Live Monitoring
Adaptive Dual-Axis Solar Tracking
Fail-Safe & Modular Design
Real-time noise reduction with adaptive spike rejection.
Real-time data visualization & remote control via web/mobile.
Increases energy capture while reducing mechanical wear.
System remains operational even if FPGA or WiFi fails.
1
2
3
4

## Slide 8: Workflow & Implementation 02

## Slide 9: Architecture
ETHER is built on a three-layer architecture:
Arduino Mega 2560 – Sensor & Actuation Layer Handles real-time sensor reading and motor control.
DE1-SoC FPGA – Computation Layer Accelerates the Kalman filter for noise reduction and predictive tracking.
ESP32 – Communication Layer Provides wireless connectivity and a real-time monitoring dashboard.
1
2
3

## Slide 10: Workflow & Implementation
Arduino Workflow
  1) Sensor Reading Reads 4 LDR sensors and Converts analog values to light intensity differences
  2) PID Control Computes azimuth & elevation errors and applies tuned PID gains to generate raw angle commands
  3) Communication A) Sends raw angles to FPGA via UART B) Receives filtered angles back C) Falls back to raw angles if FPGA times out

## Slide 11: Workflow & Implementation
ESP32 Dashboard & IoT Features
Web-Based Interface Hosted on ESP32 as a WiFi Access Point
Real-Time Display Shows raw vs. filtered angles, LDR values, servo positions, power stats
Interactive Controls Manual servo positioning via sliders
Multi-Client Support Accessible from any device with a browser

## Slide 12: Dashboard (Angle Monitoring Screen)

## Slide 13: Dashboard (Sensor Dashboard)

## Slide 14: Dashboard (Manual Control Panel)

## Slide 15: Key Implementation Choices
Modular firmware
Each platform runs independent code, communicating via clean serial protocols
Fail-safe operation System continues tracking even if FPGA or ESP32 fails

## Slide 16: FPGA Kalman Filter 03

## Slide 17: The Problem
LDR sensors provide noisy, unreliable angle data.
A standard microcontroller filtering this data is slow and compromises system responsiveness.
We need real-time, high-speed filtering to provide clean signals to the motor controller.

## Slide 18: The Solution
Implement an Adaptive Scalar Kalman Filter directly in FPGA hardware.
The filter predicts the sun's position and optimally fuses this prediction with new sensor data.

## Slide 19
Top-Level Architecture

## Slide 20
Top-Level Architecture
Our Implementation in FPGA Hardware:
  Dual Kalman Filter Cores
  Kalman-to-Avalon Bridge
  UART Controller
  Avalon-MM Interconnect connecting everything
  PIO Ports enabling processor monitoring

## Slide 21
Top-Level Architecture –cont.
Key Principle: All components communicate via the standard Avalon-MM bus, creating a modular, integrated hardware system where each part has a specialized role.

## Slide 22: The Kalman Filter Module
Core Design: Two independent, parallel filter cores
Key Design Choices:
  Fixed-Point Arithmetic (Q9.7)
  Parallel & Pipelined Execution
  Adaptive Noise Rejection

## Slide 23
The filter's operation is orchestrated by a simple, deterministic state machine in hardware:
  PREDICT
  CALCULATE R
  COMPUTE GAIN
  UPDATE
  OUTPUT
This hardware ASM ensures precise, repeatable timing (29 Cycles), which is critical for stable real-time control.
How it Works: The Filter’s ASM
Notes: PREDICT: (State Prediction) Projects the previous state estimate forward using the system model. For our quasi-static sun, this is . Also, updates the error covariance , where is the process noise, modeling uncertainty from time passing.
CALCULATE R: (Adaptive Measurement Noise) Calculates the innovation ( ) and dynamically scales the measurement noise covariance based on its magnitude. This adaptive step makes the filter robust to outliers.
COMPUTE GAIN: (Kalman Gain Calculation) Computes the optimal weighting factor, the Kalman Gain . This gain dictates how much to trust the prediction vs. the new measurement.
UPDATE: (State Update) Fuses the prediction and measurement: . This yields the new minimum mean-square error (MMSE) state estimate.
OUTPUT: (Covariance Update & Output) Updates the error covariance for the next cycle: . The new optimal estimate is then output to the motor controller.
PREDICT: (State Prediction) Projects the previous state estimate 𝑥_𝑒𝑠𝑡 forward using the system model. For our quasi-static sun, this is 𝑥_𝑝𝑟𝑒𝑑=𝑥_𝑒𝑠𝑡. Also, updates the error covariance 𝑃_𝑝𝑟𝑒𝑑=𝑃_𝑒𝑠𝑡+𝑄, where 𝑄 is the process noise, modeling uncertainty from time passing.
CALCULATE R: (Adaptive Measurement Noise) Calculates the innovation ( 𝑧−𝑥_𝑝𝑟𝑒𝑑 ) and dynamically scales the measurement noise covariance 𝑅 based on its magnitude. This adaptive step makes the filter robust to outliers.
COMPUTE GAIN: (Kalman Gain Calculation) Computes the optimal weighting factor, the Kalman Gain 𝐾=𝑃_𝑝𝑟𝑒𝑑/(𝑃_𝑝𝑟𝑒𝑑+𝑅). This gain dictates how much to trust the prediction vs. the new measurement.
UPDATE: (State Update) Fuses the prediction and measurement: 𝑥_𝑒𝑠𝑡=𝑥_𝑝𝑟𝑒𝑑+𝐾⋅"innovation". This yields the new minimum mean-square error (MMSE) state estimate.
OUTPUT: (Covariance Update & Output) Updates the error covariance for the next cycle: 𝑃_𝑒𝑠𝑡=(1−𝐾)⋅𝑃_𝑝𝑟𝑒𝑑. The new optimal estimate 𝑥_𝑒𝑠𝑡 is then output to the motor controller.

## Slide 24: Data Transfer: The EBAB-Kalman Bridge
Interfaces Kalman filter with Avalon-MM
Polls UART, assembles 4-byte angle data
Triggers Kalman filter and returns results
Handles all bus timing and flow control

## Slide 25: Analysis and Results 04

## Slide 26: Testing Methodology: Kalman Filter Verification
Goal: Prove the filter works correctly under various conditions.
Method: Comprehensive SystemVerilog simulation with 7 realistic test scenarios (5,000 samples each).

## Slide 27: Kalman Verification –cont.
Test Scenarios Include:
  Normal Tracking: With mild noise.
  Noise & Spikes: With severe noise spikes.
  Sudden Changes.

## Slide 28: Normal Incline/Decline

## Slide 29: Noisy Incline/Decline

## Slide 30: Spike Rejection

## Slide 31: Sudden Change Response

## Slide 32: AI Track: RAG Fatawa Chatbot

## Slide 34: Performance Summary

## Slide 35: FPGA Utilization
Logic Elements: 14%
DSP Blocks: 18%
Total block memory: 28%
Available Headroom  FPGA capacity is available for future upgrades

## Slide 36: Conclusion & Future Work 05

## Slide 37: Conclusion
Built a working heterogeneous solar tracker (Arduino, FPGA, ESP32)
FPGA Kalman filter reduced sensor noise by 51-74%
Proved that specialized, heterogeneous architecture works effectively
Created a blueprint for high-performance embedded systems

## Slide 38: Future Work
Self-Optimizing Filter: Use the on-chip ARM processor to dynamically adjust filter parameters.
FPGA Power Optimization: Implement advanced techniques like clock gating, dynamic frequency scaling, and low-duty-cycle operation during stable periods
3. Machine Learning Integration: Enhance existing monitoring capabilities to integrate a machine learning for fault detection and power degradation.

## Slide 39: Thanks
Any questions?