## Slide 1
An-Najah National University
Implementing Lean Six Sigma DMAIC Methodology in AL-Hijaz Chocolate Factory

## Slide 3
About
Us

## Slide 4
About
Sara Masri
Batool Almasri
Nour Al-Asaad
Tuqa Daraghmeh
Us

## Slide 5
Introduction

## Slide 6
Introduction
1
  Established in 2005, ISO 22000 certified
AL-Hijaz Chocolate Factory Overview
PTSD, CPTSD, and Trauma Definitions
Chocolate Production Process
Receiving Raw Material
Cooking & Preparation
Chocolate Fillings
Several Production Lines
Manual Production Line
Packaging
1
2
4
Chocolate Cooking
3
Manual
5
6
One Shot
Dragées
Packaging & Stickering
  6 Production Lines
Dipping

## Slide 7
Introduction
2
Chocolate Production Process
Receiving Raw Material
Cooking & Preparation
Chocolate Fillings
Several Production Lines
One Shot Production Line
Packaging
  Established in 2005, ISO 22000 certified
  Their careful selection of ingredients - cocoa, sugar, cocoa butter, oil, & milk
1
2
4
Chocolate Cooking
3
Manual
5
Dipping
6
One Shot
Dragees
Packaging & Stickering
  6 production lines
AL-Hijaz Chocolate Factory Overview

## Slide 8
Introduction
2
Chocolate Production Process
Receiving Raw Material
Cooking & Preparation
Chocolate Fillings
Several Production Lines
One Shot Production Line
Packaging
  Established in 2005, ISO 22000 certified
  Their careful selection of ingredients - cocoa, sugar, cocoa butter, oil, & milk
1
2
4
Chocolate Cooking
3
Manual
5
Dipping
6
One Shot
Dragees
Packaging & Stickering
  6 production lines
AL-Hijaz Chocolate Factory Overview
One Shot Production Line

## Slide 9
Literature Review

## Slide 10
3
Literature Review
  Lean focuses on eliminating waste (Muda)
  Goal: do more with less
  Lean is widely applied in food manufacturing to improve flow and efficiency
  Setup time is a major source of Waiting and Overprocessing waste
Lean Manufacturing
Six Sigma focuses on reducing variation and defects
Lean Six Sigma combines:
    Speed (Lean)
    Accuracy & Consistency (Six Sigma)
Six Sigma
Kaizen
Kaizen = Continuous, Incremental Improvement
Small changes lead to long-term impact
Supports sustainability of improvements after implementation

## Slide 11
DMAIC Methodology

## Slide 12
4
DMAIC Methodology
Tools Implemented:
Define
Measure
Analyze
Improve
Control
Pareto Chart
Process Flowchart
SIPOC
Data Collection
SOPs
Control Plan
I-MR Chart
Normality Test & Histogram
Project Charter
Fishbone Diagram
SMED
Process Capability Analysis
Scatter Plot

## Slide 13
Results
&
Analysis
5
Define Phase
Setup Time
Period needed to bring a production line from a non-operational state to full running capacity
One Shot Production Line
in HCF
Responsible for crafting several of the factory’s best-selling brands - Gourmet, Revera, Best, and Dragées Avola
Challenges During
Setup Phase
Waiting Time, Long Machine Setup Time, & Electrical Interruptions
Define Phase

## Slide 14
5
Define Phase
Setup Time
Period needed to bring a production line from a non-operational state to full running capacity
One Shot Production Line
in HCF
Responsible for crafting several of the factory’s best-selling brands - Gourmet, Revera, Best, and Dragées Avola
Challenges During
Setup Phase
Waiting Time, Long Machine Setup Time, & Electrical Interruptions
Define Phase
6
Define Phase
________
________
Fishbone Diagram
Project Charter
SIPOC Analysis
Process Flowchart
Define Phase Tools

## Slide 15
6
________
________
Fishbone Diagram
Project Charter
SIPOC Analysis
Process Flowchart
Define Phase Tools
7
Organized smooth workflow
Easy access to materials, minimal delays
One Shot Line:
2 Tempering → KCM → Cooling
Define Phase
Factory Layout
Define Phase

## Slide 16
7
Organized smooth workflow
Easy access to materials, minimal delays
One Shot Line:
2 Tempering → KCM → Cooling
Factory Layout
Define Phase

## Slide 17
8
Part I:
Part II:
Project Sponsor | Al-Hijaz Chocolate Factory (HCF)
Team Leader | Prof. Yahya Saleh
Project Title | Implementing Lean Six Sigma DMAIC Methodology in reducing the setup time in the One Shot production line
Problem Definition & Purpose
The problem is the long time in the setup for a One Shot production line. The goal is to prepare the production line, machines, and ensure that there isn’t any residue from the previous day in order to reduce the possibility of errors, reduce time, and improve efficiency.
Project Charter
Define Phase

## Slide 18
Business Case
The setup process takes about 125 minutes, which is longer than expected every morning to prepare and preheat the machines before production begins. This delay results in workers' idle time. The overprocessing and lack of a standardized preparation procedure led to inefficiency, reduced productivity, and higher operating costs.
Key Player |  | Scope
Sponsor | Eng. Zahra Tamimi | The project focuses on analyzing and reducing the wastes in the One Shot production line.
Team Leader | Dr. Yahya Saleh | 
Team Member | Batool, Nour, Sara, & Tuqa | 
Enablers / Risk Mitigation | Barriers / Risks
Conduct daily meetings with all team members All team members are consistently present and responsive Clear understanding of the work methodology Team members have relevant experience in similar projects Strong awareness and engagement from the team Good knowledge of industry standards and quality requirements | Lack of visits to the process location, which results in inadequate understanding of the process’s implementation Not enough time Difficulty reaching the workplace due to many challenge
Support Estimates
Top management has to recommend what is required and assist us in gathering all the information needed for the improvement process. Also, we need the support and assistance of the Quality Department.
9
Production Processes Description
Raw Material Receipt
Raw Material Inspection
Chocolate Preparation
Filling Preparation
Forming Process
Quality Assurance
Wrapping
Stickering
Packaging
Final Storage for the
Produced Chocolate
10
Define Phase
Define Phase

## Slide 19
Production Processes Description
Raw Material Receipt
Raw Material Inspection
Chocolate Preparation
Filling Preparation
Forming Process
Quality Assurance
Wrapping
Stickering
Packaging
Final Storage for the
Produced Chocolate
10
11
Define Phase
Process Flowchart
Define Phase

## Slide 20
11
Process Flowchart
SIPOC gives a high-level view of chocolate production, linking suppliers, inputs, processes, outputs, and customers to ensure efficiency, quality, and food safety
Define Phase
12
Define Phase
Notes: 17

## Slide 21
SIPOC gives a high-level view of chocolate production, linking suppliers, inputs, processes, outputs, and customers to ensure efficiency, quality, and food safety
12
Measure Phase
13
Die Exchange in KCM
Target: 15 min (rarely achieved)
Overlap: die + chocolate + filling changes
Delays: poor planning / urgent orders / weak coordination
Project Goal: Reduce delays
Machine: 4 dies → 3 nozzles + 1 nuts
Define Phase
Notes: 17

## Slide 22
13
Die Exchange in KCM
Target: 15 min (rarely achieved)
Overlap: die + chocolate + filling changes
Delays: poor planning / urgent orders / weak coordination
Project Goal: Reduce delays
Machine: 4 dies → 3 nozzles + 1 nuts
Reasons for Delays
  Switching filling type (instead of die)
  Ensuring cavities filled correctly
  Poor planning
  Last‑minute production decisions
  Weak coordination between departments
Measure Phase
14
Acceptable
Unacceptable
Measure Phase
Notes: 17

## Slide 23
Reasons for Delays
  Switching filling type (instead of die)
  Ensuring cavities filled correctly
  Poor planning
  Last‑minute production decisions
  Weak coordination between departments
14
Acceptable
Unacceptable
Chocolate Change & Impact on Die Exchange
Switching between chocolate colors (Dark ⇒ Milk)
Switching between chocolate types (Compound ⇒ Real)
Affects Taste
Affects Color
Affects Product Conformity
Process can extend to 30+ minutes
Measure Phase
15
Major Contributor to Long Changeover
Required Actions to Prevent Quality Issues
Cleaning
Mold Scraping
Removal of Contaminated Chocolate
Temperature Readjustment
Problem: Color Contamination
Impact on Die Exchange
Measure Phase
Notes: 17

## Slide 24
Chocolate Change & Impact on Die Exchange
Switching between chocolate colors (Dark ⇒ Milk)
Switching between chocolate types (Compound ⇒ Real)
Affects Taste
Affects Color
Affects Product Conformity
Process can extend to 30+ minutes
15
Major Contributor to Long Changeover
Required Actions to Prevent Quality Issues
Cleaning
Mold Scraping
Removal of Contaminated Chocolate
Temperature Readjustment
Problem: Color Contamination
Impact on Die Exchange
Monitoring Machine Downtime on the KCM Machine
Measure Phase
16
  The One Shot production line was monitored over 22 operational days
Daily Machine Downtime Summary
(Production Quantity: 600 units, 3 Workers)
Daily Machine Downtime Summary
(Production Quantity: 2364 units, 3 Workers)
Total Downtime = 137 min
Total Setup Time = 87 min
Total Changeovers = 2 times
Total Downtime = 163 min
Total Setup Time = 120 min
Total Changeovers = 1 time
Measure Phase
Notes: 17

## Slide 25
Monitoring Machine Downtime on the KCM Machine
16
  The One Shot production line was monitored over 22 operational days
Daily Machine Downtime Summary
(Production Quantity: 600 units, 3 Workers)
Daily Machine Downtime Summary
(Production Quantity: 2364 units, 3 Workers)
Total Downtime = 137 min
Total Setup Time = 87 min
Total Changeovers = 2 times
Total Downtime = 163 min
Total Setup Time = 120 min
Total Changeovers = 1 time
Root Causes of Long Setup Time
Measure Phase
17
Measure Phase
Notes: 17

## Slide 26
Root Causes of Long Setup Time
17
Pareto Chart
Measure Phase
18
Pareto chart shows that most setup-time waste comes from a few major causes. Changes in production planning, Machine Changeover Time, Product Non-conformity, & Machine Malfunctions together account for about 73% of wasted time.
Measure Phase
Notes: 17

## Slide 27
Pareto Chart
18
Pareto chart shows that most setup-time waste comes from a few major causes. Changes in production planning, Machine Changeover Time, Product Non-conformity, & Machine Malfunctions together account for about 73% of wasted time.
Normality test results show that the setup time data are normally distributed (p-value = 0.286 > 0.05). The histogram indicates setup times ranging from 80 to 200 minutes with noticeable variability, highlighting inconsistency in the process.
Normality Assessment of Setup Time
Measure Phase
19
Measure Phase
Notes: 17

## Slide 28
Normality test results show that the setup time data are normally distributed (p-value = 0.286 > 0.05). The histogram indicates setup times ranging from 80 to 200 minutes with noticeable variability, highlighting inconsistency in the process.
Normality Assessment of Setup Time
19
Measure Phase

## Slide 29
The scatter plot shows a positive relationship between changeover frequency and setup time, where more changeovers lead to longer setup times and reduce One Shot Line efficiency.
Scatter Plot
20
Measure Phase

## Slide 30
I-MR Chart
The I-MR chart shows high variability in setup time, with several points near the UCL (223 minutes)
Large MR spikes at observations 9-11 indicate significant process instability
The wide control limits (LCL = 37.4, UCL = 223) confirm that the setup process is not in control and requires improvement
21
Analyze Phase

## Slide 31
1
1
1
1
1
1
V
1
V
Process Capability Analysis
Setup time ranged from 83 to 190 minutes
Process Capability Analysis performed with USL = 150 minutes
Process mean is approximately 130 minutes
Capability indices are low (Cp = 0.81, Cpk = 0.21)
The process is not capable of consistently meeting the specification limit and needs improvement
22
Improve Phase
SMED Analysis
Observe the Process
Review steps with all teams
Externalize Changeover Steps
Streamline Internal Steps
Standardize Steps to reduce errors
23
Analyze Phase

## Slide 32
SMED Analysis
Observe the Process
Review steps with all teams
Externalize Changeover Steps
Streamline Internal Steps
Standardize Steps to reduce errors
23
Improve Phase

## Slide 33
Step | Activity | Type | Time (min)
1 | Turn off KCM | Internal | 0.5
2 | Loosen & remove bolt (quick-release) of die | Internal | 1
3 | Lower & remove old die | Internal | 1.5
4 | Move old die aside to its assigned position through transport carts | Internal | 1.5
5 | A worker ensures that the required pistons used matches the die as specified in the die report | External with 4 | —
6 | Bringing the next die from the oven through carts, aligning it carefully, & inserting it in the KCM | Internal | 2.5
7 | Tighten bolts on new die | Internal | 2
8 | Clean chocolate & filling nozzles to ensure proper flow | Internal | 2
9 | Unclog & clean any blocked nozzle cavities | Internal | 1
10 | Cast a sample mold & inspect it for defects before production | Internal | 3
Total |  |  | 15 min
Current Die Exchange Activities & Time Breakdown (Before SMED)
24

## Slide 34
Step | Activity | Type After | Time (min)
1 | Turn off KCM | Internal | 0.5
2 | Loosen & remove bolt (quick-release) of die | Internal | 1
3 | Lowering & removing old die | External | —
4 | Old die transported by helper after restart | External | —
5 | Staging the new die near the machine beforehand | External | —
6 | Align & insert new die using marked pins | Internal | 2.5
7 | Tighten bolts & alignment verification | Internal | 1.5
8 | Clean chocolate & filling nozzles to ensure proper flow | Internal | 2
9 | Unclog & clean any blocked nozzle cavities | External | —
10 | Cast a sample mold & inspect it for defects before production | Internal | 2.5
Total |  |  | 10 min
Improved Die Exchange Activities & Time Breakdown (After SMED)
25
SMED Applied
Improve Phase
1. Converted to External
2. Internal Steps Improved (still internal but faster)
Tasks | Expected Saving
Lower & remove old die | 1.5 min
Transporting old die to storage after machine restarts by helper | 1.5 min
Preheating/cleaning nozzle cavities before die change | 1 min
Internal Steps | Before | After | Saving
Turn off KCM | 0.5 | 0.5 | —
Loosening & removing (quick-release) bolts | 1 | 1 | —
Align & insert new die | 2.5 | 2.5 | —
Cleaning chocolate & fillings nozzles | 2 | 2 | —
Tightening bolts | 2 | 1.5 | 0.5 min
Trial cast mold (standardized once) | 3 | 2.5 | 0.5 min
26

## Slide 35
SMED Applied
1. Converted to External
2. Internal Steps Improved (still internal but faster)
Tasks | Expected Saving
Lower & remove old die | 1.5 min
Transporting old die to storage after machine restarts by helper | 1.5 min
Preheating/cleaning nozzle cavities before die change | 1 min
Internal Steps | Before | After | Saving
Turn off KCM | 0.5 | 0.5 | —
Loosening & removing (quick-release) bolts | 1 | 1 | —
Align & insert new die | 2.5 | 2.5 | —
Cleaning chocolate & fillings nozzles | 2 | 2 | —
Tightening bolts | 2 | 1.5 | 0.5 min
Trial cast mold (standardized once) | 3 | 2.5 | 0.5 min
26
Improve Phase
Machine Downtime Development
Providing Raw Material & Work Instructions
Future Developments
Develop SOPs for the Production Line
Improve Phase
27
Improve Phase

## Slide 36
Improve Phase
Machine Downtime Development
Providing Raw Material & Work Instructions
Future Developments
Develop SOPs for the Production Line
27
Control Plan for Monitoring Setup Time
To maintain performance monitoring of the One-Shot line
To document common setup times, changes in setup times, and any potential problems in the setup process
Operators will write the setup times and changeovers daily, shift supervisors will authenticate the documents, and the system will be in control
Control Phase
28
Improve Phase

## Slide 37
Control Plan for Monitoring Setup Time
To maintain performance monitoring of the One-Shot line
To document common setup times, changes in setup times, and any potential problems in the setup process
Operators will write the setup times and changeovers daily, shift supervisors will authenticate the documents, and the system will be in control
28
Control Phase

## Slide 38
Recommendations
&
Conclusion
Through the use of structured root-cause tools - such as Pareto analysis, I-MR charts, & Process Capability studies - the sources of loss became clearer, enabling more precise and effective improvement intervention
The introduction of standardized procedures (SOPs), SMED techniques, & Improved Workflow Organization successfully eliminated non-value-added internal activities and accelerated setup progression
Integrating Lean Six Sigma into chocolate manufacturing environments can substantially enhance productivity, reduce waste, and strengthen operational reliability
Conclusion
29

## Slide 39
Through the use of structured root-cause tools - such as Pareto analysis, I-MR charts, & Process Capability studies - the sources of loss became clearer, enabling more precise and effective improvement intervention
The introduction of standardized procedures (SOPs), SMED techniques, & Improved Workflow Organization successfully eliminated non-value-added internal activities and accelerated setup progression
Integrating Lean Six Sigma into chocolate manufacturing environments can substantially enhance productivity, reduce waste, and strengthen operational reliability
Conclusion
29
1
Strengthening Standardization & Documentation
2
Implementing Continuous SMED Development
3
Improving Production Scheduling & Communication
4
Enhancing Worker Training & Skill Utilization
5
Keeping the Process Applying Control Charts
Recommendation
30

## Slide 40
1
Strengthening Standardization & Documentation
2
Implementing Continuous SMED Development
3
Improving Production Scheduling & Communication
4
Enhancing Worker Training & Skill Utilization
5
Keeping the Process Applying Control Charts
Recommendation
30
Thank You !!

## Slide 41
Thank You !!