## Slide 1
Analysis and Design of Steel Structure Vertical Farm
(Green Sky)
Prepared by:
Khansaa Rawajbeh
Riham Jawabreh
Sandy Sabbarini
Supervisor:
Dr.Mohammad samaneh

## Slide 2
Why we choose this idea? Agriculture Future? ??

## Slide 3
2050
+ +

## Slide 4
Simple Equation (Green Revolution) =Take the forest to new heights

## Slide 5
Vertical Farm
Vertical Harvesting
Growing UP

## Slide 6
Combination of :
Biotechnology + Engineering + Data Science
+ +

## Slide 7
What plants need to grow?
water
oxygen
sunlight
Plant growth
By Carefully Controlling the environment Leads To
Extend the Growing Season .

## Slide 8
Production capacity rate 1m2 = 0.5 acres

## Slide 9
produce 20 tons of vegetables every day

## Slide 10
Rain water is collected and then reused it.
Theses gardens use up to 2/3 less water.
water

## Slide 11
Introduction:
1.1. Project Description.
Location
It is located at east of Nablus Wadi Al-Tuffah . It’s extended over an area 1000 meter square . It consists of two parts of structure one of them have an area of 600 meter square
Stories and usage
7 floors
Stories |  | Function | Area(m2) | Height(m)
1 | Ground floor | Mainly: offices and storage | 600 | 4
2-7 | Agricultural floors | Agriculture containers (50*80 cm) for crops growing | 600 | 3

## Slide 12
6
5
4
3
2
1
Used the same area of the land 6 times ,so increase the productivity not just 6 times but more
How to solve the problem?

## Slide 13
Romainville, Paris

## Slide 15
The space inside the building helps to enter the sunlight and reach all plants.
sunlight

## Slide 16
The space inside the building in helps in ventilation process.
Ventilation(oxygen)

## Slide 17
Due to ideal growing conditions, plants mature 25% faster and produce 30% more product

## Slide 18
Materials used:
A36 STEEL
Tensile Strength, Yield | 250 MPa

## Slide 19
Polycarbonate Sheets
They are transparent panels made of distinguished and strong imported materials, which are light, strong, durable and flexible compared to glass
Its advantages:
-stability of the color degree
-It is characterized by high light transmittance up to 90%.
-Resistant to mechanical stress
- Lightweight material
- Easy constructed

## Slide 20
glass
Glass curtain walls are lightweight aluminum-framed facades housing glass or metal panels.
gravity loads and wind resistance
thickness equals 10 mm

## Slide 21
compost soil
light
high quality of the soil
raising production
contain a lot of organic fertilizer
plants to grow well

## Slide 22
steel mesh
Steel Floor Grating with (6 mm) bar thickness
    high strength
    Light structure

## Slide 23
(KN/M) | Type of load
1.25 | SD
2.5 1 | LIVE GLSS
Loads in SAP

## Slide 24
Members Group: | Section type | Dimensions
Columns | H- beam | HEA220
Main Beam | I-Beam | IPE 270
Secondary Beam | I-Beam | IPE 180
Rafter Beam | I-Beam | IPE 270
Purlins | TUPE | 120Tubo
XZ Bracing | 2L-Double Angle | 2L 80×60×7×8
YZ Bracing | 2L-Double Angle | 2L 60×40×60/20
1st Floor Bracing | 2L-Double Angle | 2L 100×50×10/30
Steel Sections shown in shop drawings.:

## Slide 25
1
2
3
Compatibility check
Equilibrium check
Internal force check
Verification of the model
2.3.Structural design

## Slide 26
Verification of the model
2.3.1.Compatibility check :
From the figure, it is clear that the component of the structure looks compatible with each other.

## Slide 27
Verification of the model
2.3.2:Equilibrium check:
Type of loads Calculations | SD ( KN) | Live load (KN) | Snow load (KN)
Manual calculations | 4002 KN | 6728.5 KN | 1468.8
SAP |  | KN | 
% Difference | 2.26 % OK | 0.28% OK | 0.01% OK
Type of loads Calculations | SD ( KN) | Live load (KN) | Snow load (KN)
Manual calculations | 4002 KN | 6728.5 KN | 1468.8
SAP |  |  | 
% Difference | 2.26 % OK | 0.28% OK | 0.01% OK
Summarize the results For gravity loads :-

## Slide 28
Verification of the model
2.3.2:Equilibrium check:
For Lateral loads (Wind Load)
Max difference = *100% = *100% = 0.09%
3

## Slide 29
Verification of the model
2.3.3. Verification of Internal Forces
2.3.3.1.Stress – Strain check:
Purlins Length = 5 m
Distributed loads on purlins = 0.85 X 0.7 = 0.595 KN/m.
Live load = 0.7
The check will be done on purlins by using live loads only.

## Slide 30
2.4:Deflection Check:
:
Steel deflection limit:
Service (D+L+SD) deflection=
Service (D+L+SD) deflection= 𝐿/120
Snow load deflection =
Snow load deflection = 𝐿/180
Live load deflection =
Live load deflection = L/180
Steel deflection limit:
Verification of the model

## Slide 31
Deflection Check
the allowable deflection for (snow) = From IBC 2012 code Δallowable= 𝐿 /180 = 5/180 = 0.027 m = 27.78 mm
= Max Snow deflection from SAP = 17.66 mm < 27.78 mm (OK)
the allowable deflection for (Wind)
. From IBC 2012 code Δallowable= 𝐿 /180 = 6.8/180 = 0.037 m = 37.78 mm
Max Wind deflection from SAP = 28.8 mm < 37.78 mm (OK)
1
2

## Slide 32
Deflection Check
1
2
Service (D+L) deflection
From IBC 2012 code Δallowable = 𝐿/120 = 5/120 = 0.042 m = 41.66 mm
Max deflection from SAP = 6.47mm < 41.66 mm (OK)

## Slide 33
Member Design
Design of Secondary Beam :
.
.
.
.
.
.
.
.Iy = 101×104 mm

## Slide 34
Member Design
Design of Secondary Beam:

## Slide 35
Buckling:
The buckling force =
ØFcr = Ø * * Fy=
0.9** 240= 208 MPa
ØPn = ØFcr * Ag= 208*6430 =1337.44 kN
From SAP:
ØPn = 1194.5 kN.
Maximum load(Sap) = 328 kN.
1337.44 kN > 328 kN  Ok

## Slide 36
connections

## Slide 37
Two Rafters Connection (Apex ):

## Slide 38
Rafter-Column connection

## Slide 39
Sec-Main Beam Connection:

## Slide 40
Beam-column Connection:

## Slide 41
Beam-Column Connection hand Checks: loads in beam are: 1-moment 2-shear

## Slide 42
Assumptions:
Use 8Ø22 of A325 bolts.
Use an (E80) weld only on all member sides of (8.00 mm) thickness.
Use an (12.00 mm) steel plate of grade A36.

## Slide 43
IDEA STATICA Results

## Slide 45
Checks For the bolts: first due to moment loads:

## Slide 47
Second due to shear loads:

## Slide 48
Base plate connection
the following assumptions are made for this connection on IDEA Statica
Use 4Ø16 bolts.
.Use a (16 mm) steel plate of grade A36
.Use an (E60) weld only on the flange sides of (8.00 mm) thickness.
Use a vertical bolt spacing of (140.00 mm).
Use a horizontal bolt spacing of (90.00 mm).
Use a vertical distance between the plate edge and the bolt of (165.00 mm).
Use a horizontal distance between the plate edge and the bolt of (190.00 mm).
Use a horizontal distance between the section flange and the bolts of (60.00 mm).
Use plate dimensions of (470.00x470.00 mm).

## Slide 50
Assume Ø16 diameter For the bolts:
Shear check 115 KN < 247.5 KN
Ok
For the weld:
<
Ok
For the plate :
bearing check:
Ok
, tear-out check:
Ok Area check :
Ok

## Slide 51
Base plate Details

## Slide 52
Footing Dimensions
Maximum service reaction = 299KN
=
checking the one-way shear:
:checking The ultimate two-way shear checking

## Slide 53
Flexural Design of Footing
=