## Slide 1
An-Najah National University
Faculty of Engineering & Information Technology
Building Engineering Department
Graduation Project - II (10611591)
Redesign of Nablus Municipality Building
Prepared by group members:
Maram Ghannam
Shahd Hasan Ali
Shahd Qashoo’
Under the supervision of:
Dr. Mutasim Baba’
Presented in partial fulfillment of the requirements for Bachelor degree in Building Engineering
2021

## Slide 2: Outlines Introduction 01 Architectural Design 02 Structural Design 03 Environmental Design 04
05
06
Electro-Mechanical Design
Quantity surveying & Cost Estimate

## Slide 3: 01: Introduction
The building has been analyzed and designed from all architectural, structural, environmental, electrical and mechanical aspects, as will be explained in the following sections.

## Slide 4
Architectural Design
02

## Slide 5: 3D-Southern view

## Slide 6: 3D-Westren view

## Slide 7: 3D-North-East view

## Slide 8
Sections
Section A-A
Section B-B

## Slide 9
Elevations
South elevation
North elevation

## Slide 10
Elevations
West elevation
East elevation

## Slide 11: 03: Environmental Design
Shading analysis
Energy efficiency
Thermal analysis
Cooling & Heating analysis

## Slide 12: Energy Efficiency Strategies
Thermal insulation
Effective shading
Thermal mass

## Slide 13: Solutions Used in the Building West & East South
Vertical louvers
Horizontal shutters

## Slide 14: Shading System

## Slide 15: Shading System

## Slide 16: Shading System

## Slide 17: Thermal insulation U-value for Building Envelope
Component | U-Value (w/m2.K)
External walls | 0.384
Internal walls | 2.585
External floor | 0.453
Internal floor | 1.471
Roof | 0.389
Windows properties | 1.689

## Slide 18: Thermal Design Energy density
 | Total energy [kW/h] | Energy per total building area [kWh/m2] | Energy per conditioned building area [kWh/m2]
Total site energy | 417022.53 | 126.13 | 126.13
Net site energy | 417022.53 | 126.13 | 126.13
Total source energy | 1320710.35 | 399.45 | 399.45
Net source energy | 1320710.35 | 399.45 | 399.45

## Slide 19
Cooling & Heating Analysis

## Slide 20: Thermal Design Comfort set point not met Summery
`` | Facility [Hours]
Time set point not met during occupied heating | 1.83
Time set point not met during occupied cooling | 30.83
Time not comfortable based on simple ASHRAE 55-2004 | 354.83

## Slide 21: Thermal Design Comfort PMV index figure

## Slide 22: 04: Structural Design

## Slide 23: Code Design and analysis of the building is done according to ACI 318-14 Code. Materials - Concrete f´c = 28 Mpa for shear walls and columns specific weight of Reinforced concrete (Ɣ) = 25 KN/m³ - Steel The modulus of elasticity, Es = 200 GPa Yield strength fy = 420 Mpa. - Blocks Unit weight of blocks is considered as 12 kN/m3
General Structural Information

## Slide 24
Loads
Superimposed dead load = 4 KN/m²
Weight of Masonry wall = 21 KN/m
Live Load= 4.8 KN/m²
General Structural Information

## Slide 25
Structural analysis
Structural layout

## Slide 26: Seismic Load Analysis
Seismic code: UBC-97
Assumptions:
Seismic zone 0.20 (Nablus city)
Seismic importance factor I = 1.
Soil profile type : SB (rock)
Force reduction factor = 5.5.
Velocity dependent seismic coefficient Ca = 0.2 5)
Acceleration dependent seismic coefficient Cv = 0.2
Response spectrum scale factor = 1783.6

## Slide 27: Structural & Seismic Checks
Equilibrium check
Compatibility check
Deflection check
Stress strain check
Drift check
Mass participation ratio check
Base shear check
All checks were OK

## Slide 28: Design Elements

## Slide 29: Slab Design

## Slide 30: Slab Design

## Slide 31: Slab Design

## Slide 32: Columns Design

## Slide 33: Beams Design

## Slide 34: Footing Design
Footing Distribution

## Slide 35: Footing Design

## Slide 36: Footing Design

## Slide 37: Stair Design

## Slide 38
05: Electro-Mechanical Design

## Slide 39
Lighting Design
Lighting for first floor plan

## Slide 40
Lighting Design
Meeting Room & Auditoria

## Slide 41
Lighting Design
Office & Bathroom

## Slide 42
Lighting Design
Service Hall & Parking

## Slide 43
Lighting Design
Illuminance, Glare & Uniformity
Area | Recommended illuminance (Lux) | Design illuminance (lux)
Auditoria | 500 | 511
Meeting Room | 500 | 514
Office | 500 | 520
Bathroom | 200 | 217
Parking | 75 | 75.1
Area | Standard | Simulation Result
Auditoria | ≤19 | 18.2
Meeting Room | ≤19 | 18.1
Office | ≤19 | 13.2
Bathroom | ≤10 | 10
Area | Standard | Simulation Result
Auditoria | 0.33 | 0.2
Meeting Room | 0.6 | 0.4
Bathroom | 0.4 | 0.4
Service Hall Lighting | 0.3 | 0.1

## Slide 44
Power for first floor plan

## Slide 45: Water supply system
Total water consumption for building is: 8.208 m3.
Fixture unit
Fourth floor | Third floor | Second floor | First floor | Ground floor | floor
53 | 53 | 53 | 53 | 53 | Zone 1
- | 28 | 28 | 28 | 28 | Zone 2
53 | 81 | 81 | 81 | 81 | 
Total Fu in building = 377 |  |  |  |  | 

## Slide 46: Water supply system
Total losses zone 1
 | G.F |  | 1st.F |  | 2nd.F |  | 3rd.F |  | 4th.F | 
Pipe | Dim (inch) | Pressure loss (psi) | Dim (inch) | Pressure loss (psi) | Dim (inch) | Pressure loss (psi) | Dim (inch) | Pressure loss (psi) | Dim (inch) | Pressure loss (psi)
Vertical | 1.5 | 6.27 | 1.5 | 6.27 | 1.5 | 6.27 | 1.5 | 6.27 | 1.5 | 6.27
Horizontal | 1 | 1.02 | 1 | 1.02 | 1 | 1.02 | 1 | 1.02 | 1 | 1.02
Branch | 0.75 | 3.2 | 0.75 | 3.2 | 0.75 | 3.2 | 0.75 | 3.2 | 0.75 | 3.2
Total losses (psi) | 10.49 |  | 10.49 |  | 10.49 |  | 10.49 |  | 10.49 | 

## Slide 47: Water supply system
Total losses zone 2
 | G.F |  | 1st.F |  | 2nd.F |  | 3rd.F |  | 4th.F | 
Pipe | Dim (inch) | Pressure loss (psi) | Dim (inch) | Pressure loss (psi) | Dim (inch) | Pressure loss (psi) | Dim (inch) | Pressure loss (psi) | Dim (inch) | Pressure loss (psi)
Vertical | 1.5 | 2.74 | 1.5 | 2.74 | 1.5 | 2.74 | 1.5 | 2.74 | 1.5 | 2.74
Horizontal | 1 | 2.91 | 1 | 2.91 | 1 | 2.91 | 1 | 2.91 | 1 | 2.91
Branch | 0.75 | 1.34 | 0.75 | 1.34 | 0.75 | 1.34 | 0.75 | 1.34 | 0.75 | 1.34
Total losses (psi) | 6.99 |  | 6.99 |  | 6.99 |  | 6.99 |  | 6.99 | 

## Slide 48: Water supply system For Zone1

## Slide 49: Water supply system For Zone2

## Slide 50: Drainage system
Type of Pipe | Slope | Diameter | Pipe
PVC | Vertical | 4” | Vent
PVC | 1 % | 4” | Drainage
PVC | Vertical | 4” | Stack
PVC | 2 % | 2” | Sewer
PVC | 1 % | 6” | Drainage between manholes
Drainage system diameters

## Slide 51
Manholes plan

## Slide 52
Manholes plan

## Slide 53
Rain water plan

## Slide 54
The firefighting systems that we used
sprinkler suppression system fire extinguisher(CO2) Hose station (auxiliary system)

## Slide 55
Firefighting systems

## Slide 56: HVAC Design
Total cooling capacity is 259 kW
Total Heating capacity is 135 kW
System used is VRF(variable refrigerant flow)

## Slide 57: HVAC Design Units Used
Diffuser
Split unit
Exhausting Unit
Fan coil Unit
Outdoor Unit

## Slide 58: HVAC Design (VRF) 3rd floor plan

## Slide 59: Elevators System Design
Required number of elevators = 4 elevators
Car capacity = 3500 lb. (19 person)
Car speed = 400 fpm (2m/min)

## Slide 60
06: Quantity Surveying
Group | Total cost (NIS) | Unit cost (NIS/m2)
Structure | 14857198 | 1600
Finishing | 1125397 | 125
Mechanical | 632775 | 70
Electrical | 715867 | 80
Total | 17331237 | 1875

## Slide 61
Thank You for Listening