## Slide 1: Rick
Presented by: Ameen Kharma
Sohaib Shayeb
Supervisor: Dr.Luai Malhis

## Slide 2: Outline
What is Rick.
Motivation.
How does it work.
Technical choices.
Methods & Techniques.
Constraints.
Future work.

## Slide 3: What is Rick ?
Rick is a robot that helps people in their jobs by carrying their tools.
It can respond to their voice commands to give them a specific item.
Move wherever they desire by just moving their wrist.

## Slide 4: Motivation
People tend to use more technology in order to save time and effort.
Craftsman or carpenter uses much equipment frequently every day.

## Slide 5: How does it work?
By moving your hand you can move the robot.
The robot avoids colliding with obstacles while moving.
The robot carries the tools in a packet of 5 rooms.
It handles the tools to the user by responding to his voice commands.
The user has the option to use the mobile app to move the robot and for tools selection.

## Slide 6: Technical choices
Reading the hand movements:
  Accelerometer sensor.
Moving the wheels:
  DC Motors.
  Dual H-Bridge
Obstacles avoidance:
  IR sensors.

## Slide 7
Moving the tools packet:
  Stepper motor.
Send the hand movements signs (transmitter):
  Arduino Nano.
Data Receiver:
  Arduino Mega.
Send data from the transmitter to the receiver:
  HC-12 wireless serial port communication module.
Bluetooth module.

## Slide 8
Reading Hand Movements:
Accelerometer sensor:
Control the movement of the robot.
It will detect the movement of the user’s wrist, then send the right command to the robot to move in the applied direction.

## Slide 9
Moving the wheels:
DC-motor:
  Two DC motors to move the wheels of the robot.
  The direction of movement will be determined by detecting the movement of the user’s wrist by using the accelerometer sensor.

## Slide 10
Dual H-Bridge:
  Two DC motors to move the wheels of the robot.
  The direction of movement will be determined by detecting the movement of the user’s wrist by using the accelerometer sensor.

## Slide 11
Obstacles avoidance
  Sharp IR Sensors:
  Sense certain characteristics of its surroundings.
  Locates in the both sides of the robot, so that it can avoid hitting with walls or random obstacles.

## Slide 12
Moving the tools Packet
  Stepper Motor:
  Divides a full rotation into a number of equal steps. Its position can then be commanded to move and hold at one of these steps.

## Slide 13
Send the hand movements signs (transmitter):
Arduino Nano:
  Send the user’s command “Hand signs” from the accelerometer Sensor to the Arduino Mega.

## Slide 14
Data Receiver:
  Arduino Mega:
  Data from Arduino Nano, Mobile Bluetooth and the IR sensors will be stored in the serial port of the Arduino Mega.

## Slide 15
Send data from transmitter to receiver:
  HC-12 wireless serial port
  communication module:
Send the accelerometer data from the Arduino Nano to Arduino Mega in order to make the robot perform the right movement.

## Slide 16
Bluetooth module:
  Connected to UART of Arduino Mega.
  To send voice commands, tools selection options and DC Motor movement commands to the Arduino Mega.

## Slide 17: Constraints
Shortage of Time.
Mechanical problems.
Some electronics parts were unavailable.

## Slide 18: Future work
Enhance the selecting algorithm.
More voice commands.
Enhance the model design.
Make the robot follows the user automatically.
Apply slave-master by making a new robot, Morty.