## Slide 1: Redesign for Al Qaneer office building in Nablus city
Prepared By:
Deyaa Zyoud
Hamed Baniowda
Sameeh Mahmood
Abdul hameed Ghanem
Supervisor:
Eng. Haitham Sawalha
An-Najah National University Faculty of Engineering Building Engineering Department

## Slide 2: Contents
Introduction
Site analysis
Architectural Design
Environmental Design
Structural Design
Electro Mechanical Design
Conclusion

## Slide 3: Site Analysis

## Slide 4: Site Location
The site is located in Nablus city in AL- Bassateen area near Sufian street, Nablus is about 569 m above sea level.
Area of the land 955 m2.

## Slide 5: Site

## Slide 6: Sun path
Winter
At 12:00 am on 21/January
At 9:00 am on 21/January

## Slide 7: Sun path
Summer
At 12:00 am on 21/July
At 9:00 am on 21/July

## Slide 8: Site Analysis
Temperature

## Slide 9
Wind direction and speed
Direction of wind northern and north west and average wind speed 3.5 m/s

## Slide 10
Architectural Design

## Slide 11: Architectural Design
Al Qaneer commercial office building main spaces
Offices
Manager rooms
Meeting rooms
Cafeteria
Al Safa bank branch
Exhibitions
Parkings
Water closets
Lounge, corridors and circulation paths
Staircases
Lifts
Security room

## Slide 12
Ground floor
Function | Existing area | Standard
Corridors, Lounge | 5.7 m (width) | 1.2-1.4 m (width)
W.C | 3 | 3
Exhibition | 3 | 
Staircase and elevator |  | 30
Function | Existing area | Standard
Corridors, Lounge | 5.7 m (width) | 1.2-1.4 m (width)
W.C |  | 
Exhibition |  | 
Staircase and elevator |  | 
Function | Existing area | Standard
Corridors, Lounge | 3.15 m | 1.2-1.4 m (width)
W.C | 2.6 | 3
Staircase and elevator |  | 30
Function | Existing area | Standard
Corridors, Lounge | 3.15 m | 1.2-1.4 m (width)
W.C | 2.6 | 
Staircase and elevator |  | 
For old design

## Slide 13
Plan for basement 3, basment2 and basment1
Total area = 960

## Slide 14
Forth basement
Total area = 960

## Slide 15
First floor
Function | Existing area , width | Standard
Corridors, Lounge | 3.7 m (width) | 1.2-1.4 m (width)
W.C | 3.1 | 3
Exhibition | 36 | -
Staircase and elevator | 34 | 30
Function | Existing area , width | Standard
Corridors, Lounge | 3.7 m (width) | 1.2-1.4 m (width)
W.C |  | 
Exhibition |  | -
Staircase and elevator |  | 
Function | Existing area , width | Standard
Corridors, Lounge | 2 m (width) | 1.2-1.4 m (width)
W.C | 2 | 3
Exhibition | 42.1 | -
Staircase and elevator | 1 | 30
Function | Existing area , width | Standard
Corridors, Lounge | 2 m (width) | 1.2-1.4 m (width)
W.C |  | 
Exhibition |  | -
Staircase and elevator |  | 
For old design

## Slide 16
Second floor
Function | Existing area , width | Standard
W.C | 3.1 | 3
Staircase and elevator | 34 | 30
Cafeteria | 562 | -
exhibition | 38 | -
Function | Existing area , width | Standard
W.C |  | 
Staircase and elevator |  | 
Cafeteria |  | -
exhibition |  | -
Function | Existing area , width | Standard
W.C | 2 | 3
Staircase and elevator | 1 | 30
exhibition | 53.2 | -
Function | Existing area , width | Standard
W.C |  | 
Staircase and elevator |  | 
exhibition |  | -
For old design

## Slide 17
Typical floor
Function | Existing area, width | Standard
Corridors, Lounge | 8.7 m (width) | 1.2-1.4 m (width)
W.C | 3 | 3
Office | 3 | 12-15
Staircase and elevator | 3 | 30
Function | Existing area, width | Standard
Corridors, Lounge | 8.7 m (width) | 1.2-1.4 m (width)
W.C |  | 
Office |  | 
Staircase and elevator |  | 
Function | Existing area, width | Standard
Corridors, Lounge | 6 m (width) | 1.2-1.4 m (width)
W.C | 2 | 3
Office | 2 | 12-15
Staircase and elevator | 1 | 30
Function | Existing area, width | Standard
Corridors, Lounge | 6 m (width) | 1.2-1.4 m (width)
W.C |  | 
Office |  | 
Staircase and elevator |  | 

## Slide 18
West Elevation

## Slide 19
East Elevation

## Slide 20
  North Elevation

## Slide 21
South Elevation

## Slide 22
Section 1-1

## Slide 23
Section 2-2

## Slide 24
Evaluation for building
Function | Existing area | Standard | Comment | In old design
Office | 34 | 12-15 | Ok | -
meeting room | 3 | 12-15 | Ok | -
W.C | 3 | 3 | Ok | Not ok
exhibition | 3 |  | Ok | -
Parking | 3.5X5 m | 2 | Ok | -
Lift | 4.8 | 3.6 | Ok | Not ok (without limit)
Corridor for entrance | 5.7 m (width) | 1.2-1.4 m | Ok | not enough space to move comfortably
Function | Existing area | Standard | Comment | In old design
Office |  |  | Ok | -
meeting room |  |  | Ok | -
W.C |  |  | Ok | Not ok
exhibition |  |  | Ok | -
Parking | 3.5X5 m |  | Ok | -
Lift |  |  | Ok | Not ok (without limit)
Corridor for entrance | 5.7 m (width) | 1.2-1.4 m | Ok | not enough space to move comfortably

## Slide 25
    Environmental Design

## Slide 26
    Acoustical analysis

## Slide 27
Reverberation time (RT60)
office
cafeteria

## Slide 28
Recommended values of RT60 in office buildings

## Slide 29
Reverberation time (RT60)
At 95% occupancy | 
FREQ. | RT60
63Hz: | 0.94
125Hz: | 0.96
250Hz: | 0.89
500Hz: | 0.97
1kHz: | 0.65
2kHz: | 0.46
4kHz: | 0.47
8kHz: | 0.43
16kHz: | 0.40
Manager office
Room
(0.6-1.2)sec
RT60 recommended for office between (0.6 – 1.2)

## Slide 30
Reverberation time (RT60)
Exhibition
(1.4-2)sec
At 85 % occupancy | 
FREQ. | RT(60)
63Hz: | 0.96
125Hz: | 0.99
250Hz: | 0.94
500Hz: | 1.03
1kHz: | 0.68
2kHz: | 0.48
4kHz: | 0.48
8kHz: | 0.44
16kHz: | 0.41

## Slide 31
Reverberation time (RT60)
Cafeteria
(0.6-1)sec
At 85 % occupancy | 
FREQ. | RT(60)
63Hz: | 1.14
125Hz: | 1.02
250Hz: | 0.95
500Hz: | 1.09
1kHz: | 0.72
2kHz: | 0.52
4kHz: | 0.55
8kHz: | 0.62
16kHz: | 0.59

## Slide 32
STC for internal wall between offices
STC standard =38

## Slide 33
STC for external façade curtain wall
Curtain wall STC standard =35

## Slide 34
  Passive Analysis

## Slide 35
  Passive Analysis
Shading
Thermal analysis
Daylight

## Slide 36
Shadows from building in 21/1 at 9:00 am

## Slide 37
shadows from building in 21/7 at 9:00 am

## Slide 38: shading on the building from others
The closest building is about 30m apart
No shading on the building from others

## Slide 39
    Envelope construction details for the building
External Wall layers
U-value =0.52w/m2-k

## Slide 40
Internal Wall
U-value =1.67w/m2-k

## Slide 41
Floor layers
U-value =0.389w/m2-k

## Slide 42
Roof layers
U-value =0.389 w/m2-k

## Slide 43
Glazing
U-value =2.2 w/m2-k
properties | value
Total Solar transmission (SHGC) | 0.268
Direct Solar transmission | 0.16
Light transmission | 0.20
U-value | 2.2

## Slide 44
Thermal analysis

## Slide 45
Thermal analysis

## Slide 46
Thermal analysis

## Slide 47
Thermal analysis
Load | Value
Cooling load | 480 KW
Heating load | 161.1 KW

## Slide 48
Thermal analysis

## Slide 49
Thermal analysis
 | Total energy | Energy per total Building area(KWh/m2 ) | Energy per conditioned building area(KWh/m2 )
Total site energy | 64277.76 | 107.00 | 107.00
Total source energy | 979115.06 | 162.99 | 162.99

## Slide 50
      Daylight

## Slide 51
  Structural Aspect

## Slide 52: Design data
Cods and Standard
  ACI -318-14 for reinforced concrete structural design
  UBC -97 for seismic design.
  ASCE for load combinations.

## Slide 53: Design data
Loads
  Dead load.
  Super imposed dead load =6 kN/m2 .
  Live load = 5 kN/m2 .

## Slide 54: Design data
Seismic Loads
  The city of structure is Nablus.
  The seismic zone factor ( Z = 0.2).
  The soil profile is type .
  The acceleration seismic coefficient Ca = 0.28.
  The velocity seismic coefficient Cv = 0.4.
  The Seismic importance factor = 1.
  The structural design type is intermediate, R=5.5.

## Slide 55: Design data
Materials
  Concrete strength for slab, beams and columns f′c= 28MPa and f′c= 40MPa for footing.
  Steel yield strength Fy= 420MPa.
  Bearing capacity for soil = 250 kN/m2

## Slide 56: 3D Model form ETABS

## Slide 57: Model Checks
Compatibility check.
ناقص صورة

## Slide 58: Model Checks
Equilibrium Check.
Load Case | ETABS | Manual | Error % | Status
 | KN |  |  | 
Dead | 132261 | 131944 | 0.5 | ok
Live | 43519 | 44980 | 3.35 | ok
SID | 55370 | 58155 | 4.3 | ok

## Slide 59: Model Checks
Internal forces check.
  Done for 2 samples of slab strip, beams and columns within difference less than 10%

## Slide 60: Model Checks
Deflection checks.
  Limit =
  Maximum deflection for slab= 33.8mm.
  So, its ok.

## Slide 61: Model Checks
Modal participation mass ratio checks.
Period check.
Period from ETABS = 1.1 sec. / Period from hand calc.= 0.71sec
T from ETA BS < 140% from hand calc.
1.1 sec. > 0.997 sec.
NOT OK.

## Slide 62: Model Checks
Base shear check.
V manual = 15047
Vx =15735.67 kN > 15047 kN  Ok.
Vy= 15216.71 kN > 15047 kN  Ok.
Drift check.
#STORY |  | Limitation | state
10 | 65.45 | 70 | OK
#STORY |  | Limitation | state
10 | 65.45 | 70 | OK

## Slide 63: Structure Design (Results)
Sections Dimensions.
Member | Width | Depth
Slabs (Solid) | 25cm | 
Sabs (Ribbed) | 40cm | 
Beams (Main) | 90cm | 40cm
Beams (secondary) | 50cm | 40cm
Columns (rectangular) | 120cm | 70cm
Columns (circular) | 100cm | 
Shear Walls | 30cm | 

## Slide 64: Structure Design (Results)
Basement floor for slab & beams distributions.

## Slide 65: Structure Design (Results)
Ground floor slab & beams distributions.

## Slide 66: Structure Design (Results)
First floor for slab & beams distributions.

## Slide 67: Structure Design (Results)
Typically floor for slab & beams distributions.

## Slide 68: Structure Design (Results)
Section for tow way solid slabs.

## Slide 69: Structure Design (Results)
Section for tow way ribbed slabs.

## Slide 70: Structure Design (Results)
Beam reinforcement for B.F.(Y direction)

## Slide 71: Structure Design (Results)
Beams reinforcement for G.F, F.F and T.F.(X direction)

## Slide 72: Structure Design (Results)
Beams reinforcement for G.F, F.F and T.F.(Y direction)

## Slide 73: Structure Design (Results)
Columns reinforcement for B.F & S1,2,3.

## Slide 74: Structure Design (Results)
Columns reinforcement for B.F & S1,2,3.

## Slide 75: Structure Design (Results)
Columns reinforcement for B.F & S1,2,3.

## Slide 76: Structure Design (Results)
Columns reinforcement for S4,5,6.

## Slide 77: Structure Design (Results)
Footing.

## Slide 78
Electro mechanical system analysis

## Slide 79
Water supply system
Water consumption
Drainage system
HVAC system
Firefighting system
Elevator system
Mechanical Design

## Slide 80
    Water supply system
Pipe | Required diameter | Actual diameter
Vertical feeder | 2.5" | 3/4"and 1/2"
Horizontal pipe | 2" | 3"
Branch pipe | 0.75" | 0.62"
  Old water supply system

## Slide 81
    Water supply system
Pipe | Diameter
Vertical feeder | 1.5"
Horizontal pipe | 1"
Branch pipe | 1/2"
  New water supply system

## Slide 82
    Water consumption by people 45-70 litter for cold water
    Water consumption by people 10 litter for hot water
    Total number of people 500 person /day
    Total amount of cold fresh water 35 CM
    Total amount of hot water 5CM
    Water consumption by firefighting 10.5 CM
    Water consumption

## Slide 83
    Water drainage system
Pipe | Diameter
Vertical pipe | 4"
Horizontal pipes (lavatory) | 2"
Horizontal pipes (kitchen sink) | 2"
Horizontal pipes (W.C) | 4"
Pipes between manhole | 6"
    Old Water drainage system

## Slide 84
    Water drainage system
Pipe | Diameter
Vertical pipe | 4"
Horizontal pipes (lavatory) | 2"
Horizontal pipes (kitchen sink) | 2"
Horizontal pipes (W.C) | 4"
Pipes between manhole | 6"
    New Water drainage system

## Slide 85
    Water drainage system

## Slide 86
    Rainwater drainage system

## Slide 87
    HVAC system
VRF system was used.
Main component of VRF system is:
1. Outdoor unit
  2. Fan coil (indoor units)
  3. Ducts
  4. Diffusers
  5.Colector

## Slide 88
VRF Design
Cooling load for building = 480 kW
Outdoor unit was selected from Samsung Company.
    HVAC system
It was chosen four outdoor unit with capacity of total building capacity 137 ton DVM S, each outdoor unit 36 ton.

## Slide 89
    HVAC system
VRF Design:
Balance pressure drop method was used to find duct sizing.
For cafeteria, cooling load = 32.6KW so that the volumetric flow rate =1.71m3/s
So that, the Fan coil unit selected from TROX UK (FCU) Type PWX with volumetric flow rate 1.75 m3/s.
Kvadra diffuser was selected from Systemair Company with volumetric flow rate 0.1m3/s.

## Slide 90
    HVAC system
Duct | ύ | v | Dimeter | ΔP/El
AB | 1.71 | 5 | 0.65 | 0.35
BC | 1.41 | 3.5 | 0.56 | 0.35
CD | 1.31 | 3.3 | 0.52 | 0.35
DE | 1.11 | 3 | 0.49 | 0.35
EF | 1.01 | 2.8 | 0.46 | 0.35
FG | 0.81 | 2.5 | 0.41 | 0.35
Size of duct
Duct | ύ | v | Dimeter | ΔP/El
BI | 0.1 | 3 | 0.22 | 0.9
B1 | 0.1 | 2.8 | 0.2 | 0.88
C2 | 0.1 | 3 | 0.23 | 0.98
D6 | 0.1 | 3.1 | 0.23 | 1.13
D3 | 0.1 | 3.3 | 0.22 | 1.2
E4 | 0.1 | 3.3 | 0.2 | 1.17
F5 | 0.1 | 3.4 | 0.19 | 1.25
F7 | 0.1 | 3.4 | 0.19 | 1.28
GH | 0.1 | 3.7 | 0.17 | 1.41
Size of branch duct

## Slide 91
    HVAC system
Distribution of HVAC system at second floor

## Slide 92
Firefighting system

## Slide 93
Automatic sprinkler system
Extinguisher
Hose station
Warning signs
Heat detectors

## Slide 94
Distribution of fire suppression system
Ground floor
Typical floor

## Slide 95
Distribution of fire alarm system and egress sign
Ground floor
Typical floor

## Slide 96
Elevators design
Previous number of elevator = 2
New number of elevators = 4
Car capacity = 2000 Lb
Car speed = 600 fpm
PHC (%) = 11
I = 29.7 sec

## Slide 97
Electrical and lighting system

## Slide 98
  Luminaire used

## Slide 99
Lighting Results
Office assessment | Illuminance (Lux) | glare | uniformity
Standards | 500 | 19 | 0.6
Result | 1300 | 10.4 | 0.65
exhibition assessment | Illuminance (Lux) | glare | uniformity
Standards | 500 | 19 | 0.6
Result | 621 | 18.1 | 0.7

## Slide 100
  3D – rendering view (office)

## Slide 101
  3D – rendering view (exhibition)

## Slide 102
  3D – rendering view (parking)

## Slide 103
  Artificial Lighting
Luminaries distribution in Basement lighting

## Slide 104
  Artificial Lighting
Luminaries distribution in Ground floor lighting

## Slide 105
  Artificial Lighting
Luminaries distribution in First floor lighting

## Slide 106
  Artificial Lighting
Luminaries distribution in Second floor lighting

## Slide 107
  Artificial Lighting
Luminaries distribution in Typical floor lighting

## Slide 108
  socket
Socket distribution in Ground floor

## Slide 109
  socket
Socket distribution in First floor

## Slide 110
  socket
Socket distribution in Second floor

## Slide 111
  socket
Socket distribution in typical floor

## Slide 112
    Reflected ceiling plan

## Slide 113
Quantity Survey
Stage | Cost
Structural work | 5748883.84 NIS
Finishing | 4664908.8 NIS
Mechanical work | 2602628 NIS
Electrical work | 237608NIS
Total project cost | 13254028.64 NIS
Unit cost | 1190.83 NIS/m2

## Slide 114
Conclusion

## Slide 115
THANK YOU