## Slide 2
GP2-24/12/2016
Submitted to :
Dr. Imad Al-Qasem
Mrs. Reema Nassar
Prepared By : Mulook Shqeqat
Structural Design and Surveying of Quantities of Law and Media College at An-Najah National University – Nablus

## Slide 3: Outline
Objectives
Project Description.
SAP 3D model .
Design and Details .
Surveying of Quantities .

## Slide 4
College of Law and Media

## Slide 6
Objectives of Graduation Project
To build a 3D model for the structure using SAP2000 .
To design the structure based on ACI code .
To make a Surveying of Quantities for the structure.

## Slide 7
PART A : STRUCTURAL DESIGN

## Slide 8
Project Description
The Faculty of Law and Media is one of the projects that are constructed in An-Najah National University in Nablus . This college consists of one basement floor, ground floor and five top floors .
Use of floor | Height (m) | Area (m2) | Floor
Computer labs ,storage, control room and stadium | 4 | 1303.6 | Basement
Large and small classrooms with micro teaching lab | 4 | 554.32 | Ground
Large and small classrooms with psychology lab | 4 | 554.32 | First
Large and small classrooms with education technology lab | 4 | 554.32 | Second
Large classrooms with Dean Office, waiting and meeting halls | 4 | 554.32 | Third
Open offices space | 4 | 554.32 | Forth
Open offices space | 4 | 554.32 | Fifth
 |  | 448.72 | Roof
 | 28 | 5078.24 | Total

## Slide 9
The building is divided into two blocks in the basement floor and one block in the other floors .
Here are the two parts of the structure in the basement floor.

## Slide 10
Here are the block of the other floors

## Slide 11
System : Two Way Solid Slab
Thickness of slab = 20 cm for all slabs but 25 cm for roof slab .

## Slide 12
Material:
Are divided to :-
*Structural material
*Non- Structural Material

## Slide 13
Structural Material :
1-Concrete
Value | Property
28 Mpa | Compressive strength of concrete (f'c)
24.87 * 10³ Mpa | Modulus of Elasticity (Ec)
23 KN / m³ | Unit weight of plain concrete (γ)
25 KN / m³ | Unit weight of reinforced concrete (γ)

## Slide 14
2-Reinforcement Steel :

## Slide 15
Non – Structural Material
*Aggregate
*Blocks
*Masonry Stone
*Tiles
*Plaster
*Concrete Mortar

## Slide 16
Material | γ in KN/m³
Block | 12
Tiles | 26
Plastering | 23
Masonry stone | 26
Aggregate | 18
Concrete mortar | 23
Material unit weight

## Slide 17
Soil Properties
The soil in the site area for our structure is mainly rocky where footings shall be laid on natural excavated ground , where the bearing capacity of the soil based on the nature of the soil in the site is 350 KN/m² .

## Slide 18
Codes
* ACI 318-11 ( American Concrete Institute ) : building code requirements of structural concrete and commentary .

## Slide 19
Loads
Dead Load .
These include :- 1* O.W: self-weight of structural comp.
2* S.D : weight of non-structural comp.
WSD = W tile + W mortar + W fill + W plastering
WSD total = 0.78 + 0.46+ 1.8+ 0.345 =3.385 KN/

## Slide 20
Live Load .
Live Load ( kN/m^2) | Floor
4.79 | Basement
4.79 | Ground
4.79 | First
4.79 | Second
4.79 | Third
4.79 | Fourth
4.79 | Fifth
10 | Roof

## Slide 21
Load Combinations
Equation | Load combinations
(9-1) | U = 1.4D
(9-2) | U = 1.2D+1.6L+0.5(Lr or S or R)
(9-3) | U = 1.2D+1.6(Lr or S or R)+(1.0L or 0.5W)
(9-4) | U = 1.2D+1.0W+1.0L+0.5(Lr or S or R)
(9-5) | U = 1.2D+1.0E+1.0L+0.2S
(9-6) | U = 0.9D+1.0W
(9-7) | U = 0.9D+1.0E

## Slide 23
3D model represent a physical body using a collection of points in 3D space and it's a process of developing a mathematical representation of any three-dimensional surface of an object (either inanimate or living) via specialized software, in this project we use sap 2000 for modeling.
This part includes the analysis and design of each element structural ( slabs, beams, shear wall and column). The modeling building using SAP2000 by first definitions: : materials , sections as one-dimensional element (columns and beams )and two dimensional elements (slabs and shear wall ),and loads . Then draw each element relative to specific grade system on SAP2000.

## Slide 24
Block one in 3D

## Slide 25
Block one in 3D

## Slide 26
Sections of the members of the structure:-
Dimensions | Type | Section
Thick. 20 cm | Area | All slabs
Thick. 25 cm | Area | Roof slab
(40*70) | Rectangle | Beam
(50*50) & (65*65) | Square | Column
Thick. 20 cm | Area | Shear wall

## Slide 27
Material that is used in the project is reinforced concrete ( = 28 Mpa ) for beams and slabs, and reinforced concrete
( = 30 Mpa) for columns .
Material

## Slide 28
Modifier | Element
0.25 | Slab
0.35 | Beam
0.7 | Column
0.7 | Shear wall

## Slide 29
Loads on sap
* Load pattern definition

## Slide 30
* Load Combination

## Slide 31
Design and Details

## Slide 32
All Slabs on X – direction

## Slide 33
All Slabs on Y – direction

## Slide 34
Roof Slab on X – direction

## Slide 35
Roof Slab on Y – direction

## Slide 36
Beams Details

## Slide 37
Columns Details
Column 1
Column 2

## Slide 38
Footings Details

## Slide 42
PART B : SURVEYING OF QUANTITIES

## Slide 43
Methodology:
Work break down structure:

## Slide 44
1- Sub-Structural
1.1: Footing.
1.1.1 Blinding concrete under footings
1.1.2: Formwork for footing

## Slide 45
1.1.3: Steel reinforcement for footings
1.1.4: Concrete for footing

## Slide 46
2- Super-Structural.
2.1: Columns.
2.1.1: Formwork for columns
2.1.2: Steel reinforcement for columns.

## Slide 47
2.1.3: Concrete for columns.
2.2: Beams.
2.2.1: Formwork and concrete for Beams.

## Slide 48
2.2.2: Steel Reinforcement for Beams.
Beam No. | Length of bars m | No. of bars |  | Stirrups |  |  | Kg |  | 
B1 | 9.7 | 4 | 4 | 5 | 45 | 2.96 | 3453.3 | 2575.2 | 4023.7
B2 | 7.2 | 4 | 5 | 5 | 33 | 1.56 | 889.8 | 1274.3 | 2488.9
B3 | 22.2 | 7 | 8 | 20 | 476 | 1.56 | 3208.6 | 1718.9 | 3069.6
B4 | 26.7 | 7 | 8 | 5 | 130 | 2.96 | 1662.7 | 2067.4 | 3691.9
B5 | 18.8 | 4 | 4 | 5 | 91 | 2.96 | 1163.9 | 831.8 | 1299.8
B6 | 6.2 | 4 | 4 | 5 | 28 | 2.96 | 358.1 | 274.3 | 428.6
B7 | 18.8 | 4 | 5 | 5 | 91 | 2.96 | 2327.8 | 1663.7 | 3249.4
B8 | 18.8 | 4 | 5 | 5 | 91 | 2.96 | 1163.9 | 831.8 | 1624.7
B9 | 9.7 | 4 | 4 | 5 | 45 | 2.96 | 493.3 | 367.9 | 574.8
B10 | 22.2 | 9 | 11 | 20 | 476 | 2.96 | 869.7 | 315.7 | 602.9
B11 | 26.7 | 9 | 11 | 10 | 260 | 2.96 | 475.1 | 379.7 | 725.2
B12 | 6.2 | 4 | 4 | 5 | 28 | 2.96 | 51.2 | 39.2 | 61.2
B13 | 18.8 | 7 | 6 | 6.67 | 125 | 1.56 | 240.7 | 415.9 | 557.0
B14 | 18.8 | 4 | 4 | 5 | 91 | 1.56 | 87.6 | 118.8 | 185.7
 |  |  |  |  |  |  | 51904.16 |  | 
Beam No. | Length of bars m | No. of bars |  |  |  |  |  |  | 
B1 | 9.7 | 4 | 4 | 5 | 45 | 2.96 | 3453.3 | 2575.2 | 4023.7
B2 | 7.2 | 4 | 5 | 5 | 33 | 1.56 | 889.8 | 1274.3 | 2488.9
B3 | 22.2 | 7 | 8 | 20 | 476 | 1.56 | 3208.6 | 1718.9 | 3069.6
B4 | 26.7 | 7 | 8 | 5 | 130 | 2.96 | 1662.7 | 2067.4 | 3691.9
B5 | 18.8 | 4 | 4 | 5 | 91 | 2.96 | 1163.9 | 831.8 | 1299.8
B6 | 6.2 | 4 | 4 | 5 | 28 | 2.96 | 358.1 | 274.3 | 428.6
B7 | 18.8 | 4 | 5 | 5 | 91 | 2.96 | 2327.8 | 1663.7 | 3249.4
B8 | 18.8 | 4 | 5 | 5 | 91 | 2.96 | 1163.9 | 831.8 | 1624.7
B9 | 9.7 | 4 | 4 | 5 | 45 | 2.96 | 493.3 | 367.9 | 574.8
B10 | 22.2 | 9 | 11 | 20 | 476 | 2.96 | 869.7 | 315.7 | 602.9
B11 | 26.7 | 9 | 11 | 10 | 260 | 2.96 | 475.1 | 379.7 | 725.2
B12 | 6.2 | 4 | 4 | 5 | 28 | 2.96 | 51.2 | 39.2 | 61.2
B13 | 18.8 | 7 | 6 | 6.67 | 125 | 1.56 | 240.7 | 415.9 | 557.0
B14 | 18.8 | 4 | 4 | 5 | 91 | 1.56 | 87.6 | 118.8 | 185.7
 |  |  |  |  |  |  | 51904.16 |  | 

## Slide 49
2.3: Slabs.
2.3.1: Formwork for Slabs.
2.3.2: Concrete for Slabs.

## Slide 50
2.3.3: Reinforcement steel for Slabs.
Type | Weight of steel kg
7 floors on x-direction | 40962.76
7 floors on y-direction | 42346.56
Roof floor on x-direction | 5426.61
Roof floor on y-direction | 4973.39
TOTAL | 93709.33

## Slide 51
Price Calculations :

## Slide 52
FINAL PRICE = 861 424 . 4 $