## Slide 1
AN-NAJAH NATIONAL UNIVERSITY FACULTY OF ENGINEERING DEPARTMENT OF MECHANICAL ENGINEERING
Waste Fuel Burner
Prepared by:
Wajdi abu-muhsen
Khaled aamer
Ahmad Al-Hunate
Nabeel Abu-Omar
Submitted to:
Dr: Slameh Abd-Alfattah

## Slide 2: Outline:
      Introduction.
      Literature review.
      Objective.
      Constrains and standards.
      Methodology.
    Results and analysis.
    Discussion.
    Conclusion and recommendation.

## Slide 3: Introduction
A compressed air was used in the waste fuel burner instead of using the usual pump in burners, as a result it can be used in many applications in different places such as melting furnaces, water boilers and heating systems.
Waste fuel burner release more energy compared with normal burners. The waste fuel burner made from copper with simple basic design. Copper has a good resistance to corrosion.

## Slide 4
To solve the main problem in the traditional burner that represents in pump.
The traditional burner pump very sensitive to water and humidity and has a Default age, In addition to the high price.
Objectives
Introduction

## Slide 5: Litreture review:
A burner is a mechanical device that:
- Supplies required amount of fuel and air.
- Creates suitable conditions for rapid mixing of fuel and air.
- Produces a flame which transfers thermal energy to furnace.
In oil burners, oil is atomized into a fine spray by a spray nozzle and air is supplied for combustion in the spray chamber.
What is Burner ?

## Slide 6: Litreture review:
  Types of burner:
There are many different types of burner in use for various purposes and in various areas, depending on the supply of fuel and the purpose of the burner.

## Slide 7: Litreture review:
Gas Burner:
A gas burner is a device to generate a flame to heat up products using a gaseous fuel such as acetylene, natural gas or propane. Some burners have an air inlet to mix the fuel gas with air to make a complete combustion. Acetylene is commonly used in combination with oxygen, it has many applications such as soldering, brazing and welding
Oil Burner:
Heating device in which fuel oil is mixed with air under controlled conditions. In most burners oil is supplied under pressure to an atomizing nozzle to produce a fine spray, to which air is added by a motor-driven fan. As the cone shaped spray emerges from the nozzle, ignition is usually supplied by an electric spark to start burner.

## Slide 8: Constrains and standards:
The main constraints that we have in this project are:
The furnace was some of the main constraints.
some essential parts such as flow sensor or temperature sensor are not available in local market.
the device that would help start auto ignition by properly heating and igniting the air fuel mixture.

## Slide 9: Constrains and standards:
the furnace problem was solved by constructing a clay jar that resist high temperature.
The problem of sensor was solved by melting metals (a metal with known melting temperature) .
The ignition problem was solved using a propane gas that are ignited by electric spark to start the combustion process.

## Slide 10: Methodology:
Waste fuel burner use a small red cupper pipes and fittings to construct , the pipes and fittings are ( ) size in order to be fuel economy by withdraw small amount of fuel.
The red cupper was used in order to put up with high temperature without melting (melting temperature of 1084.62o in Celsius ), and doesn’t get rust or corrosion in our case.

## Slide 11: Methodology:

## Slide 15: Methodology:
How does Waste Fuel Burner works?
The air pressure controlled by regulator, the air was going through the elbow to the copper pipe.
The fuel valve control the fuel amount that goes throw tee fitting to burner body by high speed pressurized air and then mixed with air in the inner end of the nozzle.
The high speed of air make the mixture spray with assist of the tapered head and the nozzle. The tapered head is used to make complete mixture , nozzle is used to increase the speed of mixture to make spray .
principle of work:

## Slide 16: Results and Analysis
Efficiency:
As a result of experiments that was conducted on the Waste Fuel Burner using many types of fuel (diesel, waste oil and industrial fuel ) the following results were obtained:

## Slide 17: Results and Analysis
Diesel Experiment :

## Slide 18: Results and Analysis
Waste Oil Experiment :

## Slide 19: Results and Analysis
Industrial fuel Experiment:

## Slide 20: Results and Analysis
Friction Losses
In order to find the need of a fuel pump or not, the friction losses of fitting and pipes were found in following :
Note that the velocity were found from flow rate and continuity equation, diameter of the pipe = 0.006 m, then the area =3.07 m2

## Slide 21: Results and Analysis
Wall pipe losses:

## Slide 22: Results and Analysis
Fitting friction losses:

## Slide 23: Results and Analysis
Fitting friction losses:
Note that the area of the nozzle differs from the area of other fittings ,so that the velocity change.

## Slide 24: Results and Analysis
Head Pressure
H > Fitting losses
So that we don’t need pump

## Slide 25: Results and Analysis
Cost
Initial and annual running cost were found in comparison to the one the usual market burner cost, the following data shows the cost:
1-Initial cost :
The price of each peace used to construct waste fuel burner were estimated according to MANSOUR COMPANY in the following table:

## Slide 26: Results and Analysis

## Slide 27: Results and Analysis
2- Annual cost
Electricity and fuel consumption of the waste fuel burner were calculated on a year estimate based on current electric and fuel costs.
Electrical consumption :
The electrical consumption comes from the consuming of the air compressor , the compressor power of the 200 letter tow head motor is 4 hp, 1 hp equals to 0.746 k.Watt that’s equal about 2.984 Kw/hr. The compressor operates about 2 times per hour for 8 hours per day, each time operates about 12 minutes, the cost will be calculated per one year :

## Slide 28: Results and Analysis

## Slide 29: Results and Analysis
Fuel consumption:
1-Diesel consumption :
Waste fuel burner Consumes 7.6 letter per one hour , 2$/letter , operates 8 hours per day
(7.6 letter / hr) (8 hr operation) = (60.8letter / day )365= 22192 letter / year.
1 letter of diesel costs about 2$ => 44384$/ year.
2-Waste oil consumption :
Waste fuel burner Consumes 4. 6 letter per one hour , 0.285$/letter , operates 8 hours per day
(4.6 letter / hr ) (8 hr operation) = (36.8 letter / day 365)= 13432 letter / year.
1 letter of waste oil costs about 0.285$ => 3828.22 $/ year.

## Slide 30: Results and Analysis
3-Industrial fuel:
Waste fuel burner Consumes 6.4 letter per one hour , 0.857$/letter , operates 8 hours per day
(6.4 letter / hr) (8 hr operation) = (51.2 letter / day) 365= 18688 letter / year.
1 letter of Industrial fuel about 0.857$ => 16015.616 $/ year.
Total annual cost :
Electrical cost of the compressor = $478 /year, Waste oil cost = $3828.22 /year,
Maintenance = $200/year
Total annual cost per year = $4506.22 /year.

## Slide 31: Discussion
From the experiments that were done on waste fuel burner using many types of fuel to found the efficiency, the waste oil was the most effective fuel because of many reasons, most important reasons were : density and low consumption, high caloric value and low cost of the waste oil, the compression below shows this results :

## Slide 32: Discussion
After compression between types of fuel, the industrial fuel was the best type of fuel because of the high efficiency and caloric value.
After calculation friction losses, the head pressure had been found always to be greater than losses in pipe and fitting, total losses was found as:
Total friction losses = << head pressure =
From that we can conclude that the pump is not needed in the Waste Fuel Burner, and that improve the aim of the project.

## Slide 33: Discussion
If the efficiency and cost of the burner was a face of comparison between the traditional burner and waste fuel burner, then waste fuel burner serve the aim of the project especially it is a local industry with poor resources and possibilities in the country and uses many types of waste fuel.
Efficiency of usual burner = 70%-85% ,
Efficiency of waste fuel burner = 62% - 76.5%
The price of medium capacity for usual "diesel" burner about $765 -$1000 and the usual "industrial fuel" burner about $5714, although the waste fuel burner costs about $1134.

## Slide 34: Conclusion and Recommendation
Conclusion
Although temperature sensors and furnaces were not available, the efficiency of the burner were found in primitive methods by boiling a certain volume of water.
The group works on the efficiency to improve it, and arrive to the maximum possible complete combustion by control the air-fuel mixture, also the group works on the safety to avoid any harm could happen to the human using fire detecting sensor and solenoid valve and that rise the cost of the burner.
If the resources were available the way it should be the group can develop this project in different ways with high potentials and better efficiency .
The price and the need for the Waste Fuel Burner in our country make it very attractive to buy in comparison to the other alternatives in the local area.
Burner could be developed by adding double flame head but it could increase efficiency, cost and fuel consumption.

## Slide 35: Conclusion and Recommendation
Recommendation
The project can be improved by adding control unit in order to control all processes in the burner such as heating the fuel, self-ignition and improve safety by re-ignite the flame if it extinguished.
Using accurate temperature sensor to measure the exact temperature in the burner environment to make sure that it can be used in many applications.
In future the burner can be used for melting Iron if the cast furnaces and tools such as charcoal, Coke and melting-pot are available.

## Slide 36
Thank You
Any Questions ??