## Slide 1: An-Najah National University Engineering & IT Faculty Civil Engineering Department
Structural Design of the Faculty of Allied Medical Sciences in Arab American University –Jenin
By:
Ra’fat Abo Morad (11107047)
Yazan Abo Tahnat (11106029)
Under supervision of : Dr.Suhaib Salawdeh

## Slide 2: Outline:
Introduction.
Gravity and Lateral loads.
3D modeling using SAP.
Design of Slab.
Design of Beams.
Design of Columns and Shear walls.
Design of Footings and Ground Beams.

## Slide 3
INTRODUCTION

## Slide 4
The Faculty of Allied Medical Sciences
Location : Zababdeh – Jenin
4 Floors: Basement , 1st ,2nd , and 3rd floors.
Floor area : 1713 m²
Total Area : 6852 m²

## Slide 5
Floors consists:
Offices.
Lecture’s halls.
Laboratory.
Meeting rooms.
Mechanical and
Electrical rooms.

## Slide 7
Codes
ACI 318-11 (American Concrete Institute)
IBC-2012 (International Building Code)
UBC-97 (Uniform Building Code)
ASCE-2010 (American Society of Civil Engineers).
Israeli Standards SI 413
Jordanian National Building Code.

## Slide 8
GRAVITY & LATERAL
LOADS

## Slide 9
Loads
Gravity
Lateral
Seismic
Dead
live
Superimposed

## Slide 10
super imposed dead load (KN/m^2) | live load (KN/m^2) | Floor
7 | 2.5 | Basement
7 | 2.5 | Ground
7 | 2.5 | First
0.5 | 1 | Second
Block 1:
Block 2:
super imposed dead load (KN/m^2) | live load (KN/m^2) | Floor
5 | 5 | Basement
5 | 5 | Ground
5 | 5 | First
0.5 | 1 | Second
2.5 | 1 | Staircase
The perimeter walls have a superimposed load equal to 5.5 kN/m².

## Slide 11
Moment resisting
frame system
( Intermediate Reinforced
Concrete Moment Frames)

## Slide 12
Center of mass:
Eccentricity: ex = 1.11 m. , ey = 0.21 m.

## Slide 13
SDS=2/3*SMS
SMS= Fa * Ss
R
System
I
Fa→ site class(B), Ss
Ss= 2.5 *Z
Z→ site class(B)→ soil type
Risk category (III)
Use of Buildings and Structures

## Slide 14
Response spectrum
  A response spectrum is a plot of the maximum response amplitude (displacement, velocity, or acceleration) versus the modal period

## Slide 15: Seismic design factors
R= Modification factor
Cd= Deflection Amplification Factor

## Slide 16
Code | Value of base shear (Hand Calc.)(kN)
IBC-2012& Israeli code | 6473.74
UBC-97 | 6005.76
IBC-2012& ASCE-website | 13805.44
Block 2

## Slide 17
Load combinations
U = 1.4D
U = 1.2D + 1.6L + 0.5(Lr or S or R)
U = 1.2D + 1.6(Lr or S or R) + (1.0L or 0.5W)
U = 1.2D + 1.0W + 1.0L + 0.5(Lr or S or R)
U = 1.2D + 1.0E + 1.0L + 0.2S
U = 0.9D + 1.0W
U = 0.9D + 1.0E

## Slide 18
THREE DIMENSIONAL STRUCTURAL ANALYSIS

## Slide 19
Modifiers for each element
Modifier | Element
0.7 | Column
0.35 | Beam
0.35 | Slab
0.7 | Shear wall

## Slide 22
Rebar percentage
All is okay
Shear & torsion
No red elements
No problems
Strength check

## Slide 23
Compatibility of structural model

## Slide 24
Equilibrium
Load type | Hand results kN | SAP results kN | Difference %
Dead | 53098 | 52275.99 | 1.57
SD | 29337.56 | 29260.97 | 0.26
Live | 11014.5 | 11019.4 | 0.045

## Slide 25
Slab moments
The difference percentage is 5.1 %, which is less than 10%, OK.
Stress Strain relationship
(internal equilibrium)

## Slide 26
Beams moments
The difference percentage is 6.97%, which is less than 10%, OK.

## Slide 27
Lateral loads check
Seismic load, IBC
Direction | Hand calculation base shear(kN) | Sap base shear (kN)
X | 6473.74 | 7024
Y | 6473.74 | 7024

## Slide 28
Period and modal participation ratio

## Slide 30
Structural period( hand calculation)
Floor | Area (𝒎𝟐) | Mass (ton) | Δ (𝒎) | Δ𝟐 (𝒎𝟐) | Force (𝒌𝑵) | Force* Δ 𝒌𝑵.𝒎 | Mass*Δ𝟐 𝒕𝒐𝒏.𝒎𝟐
Basement | 946 | 2325 | 0.0001397 | 1.9488E-6 | 946 | 0.13206 | 4.11E-05
Ground | 946 | 2325 | 0.0003317 | 1.1002E-7 | 946 | 0.313788 | 2.21E-04
First | 946 | 2325 | 0.0005087 | 2.591 E-7 | 946 | 0.451514 | 4.77E-04
Second | 946 | 1658.26 | 0.0006495 | 4.212E-7 | 946 | 0.5566644 | 5.11E-04
𝑇𝑥=0.182 Sec
ASCE, Equation 15.4-6

## Slide 31
DESIGN OF SLAB

## Slide 32
Solid slab.
Thickness = 17 cm.
Shear on slab:
Max Vu = 46.27 kN
Vc = 86 kN
86 >46.27, so, shear is OK

## Slide 33
Steel reinforcement:
Using a uniform steel mesh with 4Ø12/ 1m (Top and Bottom) for all floors and roof.
(Negative and possitive)
When the moment exceeds 24 kN.m/m , use 8Ø12/ 1m (Top and Bottom)

## Slide 34
My : All moment less than 24 kN.m/m

## Slide 35
Mx : double the mesh in 3 spans

## Slide 37
DESIGN OF BEAMS

## Slide 38
All beams are drop beams.
Beams in structure classified to:
  Beam 1-A (B1-A) : (600/600).
  Beam 1-B (B1-B) : (600/600).
  Beam 2 (B2) : (800/600).
  Beam 3 (B3) : (600/500).
  Beam 4 (B4) : (1250/200).

## Slide 40
ACI318-11 Code requirements:
The value of moment and shear
computed by taking twice the
earthquake load in the load
combinations.
The first hoop shall be located not more than 50 mm from the face of a supporting member.
  .

## Slide 41
For shear and torsion |  | For flexure
 |  | As = ρbd
For shear and torsion |  | For flexure
 |  | As = ρbd
Equations:

## Slide 43
transverse steel (S2) | transverse steel until 2h(S1) | Longitudinal Steel |  | Dimension(h/d) | Beam ID
5Ø10/m | 9Ø10/m | 5Ø25 | Top | (600/600) | B1-A
 |  | 4Ø22 | Mid |  | 
 |  | 5Ø25 | Bottom |  | 
5Ø10/m | 9Ø10/m | 3Ø22 | Top | 600/600 | B1-B
 |  | 2Ø16 | Mid |  | 
 |  | 3Ø22 | Bottom |  | 
6Ø10/m | 8Ø10/m | 5Ø32 | Top | (800/600) | B2
 |  | 6Ø22 | Mid |  | 
 |  | 3Ø32 | Bottom |  | 
5Ø10/m | 9Ø10/m | 3Ø22 | Top | (600/500) | B3
 |  | 4Ø16 | Mid |  | 
 |  | 3Ø22 | Bottom |  | 
6Ø12/m | 6Ø12/m | 3Ø22 | Top | (1250/200) | B4
 |  | 8Ø16 | Mid |  | 
 |  | 3Ø22 | Bottom |  | 

## Slide 44
Beams sections: (On Face of Joints)

## Slide 45
Frames longitudinal sections:

## Slide 46
DESIGN OF COLUMNS AND SHEAR WALLS

## Slide 48
Two columns in the project:
1. C1: (450x450), 22 columns.
2. C2: (550x550), 36 columns.
Design methodology:-
The design based on taking the critical edge, intermediate, and corner columns of C1 and C2.
Drawing the interaction diagram for C1 and C2.
Using SAP to get the axial force and moments on each column.
Choosing the proper steel ratio.
Determining the spacing between hoops.

## Slide 49
ACI318-11 code requirements:
The value of moment and shear computed by taking 3 times the earthquake load in the load combinations.
Hoops Equations (ACI318-11):

## Slide 51
Vu(kN) | Mu (kN.m) | Pu (kN) | Dimensions (m) | Zone | Colum ID
84 | 138 | 1860 | 0.45 x 0.45 | A | C8
43 | 95 | 2038 | 0.45 x 0.45 | A | C11
24 | 11 | 2407 | 0.45 x 0.45 | A | C19
325 | 328 | 3092 | 0.55 x 0.55 | B | C39
57 | 151 | 3554 | 0.55 x 0.55 | B | C55
65 | 60.5 | 3688 | 0.55 x 0.55 | B | C58

## Slide 52
Chart: ΦMd
| 150.69999999999999 | 192.8 | 219.2 | 233.5 | 257.36 | 263.55 | 197.9 | 100.6 | 0 | 138 | 95 | 11
 | 2698 | 2274 | 1831.5 | 1328.36 | 1164.36 | 876.66 | 337.97 | -248 | -765.45 | 1860 | 2038 | 2407
P | 2901.7 | 2901.7 | 2698 | 2274 | 1831.5 | 1328.36 | 1164.36 | 876.66 | 337.97 | -248 | -765.45
The distribution of (M,P) point for checked 450mm-square columns on C1 interaction diagram
1%

## Slide 53
Chart: ΦMd
| 0 | 172.97 | 279 | 357 | 408 | 438 | 488 | 511 | 392.5 | 221.28 | 0 | 328 | 151 | 60.5
 | 4357 | 4357 | 4065 | 3445 | 2795 | 2065 | 1831 | 1431 | 622 | -209 | -1143 | 3092 | 3554 | 3688
P | 4357 | 4357 | 4065 | 3445 | 2795 | 2065 | 1831 | 1431 | 622 | -209 | -1143
The distribution of (M,P) point for checked 550mm-square columns on C2 interaction diagram
1%

## Slide 54
Using a steel ratio of 1% is safe and economical for all columns.
The longitudinal steel is:
8 18 for C1 (450 x 450).
12 18 for C2 (550 x 550).
Hoops:
For All columns: provide 8 Ø10/m at a distance of 0.7 m from the top
and bottom joints of columns, and 5 Ø10/m on mid of column.
Start with hoops at a distance of 5 cm from the face of supports.
Provide a lap splice length = 0.7 m.
The splicing of bars is made on the middle of columns.

## Slide 56
Hoops in column (10/m)

## Slide 58
Design of shear wall 6 :

## Slide 59
Minimum reinforcement in shear walls according to ACI318-11
Minimum ratio of vertical reinforcement area area, ρ, shall be:
  0.0012 for deformed bars not larger than 16mm in diameter with Fy not less than 420 MPa.
Minimum ratio of horizontal reinforcement area, ρ, shall be:
  0.002 for deformed bars not larger than 16mm in diameter with Fy not less than 420 MPa.
Vertical and horizontal reinforcement shall not be spaced farther apart than three times the wall thickness, nor farther apart than 450 mm.

## Slide 60
Equations:
  Compressive strength:

## Slide 61
Length of SW6 = 6.4 m.
Thickness of SW6 = 0.35 m (assumed previously)
  …. The thickness is accepted
Using SAP :
Vu (kN) | Muy (kN.m) | Mux (kN.m) | Pu (kN) | SW ID
2810 | 147 | 20150 | 7718 | SW6

## Slide 62
Use total cover = 40 mm.
, therefore, use the minimum horizontal steel according to ACI318-11:
Then, for each face of wall, → use 1Ø10/250 mm

## Slide 63
Chart: ØMnx
| 0 | 10109.775000000001 | 16414.425000000021 | 21144 | 24410.699999999928 | 26300.25 | 30530.25 | 32452.274999999998 | 25271.25 | 14616.3225 | 0
 | 24209.25 | 24209.25 | 23237.25 | 20174.25 | 16923.75 | 13390.5 | 11480.25 | 8656.5 | 3708.75 | -1242.75 | -6350.25
0.50% | 12104.625 | 12104.625 | 11618.625 | 10087.125 | 8461.875 | 6695.25 | 5740.125 | 4328.25 | 1854.375 | -621.375
0.75% | 18156.9375 | 18156.9375 | 17427.9375 | 15130.6875 | 12692.8125 | 10042.875 | 8610.1875 | 6492.375 | 2781.5625 | -932.0625 | -4762.6875
1% | 24209.25 | 24209.25 | 23237.25 | 20174.25 | 16923.75 | 13390.5 | 11480.25 | 8656.5 | 3708.75 | -1242.75 | -6350.25 | 7718
1%
0.75%
0.5%

## Slide 64
on the two sides.
on each side.
The total longitudinal steel in SW6 for each side =
→ Use 1Ø18/20cm, or 6Ø18mm/1m.

## Slide 65: DESIGN OF FOOTING

## Slide 66
Soil type : Rock.
Allowable Bearing Capacity: 300 kN/m²
Grouping of footings are shown in table below:
under column/wall | dimensions (LxB) | Number of footing | Type | Footing ID
C2,C10,C13,C14,C56 | 150 X 150 | 5 | single | F1
C3, C4, C5, C6, C9, C21, C31, C32, C33, C35, C40, C51 | 200 X 200 | 12 | single | F2
C7,C8, C18, C20, C25, C30, C41, C48, C57,C58 | 230 X 230 | 10 | single | F3
C19, C34, C45 | 250 X 250 | 3 | single | F4
SW1 , C1, C12, SW2 , C11, C22 | 1010 X150 | 2 | wall | F5
SW9,C15,C16,C17 | 760 X 200 | 1 | wall | F6
SW8 ,C43,C46,C49 | 800 X 180 | 1 | wall | F7
SW6, C44,C47,C50 | 800 X 220 | 1 | wall | F8
SW7,C52,C53,C54,C55 | 1160 X 250 | 1 | wall | F9
SW5,C42 | 400 X 250 | 1 | wall | F10
C26,C27 | 400 X 200 | 1 | Combined | F11
SW4,C36,C37,C38,C39 | 1240 X 300 | 1 | Continuous | F12
SW3 ,C32,C24,C28,C29 | 1160 X 670 | 1 | Mat | F13

## Slide 68: Design of Footing F4
Maximum load on F4 comes from C19.
Ultimate load(1.4D) (kN) | Ultimate load(1.2D+1.6L) (kN) | Service load(kN) | Live load (kN) | Dead Load | Footing Dim. | Column Dim. | Footing ID | Column ID
1869 | 2045.2 | 1612 | 277 | 1335 | 2.5 x 2.5 | 0.45 x 0.45 | F4 | C19
Ultimate Moment (kN.m) | Service load(kN.m) | Live Moment(kN.m) | Dead Moment(kN.m) | Footing Dim. | Column Dim. | Footing ID | Column ID
45.68 | 36.5 | 4.7 | 31.8 | 2.5 x 2.5 | 0.45 x 0.45 | F4 | C19

## Slide 69
As(mm²) | Thickness(m) | Vpu (kN) | Vp (kN) | Vu (kN) | Vc (kN) | Mu (kN.m) | Qmax (kN/m²) | Footing ID
1170 | 0.65 | 1626.8 | 1666.8 | 146.53 | 396.86 | 181.11 | 344.7 | F4
As(mm²) | Thickness(m) | Vpu (kN) |  | Vu (kN) |  | Mu (kN.m) | Qmax (kN/m²) | Footing ID
1170 | 0.65 | 1626.8 | 1666.8 | 146.53 | 396.86 | 181.11 | 344.7 | F4
Top steel | Bottom Steel
6 12 / m (15 bars along 2.5 m) | 6 16 / m (15 bars along 2.5 m)
Top steel | Bottom Steel

## Slide 70
Cross section in F4

## Slide 71
DESIGN OF GROUND BEAMS

## Slide 72
Ground beams:
- GB1 : (650/450).
- GB2 : (650/550).
Design philosophy:
By applying a 2 mm displacement at a joint under a footing that have the tallest ground beam.
Then, determine the area of steel by using a half of steel ratio resulting from the moment.

## Slide 73
Transverse steel | Top steel | Mid steel | Top steel | Vu (kN) | Mu (kN.m) | GB ID
9 10 / m | 4 18 | 4 18 | 3 18 | 516 | 982 | GB1
9 10 / m | 3 18 | 4 18 | 3 18 | 516 | 982 | GB2
Transverse steel | Top steel | Mid steel | Top steel | Vu (kN) | Mu (kN.m) | GB ID
 |  |  |  | 516 | 982 | GB1
 |  |  |  | 516 | 982 | GB2