## Slide 1: An-Najah National University Civil Engineering Department Analysis and Design of the Attil's Waterworks
Prepared by :
Ameed Heshme
Hossni Jallad
Hisham Hamad
Alaa Demide
Supervision : Dr. Abdel-fattah Hassan

## Slide 2: outline
Introduction
Objectives
Description of study area
Methodology
Software programs
analysis of existing water distribution network (review)
Design of Wastewater Collection Network
Design of waste water treatment plant
Results

## Slide 3: Introduction
Water take a great importance to humans in everyday life most of the activities we do need water. So that demand is continuously increasing, this means increasing the wastewater production, where wastewater constitutes about (80%-90%) of water demand

## Slide 4: Objectives
Analysis and redesign of existing water distribution network.
Design of Wastewater collection network that have life period of 30 years.
Design of waste water treatment plante that have life period of 30 years.

## Slide 5: Significance of the work
To supply water in the future at an adequate pressure and flow.
To get rid of wastewater in safe and healthy ways instead of cesspits.
To benefit from treated water and reuse in the field of agriculture
To have an economic design as possible for all networks.

## Slide 6: Study Area

## Slide 7: Area Description
Study area | Attil's town in the Tulkarm government
Area | 7337 dunams
Current population | 12000 capita
Topography | 100 m above mean sea level
Water recourses | Abu sabha well

## Slide 8: Methodology

## Slide 9: Software program
We conducted the analysis of water net work by using a software program is (Water CAD) , which used in graduation project 1 .
We conducted the design of sewerage network by using a software program is (Sewer CAD) , and the GPS-X for mathematical modeling, simulation, optimization and management of wastewater treatment plant

## Slide 10: Part 1: analysis of existing water distribution network (review)
In the Graduation Project 1 we analysis the water distribution network of Attil's town that is consist of junctions , pipes, one reservoir , one storage tank(100 m3).
It’s a Combination of both Branched and Looped network.
The Water peak demand =7260 m³/Day.

## Slide 11: Modeling and analysis of water distribution network

## Slide 12: Water Distribution Network

## Slide 13: Water Distribution Network
Elements | Number of the elements
Reservoir | 1
Storage tank | 1
Nodes | 300
Pipes | 329

## Slide 14: Water Distribution Network
Design constraints
Velocity in pipes (0.3 – 3) m/s.
Pressure at junctions (20-100) mH20.

## Slide 15: Results of modeling:
After run the model we get the following results:
Pressure at nodes (m H2O(

## Slide 16: Results of modeling:
Velocity in pipes (m/s)

## Slide 17: Part 2: Design of Wastewater Collection Network

## Slide 18: Waste Water Network Components
Manholes
Conduits
Outfall

## Slide 19: Waste Water Network Components
Manholes
Manholes are used for making connections, performing maintenance on underground and buried public utility including sewers and storm drains, and for inspection.
Distance between manholes varies with 30-50 m
Made of Concrete material

## Slide 20: Waste Water Network Components
Conduits (Sewage)
Sewage: the liquid waste conveyed by a sewer and may include domestic and industrial discharges as well as storm sewage and infiltration.
Made of PVC material.

## Slide 21: Waste Water Network Components
Why was the PVC material selected?

## Slide 22: Outfall
Point where wastewater discharges out of particular area usually being at lowest elevation, with looking forward a good position to construct treatment plant.

## Slide 23: Population prediction Formulas
Growth rate P=P0
Geometric growth rate P=P0
Arithmetic growth rate P=P0+kt
In our project we consider that number of population is equal to 25000 capita .
method used | (capita ) Number of population
Growth rate | 24036
Geometric growth | 16810
Arithmetic growth | 14245

## Slide 24: Load calculation
We calculated the manholes loads by preparing excel sheet after counting and estimating the number of houses expected to be present in the town in the future period.
Total load (
= * 0.85) = 8160
water consumption | 120 L/C.d
wastewater generation | 85%
infiltration rate | 20%
Maximum hourly factor | 3
design period | 30 years

## Slide 25: Hydraulic equations
In our project, we used the Manning formula in designing gravity sewer lines, which is defined as:
Q = (1/n √S
Where:
Q = Flow rate in m3/s
A = Cross sectional area of the pipe in m2
R = Hydraulic Radius of the pipe in m (Area/ wetted perimeter)
S = Slope of conduit

## Slide 26: Design Constrains for sewerage networks
Velocity :the velocity range is between (0.6-3) m/s
Slope : the slope range is between (1-12)%
Cover depth : the cover range is between (1-5) m

## Slide 27: sewerage network layout

## Slide 28: General results
After we adjusted the network in SewerCAD informed that the calculations were successful. That means that the design of the network was logical.
Number of manholes | Number of conduits | Number of outfall | Total length of conduits | Diameters of pipes | Lowest elevation | Highest elevation
820 | 820 | 1 | 29,507 m | 8,10,12,15 inch | 70 m | 152.09 m

## Slide 29: Results of velocities in conduits (m/s)
The figure below show that all velocities were within range and it's acceptable .

## Slide 30: Results of Slope in conduits (%)
The figure below show that all values of slope were within range and it's acceptable too .

## Slide 31: Results of Cover depth in conduits (m)
The problem that we faced is some conduits have cover depth more than 5m at the outfall point and it's acceptable in reality .

## Slide 32: Outfall
the amount of flow out that will be discharged from the sewerage network is 8181 .

## Slide 33: Waste water treatment plant location
Proposed locations to construct the treatment plant

## Slide 34: Waste water treatment plant location
Criteria for selection the site for wastewater treatment plant

## Slide 35: Waste water treatment plant location
After studying the suggested two sites it is expected to set up plant on the western side of the town (location 2 ) , for several important reasons :
lower of the zone About mean sea level
Stay away from the center of the city and to avoid happen any flooding
proximity as much as possible from the outfall of water drainage network
proximity the location from the valley Which passes from the town.

## Slide 36: Waste water treatment plant location
WWTP location by contour map

## Slide 37: Waste water treatment plant location
WWTP location by satellite

## Slide 38: Part 3 : Design of waste water treatment plant

## Slide 39: Introduction
After Analysis and design stage were done for Attil networks , and because of use water in domestic residences, commercial properties, and agriculture, this produces a huge amount of wastewater and this wastewater contains a wide range of contaminants so the ideal solution to dispose from these contaminants is to collect and treat it

## Slide 40: Calculation of influent flow
The amount of wastewater that discharged from the outfall is the amount of flow that will be processed within the plant .
Total load (
= * 0.85 ) = 8160
Future water consumption | 120 L/c.d
Wastewater generation | 85 %
Maximum hourly factor | 3
Infiltration | 20 %

## Slide 41: Characteristics of the plant’s influent
Assumptions
Characteristic | Value in (g/c.d) | Value in (mg/liter)
BOD5 | 50 | 490
COD | 60 | 588
COD/BOD5 | 1.2 | 1.2
TSS | 60 | 588
TKN | 6 | 59
NH3 | 4.5 | 44

## Slide 42: Characteristics of the plant’s influent
We converting the previous values as follow :
Characteristic (mg/l) =
Total average flow = population*consumption* waste water generation

## Slide 43: WWTP Elements and Processes
Preliminary Treatment
Primary Treatment
Secondary Treatment

## Slide 44: WWTP Elements and Processes

## Slide 45: plant layout

## Slide 46: Preliminary Treatment
At most plants preliminary treatment is used to protect pumping equipment and facilitate subsequent treatment processes .

## Slide 47: Preliminary Treatment
Preliminary devices
Coarse screens
Fine screens
Grit chamber

## Slide 48: Preliminary Treatment
Bar screens
Bar screens are used to retain solids found in the influent wastewater to the treatment plant. The principal role of screening is to remove coarse materials from the flow stream.

## Slide 49: Preliminary Treatment
Grit chamber
Grit chambers are long narrow tanks that are designed to slow down the flow so that solids such as sand, coffee grounds, and eggshells will settle out of the water. Grit causes excessive wear and tear on pumps and other plant equipment.

## Slide 50: Primary Treatment
A physical process.
Wastewater flow is slowed down and suspended solids settle to the bottom by gravity.
The material that settles is called sludge.
Sludge from the primary sedimentation tanks is pumped to the sludge thickener.

## Slide 51: Primary Treatment

## Slide 52: Primary Treatment
The efficiency of COD/BOD removal in primary sedimentation tank is between 30~50 % while TSS removal between 50~70%.
Criteria and standards
Overflow rate (V0) | (30-50)
Detention time (Hr) | (1-3) hour
Overflow rate (V0) | 
Detention time (Hr) | (1-3) hour

## Slide 53: Secondary Treatment
Secondary treatment is a biological process
Utilizes bacteria and algae to metabolize organic matter in the wastewater

## Slide 54: Secondary Treatment
Anoxic tank
Aeration tank
Secondary sedimentation tank

## Slide 55: Secondary Treatment
Anoxic Tank
Anoxic mixers are used as de-nitrification basins in waste water treatment plants .
Anoxic tank breaks down the nitrate in the waste to use as an oxygen source (energy source).
The oxygen is consumed by the bacteria and the nitrogen gas releases to the atmosphere.

## Slide 56: Secondary Treatment

## Slide 57: Secondary Treatment
Aeration tank: (Activated Sludge)
The main purpose from activated sludge process is to oxidizing carbonaceous biological matter, oxidizing nitrogenous matter: mainly ammonium and nitrogen in biological matter, removing nutrients.

## Slide 58: Secondary Treatment
Criteria and standards
process | BOD Loading (gBOD/m3.d) | MLSS (mg/l) | F/M Ratio (gBOD/gMLSS.d) | Aeration Period (hr)
extended aeration | 320-160 | 2000-8000 | 0.05-0.2 | 20-30

## Slide 59: Secondary Treatment
Secondary sedimentation tank
Secondary treatment is a treatment process for wastewater to achieve a certain degree of effluent quality , At this stage the BOD may be reduced to approximately (80 – 85)% of the influent level and (90-95)% suspended solids are removed .

## Slide 60: Secondary Treatment
Criteria and standards
The amount of flow that is pumped back to the end of primary tank is taken proportionally from flow that contained in the secondary tank and this percentage is between (80%-100%) .
Recycle activated sludge (RAS) = 0.8 *8200 = 6560
Overflow rate (V0) | 15-32
Detention time ( Hr) | 2-4
 | 15-32
Detention time ( Hr) | 2-4

## Slide 61: Secondary Treatment

## Slide 62: Secondary Treatment
Sludge disposal
Sludge is mostly water with lesser amounts of solid material.
Sludge treatment is focused on reducing sludge weight and volume to reduce disposal costs and reducing potential health risks of disposal options.
The choice of a sludge treatment method depends on the volume of sludge generated.

## Slide 63: Secondary Treatment
Drying beds
Drying beds is suitable for rural communities, while limited land availability
Most widely used method for sludge dewatering.
Cheap and simple method to dispose from sludge

## Slide 64: Secondary Treatment
Calculations of sludge production
Amount of sludge from P.S.T = 82 * 0.79 =64.78 /day
Amount of sludge from S.S.T = 6560 * 0.98 = 6428.8 /day
Total sludge = 64.78 + 6428.8 = 6493.58 /day
Assuming that the thickness of sludge layer in the drying bed = 20 cm
Surface area of drying bed = 6493.58 / 0.2 = 32467.9
On average the sludge needs to five days to dry and collect them until they are transferred for using in other fields such as plant fertilizer .
Total area = 32467.9*5=162339.5

## Slide 65: Results

## Slide 66: Effectiveness of removing contaminants
Characteristic | Influent (mg/l) | Effluent (mg/l) | Efficiency %
TSS | 588 | 26.79 | 95.4
COD | 588 | 42.66 | 92.7
 | 490 | 3.61 | 99.2
TKN | 59 | 1.46 | 97.5
Characteristic | Influent (mg/l) | Effluent (mg/l) | Efficiency %
TSS | 588 | 26.79 | 95.4
COD | 588 | 42.66 | 92.7
 | 490 | 3.61 | 99.2
TKN | 59 | 1.46 | 97.5

## Slide 67: Palestinian standard and specification for water (TR34-2012)

## Slide 68: Comparing finally results with specification