## Slide 1: Graduation Project
Prepared by : Mohammad Ziyad Drawi
Omar Khalid Abu Al-Wafa
Osama Amin Mashhari
Saeed Muayyad Saymeh

## Slide 2: Big Boulder Retaining Walls

## Slide 3: Graduation Project part one
The first graduation project was a theoretical study
Focused on retaining walls and their importance in civil engineering
No structural design was performed – it was research-based

## Slide 4: Advantages and Disadvantages of Big Boulder Walls
Benefits of Big Boulder Retaining Walls
Environmentally friendly (uses natural materials).
Strong and durable, requiring low maintenance.
Aesthetic appeal, blending naturally with landscapes.
Environmental Impact
Water Flow and Drainage Issues

## Slide 5: Challenges & Limitations
Challenges of Using Big Boulder Walls
Requires precise placement and heavy machinery.
Can be costly due to material transportation.
Not suitable for all soil types and conditions.

## Slide 6: Real-Life Applications
Where Are These Walls Used?
Highways & Roads: Prevents erosion and landslides.
Mountain Slopes: Stabilizes steep terrains.
Coastal Protection: Protects shorelines from wave erosion.

## Slide 7: History of Big Boulder Retaining Walls

## Slide 8: Rockery Design in Federal Road Construction
Historical use
FHWA guidelines
Key principles

## Slide 9: Causes of Rock Wall Collapse

## Slide 10: Geological Factors
Rock type and structure
Soil conditions
Slope angle

## Slide 11: Weathering
Physical weathering
Chemical weathering

## Slide 12: Human Activities
Excavation
Vibrations
Loading

## Slide 14: Solutions to Prevent Rock Wall Collapse 1. Rockfall Mitigation
Shotcrete
Rock bolts

## Slide 16
Our second graduation project focuses on retaining walls
It compares two main types
Reinforced Concrete Retaining Wall
Big Boulder Retaining Wall

## Slide 17: Project Goals
Analyze the structural behavior of both wall types.
Compare manual results with software outputs.
Recommend the best option based on site conditions.

## Slide 18: Design of Reinforced Concrete Retaining Wall
Manual design of a reinforced concrete retaining wall.
Results were compared with software output (Prokon).
Key checks: sliding, overturning, and bearing pressure.

## Slide 19: Manual vs. Prokon calculation
Manual calculations were close to the software results.
Safety factors were satisfied in both methods.
Minor differences due to calculation assumptions.

## Slide 20: Design of Big Boulder Retaining Wall
Large boulders were assumed with specific dimensions.
Manual analysis for sliding and overturning was done.
Results were compared with software modeling.

## Slide 21: Manual vs. Prokon calculation
Manual results were close to software outcomes.
Wall showed acceptable stability under expected conditions.
Big boulder walls perform well in natural terrain.

## Slide 22
Design of a Reinforced Concrete Retaining Wall
PROKON software was used for wall design
Constant value that uses it in design

## Slide 23
Preliminary dimensions for cantilever wall
Top Stem ≥ 200mm(minimum)
Bottom stem =0.1*H
Base thickness=0.1*H
Base length is about (0.33 to 0.75 )*h
Heel length ≥ 1.5*toe length

## Slide 24
In put data :
Reinforced Concrete Retaining wall with height (H1) = 6 m

## Slide 25
Reinforced Concrete Retaining wall with height (H1) = 6 m
Output data:

## Slide 26: * Reinforcing bars

## Slide 27
* input and output values
In put data |  |  | Results | 
H1 | BL (Base length) | FS slip >1.5 | FS ovt >2 | Pmax < 220 (kpa)
3 | 2.2 | 2.27OK | 6.28 OK | 54.2 OK
4.5 | 3.1 | 2.43 OK | 5.43 OK | 106.6 OK
6 | 5.6 | 2.9 OK | 13.11 OK | 120.2 OK
7.5 | 7.35 | 3.08 OK | 15.38 OK | 153.1 OK
9 | 7.9 | 2.81 OK | 11.83 OK | 170.6 OK
10.5 | 9.05 | 2.78 OK | 11.48 OK | 195.7 OK
12 | 10.2 | 2.76 OK | 11.23 OK | 220.8 OK
Pmin < 220 (kpa)
48.0 OK
56.3 OK
60.3 OK
67.8 OK
91.9 OK
107.8 OK
123.66 OK

## Slide 28
Comparing manual results with the program's design results
For reinforcing retaining wall height 6m
Prokon in put and out put data
Hand calculations:
In put data |  |  | Results | 
H1 | BL (Base length) | FS slip >1.5 | FS ovt >2 | Pmax < 220 (Kpa)
6 | 5.6 | 2.9 OK | 13.11 OK | 120.2 OK
In put data |  |  | Results | 
H1 | BL (Base length) | FS slip >1.5 | FS ovt >2 | Pmax < 220 (Kpa)
6 | 5.6 | 2.16 | 1.55 | 98.1 kPa

## Slide 29
Design of a Big Boulder Retaining Wall
Constant value that uses it in design

## Slide 30
In put data in prokon

## Slide 31
Big boulder wall with height (H1) = 4.5m
In put data
Out put data

## Slide 32
The wall was designed completely twice.
The first time, no adjustments were made to the values of Ab & X.
This table is contained input and output values without any editing
In put data |  |  |  | Results | 
H1 | Ab | X | FS slid >1.5 | FS ovt >2 | Pmax < 220
3 | 1.5 | 0.2 | 2.48 OK | 8.51 OK | 134.3 OK
4.5 | 2.25 | 0.4 | 2.30 OK | 23.60 OK | 195.3 OK
6 | 3 | 0.6 | 2.19 OK | 19.58 OK | 260.8 NOT OK
7.5 | 3.75 | 0.8 | 2.15 OK | 22.56 OK | 319.7 NOT OK
9 | 4.5 | 1 | 2.13 OK | 27.83 OK | 377.5 NOT OK
10.5 | 5.25 | 1.2 | 2.12 OK | 26.66 OK | 434.6 NOTOK
12 | 6 | 1.4 | 2.11 OK | 28.21 OK | 491.2 NOT OK

## Slide 33
In put data |  |  |  | Results | 
H1 (m) | Ab (m) | X (m) | FS slid >1.5 | FS OVT >2 | Pmax < 220
3 | 1.5 | 0.2 | 2.48 OK | 8.51 OK | 134.3
4.5 | 2.25 | 0.4 | 2.30 OK | 23.60 OK | 195.3
6 | 3.5 | 0.6 | 2.46 OK | 11.37 OK | 225.8
7.5 | 4.5 | 1 | 2.47 OK | 24.52 OK | 246.25
9 | 6.5 | 1.1 | 2.88 OK | -5.22 OK No overturning | 263.44
10.5 | 7.5 | 2 | 2.75 OK | -6.73 OK No overturning | 269.2
12 | 8 | 3 | 2.52 OK | 12.80 OK | 282.37
This table is contained input and output values after editing
The second time, some adjustments were made to the values of Ab & X.

## Slide 34
What is the purpose of changing these dimensions?
1- Reducing the pressure value on the base.
2- Ensuring that the wall is safer in terms of sliding and over turning.
Based on the final design results it has been concluded that:
All security transaction values are acceptable.
Some pressure values on the base exceeded 220 Kpa.
To solve this problem there is two suggestions:
Adding a base course layer.
Adding a concrete layer.

## Slide 35
Comparing manual results with the program's design results
For wall height 6m
In put data | Results
Prokon in put and out put data
Hand calculations:
6 | 3.5 | 0.6 | 2.46 OK | 11.37 OK | 225.8
H1 (m) | Ab (m) | X (m) | FS slid >1.5 | FS ovt >2 | Pmax < 220
In put data | Results
H1 (m) | Ab (m) | X (m) | FS slid >1.5 | FS ovt >2 | Pmax < 220
6 | 3.5 | 0.6 | 2.04 OK | 4.46 OK | 104.8

## Slide 36
Final shape for big boulder retaining wall

## Slide 37: (Concrete Retaining Walls) VS (Big Boulder Retaining Walls)
The comparison will be through these aspects:
Cost
Beauty
Construction Time
Drainage

## Slide 38
Cost
For big boulder retaining wall:
cost includes:
Transporting stones from the source
operating bulldozers
performing backfilling behind the wall
supervision.
The cost of one square meter is 400 NIS for base width ≤1.5m.
base width > 1.5m, the cost becomes double the original cost.

## Slide 40
2) For concrete retaining wall:
cost includes:
Workers' wages
Reinforcement steel
Concrete
supervision
The cost of executing one cubic meter is 1200 NIS

## Slide 41
Area of base = (0.75+0.3+1.17)*0.3=0.666m^2
Area of stem = 0.5*(0.3+0.2) * (3-0.3)=0.675m^2
Total area =0.66+0.675=1.341m^2
Volume = 1*1.341=1.341m^3
Cost = 1200*1.341=1609.2 NIS

## Slide 42
Beauty
Big boulder retaining wall
Concrete retaining wall

## Slide 43
Construction Time
Building Concrete retaining wall
Building Big boulder retaining wall

## Slide 44
Drainage
Big boulder retaining wall
Concrete retaining wall

## Slide 45: Concrete Wall vs. Big boulder Wall Best type depends on site conditions.
Concrete wall: stronger and more precise.
Big Boulder wall: faster and cheaper to construct.

## Slide 46
This is our graduation project, which represents the culmination of our academic journey in civil engineering. It is not just a scientific research, but a commitment from us as future engineers to build a safer and more sustainable world, brick by brick 🏗️🌍. Thank you for listening, and we are ready to answer your questions.