## Slide 1: An-Najah National University Faculty of Engineering Civil Engineering Department
“Software for Retaining Walls Design”
By: Azzam Allam Naji Alrandi
Supervised by: Dr. Mahmoud Dwaikat
2014/2013

## Slide 2: Content List
Introduction
The proposed Software
Theories used in the software

## Slide 3
Introduction
Retaining Walls
Retaining Walls Types
Retaining walls Importance
Retaining Walls In Palestine

## Slide 4: Retaining Walls
Retaining walls are used to hold back masses of earth or other loose material.
Retaining walls are generally made of masonry, stone, brick, Concrete, vinyl, steel or timber.

## Slide 7: Retaining Walls Types
Gravity Retaining Walls.
Semigravity Retaining Walls
Cantilever Retaining Walls
Counterfort Retaining Walls.
Rockery Retaining Walls.

## Slide 8: Gravity Retaining Walls
They depend for stability on their own weight and any soil resting on the masonry
They are constructed with plain concrete or stone masonry
This type of construction is not economical for high walls more than 3m

## Slide 9: Semigravity Retaining Walls
When minimizing the size of wall sections is required
Small amount of steel may be used for the construction of gravity walls

## Slide 10: Cantilever Retaining Walls
They are made of reinforced concrete that consists of a thin stem and a base slab
This type of wall is economical to a height of about 8 m

## Slide 11: Counterfort Retaining Walls
They are similar to cantilever walls
They have thin vertical concrete slabs known as counterforts that tie the wall and the base slab together
The purpose of the counterforts is to reduce the shear and the bending moments and to use it for great height.

## Slide 12: Rockery Retaining Walls
They are composed of large blocks of stacked rock.
These rocks are heavy enough and dimensionally adequate to form a structure that resists overturning and sliding forces.
Rockeries can be treated as gravity walls

## Slide 13: Retaining Walls Importance
Retaining Walls hold back the earth.
Retaining Walls give more usable Land.
Retaining Walls keep the ground from washing away.

## Slide 14: Retaining Walls Importance
Retaining Walls Save human Lives
Retaining Walls Protect property
Retaining Walls protect near structures

## Slide 15: Proper Design Importance of Retaining Walls

## Slide 16: Proper Design Importance of Retaining Walls

## Slide 17: Proper Design Importance of Retaining Walls

## Slide 18: Proper Design Importance of Retaining Walls

## Slide 19: Proper Design Importance of Retaining Walls

## Slide 20: Proper Design Importance of Retaining Walls

## Slide 21: Proper Design Importance of Retaining Walls

## Slide 22: Retaining Walls In Palestine
In Palestine using retaining walls is very common because of :
The mountainous topography.
The familiarity for workmanship and
The availability of its materials

## Slide 23
The Proposed Software
Existing Software
Proposed Software
Comparison

## Slide 24: Existing Software
Two Types :
Based on exact calculations.
Based on finite element meshing and discretization.

## Slide 25: Existing Software Type 1
They used specific equations for calculating pressures and internal stresses.
Thousands of programs are existed
Prokon , Masterseries..etc
The nearly Common one is Prokon

## Slide 26: Prokon Software
Prokon is not specified for retaining walls
The program can consider cantilever
Can Design for Seismic Condition
The most common use of the program is to analyses a wall with dimensions as entered

## Slide 27: Prokon Software
It allows the user to choose between the Rankine and Coulomb theories.
A water table can be specified; it may even be taken above the soil surface to model a liquid retaining wall
Functions are available to optimize certain wall dimensions, e.g. the depth of the toe needed to resist sliding

## Slide 28: Existing Software Type 2
Based on finite element meshing and discretization, which solves the problem by numerical schemes.
These program required a well understanding of finite element principles by the user that working with it.
The most common programs SAP2000/SAFE

## Slide 29: SAP2000 Software
This program and all the finite element program are not advisable since unnecessarily overkill and very hard are needed to accurately model
It’s a tedious, time consuming and very complex to use SAP in the design of retaining walls
SAP2000 is not meant for retaining wall structures, but rather too general to be used.
For additional information refer to the report pg. 2-3

## Slide 30: Proposed Software
It’s a dedicated program that will be developed for Palestinian local use
Various types of retaining walls will be considered, each type needs a whole separated software (Gravity,Cantilever,Counterfort,Rockery).
The program will design for seismic condition in a very modern way
Hydrostatic and hydrodynamic analysis in the proposed software will be considered

## Slide 31: Proposed Software
The program will deal with more than a soil layer.
It allows the user to choose between the Rankine and Coulomb theories in static Design
It allows the user to choose between Pseudo dynamic and Pseudo Static approaches In the seismic Design

## Slide 32: Proposed Software
In Seismic design of Gravity retaining wall, two options are available for the user
The program will allow the user to design a Gravity Wall based on a preselected displacement
or neglected one (no significant movement).
This software stands basically on the modern ways for design of retaining walls.
The software checks the geotechnical and structure aspects requirements

## Slide 33: Proposed Software
The program let you enter a numerical value of the desired dimensions
or by modifying graphical drawing of the wall dynamically via up-down numeric bottom.
The program Can OPTIMIZE

## Slide 34: Proposed Software
An optimization option for certain selected dimensions is available
A fully dimensions optimization is also provided saving 25-40% of the total cost
In the case of reinforced wall structure the software will gives you the most economical amount of steel that satisfy the structure design.
The software will be user-friendly and flexible

## Slide 35: Proposed Software
The software can consider surcharge loads
The software provides an option for calculating the bearing capacity under seismic conditions
The program can consider Line and point loads
The software will consider dynamic pressure for saturated fill

## Slide 36: Proposed Software
The software will consider changeable angle of the backfill.
The software will also consider changeable angle of the back face of the wall.
The program will provide a detailed reinforced section ready to be constructed
The program will provide summary sheet

## Slide 38: Comparison
A comparison between Prokon and the proposed software will be presented here

## Slide 39
Features | Prokon | Proposed Software
Wall Types | Cantilever | Gravity,Cantilever,Counerfort, Rockery
Lateral pressure in static conditions | Rankine coulomb | Rankine coulomb
Lateral pressure in seismic conditions | Pseudo Static | Pseudo Static Pseudo Dynamic
Water Pressure | Hydrostatic | Hydrostatic Hydro Dynamic
Dynamic pressure of Saturated soil | No consideration | Considered
Seismic Bearing Capacity | Entered by the user | Could be calculated
Optimization Limit | Certain and limited | Fully Optimization
Area of steel optimization | Not Available | Available
Optimization mechanism | Some Functions | Artificial Intelligence Algorithms

## Slide 40
Theories used in the software (some selected)
Lateral Earth Pressure
Hydrodynamic Water Pressure
Bearing capacity under seismic condition
Seismic Design Consideration
Optimization

## Slide 41: Lateral Earth pressure
Lateral Earth Pressure In Static Conditions
A at Rest
Rankine Theory
Coulomb Theory
Lateral Earth Pressure In Seismic Conditions
Pseudo Static
Pseudo Dynamic

## Slide 42: Lateral earth pressure in Static Conditions
The wall may be restrained from moving (a).
The wall may tilt away from the soil that is retained (b).
The wall may be pushed into the soil that is retained (c).

## Slide 43: Lateral earth pressure at Rest
If the wall is at rest and is not allowed to move at all, either away from the soil mass or into the soil mass (i.e., there is zero horizontal strain), the lateral pressure at a depth z is

## Slide 44: Rankine Lateral Active earth pressure
If a wall tends to move away from the soil a distance ∆x

## Slide 45: Rankine’s Lateral Active earth pressure
The soil pressure on the wall at any depth will decrease
The Active force per unit length of the wall can be determined from the area of the pressure diagram

## Slide 46: Rankine’s Passive Earth Pressure
If the wall is pushed into the soil mass by an amount ∆x

## Slide 47: Rankine Passive Earth Pressure
The horizontal stress will increase
The passive force per unit length of the wall can be determined from the area of the pressure diagram

## Slide 48: Coulomb’s Active Earth Pressure:
Coulomb proposed a theory for calculating the lateral earth pressure on a retaining wall with granular soil backfill.
This theory takes wall friction into consideration.

## Slide 49: Coulomb’s Active Earth Pressure:
In the actual design of retaining walls, the value of the wall friction angle δ is assumed to be between ϕ`/2 and 2/3ϕ`
This active force, Pa, can be calculated as shown to the right

## Slide 50: Coulomb’s Passive Earth Pressure:
Coulomb theory can also be used to calculate passive pressure

## Slide 51: Coulomb’s Passive Earth Pressure:
The Passive earth pressure by coulomb is given by
In the actual design of retaining walls, the value of the wall friction angle δ is assumed to be between ϕ`/2 and 2/3ϕ`

## Slide 52: Lateral earth pressure in Seismic Conditions
Pseudo Static
Pseudo Dynamic
Study of seismic earth pressure is essential for the safe design of retaining wall in the seismic zone,
The most two common approaches for this purpose are

## Slide 53: Pseudo Static
Okabe (1926) and Mononobe and Matsuo (1929), had the first pioneer research in determining the seismic active earth pressure due to earthquake loading this conventional work is known as Mononobe–Okabe method
Mononobe-Okabe Considers the dynamic nature of earthquake loading in a very approximate way without taking any effect of time
The disruption of the pressure behind the wall is assumed to be linear
It neglects many important factors that should be taken in the case of seismic analysis

## Slide 54: Pseudo Static
The additional forces acting on the soil failure wedge are khW and kvW in the horizontal and vertical direction respectively
kh and kv may be defined as

## Slide 55: Pseudo Static
The relation for the active force per unit length of the wall (Pae) can be determined as Mononobe–Okabe solution as shown
kh should be ≤ (1-kv).

## Slide 56: Pseudo Static
The relation for the active force per unit length of the wall (Pae) can be determined as Mononobe–Okabe solution as shown
To prevent shear fluidization ϕ>.

## Slide 57: Pseudo Static
The relation for the Passive force per unit length of the wall (Pap) can also be determined by M-O
The lateral passive earth coefficient

## Slide 58: Mononobe–Okabe Limitation
Mononobe–Okabe solution has some drawbacks that make the results are true in its assumption range only, and in many other practical cases, M-O method is not applicable.
1. No continues backfill slopes.
2. Cohesive soils, and
3. Rising water behind the wall
An extension of ‘‘Mononobe-Okabe’’ method for seismic design of Retaining Walls were presented in 2012 and 2013 , for more detail refer to the report pg.56

## Slide 59: Pseudo Dynamic Analysis
The time and phase difference due to finite shear wave propagation behind a retaining wall was considered.
Shear wave velocity (Vs)
Primary wave velocity (Vp)
The horizontal and vertical seismic accelerations (khg and kvg).

## Slide 60: Pseudo Dynamic Analysis
The period of lateral shaking
The time Effect
The soil Amplification
The acceleration at any depth z and time t are changing

## Slide 61: Pseudo Dynamic Analysis
The time Effect
The soil Amplification
The acceleration at any depth z and time t are changing

## Slide 62: Pseudo Dynamic Analysis
The total (static + seismic) active thrust, Pae (t) can be obtained by considering the equilibrium of the forces and hence Pae(t) can be expressed as follows

## Slide 63: Pseudo Dynamic Analysis
The lateral earth pressure coefficient can be determined by optimize Kae function to the maximum value with respect to t/T and α
So an Optimization is needed

## Slide 64: Pseudo Dynamic Analysis
The seismic active earth pressure Pae calculated by:
Pae =0.5Kaeϒ H2

## Slide 65: Bearing capacity under seismic condition
The response of a footing to dynamic loads is affected by the
(1) Nature and magnitude of dynamic loads,
(2) Number of pulses and
(3) The strain rate response of soil.

## Slide 66: Bearing capacity under seismic condition

## Slide 67: Bearing capacity under seismic condition
Shallow foundations for seismic loads are usually designed by the equivalent static approach.
The foundations are considered as eccentrically loaded with inclined load (combination of vertical + horizontal load) and the ultimate bearing capacity is accordingly estimated

## Slide 68: Bearing capacity under seismic condition
To account for the effect of dynamic nature of the load, the bearing capacity factors are determined by using dynamic angle of internal friction, which is taken as 2-degrees less than its static value.
Building Codes generally permit an increase of 33 % in allowable bearing capacity when earthquake loads in addition to static loads are used in design of the foundation

## Slide 69: Bearing capacity under seismic condition
This recommendation may be reasonable for dense granular soils, stiff to very stiff clays or hard bedrocks
But is not applicable for friable rock, loose soils susceptible to liquefaction or pore water pressure increase, sensitive clays or clays likely to undergo plastic flow.

## Slide 70: Bearing capacity under seismic condition
However, the dynamic bearing capacity is lower than the static bearing capacity. This observation is further supported by results of experimental studies on small footings on surface of sand.
Wherein dynamic bearing capacity was about 30 % lower than static bearing capacity. Therefore, the increase in bearing capacity permitted by codes should be taken with a caution.

## Slide 71: Bearing capacity under seismic condition

## Slide 72: Bearing capacity under seismic condition

## Slide 73: Bearing capacity under seismic condition
Budhu and Al-karni assumed Logarithmic failure surfaces to determine the seismic bearing capacity of soils.
They suggested modifications to the equations commonly used for static bearing capacity to obtain the dynamic bearing capacity as follows:

## Slide 74: Bearing capacity under seismic condition

## Slide 75: Pseudo Dynamic Analysis
An experimental study was also conducted by Al-Karni and Budhu on model footing to study the response under horizontal acceleration and compared the results with the approach suggested before

## Slide 76: Hydrodynamic pressure
In 1933 Westergaard presented a theory for calculating the hydrodynamic pressure, his theory applies under the following assumptions:
Free water (no backfill)
Vertical wall face
Very large (theoretically infinite) extent of water basin

## Slide 77: Hydrodynamic pressure

## Slide 78: Hydrodynamic pressure
It should be noted that the solution by Westergaard represents an approximation, which is generally on the safe side (over-estimated)
More exact solutions were derived by Werner and sundquist and Bustamante and flores

## Slide 79: Hydrodynamic pressure

## Slide 80: Hydrodynamic pressure

## Slide 81: Hydrodynamic pressure
Modification takes into account the width tank of water ,wall inclination , saturated backfill were presented In the report chapter 3,section 4

## Slide 82: Seismic Design Consideration
For Gravity and Rockery Retaining Walls since they get their strength from their own weight, the inertia forces both in horizontal and vertical direction will be considered in caution.
The inertia Forces will be consider also in Cantilever RW
For Design of Gravity Retaining Walls Under earthquake conditions, two options are available
Limited lateral displacement
Tolerable displacement

## Slide 83: Optimization
Engineering structures are always related to cost, and cost could be the most dominate factor for many cases
Retaining walls dimensions had to be proportioned, and the chosen dimensions are checked to make sure they satisfy the external and internal stability
Infinite number of solutions may exist, each combination of the dimensions represent a solution

## Slide 84: Optimization
However among these infinite solutions there is an optimum one
A factor of safety 1.5 must be achieved to satisfy the sliding stability, a factor of safety of 2 would satisfy this condition; also a factor of safety of 1.7 would be adequate.
However from an economical perspective this addition 0.3 value represent cost, additional cost.

## Slide 85: Optimization
For megastructure this additional cost could be huge, especially if a 1.5 factor of safety is possible to be achieved,
And that will be the special touch in the proposed software
Based on brand-new algorithms, this goal has been trying to be achieved for months.
The optimum dimensions of a retaining wall that satisfy the internal ,external stability and the minimum cost at the same time, were generated.

## Slide 86: Optimization
There are two general methods to optimize a function, namely
Mathematical programming and
Meta- heuristic method
The first method use gradient information to search the solution space near an initial starting point, for effective implementation of these methods, the variables and cost function of the generators need to be continuous,
Furthermore, a good starting point is vital for these methods to be executed successfully.

## Slide 87: Optimization
In many optimization problems, prohibited zones, side limits, and non-smooth or non-convex cost functions need to be considered
As a result, these non-convex optimization problems cannot be solved by the traditional mathematical programming methods
As an alternative to the conventional mathematical approaches, the meta-herustic optimization techniques have been used to obtain the global or near-global optimum solutions.

## Slide 88: Optimization
The Meta-hurstic searches are based on algorithms
Meta-hurstic solution are good, but not necessarily optimal.
Meta-hurstic do not require the derivatives of the objective function and constraints and
They are probabilistic Not deterministic.
They alleviate the need for continuous cost functions and variables used for mathematical optimization methods.
.

## Slide 89: Algorithms
Nature has always been a major source of inspiration to engineers and natural philosophers.
Many meta-heuristic approaches are inspired by solutions that nature herself seems to have chosen for hard problems.
The Evolutionary Algorithm and the Genetic Algorithm are inspired from the biological evolutionary process.
.

## Slide 90
Ant Colony Optimization

## Slide 91: Algorithms
Particle Swarm Optimization

## Slide 92: Algorithms

## Slide 93: Algorithms

## Slide 94: Charged System Search (CSS) Algorithm (Kaveh & Talatahari, January 2010)
It’s based on principles from physics and mechanics.
The governing Coulomb law from physics and the governing motion from Newtonian mechanics are the basic for this algorithm.
The electric force between charged spheres A and B causes the spheres to either attract or repel each other, and the resulting motion causes the suspended fiber to twist

## Slide 95: Charged System Search (CSS) Algorithm
Coulomb’s experiments showed that the electric force between two stationary charged particles
Is inversely proportional to the square of the separation distance between the particles and directed along the line joining them;
Is proportional to the product of the charges qi and q j on the two particles; and
Is attractive if the charges are of opposite sign, and repulsive if the charges have the same sign.

## Slide 96: Charged System Search (CSS) Algorithm
Coulomb’s law provides the magnitude of the electric force (Coulomb force) between the two point-charges as
The electric field Ei j at a point outside the sphere is defined as
The magnitude of the electric field at a point inside the sphere can be obtained using Gauss’s law. This is expressed as

## Slide 97: Charged System Search (CSS) Algorithm
The electric field of a group of charges (by superposition) can be
expressed as
Ei,j is equal to
The magnitude and direction of the resultant force on a charge q j at position r j due to the electric field of a charge qi at position ri

## Slide 98: Charged System Search (CSS) Algorithm
For multiple charged particles, this can be summarized as follows
Newtonian mechanics laws:
The motion of a particle is completely known if the particle’s position in space is known at all times
The acceleration of the particle

## Slide 99: Charged System Search (CSS) Algorithm
The displacement of any object as a function of time is obtained
approximately as
Newton’s second law
By substituting the previous two equations, we get

## Slide 100: Charged System Search (CSS) Algorithm
Methodology
In the CSS, each solution candidate Xi containing a number of decision variables (i.e.Xi={xi,j}) is considered as a charged particle.
The charged particle is affected by the electrical fields of the other agents. The quantity of the resultant ,and the quality of the movement is determined using the Newtonian mechanics laws.
It seems that an agent with good results must exert a stronger force than the bad ones, so the amount of the charge will be defined considering the objective function value, fit (i).

## Slide 101: Charged System Search (CSS) Algorithm
CSS considers a number of Charged Particles (CP). Each CP has a magnitude of charge (qi ) and as a result creates an electrical field around its space.
The magnitude of the charge is defined considering the quality of its solution, as follows:
The separation distance rij between two charged particles is defined as follows:

## Slide 102: Charged System Search (CSS) Algorithm
The initial positions of CPs are determined randomly in the search space
All good CPs can attract bad CPs and only some of bad agents attract good agents, considering following
The initial velocities of charged particles are zero

## Slide 103: Charged System Search (CSS) Algorithm
If a bad CP attracts a good CP, the exploration is provided. When a CP moves toward a good agent it improve its performance.
Moving a good CP toward a bad one may cause losing the previous good solution or at least increasing the computational cost to find a good solution.
To resolve this problem, a memory, which saves the best-so-far solution, can be considered

## Slide 104: Charged System Search (CSS) Algorithm
The value of the resultant electrical force acting on a CP is determined from
the aforementioned equation
The new position and velocity of each CP is determined considering

## Slide 105: Charged System Search (CSS) Algorithm
Where
ka is the acceleration coefficient;
kv is the velocity coefficient to control the influence of the previous velocity;
rand j 1 and rand j 2 are two random numbers uniformly distributed in the range of (0,1).
Here, m j is the mass of the jth CP which is equal to qj.
Δt is the time step and is set to unity

## Slide 106: Charged System Search (CSS) Algorithm
ka is a control parameter of the exploitation. Therefore, choosing an incremental function can improve the performance of the algorithm.
The velocity coefficient kv controls the exploration process and therefore a decreasing function can be selected.
Thus, kv and ka are defined as

## Slide 108: Validation of CSS
More than fifteen benchmark functions, comparison with another well-known algorithm, and numerical examples, were all used to test this algorithm and it shows perfect results.
From 2010 to 2012 the same authors published studies about using this algorithm in many Engineering problems, such as Trusses, Hydraulic composite open channels, tension/compression springs design, Welded beams design, Gravity retaining walls, Design of an I-shaped beam, Design of a reinforced concrete beam, and design of a Tubular column.

## Slide 109: Css In the proposed software
The CSS will be used to optimum the seismic design of gravity retaining walls, which may be expressed as

## Slide 110: Css In the proposed software
With truly much efforts have been done, I was able to modify the algorithm procedures to specified specific dimensions that wanted to be optimized and keep choice for the user to choose some fixed ones.

## Slide 111: Harmony Search (HS) Algorithm (Kang & Zong، September 2004)
It was conceptualized using the musical process of searching for a perfect state of harmony

## Slide 112: Harmony Search (HS) Algorithm
Musical performances seek to find pleasing harmony (a perfect state) as determined by an aesthetic standard, just as the optimization process seeks to find a global solution (a perfect state) as determined by an objective function
The HS meta-heuristic algorithm was derived based on natural musical performance processes that occur when a musician searches for a better state of harmony, such as during jazz improvisation

## Slide 113: Harmony Search (HS) Algorithm

## Slide 114: Harmony Search (HS) Algorithm
The optimization procedure of the HS meta-heuristic algorithm, which consists of Steps as follows
Step 1. Initialize the optimization problem and algorithm parameters.
Step 2. Initialize the harmony memory (HM).
Step 3. Improvise a new harmony from the HM. Step 4. Update the HM.
Step 5. Repeat Steps 3 and 4 until the termination criterion is satisfied.

## Slide 115: Harmony Search (HS) Algorithm

## Slide 116: Harmony Search (HS) Algorithm
In Step 2, (HM) ‘‘Harmony memory’’ matrix s filled with randomly generated solution vectors and sorted by the values of the objective function, f(x).
In Step 3, a New Harmony vector, x` =(x`1; x`2; . . . x`N ) is generated from the HM based on memory considerations, pitch adjustments, and randomization,

## Slide 117: Hs In the proposed software
The Design of conventional retaining walls consists of two phases:
1. Check for stability
• Check for overturning
• Check for sliding
• Check for bearing capacity failure
2. Checking of each component for strength and the steel reinforcement

## Slide 118: Hs In the proposed software
Then the algorithm checks the wall for stability and if the dimensions satisfy stability criteria,
The algorithm calculate the required reinforcement and checks the strength.
Harmony Search algorithm tries to find the best value for each design variable to minimize the objective function.

## Slide 119: Hs In the proposed software
The objective function can be expressed as follows:
Q=Vconc×(C1+C2)+Wsteel×(C3+C4)
By considering Q`=Q/ (C1+C2), we have:
Minimize Q = Vconc + Wsteel ()
Subjected to:
FS (overturning) ≥2
FS(sliding)≥1.2
Mu ≤ (fbMn)
Vu ≤ fvVc
FS(bearing capacity)≥2

## Slide 120: Hs In the proposed software
C1 and C2 are the cost of the concrete and steel ($/Ib or $/kg), C3 and C4 are the cost of concreting and erecting reinforcement ($/Ib or $/kg).
Experience show the value of () is in the range of 0.035 to 0.045.

## Slide 121: An-Najah National University Faculty of Engineering Civil Engineering Department
“Software for Retaining Walls Design”
By: Azzam Allam Naji Alrandi
Supervised by: Dr. Mahmoud Dwaikat
2014/2013

## Slide 122: Content List
Introduction
WoD Software
Practical Example

## Slide 123: WoD Software
What Is WoD?
WoD is a new software dedicated For Retaining Walls Design
It was written Using Two programing Languages Matlab And c#
The GUI Was Designed by C# , The core via Matlab
Three Different Disciplines were Combined, Civil Engineering Computer Engineering and Information Technology.

## Slide 124: WoD Software
Various types of Retaining walls are considered, each type needs a whole separated software (Gravity,Cantilever,Counterfort).
WoD designs for Static And Seismic conditions
The software deals with Water Level
Hydrostatic and hydrodynamic analysis are considered

## Slide 125: WoD Software
The software considers dynamic pressure for saturated fill
It allows the user to choose between the Rankine and Coulomb theories in static Design
It allows the user to choose between Pseudo dynamic and Pseudo Static approaches In the seismic Design

## Slide 126: WoD Software
In Seismic design of Gravity retaining wall, two options are available for the user (Europe Code 2003)
The program will allow the user to design a Gravity Wall based on a preselected displacement
or neglected one (no significant movement).
The software checks the geotechnical and structure aspects requirements

## Slide 127: WoD Software
The software considers surcharge loads
The program considers vertical and Horizontal point loads

## Slide 128: WoD Software
An optimization option for certain selected dimensions is available
A fully dimensions optimization is also provided saving 25-40% of the total cost
In the case of reinforced wall structure the software gives you the most economical amount of steel that satisfy the structure design.
The Software Optimizes the number of bars in each meter.

## Slide 129: WoD Software
The software will consider changeable angle of the backfill.
The software also considers changeable angle of the back face of the wall.
The program provides AutoCAD detailed reinforced section ready to be constructed
The program provides summary sheet

## Slide 130: WoD Software
A database was Provided to save the users results
The software Calculates the martials quantity and cost of the corresponding Designed Retaining wall
The software can search more than a trial in each Run

## Slide 131
Features | Prokon | Proposed Software
Wall Types | Cantilever, Gravity | Gravity,Cantilever,Counerfort,
Lateral pressure in static conditions | Rankine coulomb | Rankine coulomb
Lateral pressure in seismic conditions | Pseudo Static | Pseudo Static Pseudo Dynamic
Water Pressure | Hydrostatic | Hydrostatic Hydro Dynamic
Dynamic pressure of Saturated soil | No consideration | Considered
AutoCAD Drawings | not Available | Available
Optimization Limit | Certain and limited | Fully Optimization
Area of steel optimization | Not Available | Available
Optimization mechanism | Some Functions | Artificial Intelligence Algorithms

## Slide 132: WoD Software
To WoD Software

## Slide 133: WoD Software
Practical Example:

## Slide 134: WoD Software
Present Outputs , AutoCAD + Reports

## Slide 135: WoD Software
Thank you

## Slide 137: Question ?