## Slide 1: Smart ready-mix concrete plant
Prepared by: Ameer Salam
Mosab Bani jaber
Supervisor: Dr. Samer Mayaleh

## Slide 2: Introduction
The concrete industry is important globally, especially in Palestine, where it is vital for infrastructure and reconstruction projects, contributing to the economy and creating job opportunities.
The following graph shows the percentages of factories in each region in Palestine.
Chart: 
| Jenin | Tubas and the Northern Jordan Valley | Tulkarm | Nablus | Qalqilya | Salfit | Ramallah and Al-Bireh | Jericho and the Jordan Valley | Jerusalem | Bethlehem | Hebron | North Gaza | Gaza | Dair Al Balah | Khan Younes | Rafah
Number of Factories | 11 | 1 | 6 | 8 | 5 | 3 | 8 | 2 | 6 | 12 | 16 | 5 | 7 | 8 | 1 | 10

## Slide 3: Introduction
There are two types of concrete factories in Palestine:
Dry mix concrete plant
Wet mix concrete plant
The feature | Wet concrete plant | Dry concrete plant
Mixing method | Mix all ingredients together | Mix the dry ingredients first, then add the water
The quality | Higher quality | Lower quality
The cost | Higher cost | lower price or cheaper
Flexibility | Less flexible | More flexible
Applications | Applications that require high quality Such as bridges and tunnels | Applications that do not require high quality such as sidewalks and roads

## Slide 6
Challenges encountered by ready-mixed concrete factories in Palestine:
  Inadequate control programs:

## Slide 7
2. Error in weight measurement.

## Slide 8
3. Human errors

## Slide 9: 4. Weather-related problems
Rainfall can harm concrete quality, especially during curing. Excess rainwater dilutes the mix, weakening the final product.
High humidity can slow down the curing process of concrete. Curing is essential for the development of strength and durability,

## Slide 10: Objectives
Enhance efficiency by streamlining processes
improving accuracy
reducing costs
ensuring consistent quality
increasing safety
enabling remote monitoring and control

## Slide 11: Methodology
A control system was created that simulates the real system of a concrete plant without using additional units, such as load modules and analog modules, due to their high cost.
This method is used to test the system, inspect it, and experiment with its features.

## Slide 12: Interface design for Control and Monitoring (SCADA)
The factory control interface was created using DIA View software.

## Slide 13: Chosen PLC
DVP-14 SS2
Economic and Compact PLC. Max. 480 I/O points:
Adopts 32-bit CPU
Program capacity: 8k steps/Data register: 5k words
Higher execution speed compared to the \ competition: LD: 0.35μς, ΜΟΥ: 3.4με
Built-in RS-232 and RS-485 ports (Master/Slave)
Supports standard MODBUS ASCII/RTU protocol and PLC Link function

## Slide 15: Serial Communications

## Slide 16: The difference between RS-485 and RS-232 :
The feature | RS-485 | RS-232
Definition | Multi-point communication standard | Single-ended communication standard
Wiring | Differential (twisted pair) | Single-ended
Maximum Cable Length | Up to 1200 meters | up to 20 meters
Maximum Data Rate | Up to 50 Mbps (for short distances) | Up to 20 Kbps (for short distances)
Noise Immunity | High | Low
Voltage Levels | (±1.5 to ±6)V | (±5 to ±15)V
Number of Devices | Up to 32 Master and 32 Slave | Typically one transmitter and one receiver

## Slide 17: The difference between RTU and ASCII:
The feature | RTU | ASCII
Data format | Binary | Text-based (human-readable)
Transmission Speed | Faster | Slower
Error Rate | More | less
Applications | Industrial automation, harsh environments | development

## Slide 18
RS-232

## Slide 19: Future work
Future work includes:
Developing the SCADA program and programming the PLC for the ready-mixed concrete control system.
Utilizing load cell units and adding an analog unit to network sensors like Moisture Sensors and RFID Sensors.
Employing the latest AI and machine learning technologies to optimize the control system efficiency.
Designing a user-friendly SCADA interface for easy operation and monitoring, with multiple communication options for different clients
Enhancements will focus on:
Real-time data acquisition and analysis for predictive maintenance and reduced downtime.
Integration with cloud services for remote monitoring and control worldwide.
Supporting mobile device compatibility for operational flexibility.

## Slide 20
MERCI !
Its NOT the End, Its just the beginning of a GREAT Journey…