## Slide 1
Smart Shoe
Seminar 2
Submitted To: Dr. Ra’ed Jaber
Prepared by: Sa’ed Qariab Mos’ab Naffa’a
S
mart hoe

## Slide 2
Have you ever got confused from the traditional navigation !
Not hearing the instructions clearly.
Deaf people.
S
mart hoe
Problem and Purpose
Imagine how much convenient you would be !

## Slide 3: Introduction
Our project would revolve around coming with a smart shoe prototype .
Smart Shoe provides a reliable and unique way for indoor and outdoor navigation according to the idea of haptic feedback.
Distraction-free way.
Pressure sensing unit to give accurate information about the user’s foot pressure distribution while walking, jogging or running.
S
mart hoe

## Slide 4
S
mart hoe
Android Application
Google Mapping Database
Bluetooth Chip
Vibration Motor Unit
Arduino Pro Mini
Analog I/O
3.3v power supply
3.3v power supply
5v power supply
5v power supply
Android Maps Navigation
Smart Bluetooth Sync
Serial Cable
PWM Control
Power Unit
Pressure Sensing Unit
Block Diagram

## Slide 5
S
mart hoe
Google Mapping Database
Google Mapping Database & Android App.
Extensive mapping database
Android Application
Accessibility Service
Control signals
Pairing
FSR information

## Slide 6
S
mart hoe
Bluetooth Chip
Bluetooth Chip (HC-06)
Automatic Sync in close range(30cm to 200cm).
Receives and sends Messages without significant delays.
Supports v2.0 :compatibility with all Bluetooth Supported Smartphones.
The contents of the Bluetooth Message packet are minimized.
3.3v Power supply.

## Slide 7
S
mart hoe
Arduino Pro Mini
Arduino Pro Mini 5v/16Mhz
It supports 6 PWM outputs, UART communication interfaces and up to 6 analog inputs.
This makes the Arduino Pro Mini well suited for the requirements of the device.
The small size of the Arduino Pro Mini suits our compact distributed design.
Running at clock cycle of 16MHz,and 5V power supply.

## Slide 8
S
mart hoe
Vibration Motor Unit
3.3V power supply
Microcontroller sends 6 PWM signals
Motors vibrate depending on PWM control signals sent from the microcontroller.
A single motor requires 60mA
Light weight and easy to layout.
Coin Vibration Motor

## Slide 9
S
mart hoe
Vibration Motor Unit
The Arduino has Maximum peak current capacity of 50 mA. Consequently, the total current draw for the motors unit is 360mA.
To overcome this shortcoming, we had to use an N-MOSFET to drive the vibration motor.
The purpose of the N-Channel MOSFET (NDS331N ) is to act as switch.
In our design, V(DS) = 3.3V provided by the battery.
Our design uses pull down resistor of R= 50kΩ to eliminate the floating.
VM Circuit Diagram

## Slide 10
S
mart hoe
Vibration Motors Layout

## Slide 11
S
mart hoe
Pressure Sensing Unit
5V input power supply.
Microcontroller measures analog input (0 –1023) voltage across Force Sensitive Resistor.
FSR is to measure foot pressure distribution for the arches and heels.
Pressure Sensor(FSR)

## Slide 12
S
mart hoe
Pressure Sensing Unit
FSR Circuit Diagram
FSR Layout
27KΩ
High Series Resistance: for reducing current draw and to provide a voltage sweep from 0V to 5Vacross the FSR

## Slide 13
S
mart hoe
Power Unit & Charging Cable
5V input power supply to the charger is provided by a USB cable through a two-pin charging socket.
Charging Cable
3.7V LiPO Battery

## Slide 14
S
mart hoe
Power Budget
160 mW
0 mW
1) Assuming the motor vibrates for (3-5) second every 20 seconds. 2) For 1 minute it will vibrate 3 times for 15 sec. 3)For 1 hour 900 vib*h 4)power for the VM : P=160/(60*60)=0.04 mW/h Average power consumption =900 * 0.04= 36 mW
Vibration Motor
When Running
When Sopped
Average Power Consumption

## Slide 15
S
mart hoe
Power Budget
Arduino Pro Mini
5mW when on
Average Power Consumption : 5mW
86.4mW when sending/receiving messages
3.24μW when in sleep mode
Average Power Consumption : 17.28mW
Bluetooth Chip
Pressure Sensing Unit
2.7mW at maximum feet pressure
0.24mW at minimum feet pressure
Average power consumption : 1.38mW

## Slide 16
S
mart hoe
Power Budget
Average Battery life: =Total energy stored in battery/Total average power consumption
= 3145/72.73 = 43.24212 working hours
1 day 19 hours 24 minutes and 20 seconds
Total Power =72.73 mW
Total energy stored in the battery : 850mAh = 3.7*850 = 3145 mWh

## Slide 17: pic

## Slide 18: test
video

## Slide 19: shoe

## Slide 20: result
1) FSR curve

## Slide 21
2) FSR scale :

## Slide 22
Application interface :

## Slide 23
S
mart hoe
Conclusion
We created a design for each circuit in the project .
Our biggest achievement was to know what is the smallest components to use, how to get them.
Achievements :
Uncertainties :
Although our design is extremely light weight , we aren’t sure if the users will become used to the added weight.
However, these results could be different for different people and we will have to perform further tests.

## Slide 24
S
mart hoe
Complete Circuit Scheme

## Slide 25
S
mart hoe
Bill Of Materials

## Slide 26
S
mart hoe
SWOT Analysis
Strengths
Modular Design Cost Effective User Comfort
Weaknesses
Additional shoe weight
Threats
Nike’s electronic shoes
Opportunities
Navigation Accessory
Athletics
Virtual Reality
Application Development Platform

## Slide 27
S
mart hoe
Questions !

## Slide 28
S
mart hoe
Thank You